ANNEX 1

Interference Analyses for NPOESS satellites

to METOP earth stations around 1.7 and 7.8 GHz

# GENERAL CONSIDERATIONS

An interference assessment from the meteorological satellite system NPOESS into METOP Earth stations receiving around 1.7 and 7.8 GHz has been conducted by means of the radio frequency interference assessment tool RFIAT. One METOP satellite with an orbital altitude of 825 km and an ascending equator crossing time of 21:30 hrs has been assumed. Three NPOESS satellites with orbital heights of 828 km and ascending equator crossing times of 13:30 hrs, 17:30 hrs and 21:30 hrs have been considered. All satellites transmit both in the band 1698-1710 MHz and 7750-7850 MHz and interference will therefore occur for some time when the orbital positions of the METOP and NPOESS satellites overlap. This happens in general every approximately 113 days. Minimum elevation angles of 5 degrees were assumed for all earth stations. Polarisation and atmospheric losses were not taken into account. Exact spectral overlap and Doppler effects can be taken into account with the interference assessment software so that the actual spectral interference component has been assessed.

# ANALYSIS FOR THE BAND  1698-1710 MHz

## System Characteristics and Assumptions

NPOESS satellites transmit a 12 MHz signal in broadcast mode on a centre frequency of 1704 MHz. METOP earth stations receive data within a 4.5 MHz bandwidth on the frequencies 1701.3 and 1707 MHz, respectively. Main stations with a diameter around 10 meter as well as user stations with around 2 m diameter have been considered. The key simulation parameters are given in table 1. The detailed simulation parameters for the worst case are attached in Annex 1.

|  | NPOESS | METOP |  |
| --- | --- | --- | --- |
| Orbital height | 828 | 825 | km |
| Equator crossing time (ascending) | 13:30, 17:30, 21:30 | 21:30 | hrs |
| Inclination | 98.727 | 98.714 | deg. |
| Center frequency | 1704 | 1701.3, 1707 | MHz |
| Signal bandwidth | 12 | 4.5 | MHz |
| Effective power into antenna | 13.6 | 5.5 | dBW |
| Antenna patterns | see Figure 1 | see Figure 1 | dBi |
| Earth station antenna gain | n.a. | 27, 42 | dBi |
| System noise temperature | n.a. | 150 | K |
| Required C/(N+I) | n.a. | 17 | dB |
| Required Eb/(No+Io) | n.a. | 4 | dB |

Table  1:   Key system parameters for 1.7 GHz systems

Figure  1:   Assumed satellite antenna gains

Figure 1 shows the assumed antenna gains for both satellites. For METOP, only EIRP levels were available. The antenna gains have been estimated by assuming an effective power of approximately 5.5 dBW into the antenna. This power level is based on a maximum peak power of 8 dBW and 2.5 dB feeder loss. For the carrier and data recovery loops, a technical degradation of 1 dB has been taken into account. The assumed carrier loop bandwidth is 3 kHz.

## Simulation Results

Table 2 shows a summary of the simulation results for various cases considered. High Resolution User Stations (HRUS) have been assumed at an equatorial location in Kampala and a high latitude location in Svalbard with results showing little dependency on station latitude. Main station locations are Svalbard and Mas Palomas.  The highest levels of interference occur for the 21:30 hrs equatorial crossing for both satellites as the orbits overlap approximately every 113 days. The interference around 1701.3 MHz is slightly higher than around 1707 MHz but the difference is practically insignificant.

|  | No/Io | Es/(No+Io) | C/(N+I) |
| --- | --- | --- | --- |
| NPOESS 13:30 hrs into 2m HRUS at 78° and 1701.3 MHz | 6.20% | 0.39% | 0.03% |
| NPOESS 17:30 hrs into 2m HRUS at 78° and 1701.3 MHz | 7.38% | 0.63% | 0.06% |
| NPOESS 21:30 hrs into 2m HRUS at 78° and 1701.3 MHz | 9.79% | 2.94% | 0.84% |
| NPOESS 21:30 hrs into 2m HRUS at 0° and 1701.3 MHz | 9.36% | 2.80% | 0.62% |
| NPOESS 21:30 hrs into 2m HRUS at 78° and 1707 MHz | 9.39% | 2.84% | 0.80% |
| NPOESS 21:30 hrs into 10m main station in Svalbard | 4.43% | 0.28% | 0.13% |
| NPOESS 21:30 hrs into 10m main station in Mas Palomas | 4.49% | 0.46% | 0.30% |

Table  2:   Interference percentage for various earth stations

Figure  2:   Es/(No+Io) levels at HRUS station

Figure  3:   Es/(No+Io) levels during maximum interference at HRUS station

Figure  4:   Interference density distribution at HRUS station

Figure  5:   Es/(No+Io) probability distribution at Main and HRUS stations

Figure  6:   Probability distribution for various parameters at HRUS station

Figure  7:   Probability distribution for various parameters at Svalbard main station

Figure 2 shows the obtained Es/(No+Io) levels over a full overlap period for the worst case of both satellites at 21:30 equatorial crossing time and high latitude HRUS location. Figure 3 shows a magnification of figure 2 around the maximum interference occurrence. Figure 4 shows the interference density distribution. Figure 5 shows a comparison between Es/(No+Io) results obtained for an HRUS at Svalbard, a main station at Svalbard and a main station in Mas Palomas. Figure 6 shows the probability distribution for No/Io, Es/(No+Io) and C/(N+I) for an HRUS at Svalbard. Figure 7 shows the probability distribution for No/Io, Es/(No+Io) and C/(N+I) for a main station at Svalbard.

The simulation duration for the most sensitive cases was a full overlap period (113 days) with 1 second intervals. For less sensitive cases, a time interval of 6 seconds has been selected.

It shall be noted that in this assessment, the C/(N+I) is the actually available signal to noise and interference ratio in the carrier tracking loop based on 12 dB double squaring loss with respect to the full signal power fed into the suppressed carrier recovery circuit. It is not the often erroneously used ITU terminology for C/N as the general signal to noise ratio. The actual data quality assessment is based upon the Eb/No requirements.

# ANALYSIS FOR THE BAND  7750-7850 MHz

## System Characteristics and Assumptions

NPOESS operates an HRD service in broadcast mode with a carrier frequency of 7812 MHz and a bandwidth of 35 MHz. METOP earth stations receive data within a 63 MHz bandwidth on a carrier frequency of 7800 MHz. Three main stations with a diameter between 10 and 13 meters have been considered for METOP data reception. The locations are Svalbard, Mas Palomas and Fairbanks. The key simulation parameters are given in Table 3. The detailed simulation parameters for the main station in Svalbard are attached in Annex 2.

|  | NPOESS | METOP |  |
| --- | --- | --- | --- |
| Orbital height | 828 | 825 | km |
| Equator crossing time (ascending) | 13:30, 17:30, 21:30 | 21:30 | hrs |
| Center frequency | 7812 | 7800 | MHz |
| Signal bandwidth | 35 | 63 | MHz |
| Effective power into antenna | 19 | 14.3 | dBW |
| Antenna patterns | see Figure 8 | see Figure 8 | dBi |
| Earth station antenna gain | n.a. | 55, 58.6 | dBi |
| System noise temperature | n.a. | 180 | K |
| Required C/(N+I) | n.a. | 17 | dB |
| Required Eb/(No+Io) | n.a. | 7 | dB |

Table  3:   Key system parameters for 7.8 GHz systems

Figure 8 shows the assumed antenna gains for both satellites. For METOP, a peak power level of 14.3 dBW has been assumed with feeder losses around 2.5 dB. For the carrier and data recovery loops, a technical degradation of 1 dB has been taken into account. The assumed carrier loop bandwidth is 30 kHz.

Figure  8:   Assumed satellite antenna gains

## Simulation Results

Table 4 shows a summary of the simulation results for various cases considered. Main station locations are Svalbard, Madrid and Fairbanks.  The highest levels of interference occur for the 21:30 hrs equatorial crossing for both satellites.

|  | No/Io | Es/(No+Io) | C/(N+I) |
| --- | --- | --- | --- |
| NPOESS 13:30 hrs into Svalbard | 0.003% | 0.002% | 0.000% |
| NPOESS 17:30 hrs into Svalbard | 0.007% | 0.004% | 0.000% |
| NPOESS 21:30 hrs into Svalbard | 0.954% | 0.143% | 0.066% |
| NPOESS 21:30 hrs into Madrid | 0.898% | 0.229% | 0.133% |
| NPOESS 21:30 hrs into Fairbanks | 0.978% | 0.169% | 0.084% |

Table  4:   Interference percentage for various earth stations

Figure 9 shows the obtained Es/(No+Io) levels over a full overlap period for the case of both satellites at 21:30 equatorial crossing time and the main station at Svalbard. Figure 10 shows a magnification of figure 9 around the maximum interference occurrence. Figure 11 shows the probability distribution for No/Io, Es/(No+Io) and C/(N+I) for the main station in Svalbard. Figure 12 shows a comparison between Es/(No+Io) results obtained for the 3 main station locations at Svalbard, Madrid and Fairbanks. Figure 13 shows the interference density distribution for the main station at Svalbard. The simulation duration for all cases was a full overlap period based on 113 days with 1 second intervals.

Figure  9:   Es/(No+Io) levels at Svalbard station

Figure  10:   Es/(No+Io) levels during maximum interference at Svalbard

Figure  11:   Probability distribution for various parameters at Svalbard

Figure  12:   Es/(No+Io) probability distribution at Main stations

Figure  13:   Interference density distribution at Svalbard

# Conclusions

- Worst cases are obtained when both satellites have the same equatorial crossing times as the orbits will occasionally overlap. For the selected orbit heights, this would occur approximately every 113 days.

- Significant data loss for up to 3% of time will occur around 1.7 GHz

- Data loss for up to 0.23% of time will occur around 7.8 GHz

- Interference levels and statistics are rather independent of station locations.

- Interference could be minimized by phasing the satellites in a way that they have identical orbital periods but a small orbital separation angle. This technique is already successfully applied to a number of low earth orbiting satellites operating around 8.2 GHz. At 7.8 GHz. less than 1 degree orbital separation would already be sufficient for a 10 m antenna to reduce interference levels by more than 30 dB.

Annex 1 - INTERFERENCE  ASSESSMENT  SUMMARY EXAMPLE FOR 1.7 GHz

--------------------------------------------------------------------------

Set-Up File     = METOP-NPOESS-1701-2130	 Date: 26.03.2004 - 21:52:17

Simulation time = 170.000 days 	 Time step = 1.00 s

VICTIM TRANSMITTER   =  Satellite  METOP

semimajor axis                     	 = 7203.144 km

eccentricity                       	 = 0.00000

inclination angle                  	 = 98.714 deg.

right ascension angle              	 = 322.500 deg.

argument of perigee                	 = 0.000 deg.

mean anomaly                       	 = 0.000 deg.

satellite epoch                    	 = 24.02.2004 - 12:00:00

RF power level                     	 = 8.00 dBW

feeder loss                        	 = 2.50 dB

antenna type                       	 = User-Design

maximum antenna gain               	 = 6.00  dBi

transmitter frequency              	 = 1.70130 GHz

modulation                         	 = QPSK

modulation index                   	 = 1.57  rad

rel. carrier power level           	 = -12.000 dB

rel. data power level              	 = 0.000 dB

subcarrier frequency               	 = 0.000 kHz

symbol rate                        	 = 4500.000 ks/s

VICTIM RECEIVER   =  Earth Station  Svalbard

location longitude                 	 = 16.033 deg.

location latitude                  	 = 78.158 deg.

location altitude                  	 = 0.100 km

minimum elevation                  	 = 5.000 deg.

noise temperature                  	 = 150.00 K

antenna type                       	 = Parabolic-APP 8

maximum antenna gain               	 = 27.12 dBi

antenna diameter                   	 = 1.80 m

antenna efficiency                 	 = 50.00 %

RF data bandwidth                  	 = 4500.000 kHz

data loop degradation              	 = 1.000 dB

carrier loop bandwidth             	 = 3.000 kHz

carrier loop degradation           	 = 1.000 dB

INTERFERING TRANSMITTER  - 1  = Satellite  NPOESS

semimajor axis                     	 = 7206.144 km

eccentricity                       	 = 0.00000

inclination angle                  	 = 98.727 deg.

right ascension angle              	 = 322.500 deg.

argument of perigee                	 = 0.000 deg.

mean anomaly                       	 = 0.000 deg.

satellite epoch                    	 = 24.02.2004 - 12:00:00

RF power level                     	 = 13.60 dBW

antenna type                       	 = User-Design

maximum antenna gain               	 = 6.00  dBi

transmitter frequency              	 = 1.70400 GHz

modulation                         	 = QPSK

modulation index                   	 = 1.57  rad

rel. carrier power level           	 = -12.000 dB

rel. data power level              	 = 0.000 dB

subcarrier frequency               	 = 0.000 kHz

symbol rate                        	 = 12000.000 ks/s

RF interferer bandwidth            	 = 12000. kHz

Polarisation discrimination        	 = 0.0 dB

Environmental attenuation          	 = 0.0 dB

Continuous Interference Transmission     = ON

INTERFERING RECEIVER  -   1  = Earth Station  Svalbard-NPOESS

location longitude                 	 = 15.450 deg.

location latitude                  	 = 78.220 deg.

location altitude                  	 = 0.100 km

minimum elevation                  	 = 5.000 deg.

Objective Criterion:     Io          	 = -182.8 dBW/kHz

Interferer main lobe approximation     	 = ON

Interferer full spectrum calculation   	 = OFF

Doppler Assessment at Victim Receiver  	 = ON

Earth Oblateness Compensation          	 = ON

Victim RX is in view of Victim TX for         22509.70 min  =    13.83 %

Victim RX has a link to Victim TX for         17502.90 min  =    10.76 %

Victim RX is in view of Interferer   1        22556.70 min  =    13.86 %

Active Victim RX is in view of Interferer      2499.20 min  =    1.54 %

Interfering RX is in view of Interferer       22569.00 min  =   13.87 %

Active Victim RX receives Interference         2499.20 min  =    1.54 %

No/Io        Es/Io      Es/(No+Io)     C/(N+I)

-------------------------------------------------

Objective Criterion in dB               5.96        10.97         4.00        17.00

Objective Criterion not met             9.7887%      3.7325%      2.9378%      0.8404%

Maximum criterion deviation (dB)       28.88        17.54        13.59         3.85

Number of events with criteria not met   306          150          134           41

Total duration of such events (min)  1713.30       653.30       514.20       147.10

Shortest event duration      (min)      0.10         0.10         0.10         0.10

Longest event duration       (min)     12.90        12.90        12.90        12.50

Average duration of events   (min)      5.60         4.36         3.84         3.59

Number of events with criteria met       252           96           83           20

Shortest event duration      (min)      0.10         0.10         0.10         0.10

Longest event duration       (min)  13857.60     16106.20     16346.90     17250.10

Average duration of events   (min)     62.66       175.52       204.68       867.79

Annex 2 - INTERFERENCE  ASSESSMENT  SUMMARY EXAMPLE FOR 7.8 GHz

--------------------------------------------------------------------------

Set-Up File     = METOP-NPOESS-7800-2130-SVB-1s	 Date: 27.03.2004 - 15:09:48

Simulation time = 170.000 days 	 Time step = 1.00 s

VICTIM TRANSMITTER   =  Satellite  METOP

semimajor axis                     	 = 7203.144 km

eccentricity                       	 = 0.00000

inclination angle                  	 = 98.714 deg.

right ascension angle              	 = 322.500 deg.

argument of perigee                	 = 0.000 deg.

mean anomaly                       	 = 0.000 deg.

satellite epoch                    	 = 24.02.2004 - 12:00:00

RF power level                     	 = 14.30 dBW

feeder loss                        	 = 2.50 dB

antenna type                       	 = User-Design

maximum antenna gain               	 = 6.00  dBi

transmitter frequency              	 = 7.80000 GHz

modulation                         	 = QPSK

modulation index                   	 = 1.57  rad

rel. carrier power level           	 = -12.000 dB

rel. data power level              	 = 0.000 dB

subcarrier frequency               	 = 0.000 kHz

symbol rate                        	 = 63000.000 ks/s

VICTIM RECEIVER   =  Earth Station  Svalbard

location longitude                 	 = 16.033 deg.

location latitude                  	 = 78.158 deg.

location altitude                  	 = 0.100 km

minimum elevation                  	 = 5.000 deg.

noise temperature                  	 = 180.00 K

antenna type                       	 = Parabolic-APP 8

maximum antenna gain               	 = 55.07 dBi

antenna diameter                   	 = 10.00 m

antenna efficiency                 	 = 48.00 %

RF data bandwidth                  	 = 63000.000 kHz

data loop degradation              	 = 1.000 dB

carrier loop bandwidth             	 = 30.000 kHz

carrier loop degradation           	 = 1.000 dB

INTERFERING TRANSMITTER  - 1  = Satellite  NPOESS

semimajor axis                     	 = 7206.144 km

eccentricity                       	 = 0.00000

inclination angle                  	 = 98.727 deg.

right ascension angle              	 = 322.500 deg.

argument of perigee                	 = 0.000 deg.

mean anomaly                       	 = 0.000 deg.

satellite epoch                    	 = 24.02.2004 - 12:00:00

RF power level                     	 = 19.00 dBW

antenna type                       	 = User-Design

maximum antenna gain               	 = 6.00  dBi

transmitter frequency              	 = 7.81200 GHz

modulation                         	 = QPSK

modulation index                   	 = 1.57  rad

rel. carrier power level           	 = -12.000 dB

rel. data power level              	 = 0.000 dB

subcarrier frequency               	 = 0.000 kHz

symbol rate                        	 = 35000.000 ks/s

RF interferer bandwidth            	 = 35000. kHz

Polarisation discrimination        	 = 0.0 dB

Environmental attenuation          	 = 0.0 dB

Continuous Interference Transmission     = ON

INTERFERING RECEIVER  -   1  = Earth Station  Svalbard-NPOESS

location longitude                 	 = 15.450 deg.

location latitude                  	 = 78.220 deg.

location altitude                  	 = 0.100 km

minimum elevation                  	 = 5.000 deg.

Objective Criterion:     Io          	 = -182.0 dBW/kHz

Interferer main lobe approximation     	 = OFF

Interferer full spectrum calculation   	 = OFF

Doppler Assessment at Victim Receiver  	 = ON

Earth Oblateness Compensation          	 = ON

Victim RX is in view of Victim TX for         33865.34 min  =    13.83 %

Victim RX has a link to Victim TX for         26326.78 min  =    10.75 %

Victim RX is in view of Interferer   1        33936.45 min  =    13.86 %

Active Victim RX is in view of Interferer      3733.13 min  =    1.52 %

Interfering RX is in view of Interferer       33959.14 min  =   13.87 %

Active Victim RX receives Interference         3733.13 min  =    1.52 %

No/Io        Es/Io      Es/(No+Io)     C/(N+I)

-------------------------------------------------

Objective Criterion in dB               6.00        13.97         7.00        17.00

Objective Criterion not met             0.9540%      0.1909%      0.1433%      0.0662%

Maximum criterion deviation (dB)       39.65        24.03        20.06        11.39

Number of events with criteria not met    69           37           23            2

Total duration of such events (min)   251.15        50.27        37.72        17.42

Shortest event duration      (min)      0.02         0.02         0.03         7.78

Longest event duration       (min)     12.55         9.63         9.63         9.63

Average duration of events   (min)      3.64         1.36         1.64         8.71

Number of events with criteria met        35           30           18            2

Shortest event duration      (min)      0.02         0.03         0.02     17482.75

Longest event duration       (min)  17246.50     17439.23     17452.13     17482.75

Average duration of events   (min)    745.02       875.88      1460.50     13154.68