WORLD METEOROLOGICAL ORGANIZATION

COMMISSION FOR BASIC SYSTEMS

OPAG ON INFORMATION SYSTEMS AND SERVICES

MEETING OF THE EXPERT TEAM ON EVOLUTION OF DATA FORMATS

FINAL REPORT

MONTEREY, USA, 4-9 OCTOBER 1999

REPORT OF MEETING OF EXPERT TEAM ON EVOLUTION OF DATA FORMATS

-	CONTENTS

PAGE

1.	ORGANIZATION OF THE MEETING		 3

1.1	Opening of the Meeting		 3

1.2	Approval of the agenda		 3

2 	GRIB CODE

  - Further develop (and finalize) GRIB2 with a view to CBS final endorsement	 3

2.2	Regulations for wind coding at the North and South Poles for GRIB1 and GRIB2	 5

- STANDARD DATA FORMAT FOR EXCHANGE OF IMAGERY AND OTHER

SATELLITE PRODUCTS								 5

- DEVELOPMENT OF FILE CONTENT DESCRIPTION-METADATA

STANDARDS										 5

5.	ADDITIONS TO BUFR AND CREX							 6

5.1	Modifications required for Automatic Stations observations				 6

  - Consideration of urgent tables additions to BUFR/CREX for fast-track (to be

operational on May 2000)								 7

  - Other additions									 8

6.	RESULTS OF QUESTIONNAIRE ON WMO CODES				 8

- ENCODING AND DECODING SOFTWARE FOR BUFR/CREX AND THE

NEW EDITION OF GRIB								 9

8.	MIGRATION STRATEGY								10

- POCEDURES FOR AMENDMENT TO THE MANUAL ON CODES		11

- CLOSURE OF THE MEETING							11

ANNEX TO PARAGRAPH 1.1.1	LIST OF PARTICIPANTS				12

ANNEX TO PARAGRAPH 4.2	FILE CONTENT METADATA DESCRIPTION	15

ANNEX TO PARAGRAPH 5.1.3	ADDITIONS IN BUFR AND CREX			24

ANNEX TO PARAGRAPH 5.2.1.1	ADDITIONS TO BUFR REQUESTED BY DBCP	25

ANNEX TO PARAGRAPH 5.2.1.2	ADDITIONS FOR OCEANOGRAPHY		27

ANNEX TO PARAGRAPH 5.2.1.3	SATELLITE NUMBERS				27

ANNEX TO PARAGRAPH 5.2.1.4	REQUIREMENT FOR TCP				28

ANNEX TO PARAGRAPH 5.2.2	QUIKSCAT DATA ADDITIONS			29

ANNEX TO PARAGRAPH 5.3.1	GEOSTATIONARY SAT. RADIANCE DATA		34

ANNEX TO PARAGRAPH 5.3.2	SATELLITE DERIVED WIND COMPUTATION	35

ANNEX TO PARAGRAPH 5.3.4	ADDITION FOR RADIOLOGICAL SOUNDINGS	36

ANNEX TO PARAGRAPH 6.2	RESULTS OF QUESTIONNAIRE ON CODES	38

ANNEX TO PARAGRAPH 8.1	PROPOSAL FOR A MIGRATION STRATEGY	60

ANNEX TO PARAGRAPH 9.1	POCEDURES FOR AMENDMENT TO CODES 	63

ANNEX TO PARAGRAPH 2.1.8	FM 92-XII GRIB					65

ANNEX				LIST OF ACRONYMS				118

REPORT OF MEETING OF EXPERT TEAM ON EVOLUTION OF DATA FORMATS

(Monterey, 4-9 October 1999)

1.	ORGANIZATION OF THE MEETING

1.1	Opening of the Meeting

1.1.1	The Meeting of the Expert Team on Evolution of Data Formats (ET/EDF) took place at the Fleet Numerical Meteorology and Oceanography Centre (FNMOC) in Monterey, California, USA from 4 to 9 October 1999 (the participants’ list can be found in Annex to this paragraph).  The Meeting was opened on Monday 4 October at 9 a.m. by Dr Paul Moersdorf, Chief Scientist of FNMOC.  Dr Moersdorf welcomed the participants and stressed the importance of Codes in the processing of meteorological information, in particular for the feeding of Numerical Models for all the forecasting and climate prediction applications.  He wished a good stay and a very useful and successful working week for all the participants.

1.1.2	The WMO Secretariat representative, Mr Joël Martellet, welcomed the participants and thanked FNMOC for hosting the Meeting and providing excellent assistance and facilities.  He recalled that the primary goal of this Expert Team was to further develop GRIB Edition 2 and finalize it for approval by CBS 2000 with a view to its implementation in November 2001.  The Team had also to propose a standard format for exchange of imagery and other satellite products and to further develop metadata standards.  It had to investigate how encoding/decoding software for BUFR/CREX and GRIB, could be developed, distributed and maintained so as to facilitate the wider use of these data representation codes.  In relation to this project, the Team would discuss results of the questionnaire on WMO Codes, and envisage a strategy to migrate progressively to WMO Table Driven Codes.  The Team would also study new regulations for Code Changes.  Finally, it would have to consider urgent additions to Code Tables for fast-track approval in view of their implementation on 3 May 2000.

1.1.3	Dr Cliff Dey, from USA, as chairman of the Expert Team, lead the Team with diplomacy and efficiency.

1.2	Approval of the agenda

The Team agreed to the content of the agenda as proposed (see Table of Contents in front).

2.	GRIB CODE

2.1	Further develop (and finalize) GRIB2 with a view to CBS final endorsement

2.1.1	 The WMO representative reviewed the history of the development of GRIB Edition 2 (GRIB 2) and recalled that a previous meeting for the development of GRIB 2 has laid out requirements, which needed to be repeated here.  If GRIB 2 is to enable the representation of new products available today, e.g., ensemble forecasts, it would need to provide easy facilities for expansion and additions.  GRIB 2 structure should therefore be more modular and object oriented than GRIB Edition 1 (GRIB 1).  In that way, future extensions will not upset support software.  Definition of parameters or attributes should be separated in functionality and dimension so that items related to time, purpose, production method, space, etc. are independent (orthogonal), which will make software maintenance easier when descriptions of new products or new parameters are required.  It was pointed out that GRIB 2 was initiated due to requirements for the representation of array-type data that GRIB Edition 1 was unable to meet.  The first proposal for a structure for GRIB Edition 2 was prepared in 1996 and approved by CBS XI.  However, that proposal was, in retrospect, too complicated and therefore little work was done on developing it.  Consequently, an Expert Meeting on the Development of Edition 2 of WMO GRIB Code was held in December 2-5, 1997 in Silver Spring, Md.

2.1.2	At this Meeting, a new general structure for GRIB2 was recommended, but few details were provided.  Subsequently, the chairmen of the Working Group on Data Management and the Subgroup on Data Representation and Codes collaborated to refine the structure of GRIB2 and prepare a complete set of draft GRIB2 regulations.  The WGDM recommended it for approval by CBS Ext. ‘98 for experimental use, and CBS Ext. ’98 approved the WGDM recommendation.  Some further work was done after CBS Ext. ’98 by experts of Japan and the United States in collaboration with a project of the United States NWS to develop GRIB2 encoding and decoding software.

2.1.3	The task of this Expert Team was to complete the specification of GRIB2 and organization a validation program with a view to submitting it to CBS XII for approval as an operational data representation form.  The Team began its work by reviewing the current version of the specifications of GRIB2 and making improvements as required.

2.1.4	The Team found the basic structure of the current evolution of GRIB2 to be sound.  However, the Team did agree that allowable repeated sequences should include the Local Use Section in addition to the already permitted Grid Definition, Product Definition, Data Representation Bit-map and Data Sections.   In addition, appropriate code tables were added to the basic templates in order to make them more general and reduce the number needed.

2.1.5	A number of templates were added to make the code form more complete.  All Grid Definition Templates currently permitted in GRIB 1 were added to GRIB2.  Product Definition Templates were added to permit encoding of ensemble, probability, and percentile forecasts, forecast errors fields, matrices, satellite image data, the analysis and forecast of accumulated and averaged parameters, and enhanced capability to describe fields involving multiple time periods.  Complete specification of the GRIB 1 simple and equivalent complex packing methods were added, as well as an efficient difference-packing scheme.  A recently developed wavelet packing approach, a lossy compression scheme that promises quite efficient packing of image data intended for subjective interpretation and visualization was discussed, but approval was delayed until more information on the scheme could be obtained.

2.1.6	Several simple modifications were made to enhance the efficiency of GRIB2 as well.  Although it remains the policy to encourage specification of the grid definition in each GRIB2 message, the Team acknowledged that some planned grid definitions promise to be quite extensive and would increase the size of archives of these data.  It was therefore decided to permit specification of the grid definition by use of a code table defined by the originating center.  Additional information was added to the Grid Definition and Data Representation Sections to remove the necessity of specifying the number of unused bits at the end of the Bit-map and Data Sections.  Re-use of a previously defined bit map was permitted to reduce overhead and consequently permit the same information to be carried in smaller GRIB2 messages.

2.1.7	Notes in grid definition templates regarding missing and negative values and the specification of latitude and longitude were found to be of fundamental importance rather than simply suggestions for good practice.  These were converted into regulations to give them more force.  The team also indicated the need for a document explaining in simple term the advantages, principles and main features of GRIB2 to introduce it to the WMO community.  Furthermore, a Guide was required and will have to be developed following the validation, test and operational implementation period, when the new code form will be more stabilized.

2.1.8	Finally the Team recognized that although the specification of GRIB2 is now rather complete, testing is needed to validate its readiness for use as an operational data representation form.  The representatives of the United States, France, and Japan generously agreed to carry out a set of tests in time for possible submission of GRIB 2 to CBS.  The meeting of the ICT/DRC, to be held in April, 2000, will assess the results of the validation tests and decide whether or not GRIB 2 is ready for submission to CBS XII for approval as an operational data representation form. The description of GRIB 2 approved by the Team is in the Annex to this paragraph.

2.2	Regulations for Wind Coding at the North and South Poles for GRIB 1 and GRIB 2

2.2.1	The Team noted there are no specific regulations for encoding vector components at the North and South Poles in GRIB 1.  This has led to a variety of different procedures being used by the NMCs for products exchanged over the GTS and has made processing these fields unnecessarily complicated for users of these products.  Since these procedures have been in use for many years, it was not felt that new regulations to rectify the situation should be added to GRIB1 at this time.  However, new regulations to standardize the encoding of vector components over the North and South Poles were added to GRIB2.  It was recommended that the Secretariat should inform ICAO regarding the situation in GRIB1.

3.	STANDARD DATA FORMAT FOR EXCHANGE OF IMAGERY AND OTHER SATELLITE PRODUCTS

  - The Team examined the applicability of BUFR and GRIB for the representation of high-resolution satellite products.  After considering the advantages and disadvantages of BUFR and GRIB 1, and taking into account the status of GRIB2, it was agreed that:

- GRIB 1 is not appropriate for the representation of high-resolution satellite products.  This was primarily due to the inability to represent multiple parameter values at each grid point.

- With the additions planned for GRIB2, the representation of high-resolution satellite products will be possible in that format.  All of the requirements will be met by using primary and secondary bit maps to allow for non-continuous area coverage and by using a matrix of values per grid point to allow for the complexity of satellite data.  Associated values, such as quality control data, could be appended to the data by using a previously defined bit map, and having repeated fields after the primary data values.  Furthermore, the expanded compression capability offered in GRIB2 provides efficient packing for satellite image data.

- BUFR can be and is being used for the representation of high-resolution satellite products.  The disadvantage of BUFR is that many messages are required for one product, in order not to impose large resource requirements on the decoding and encoding applications.  The constraint is already implicitly imposed by limiting the number of octets available for defining the number of subsets and the total message length.  The class 30 entries for representing pixel values needed to be updated to allow for the unambiguous representation of both saturated pixels and missing data, and might be simplified by the use of a significance qualifier for the type of pixel.  A proposal for this will be presented to the ICT/DR&C in April 2000.

3.2	In conclusion, either GRIB2 or BUFR could be used for the representation of high-resolution satellite products, and no new code form was required for this purpose.

4.	DEVELOPMENT OF FILE CONTENT DESCRIPTION METADATA STANDARDS

4.1	As part of plans for an enhanced GTS featuring TCP/IP protocols to permit file transfer capability, the Expert Team was tasked to develop standards for file content description metadata to accompany these files.  This metadata would be in a separate file but would be linked to the file being exchanged.  The standards should be easy to process and interpret, yet be robust enough to adapt to as yet unforeseen new requirements for file description.

4.2	The Team considered a proposal for such standard based on an extensive set of “information elements”.  Each information element would consist of a unique two-letter identification followed by an equal sign and element information.  Any subset of information elements could be assembled in any order by the center generating the file to be transferred.  New information elements could be easily added, making the proposed form robust enough to address future requirements.  It was indicated that repetition of the description for several data sets in the same file was possible.  The standard can be found in Annex to this paragraph.

4.3	The Team agreed that the standard was good and is capable of describing well all attributes of all possible data sets.  However, the Team discussed the purpose of that metadata description.  The main use would probably be to help the routing of files in the enhanced GTS by inserting this information in an attached descriptor file.  The standard was not found appropriate for catalogue description, since most data processing Centres had developed their own description system.  However, although a general standard to describe data sets within the Meteorological Community could be useful, it was felt that there was no reason to impose such a standard at this time.  It was recommended the matter be addressed to the Telecommunication Teams for further review, to ensure the proposed standard is capable of fulfilling their requirement.  The matter will have to be reviewed further by the ICT in April 2000.

4.4	The Team also noted that a “tagged-file” format was standard for commonly used Internet image formats such as GIF, JPEG, and PNG.  The “tagged-file” contains a section into which metadata such as that described in Paragraph 4.2 could be placed.  This feature would provide a simple way of incorporating such metadata into files containing data encoded in these formats.  That proposal was found interesting, but it was mentioned that these standards, although widely used to exchange information, were not appropriate for storing and archiving images which were far more efficiently stored by using direct video medium systems.  The standard TIFF should have been mentioned also for images standard.

5.	ADDITIONS TO BUFR AND CREX

5.1	Modifications required for Automatic Stations observations

5.1.1	An Expert Meeting on Requirements and Representation of Data from Automatic Weather Stations in De Bilt, Netherlands (19-23 April 1999) studied the problems linked to the coding of automatic station observations and requirements for modifications or additions to WMO Codes.  The ET/EDF examined the conclusion of that Expert Meeting.

5.1.2	The ET/EDF found unfortunate the difference between the statement stressing that BUFR/CREX were totally suitable for the purpose of reporting automatic observations (offering flexibility and expandability to answer new requirements), and the statement saying that the global application of BUFR and CREX can probably not be done within the next decade so the current operationally used alpha-numeric codes must continue to be applied within the next decade.  The ET/EDF regretted the absence of a suggestion for a double dissemination in BUFR and SYNOP for a transition period.  The double dissemination in traditional codes as well as in BUFR (or CREX) can already be envisaged today, so the manufacturers could start developments right now.  The demand for transmission of additional parameters will only expand during the next ten years and beyond, and development of BUFR and CREX capability cannot wait for another ten years or more to begin.

5.1.3	The ET/EDF agreed to transmit the suggestion made last year for additions to BUFR and CREX for precipitation quantitative values (as found in Annex to this paragraph) to the CBS/ET on Requirements and Representation of Data from Automatic Weather Stations, with a view to their approval and further consideration by the ICT on DR&C, and then CBS.

5.1.4	However, the Team considered the addition proposed by the Expert Meeting, to the character codes SYNOP for reporting quantitative precipitation by addition of a Code Table transmitted in a group 9 of Section 3, was not satisfactory for international exchange beyond a region.  Although this proposal could be retained by a Regional Association, it was not acceptable for inclusion in the International Manual, and the Team stressed that if the transmission of such parameters was crucial, the use of BUFR (or if not possible CREX) was the only way to go.  The Team agreed that a training campaign was needed to explain all the advantages of table-driven Codes and develop the use of BUFR (and CREX).  The Team recommended the production of a simple publication expressing simply and clearly all the advantages of the table driven Codes.

5.2	Consideration of urgent tables additions to BUFR/CREX for fast-track (to be operational on May 2000)

5.2.1	Requests recorded by the Secretariat:

5.2.1.1	The Drifting Buoy Cooperation Panel had requested a set of additions to BUFR Tables.  The Team agreed to this proposal with the exception of the high accuracy height above station which could be solved by a data description operator for a change of scale of 1.  The proposal is found in Annex to this paragraph.

5.2.1.2	The Team agreed to the addition of two entries requested by IOC.  Japan requested the addition of one entry in the table giving the Method of current measurement, which the Team approved.  The two proposals are found in Annex to this paragraph.

5.2.1.3	The Team agreed that changes and additional entries be introduced for Satellite Numbers in Common Table C-5, as found in Annex to this paragraph.

5.2.1.4	The Team agreed to recommend the changes requested by the Tropical Cyclone Programme. to enable the coding of 10 characters storm names and the addition of RSMC Fiji zone in the South Pacific.

5.2.1.5	The Team found that the CREX regulation 95.3.3.1 had to be amended, for consistency on an editorial point of view, because data description operators could contain a negative sign (-yy) and not only 3 digits.  It was recommended to add: at the end of regulation 95.3.3.1:

95.3.3.1	After the CREX table descriptor and the CREX Table A descriptor,  Section 1 shall have one or more  data descriptor(s).  Data descriptors shall be preceded by a space character as separator.   Data descriptors shall occupy 6 characters.  Each descriptor shall have 3 parts: F(1 letter), xx(2 digits), yyy(3 digits or - sign followed by 2 digits for C02yyy data description operator for negative scales - see CREX TABLE C).

5.2.2	The Team considered additional table entries required to encode the data in BUFR of NASA's QuikScat ocean-viewing satellite which had been launched on 19 June 1999 and has a scatterometer radar instrument to be used in mapping winds over the ocean.  The additions were recommended with the remarks that further validations could be performed before the end of 1999.  The additions are listed in Annex to this paragraph.

5.3	Other additions

5.3.1	EUMETSAT requested table additions for EUMETSAT’s new radiance products and future METEOSAT Second Generation radiance products.  EUMETSAT currently generates radiance data from its Meteosat 5 and Meteosat 7 spacecraft.  The radiance data from METEOSAT 5 and 7 have been exchanged between EUMETSAT and ECMWF since January 1999 on the GTS, using the proposed new descriptors.  The Team agreed to recommend the proposed additions found in Annex to this paragraph.

5.3.2	At the request of EUMETSAT, the Team agreed to update slighly the definition of two entries in BUFR Code Table 0 02 023 (satellite derived wind computation method) to eliminate ambiguities.  The modifications proposed are defined in Annex to this paragraph.

5.3.3	For the interchange of Windprofiler and RASS (Radio-Acoustic Sounding System) data between member states, the European COST-76 Management Committee identified the need to define and agree on a standard BUFR format internationally.  The Team examined the new entries needed for encoding or decoding of windprofiler/RASS data.  Although the entries looked correct, the team recommended more validation be performed, at least between two Centres, before the Meeting of the ICT on DR&C in April.  The ICT might then recommend the additions for fast-track to be implemented in November 2000.

5.3.4	Radiological soundings in CREX had been exchanged for validation between the Czech Republic and Finland.  The Team approved the new entries required by the Czech Republic for that purpose.  They are found in Annex to this paragraph.  It was however found that it was premature to introduce a common sequence entry for these radilogical reports since that was not clearly requested in the document.

5.3.5	The Meeting of the Working Group on Data Management/Sub-group on Data Representation and Codes in Montreal in April 1998 made a proposal to correct the present BUFR descriptors for precipitation and depth of snow, which were in fact wrongly combining physical values and code values in the same descriptor.  This proposal was subsequently approved by the Working Group on Data Management and by CBS for implementation in May 2000.  The Team studied this proposal again and agreed that it would not solve the problem, and that further study was necessary to prepare an acceptable solution for submission to the ICT in April 2000 with a view to its endorsement by CBS.  Meanwhile it is proposed that through the fast track procedure these proposed changes approved by CBS be withdrawn and not implemented in May 2000.

6.	RESULTS OF QUESTIONNAIRE ON WMO CODES

6.1	The last Working Group on Data Management recommended that the Sub-Group on Data Representation and Codes (SGDR&C) distribute a questionnaire to ask each Member of WMO which codes they use, how they use them, and the operational and planned capabilities for automatic processing of these data.  The SGDR&C had also asked to develop and circulate as widely as possible a survey to identify the views of users and producers of data in regard to CREX, BUFR, and traditional Codes.

6.2	The questionnaire was sent to 185 Member Countries of WMO in September 1998.  The deadline for replies was 1 February 1999, but some answers arrived in May.  Fifty-seven countries answered.  The results of the questionnaire can be found in Annex to this paragraph.

6.3	The Team examined the results of the questionnaire and found that it was giving a very good snapshot of the situation of WMO Codes processing by the Members. It was noted that almost all the traditional alphanumeric codes were used and that there was no ground to propose the deprecation of obsolete codes, since almost all were used.  It was agreed that, although it seemed that only two main operating systems were used by the Members (UNIX and MS/DOS) to process WMO Code, it would be difficult to ensure portability of decoder/encoder between different machines with different versions or “dialects” of UNIX.

6.4	The Team stressed that the questionnaire showed how training on BUFR, CREX and GRIB 2 would be important for some countries.  Demonstration of use of BUFR with some display features was required to explain well all the advantages of the code.

7.	ENCODING AND DECODING SOFTWARE FOR BUFR, CREX, AND THE NEW EDITION OF GRIB

7.1	The Team emphasized the importance of providing and supporting encoding and decoding software to Members to assist them in using the new table-driven data representation forms GRIB, BUFR, and CREX.  In this regard, the Team felt provision of and support for “load-and-go” software for the WMO table-driven data representation forms was a critical component of any strategy to migrate to use of these forms by the WMO community.

7.2	It was also noted that some numerical centers already make available their software to encode and decode the WMO table-driven data representation forms at a nominal cost.  However, despite the recognition of the importance of this service, the Team agreed that those numerical centers do not have the resources to provide the level of support required, as they are not funded specifically for that purpose.

7.3	With this in mind, the Team agreed on an approach to provide and support the required software within the WMO community.  The Team fully agreed that, in principle, it was an excellent idea to have a "software -house " project to provide GRIB/BUFR/CREX encoders/decoders free to the WMO community.  However, for the time being, no Centre could undertake the project without appropriate resources.  It was estimated that the minimum requirement would be for two persons full time.

7.4	Different "dialects" and versions of operating systems and languages (for ex. UNIX and C) were seen as difficulties but not insurmountable ones.  The big problem was finding resources for the project and it was suggested that under somehow the auspices of WMO, such funding might be provided.

7.5	The team recognized that there were needs to be satisfied, and proposed CBS to consider the following project, which took into account the results of the questionnaire as described in chapter 6:

- To decide on a standard output format for the decoded output and a standard interface to applications.

- To build portable software to decode BUFR, CREX and GRIB to the format mentioned above.  At a minimum, the software should compile and run on the most common dialects of UNIX (including LINUX) and MS/DOS-WINDOWS.  The language used should be widely available software on a wide variety of hardware, such as FORTRAN and C.

- To apply the same process for encoding data.

- The software will be developed under the responsibility and supervision of a major NWP Centre.

- The software will be distributed to WMO Members, maintained and upgraded when required.  Queries will be answered.

vi) 	Some funding, built up under some WMO auspices, would provide the salary support for two persons needed to perform the task.

7.6	The Team recommended that WMO hire a consultant from one of the NWP advanced Centres to write the technical specifications of the project.  The Team wished to be informed of the project document.

8.	MIGRATION STRATEGY

8.1	The Team considered a possible migration strategy with a view to using the BUFR Code Form for observation data to meet all requirements of expansion and flexibility for the transmission of new parameters and data types, as proposed by the Secretariat.  The Team agreed that it could be a good scheme.  It was stressed however that double transmission in BUFR as well as in traditional alphanumeric Codes for the same data, could overburden the telecommunication MSS Centres and that it should be introduced very progressively.  In parallel, a new scheme of data flow within the GTS, organized around Regional Data Bank Centres as described in the proposal found in Annex to this paragraph, could be introduced.

8.2	Related to the promotion of BUFR, a discussion took place on the role of CREX.  The issue was the coupling of CREX and BUFR Tables.  The issue was whether or not descriptors should have the same name and number in the two codes.  The units in CREX are those in common use and the units in BUFR are SI.  One opinion was that coupling the two Codes, as they are now, would give somehow less flexibility in CREX, but would always make the shift to BUFR easy.  Disconnecting the Codes would make the CREX code even more user friendly, but may in the future make the switch to BUFR more painful.  There was no consensus on that issue.  The situation shall be reviewed further by the ICT.

8.3	The Team also recommended the ICT produce templates of traditional observation data in BUFR (i.e. SYNOP, SHIP, TEMP, PILOT, BUOY, etc..), develop single common sequences for these observations, and propose a good training programme with simple documentation explaining the advantage of the table driven codes (The Expert from Canada, Robert Mailhot volunteered to provide the template for automatic stations data in BUFR).

  - The Team proposed that further work be performed within CBS on a migration strategy:

(I)	Examine the observations data flows within the WWW, from the view of the end user, in an “application oriented manner”;

(II)	Develop and recommend a proposal for a new and more efficient data flow within the WWW, considering the creation of Regional Data Bank Centres (RDBCs) and submit the recommendation to CBS;

(III)	Define and recommend to CBS a migration strategy to optimize data acquisition and satisfy the requirements for new observed parameters.

8.5	It was suggested that a document based on the Annex to paragraph 8 expressing these ideas and new concepts be submitted to the Inter-programme Expert Team on Future WMO Information Systems (Melbourne, 1 - 5 November 1999), and to the Implementation Coordination Team on Information Exchange Management.  The Team recommended CBS create an Expert Team on Migration Strategy and Data Flows that would study and produce a sound new scheme for the World Weather Watch Data Flows.  The ET on Migration Strategy and Data Flows should comprise experts on telecommunication, data representation and data processing.

9.	PROCEDURES FOR AMENDMENT TO THE MANUAL ON CODES

9.1	The Team considered a simplified version of the Procedures for amendment to the Manual on Codes as described in Annex to this paragraph.  It was stated that the table numbers referred to in paragraph 2.1 should also contain GRIB 2 code tables.  It was agreed that those procedures, since a slightly more complicated version had already practically approved by CBS Ext. 98, be submitted again at CBS XII with a view to its endorsement, after further consideration by the meeting of ICT DR&C in April 2000.

10.	CLOSURE OF THE MEETING

10.1	The meeting was closed by Dr Cliff Dey, the chairman of the ET on EDF at 12.30 p.m. on Saturday 9 October 1999.

ANNEX TO PARAGRAPH 1.1.1

CBS EXPERT TEAM ON EVOLUTION OF DATA FORMATS

Monterey, Carlifornia, USA, 4-9 October 1999

LIST OF PARTICIPANTS

| USA | Dr Clifford DEY, Chairman National Weather Service, NOAA 5200 Auth Road CAMP SPRINGS, MD 20746-4304 USA Tel: +1 301 763 8000 ext. 7108 Fax: +1 301 763 8381 Email: Cliff.Dey@noaa.gov |
| --- | --- |
| AUSTRALIA | Mr Charles SANDERS Bureau of Meteorology GPO Box 1289K MELBOURNE VIC 3001 AUSTRALIA Tel: +613 9669 4043 Fax: +613 9669 4023 Email: c.sanders@bom.gov.au |
| CANADA | Mr Robert MAILHOT Canadian Meteorological Centre 2121 Trans-Canada Highway DORVAL, QUEBEC CANADA H9P 1J3 Tel: +1 514 421 4633 Fax: +1 514 421 4679 Email: robert.mailhot@ec.gc.ca |
| FRANCE | Ms Madeleine CERON Météo-France 42 Avenue Coriolis 31057 TOULOUSE CEDEX FRANCE Tel: +33 5 6107 8241 Fax: +33 5 6107 8109 Email: madeleine.ceron@meteo.fr |
| FRANCE | Mr Jean CLOCHARD Météo-France 42 Avenue Coriolis 31057 TOULOUSE CEDEX FRANCE Tel: +33 5 61 07 81 04 Fax: + 33 5 61 07 81 09 Email: jean.clochard@meteo.fr |
| GERMANY | Mr Juergen BOETTCHER Deutscher Wetterdienst Zentralamt. Frankfurter Str. 135 D-63067 OFFENBACH GERMANY Tel: +49 69 8062 2647 Fax: +49 69 8062 Email: juergen.boettcher@dwd.de |
| JAPAN | Mr Keiichi KASHIWAGI Japan Meteorological Agency 3-235 Nakakiyoto, Kiyose TOKYO 204-0012 JAPAN Tel: +81 424 936 466 Fax: +81 424 936 056 Email: kashiwagi@naps.kishou.go.jp |
| ECMWF | Mr John HENNESSY ECMWF Shinfield Park READING, BERKSHIRE RG2 9AX UNITED KINGDOM Tel: +44 118 949 9400 Fax: +44 118 986 9450 Email: john.hennessy@ecmwf.int |
| EUMETSAT | Dr Simon ELLIOTT EUMETSAT Am Kavalleriesand 31 D-64295 DARMSTADT GERMANY Tel: +49 6151 807 365 Fax: +49 6151 807 304 Email: elliott@eumetsat.de |
| USA-AFWA | Paul A. ZAMISKA HQ AFWA/SCSV 106 Peacekeeper Dr. STE 2N3 OFFUTT AFB, NE 68113-4039 USA Tel: +1 402 294 3947 Email: |
| USA-AFWA | TSgt Daniel M. MCCORMICK HQ AFWA/DNXM 106 Peacekeeper Dr. STE 2N3 OFFUTT AFB, NE 68113-4039 USA Tel: +1 402 294 5558 Email: Daniel.McCormick |
| USA-AFWA | Walter "Doug" WILKERSON HQ AFWA/XOOP (ACS) 106 Peacekeeper Dr. STE 2N3 OFFUTT AFB, NE 68113-4039 USA Tel: +1 402 294 9774 Fax: +1 402 294 1637 Email: Walter.wilkerson |
| USA-FNMOC | Mr Czec PANEK FLENMMETOCCEN 7 Grace Hopper Ave. Monterey California 93943 USA Tel: +1 408 656 43 48 Fax: +1 408 656 44 89 Email: |
| USA-FNMOC | Ms Darlene HARDENBURGER FNMMOC 7 Grace Hopper Ave. Monterey California 93943 USA Tel: +1 408 656 43 77 Fax: +1 408 656 44 89 Email: |
| USA-NWS | Dr Harry R. GLAHN National Weather Service/NOAA 3125 East West Hwy Silver Spring, MD 20910 USA Tel: +1 301 713 17 68 Fax: +1 301 713 0003 Email: |
| WMO Secretariat | Mr Joël MARTELLET Data Processing System World Weather Watch WMO CP. no 2300 CH-1211 Geneva 2 Switzerland Tel.: +41 22 730 83 13 Fax: +41 22 733 02 42 Internet: joel@www.wmo.ch |

##### ANNEX TO PARAGRAPH 4.2

FILE CONTENT METADATA DESCRIPTION STANDARD

- Basic Features

These proposed standards incorporate several basic features.  Each file content description consists of an integer indicating the total number of octets used by the  description, followed by a number of human readable information elements.  Each information element consists of an element identification made up of two capital letters followed by an equal sign and element information.  The centers originating files to be transferred are allowed to assemble the information elements in the file content description as they see fit.  Nevertheless, the resulting descriptions are still unambiguous, human readable, and easily convertible into directory locations and file names by the recipients.

II. 	Proposed Standards

A file content description section would be required at the beginning of every file exchanged over the enhanced GTS.  The first two octets of each file content description section contains the total number of octets (n) the section uses.  The following n-2 octets contains the file content description character string itself.

The file content description character string consists of a number of human-readable information elements.  The information elements are separated by a carriage return or line feed.  Each information element consists of a two character element ID followed by the equal sign and element information.  All characters in the file content description character string are from the CCITT IA5 character set.  Alphabetic or alphanumeric entries are used for the information elements whenever possible and the allowable character set is restricted to A-Z, a-z, 0-9, equal sign (=) and hyphen  (-).  Use of the hyphen is reserved for indicating that the information element is a spatial or temporal interval.

It is critical that the structure of each information element be internationally coordinated.  Although the total number of information elements needed cannot be known a. priori, an initial set can be formulated and additional ones added as required.  The following proposed description of some useful information elements  adheres to these basic principles.

server location		==>  SL=cccnnnsss

originating center		==>  OC=cccnnnsss

data owner		==>  OW=cccnnnsss

documents		==>  DO=dddd

tables			==>  TB=tttt

reference date		==>  RD=yyyymmdd

reference time		==>  RT=hhnnss

date			==>  DD=yyyymmdd

time			==>  DT=hhnnss

date period		==>  DP=yyyy1mm1dd1-yyyy2mm2dd2

time period		==>  TP=hh1nn1-hh2nn2

generating process		==>  GP=ppppp

area of data		==>  AR=aaaaaaaa

data format		==>  DF=ffff

data status		==>  ST=stat

model type		==>  MT=mmmmm

model run		==>  MR=rrr

cycle of run		==>  CY=hh

level of data	==>  LV=sddddd

layer of data	==>  LY=sddddd1-sddddd2

grid		==>  GR=gggggggg

parameter	==>  PA=pppppppp

data category	==>  DC=ccccc

data subcategory	==>  DS=sssss

file name layout	==>  FL=lllll

file cycle number	==>  CY=xxxxx

customer	==>  CU=uuuuu

sequence number	==>  SN=xxxx

These information elements are described in detail in Appendix A.  It should be noted that the above list of information elements is not exhaustive and more can be anticipated to be needed.  Furthermore, several tables in Appendix A are incomplete and others will need to be developed and maintained by the center responsible for creating the file.

III. 	Example

As an example of the application of these proposed standards, the United States National Centers for Environmental Prediction (NCEP) might choose to assemble the above information elements into the following generic file content description character string:

(originating center)

(reference date)

(reference time)

(generating process)

(data time period)

(area of data)

(data format)

(data discipline)

(data category)

(data subcategory)

Symbolically, this would appear as:

OC=cccnnnsss

RD=yyyymmdd

RT=hhnnss

GP=ppppp

TP=hh1nn1-hh2nn2

AR=aaaaaaaa

DF=ffff

DI=iiiii

DC=ccccc

DS=sssss

A file of radiosonde observations from fixed land sites for the period from 3 hours prior to 2 hours 59 minutes after a reference date/time of 1 October, 1999, 1200 UTC encoded in BUFR would then be accompanied by the following file content description character string when exchanged over the GTS:

OC=usa007003

RD=19991001

RT=120000

GP=obvns

TP=0300-0259

AR=allglobe

DF=bufr

DI=meteo

DC=vsndn

DS=raobf

Note that other centers would be free to organize their file content description character strings for the same observational data with a different combination of information elements or with the same information elements but in a different order.

Appendix A:		Description of Information Elements

server location 	==> SL=cccnnnsss

where

SL		==> Indicator for information element “server location”

ccc		==> country

nnn		==> center

sss		==> subcenter

customer		==> CU=ttttt

where

CU		==> Indicator for directory level “customer”

ttttt		==> two to five alphanumeric characters

data owner		==> OW=cccnnnsss

where

OW		==> Indicator for information element “data owner”

ccc		==> country

nnn		==> center

sss		==> subcenter

documents		==> DO=dddd

where

DO		==> Indicator for information element “documents”

dddd = tcom	==> telecommunications documents

dddd = code	==> data representation (code) form documents

dddd = prod	==> production documents

dddd = drft	==> draft documents

tables			==> TB=tttt

where

TB		==> Indicator for information element “tables”

tttt = stns	==> observing station information

tttt = bufr	==> BUFR tables

tttt = crex	==> CREX tables

tttt = grib	==> GRIB tables

reference date	==> RD=yyyymmdd

where

RD		==> Indicator for information element “reference date”

yyyy		==> 4-digit Year

mm		==> month

dd		==> day

reference time	==> RT=hhnnss

where

RT		==> Indicator for information element “reference time”

hh		==> hour

nn		==> minute

ss		==> second

date			==> DD=yyyymmdd

where

DD		==> Indicator for information element “date”

yyyy		==> 4-digit Year

mm		==> month

dd		==> day

time			==> DT=hhnnss

where

DT		==> Indicator for information element “time”

hh		==> hour

nn		==> minute

ss		==> second

date period	==> DP=yyyy1mm1dd1-yyyy2mm2dd2

where

DP		==> Indicator for information element “date period”

yy1		==> number of years (00-99) before reference date/time date

period begins

mm1		==> number of months (00-12) before reference date/time date

period begins

dd1		==> number of days (00-31) before reference date/time date period begins

yy2		==> number of years (00-99) after reference date/time date period ends

mm2		==> number of months (00-12)after reference date/time date period ends

dd2		==> number of days (00-31)after reference date/time date period ends

time period	==> TP=hh1nn1-hh2nn2

where

TP		==> Indicator for information element “time period”

hh1		==> number of hours (00-99) before reference date/time time period begins

nn1		==> number of minutes (00-99) before reference date/time time period

begins

hh2		==> number of hours (00-99) after reference date/time time period ends

nn2		==> number of minutes (00-99) after reference date/time time period ends

generating process 	==> GP=ppppp

where

GP	==> Indicator for information element “generating process”

ppppp = obsvns 	==> observations

ppppp = agrids 	==> analysis grids

ppppp = agrphs 	==> analysis graphics

ppppp = fgrids 	==> forecast grids

ppppp = fgrphs 	==> forecast graphics

ppppp = warngs 	==> warnings

ppppp = discs	==> discussions

area of data		==> AR=aaaaaaaa

where

AR		==> Indicator for information element “area of data”

aaaaaaaa	==> is a string of eight characters.  International coordination

of a group of frequently-used areas would be useful.

data format      	==> DF=ff

where

DF		==> Indicator for information element “data format”

ff = an	==> WMO character

ff = bl		==> bulletins of raw observations as exchanged on the GTS

ff = bu	==> WMO BUFR

ff = cr		==> WMO CREX

ff = c5		==> CCITT International Alphabet #5

ff = f1		==> CCITT T4-1D facsimile

ff = f2		==> CCITT T4-2D facsimile

ff = gi		==> GIF

ff = gr		==> WMO GRIB (binary)

ff = gt		==> mixed information as exchanged on the GTS

ff = jp		==> JPEG

type of model	==>  MT=mmmmm

where

MT		==> Indicator for information element “type of model”

Mmmmm	==> is a string of five characters indicating the type of model

used (table maintained by originating center)

run of model		==> MR=rrr

where

MR		==> Indicator for information element “run of model”

Rrr	==> is a string of three characters indicating the model run

table maintained by originating center)

cycle of run		==> CY=hh

where

CY		==> Indicator for information element “cycle of run”

hh		==> cycle time in hours

level of data		==> LV=sddddd

where

LV		==> Indicator for information element “level of data”

s = p		==> pressure

s = h		==> height

s = t		==> potential temperature

s = s		==> sigma

ddddd		==> value of surface.  Multiple levels are indicated by setting  ddddd = 99999.

layer of data		==> LY=s1ddddd1-s2ddddd2

where

{LY|ly}	==> Indicator for information element “level of data”

{s1|s2} = p	==> pressure

{s1|s2} = h	==> height

{s1|s2} = t	==> potential temperature

{s1|s2} = s	==> sigma

ddddd1	==> value of lower surface of layer of type s1.

ddddd2	==> value of upper surface of layer of type s2.

(multiple layers are indicated by setting ddddd1 = ddddd2 = 99999)

grid			==> GR=gggggggg

where

GR		==> Indicator for information element “grid”

gggggggg	==> is a string of eight characters indicating the grid used

(table maintained by originating center).   Multiple grids are indicated by setting gggggggg = allgrids.  International coordination of a group of frequently-used grids would be useful.

parameter		==> PA=pppppppp

where

PA		==> Indicator for information element “parameter”

pppppppp	==> is a string of eight characters indicating the parameter

(table maintained by originating center).  Multiple parameters are indicated by setting pppppppp = allparms.    International coordination of a group of frequently-used parameters would be useful.

data category	==> DC=ccccc

where

DC	==> Indicator for information element “data category”

ccccc = sflnd	==> Surface data - land

ccccc = sfmar	==> Surface data - sea

ccccc = vsndn	==> Vertical sounding - other than satellite

ccccc = vsnds	==> Vertical sounding - satellite

ccccc = sluan	==> Single level upper-air data - other than satellite

ccccc = sluas	==> Single-level upper-air data - satellite

ccccc = sfsat	==> Surface data - satellite

ccccc = altyp	==> More than one data category present; DS is not used in this case

data subcategory		==> DS=sssss

where

DS		==> Indicator for information element “data subcategory”

when ccccc = sflnd,

sssss = synop		==> Synoptic - manual and automatic

sssss = avnma		==> Aviation - manual

sssss = amosx		==> Aviation - AMOS

sssss = ramos		==> Aviation - RAMOS

sssss = autob		==> Aviation - AUTOB

sssss = asosx		==> Aviation - ASOS

sssss = metar		==> Aviation - METAR

sssss = awosx		==> Aviation - AWOS

sssss = coavn		==> Synoptic - converted aviation

sssss = autox		==> Aviation - AUTO(0-9)

sssss = coops		==> Cooperative - SHEF

sssss = sclim		==> Aviation - Supplementary Climat Data Report

sssss = allsc		==> All sub-categories

when ccccc = sfmar,

sssss = ships		==> Ship - manual and automatic

sssss = dbuoy		==> Drifting buoy

sssss = mbuoy		==> Moored buoy

sssss = lcman		==> Land-based CMAN station

sssss = oilrg		==> Oil rig or platform

sssss = slpbg		==> Sea level pressure bogus

sssss = wavob		==> WAVEOB

sssss = allsc		==> All sub-categories

when ccccc = vsndn,

sssss = raobf	==> Rawinsonde - fixed land

sssss = raobm	==> Rawinsonde - mobile land

sssss = raobs	==> Rawinsonde - ship

sssss = dropw	==> Dropwinsonde

sssss = pibal	==> Pibal

sssss = prflr	==> Profiler

sssss = nxrdw	==> NEXRAD winds

sssss = allsc	==> All sub-categories

when ccccc = vsnds,

sssss = geost	==> Geostationary

sssss = mstbg	==> Moisture bogus

sssss = tovsx	==> Polar orbiting - TOVS

sssss = synsy	==> Sun synchronous

when ccccc = sluan

sssss = airep	==> AIREP

sssss = pirep	==> PIREP

sssss = asdar	==> ASDAR

sssss = acars	==> ACARS

sssss = recco	==> RECCO - flight level

sssss = allsc	==> All sub-categories

when ccccc = sluas

sssss = infus	==> Winds derived from cloud motion observed infrared

channels by the United States

sssss = visus	==> Winds derived from cloud motion observed in visible

channels by the United States

sssss = h20us	==> Winds derived from motion observed in water vapour channels

by the United States

sssss = comus	==> Winds derived from motion observed in a combination of

spectral channels by the United States

sssss = infin	==> Winds derived from cloud motion observed in infrared

channels by India

sssss = visin	==> Winds derived from cloud motion observed in visible channels

by India

sssss = h20in	==> Winds derived from motion observed in water vapour channels

by India

sssss = comin	==> Winds derived from motion observed in a combination of

spectral channels by India

sssss = infja	==> Winds derived from cloud motion observed in infrared

channels by Japan

sssss = visja	==> Winds derived from cloud motion observed in visible

channels by Japan

sssss = h20ja	==> Winds derived from motion observed in water  vapour

channels by Japan

sssss = comja	==> Winds derived from motion observed in a combination of

spectral channels by Japan

sssss = infeu	==> Winds derived from cloud motion observed in infrared

channels by EUMETSAT

sssss = viseu	==> Winds derived from cloud motion observed in visible

channels by EUMETSAT

sssss = h20eu	==> Winds derived from motion observed in water vapour channels

by EUMETSAT

sssss = comeu	==> Winds derived from motion observed in a combination of

spectral channels by EUMETSAT

sssss = allsc	==> All sub-categories

when ccccc = sfsat,

sssss = ssmit		==> SSM/I - Brightness Temperatures

sssss = ssmip		==> SSM/I - Derived Products

sssss = ersar		==> ERS/SAR

sssss = erswn		==> ERS/scatterometer Winds

sssss = ersal		==> ERS/Radar altimeter Data

sssss = sstnv		==> DOD/Navy sea surface temperatures

sssss = sstns		==> DOC/NESDIS sea surface temperatures

sssss = allsc		==> All sub-categories

file name layout		==> FL=lllll

where

FL		==> Indicator for information element “file name layout”

lllll		==> is a string of five characters indicating the file name

structure used for an individual file (table maintained by

originating center).

file cycle number		==> CY=xxxx

where

CY		==> Indicator for information element “file cycle number”

xxxx					==> two or four digit file cycle number

sequence number		==> SN=xx(xx)

where

SN		==> Indicator for information element “sequence number”

xx(xx) = 01(01)

thru 99(99)		==>sequence number, length of two or four digits determined when number of subdirectories or files are established by center writing the files

customer		==> {CU|cu}.lllll

where

CU		==> Indicator for information element “customer”

lllll = kwbc		==> RTH Washington

lllll = fnoc		==> Fleet Numerical Oceanographic Center

lllll = knhc		==> National Hurricane Center

lllll = mitre		==> Company name

lllll = faa		==> Federal Aviation Administration

lllll = genrl		==> general purpose files (implies file content is not restricted by any intended customer)

ANNEX TO PARAGRAPH 5.1.3

ADDITIONS IN BUFR AND CREX

Add in BUFR and CREX the following entries:

Class 08:

0 08 065	Type of precipitation	Flag table	0	0	12

B 08 065		Flag table	0	0	4

0 08 066	Precipitation occurrence	Code table	0	0	3

B 08 066		Code table	0	0	1

Class 13:

0 13 055	Intensity of precipitation 	kgm-2s-1 	4	0	8

B 13 055		mm/h	1	0	4

0 13 058	Size of precipitating element m		4	0	7

B 13 058		mm		1	0	3

0 13 059	Number of flashes)	Numeric	0	0	7

(thunderstorm

B 13 059				0	0	3

Flag Table		0 08 065

Type of precipitation

- Rain

- Drizzle

- Solid precipitation (Snow or snow grains or ice pellets or ice crystals)

- Hail

- Thunderstorm, if precipitation occurs at the same time

6-11	Reserved

All 12	Missing value

Note:	Mixed precipitation is indicated by setting to one the bits of all the observed single types of precipitation

Code Table		0 08 066

Precipitation occurrence

0	Reserved

1	Continuous

2	Shower

3	Intermittent precipitation

4-6	Reserved

7	Missing value

ANNEX TO PARAGRAPH 5.2.1.1

ADDITIONS TO BUFR REQUESTED BY DBCP

There is a need to create the following new descriptors and associated tables:

Proposed new descriptors and associated tables:

- 0 25 086	Depth correction indicator. Indication whether probe depths as reported in Section 3 are corrected using hydrostatic pressure or not.

| Table B reference | Unit | Scale | Reference value | Data width (bits) |
| --- | --- | --- | --- | --- |
| 0 25 086 | Code table | 0 | 0 | 2 |

CREX: B25086	  Code table	0			      1

Associated code table:

| Code figure | Depth correction indicator |
| --- | --- |
| 0 | Depths are not corrected |
| 1 | Depth are corrected |
| 2 | Reserved |
| 3 | Missing |

- 0 02 168	Hydrostatic pressure of lower end of cable (thermistor string). Pressure is expressed in units of 1000 Pa (i.e. centibars). This indicator must be followed by 0 02 035 (Cable length) indicator.

| Table B reference | Unit | Scale | Reference value | Data width (bits) |
| --- | --- | --- | --- | --- |
| 0 02 168 | Pa | -3 | 0 | 16 |

CREX: B 02 168	   KPa		0			       5

- 0 07 064	Height above station at which sensor height is artificially corrected to standard value using formula. For example standard height for wind is 10 meters but anemometers on buoys are placed at much lower height; such height is sometimes corrected using formula).

| Table B reference | Unit | Scale | Reference value | Data width (bits) |
| --- | --- | --- | --- | --- |
| 0 07 064 | m | 0 | 0 | 4 |

CREX:     B 07 064		  m		0			      2

- 0 02 169	Anemometer type

A new BUFR table will have to be proposed for encoding Anemometer type.

| Code figure | Anemometer type |
| --- | --- |
| 0 | Cup rotor |
| 1 | Propeller rotor |
| 2 | Wind Observation Through Ambient Noise (WOTAN) |
| 3-14 | Reserved |
| 15 | Missing value |

Rename descriptor 0-02-148 "Location System" to "Data collection and/or location system".

- 0-02-148	Data collection and/or location system

New entries proposed in associated code table

| Code figure | Data collection and/or location system |
| --- | --- |
| 3 | GOES DCP |
| 4 | METEOSAT DCP |
| 5-30 | Reserved |

ANNEX TO PARAGRAPH 5.2.1.2

Add in Common Code Table C-3 (Code Table 1770):

510	Sparton 536 AXBT	a= 1.524, b= 0

In Common Code Table C-4 (Code Table 4770):

- Lockheed-Sanders Model OL5005

Add to Table 0 02 030 (BUFR) and in Table 2266 (Volume I.1) the following entry:

Code	Meaning

1	ADCP (Acoustic Doppler Current Profiler)

ANNEX TO PARAGRAPH 5.2.1.3

SATELLITE NUMBERS in Common Code Table C-5

Change the following entryies:

220	220	LANDSAT 5

221	221	LANDSAT 4

222	222	LANDSAT 7 (no change)

Add:

059 METEOSAT 2

120 ADEOS....

.......................

281 QUIKSCAT

ANNEX TO PARAGRAPH 5.2.1.4

REQUIREMENT FOR NEW WMO STORM NAME (10 CHARACTERS) AND OCEAN BASIN LETTER

(Requested by the Tropical Cyclone Programme)

New descriptors in BUFR and CREX:

BUFR:

0 01 027	WMO long storm name	CCITT IA5	0	0	80

CREX:

B 01 027	WMO long storm name	CCITT IA5	0		80

BUFR:

Add note to 0 01 026:  Descriptor 0 01 027 should be used instead of 0 01 026 to encode this element

And in Note 2 of table for Class 1, change 0 01 026 to 0 01 027

CREX:

Add note to B 01 026:  Descriptor B 01 027 should be used instead of B 01 026 to encode this element

And in Note 2 of table for Class 1, change B 01 026 to B 01 027

In Note 1 of table for Class 1 in BUFR and CREX, add in the list the letter F:

F   RSMC Nadi’s zone in South Pacific

ANNEX TO PARAGRAPH 5.2.2

The QuikScat data should be represented with one Table D entry: 312026

These are the sequences needed for BUFR Table D:

312026  301046

301011

301013

301023

312031

101004

312030

021110

301023

321027

021111

301023

321027

021112

301023

321027

021113

301023

321027

301046  001007

001012

002048

021119

025060

202124

002026

002027

202000

005040

312030  201130

202129

011012

202000

201000

011052

201135

202130

011011

202000

201000

011053

021104

312031  005034

006034

021109

011081

011082

021101

021102

021103

321027  021118

202129

201132

002112

201000

201131

002111

201000

202000

002104

021105

021106

021107

021114

021115

021116

008018

021117

Table B new entries required

005034	ALONG TRACK ROW NUMBER	NUMERIC	0	0	11

006034	CROSS TRACK CELL NUMBER	NUMERIC	0	0	7

008018	SEAWINDS LAND/ICE SURFACE	FLAG TABLE	0	0	17

TYPE

011052	FORMAL UNCERTAINTY IN WIND	M/S	2	0	14

SPEED

011053	FORMAL UNCERTAINTY IN WIND	DEGREE TRUE	2	0	15

DIRECTION

011081	MODEL WIND DIRECTION AT 10 M	DEGREE TRUE	2	0	16

011082	MODEL WIND SPEED AT 10 M	M/S	2	0	13

021101	NUMBER OF VECTOR AMBIGUITIES	NUMERIC	0	0	3

021102	INDEX OF SELECTED WIND VECTOR	NUMERIC	0	0	3

021103	TOTAL NUMBER OF SIGMA-0	NUMERIC	0	0	5

MEASUREMENTS

021104	LIKELIHOOD COMPUTED FOR	NUMERIC	3	-30000	15

SOLUTION

021105	NORMALIZED RADAR CROSS	dB	2	-10000	14

SECTION

021106	Kp VARIANCE COEFFICIENT (ALPHA)	NUMERIC	3	0	14

021107	Kp VARIANCE COEFFICIENT (BETA)	NUMERIC	8	0	16

021109	SEAWINDS WIND VECTOR CELL	FLAG TABLE	0	0	17

QUALITY

021110	NUMBER OF INNER-BEAM	NUMERIC	0	0	6

SIGMA-0 (FORWARD OF SATELLITE)

021111	NUMBER OF OUTER-BEAM	NUMERIC	0	0	6

SIGMA-0 (FORWARD OF SATELLITE)

021112	NUMBER OF INNER-BEAM	NUMERIC	0	0	6

SIGMA-0 (AFT OF SATELLITE)

021113	NUMBER OF OUTER-BEAM	NUMERIC	0	0	6

SIGMA-0 (AFT OF SATELLITE)

021114	Kp VARIANCE COEFFICIENT (GAMMA)	 dB	3	-140000	18

021115	SEAWINDS SIGMA-0 QUALITY	FLAG TABLE	0	0	17

021116	SEAWINDS SIGMA-0 MODE	FLAG TABLE	0	0	17

021117	SIGMA-0 VARIANCE	NUMERIC	2	0	16

QUALITY CONTROL

021118	ATTENUATION CORRECTION	dB	2	-10000	14

ON SIGMA-0

021119	WIND SCATTEROMETER	CODE TABLE	0	0	6

GEOPHYSICAL MODEL FUNCTION

New entries in existing Code Table 002048: Satellite sensor indicator

Add two new entries:

Code figure	Meaning

- NSCAT

- SEA WINDS

Flag Table 008018

Bit number    Meaning

1             LAND IS PRESENT

2             SURFACE ICE MAP INDICATES ICE IS PRESENT

3-10          RESERVED

11            ICE MAP DATA NOT AVAILABLE

12            ATTENUATION MAP DATA NOT AVAILABLE

13-16         RESERVED

All 17        MISSING VALUE

Flag Table 021109

Bit	Meaning

number

1       NOT ENOUGH GOOD SIGMA-0 AVAILABLE FOR WIND RETRIEVAL

2       POOR AZIMUTH DIVERSITY AMONG SIGMA0- FOR  WIND RETRIEVAL

3-7     RESERVED

8       SOME PORTION OF WIND VECTOR CELL IS OVER LAND

9       SOME PORTION OF WIND VECTOR CELL IS OVER ICE

10      WIND RETRIEVAL NOT PERFORMED FOR WIND  VECTOR CELL

11      REPORTED WIND SPEED IS GREATER THAN 30 M/S

12      REPORTED WIND SPEED IS LESS THAN OR EQUAL TO 3 M/S

13-16   RESERVED

ALL 17  MISSING VALUE

Flag Table 021115

Bit	Meaning

number

1      SIGMA-0 MEASUREMENT IS NOT USABLE

2      SIGNAL TO NOISE RATIO IS LOW

3      SIGMA-0 IS NEGATIVE

4      SIGMA-0 IS OUTSIDE OF ACCEPTABLE RANGE

5      SCATTEROMETER PULSE QUALITY

IS NOT ACCEPTABLE

6      SIGMA-0 CELL LOCATION ALGORITHM DOES NOT CONVERGE

7      FREQUENCY SHIFT LIES BEYOND THE RANGE OF THE X FACTOR TABLE

8      SPACECRAFT TEMPERATURE IS BEYOND

CALIBRATION COEFFICIENT RANGE

9      NO APPLICABLE ATITUDE RECORDS WERE FOUND FOR THIS SIGMA-0

10     INTERPOLATED IPHEMEORIS DATA ARE NOT ACCEPTABLE FOR THIS

SIGMA-0

11-16  RESERVED

All 17 MISSING VALUE

Flag Table 021116

Bit	Meaning

number

1      CALIBRATION/MEASUREMENT PULSE FLAG (1)

2      CALIBRATION/MEASUREMENT PULSE FLAG (2)

3      OUTER ANTENNA BEAM

4      SIGMA-0 CELL IS AFT OF SPACECRAFT

5      CURRENT MODE (1)

6      CURRENT MODE (2)

7      EFFECTIVE GATE WIDTH - SLICE RESOLUTION (1)

8      EFFECTIVE GATE WIDTH - SLICE RESOLUTION (2)

9      EFFECTIVE GATE WIDTH - SLICE RESOLUTION (3)

10     LOW RESOLUTION MODE - WHOLE PULSE DATA

11     SCATTEROMETER ELECTRONIC SUBSYSTEM B

12     ALTERNATE SPIN RATE - 19.8 RPM

13     RECEIVER PROTECTION ON

14     SLICES PER COMPOSITE FLAG(1)

15     SLICES PER COMPOSITE FLAG(2)

16     SLICES PER COMPOSITE FLAG(3)

ALL 17 MISSING VALUE

Code Table 021119

Code figure    Meaning

0         RESERVED

1         SASS

2         SASS2

3         NSCAT0

4         NSCAT1

5         NSCAT2

6         QSCAT0

7         QSCAT1

8 -30     RESERVED

31        CMOD1

32        CMOD2

33        CMOD3

34        CMOD4

35        CMOD5

36-62     RESERVED

63        MISSING VALUE

ANNEX TO PARAGRAPH 5.3.1

Sequences needed for Geostationary satelite radiance data in BUFR Table D :

Meteosat radiance data

310015  301072

007024

010002

303041

101003

304032

002152

002024

007004

007004

013003

101003

304033

Meteosat Second Generation (MSG) radiance data

310016  301072

007024

010002

303041

101012

304032

002152

002024

007004

007004

013003

101012

304033

Cloud fraction

304032  002153

002154

020081

020082

020012

Clear sky radiance

304033  002152

002166

002167

002153

002154

012075

012076

012063

Table B new entries required

012075 SPECTRAL RADIANCE	Wm-1sr-1     10     0   31

012076 RADIANCE			Wm-2sr-1      3      0   16

Add note to descriptor: 0 12 072: Descriptor 0 12 076 should be used instead of descriptor 0 12 072 to encode Radiance.

ANNEX TO PARAGRAPH 5.3.2

Code table 0 02 023 - satellite derived wind computation method

Add entry 	0	Reserved

Modify entries 3 and 7 as:

3	Wind derived from cloud motion observed in the water vapour channel

7	Wind derived from motion observed in the water vapour channel (cloud or clear air not specified)

ANNEX TO PARAGRAPH 5.3.4

ADDITION FOR RADIOLOGICAL SOUNDINGS

Proposal for new descriptors in CREX (and BUFR)

The following new descriptors are proposed:

|  |  | unit | scale | Ref. value | data width |
| --- | --- | --- | --- | --- | --- |
| 008008 | Radiation vertical sounding significance | flag table | 0 | 0 | 9 |
| B08008 | Radiation vertical sounding significance | flag table | 0 |  | 3 |

|  | bit 1 | = surface |
| --- | --- | --- |
|  | bit 2 | = standard level |
|  | bit 3 | = tropopause level |
|  | bit 4 | = level of beta radiation maximum |
|  | bit 5 | = level of gammma radiation maximum |
|  | bit 6 | = minimum pressure level |
|  | bit 7 | = reserved |
|  | bit 8 | = level of undetermined significance |
|  | all 9 | = missing value |

|  |  | unit | scale | Ref. value | data width |
| --- | --- | --- | --- | --- | --- |
| 007009 | Geopotential height | gpm | 0 | 0 | 17 |
| B07009 | Geopotential height | gpm | 0 |  | 5 |
| 010009 | Geopotential height | gpm | 0 | 0 | 17 |
| B10009 | Geopotential height | gpm | 0 |  | 5 |

In the proposed template (see par. 4), only the descriptor B10009 is needed. According to the recommendation of  Mr. Robert Mailhot, a similar descriptor in class 7 (B07009) is proposed for the sake of completeness.

|  |  | unit | scale | Ref. value | data width |
| --- | --- | --- | --- | --- | --- |
| 024023 | Pulse rate of beta radiation | count per sec | 1 | 0 | 14 |
| B24023 | Pulse rate of beta radiation | count per sec | 1 |  | 4 |
| 024024 | Pulse rate of gamma radiation | count per sec | 1 | 0 | 14 |
| B24024 | Pulse rate of gamma radiation | count per sec | 1 |  | 4 |

In the template of a radiological sounding, the descriptor D01024 is used for the sequence B05002 (latitude of coarse accuracy), B06002 (longitude of coarse accuracy) and B07001 (height)], although D01022 should be used according to the current CREX documentation.  D01022 should also be replaced by D01024 in the descriptors D01075, D07041, D07042, D07043 and D07044 (descriptors for ozone measurements).

The descriptor D01075 is called “Ozone sounding identification”.  This descriptor is, however, suitable for the identification of any vertical sounding, e.g. also for radiological sounding or for sounding data of high vertical resolution.  Therefore it is proposed to rename this descriptor to make it available for a more general usage: "Sounding identification".

## ANNEX TO PARAGRAPH 6.2

RESULTS OF QUESTIONNAIRE ON WMO CODES

1.	Fifty-seven countries answered:

2.	From RA I,  9 countries answered.

From RA II, 14 countries answered.

From RA III,  6 countries answered.

From RA IV,  1 country answered.

From RA V,  5 countries answered.

From RA VI, 22 countries answered.

- RESULTS Compilation of replies

The results of the questionnaire can be found in Appendices A, B and C.

4.	USE OF WMO CODES (see Appendix A)

4.1	The most used WMO codes for encoding and transmitting information are SYNOP and CLIMAT (all countries-100%, then TEMP (56 countries-98%), METAR (55 countries-97%), TAF (48 countries-84%), SPECI (46 countries-81%), CLIMAT TEMP (44 countries-77%), PILOT (39 countries-68%) and SHIP (36 countries-63%).

4.2	Surprisingly, 12 (21%) countries code data in RADOB, 12 (21%) in TEMP SHIP and 10 (18%) in HYDRA.

4.3	Only one country encodes in CODAR (manually), one in ICEAN (manually), one in WAVEOB (automated), one in SFAZI and one in SFAZU.

4.4	FM 49 GRAF and FM 73 NACLI, CLINP, SPCLI, CLISA, INCLI are the only 2 codes which are not reported to be generated by any country.

4.5	Two other codes are not encoded: SFLOC and SARAD, but they are received by some centres (2 and 4 respectively).

4.6	FM 57 RADOF was omitted by mistake from this questionnaire.  We know that in RA VI, this code is used for some bi-lateral exchanges.

4.7	Only 12 (21%) countries code data in BUFR, of which 7 (12%) are coding BUFR data at the observing platform or site, 10 (18%) at a processing centre and 1 at the telecommunication centre only.

4.8	Only 3 (5.3%) countries are coding in CREX of which 2 (3.5%) are reporting coding CREX data at the observing platform or site and 2 (3.5%) at a processing centre.

4.9	Fourteen (25%) countries reported they generate GRIB reports when only 8 (14%) generate GRID reports.

AUTOMATION FOR ENCODING (see Appendix B)

5.1 From RA I, 9 countries answered, 2 reported some automation in encoding of observations or products

1 reported extensive automation

From RA II, 14 countries answered,	2 reported some automation in encoding of observations or products

3 reported extensive automation

From RA III,  6 countries answered,	1 reported some automation in encoding of observations or products

1 reported extensive automation

From RA IV,  1 country answered and reported extensive automation in encoding of observations or products

From RA V,  5 countries answered,	1 reported some automation in encoding of observations or products

1 reported extensive automation

From RA VI, 22 countries answered,	8 reported some automation in encoding of observations or products

8 reported extensive automation

5.2	Fourteen countries reported some automation in encoding of observations or products and 15 countries reported extensive automation.  In total 29 countries out of 57 reported automation in encoding of observations.

5.3	The countries seem to use many different computers and operating systems for encoding reports.  For example, out of 20 countries reporting automatic encoding of SYNOP, 18 different combinations of systems are reported.  Sometimes there are more different systems used than countries.

5.4	Overall, the main operating systems to be used are UNIX followed by MS-DOS, for languages FORTRAN 77 and C are mentioned the most.  GRIB and BUFR are not processed under MS-DOS, but all under UNIX, with FORTRAN 77 and C.  GRIB is indeed usually processed on bigger machines (CRAY, NEC).

ARCHIVING OF OBSERVATIONS MESSAGES

6.1	About two thirds of the countries reported they archive observations.  About half reported they archive in the WMO Alphanumeric Code format, the other half in a different format, which is for one third BUFR.

6.2	Almost all the countries encoding BUFR, GRIB and CREX, archive these messages, but one fifth archive them in a different format!  One country indicated it archives CREX in BUFR, which is indeed very natural!

DECODING-PROCESSING OF WMO CODES (see Appendix C)

7.	Thirty-four countries reported some automation for decoding or processing alphanumeric codes.  A great variety of platforms are used by the Members, however SGI is reported 10 times and PC type systems 18 times.  The operating system UNIX is reported 17 times, MS-DOS 15 times.  FORTRAN 77 is used 18 times, C 16 times.

BUFR

8.	Thirty-eight countries reported using BUFR.  Twice more countries reported for DECODING than for ENCODING.  Countries indicated use of BUFR for all types of data, but mostly for satellites and RADAR data.  Three countries reported they use it for automated station data.  It is indeed used for archiving.

8.1	The advantages of BUFR are well known and listed again by the countries:

Overall very powerful

Compactness of data (5), Save disk memory, Save disk space

Self defined

Expandable for local or international applications (2)

Fully flexible (2)

Easy to add or change observational elements (2)

Universal Code Form (3), Manage any type of data

The only possibility for composition of RADAR data

Embedded auto-control (?)

Efficient for data processing and transmission

Convenient for calculation

Allows easy conversion into internal format (?)

Machine independent(?)

Portability and uniformity

8.2	The disadvantages are less known but the countries made a good list:

Not human readable (6), binary

Coordination between data source and data recipient to ensure the same interpretation

Tables updating and coordination heavy (4)

High requirement for the used computer

Requires a sophisticated ENCODER/DECODER (3), Difficulty in coding and decoding

For transmission, it requires X25 or TCP/IP

Possible confusion within tables (2)

Complexity (2)

Too strict rules (?)

Decrease accuracy (?)

Missing standard encoders/decoders for different platforms.

CREX

9.	Only 3 countries indicated they use CREX, however 23 countries plan to use CREX in the future.  Twenty-one said they had no plan to use it.  The question which can be further asked is: do they know about CREX?  Many countries indicated they planned to use CREX to replace traditional codes.  It is currently used for Ozone data exchange (3 countries), typhoon forecast information (1 country), for hydrology (1 country).

9.1	Countries listed the following advantages of CREX:

Close relationship to BUFR, good solution for simple needs, human readable (in recurring cases), flexible

Experience of using CREX will be helpful for migration to BUFR

Similarity of the concept of CREX and BUFR (flexibility, expandability)

CREX can prevent the proliferation of new various alphanumeric codes (3)

CREX allows direct readability without various decoder

CREX does not require X25 nor TCP/IP for transmission

CREX allows data representation in commonly used units

General Code (universality)

Flexibility allowing to provide different data in different situation

Easy to use code

Flexibility of tables, can be used by not automated centres.

9.2	The main advantages of CREX which were expressed by the countries, were really to avoid the proliferation of new alphanumeric codes, the flexibility and the ease of use.

9.3	The countries listed the following disadvantages of CREX (comments by secretariat in italics):

Octal representation of flag tables, limitation for satellite data, less flexible than BUFR (?), not really readable when content varies, does not compress data (but one can use ZIP), coordination of tables, coordination between data source and data recipient (at the beginning)

Transition of traditional character codes to CREX would require modifications of the existing software

Cost for renewal of existing software

Could be too long a message (3), CREX is not volume efficient

Lack experienced staff (training necessary)

PLAN

10.	The main disadvantage expressed by the countries is the size of CREX messages.  Perhaps, to counter that, a standard compressing package could be suggested.  Clearly the cost to renew the existing software is a big hurdle.  Only new data types without an existing WMO code should be considered to coded in CREX.  A recognized WMO software house should offer standard encoder/decoder software packages, for both CREX and BUFR.  Definitely, training should be provided.  Heavy and intensive training would be required for programmers if encoder/decoders were not available, however if they are, a light training, more simple and just informative will be sufficient for BUFR.  CREX can be easily fully understood within a few hours.

10.1	Countries listed the computers where they use or plan to use a BUFR or CREX decoder software.  SGI and PC types are the most used machines (see logically the same in parag. 7.1).  UNIX and MS-DOS will be the most use operating systems.  FORTRAN and C are the winners for the languages.

10.2	The list of data which cannot fit in present WMO alphanumeric codes is impressive.  Indeed there are the wind profilers, satellites, the ACARS and RADAR data, for which BUFR is the answer.  Nevertheless, 8 countries indicated there were no data which did not fit the WMO alphanumeric codes, perhaps because they do not have new requirements. Countries listed new data types which should be considered with attention:

Monitoring reports of regional synoptic network

High resolution products

Forecast vertical profiles

Radiological sounding

Air pollution data (use internal character code)

Agrometeorological (use internal character code)

Observations and predictions of ENSO, Developing anomalies, ITCZ data, Soil hydrological bilan

Pictorial information

Advisories, Forecasts

Aeronautical data and information

Some aircraft and radiation data

Measured data from automatic station.

CANDIDATES FOR REPRESENTATION AND EXCHANGE

11.	There are two groups of countries: those that said that CREX could transmit all data, and those that limit it to the new data types for which there is no existing alphanumeric WMO codes.  The same answer is made for BUFR.

APPENDIX A

Questionnaire on Use of WMO Codes

| Code | Encoding | Transmitted by telecomm. Centre | Received by GDPS Center | Archived by agency |
| --- | --- | --- | --- | --- |
|  | At Observing Site or Platform | At a processing Centre | At telecom-munication Centre only | If automated, indicate: computer, operating system, encoder language (e.g. CRAY J916, UNIX, FORTRAN 77) | Domes-tically | Interna-tionally | from some other domestic source | from an interna-tional source | (specify archive format if different) |
| FM 12 SYNOP | 56 | 11 | 2 | 20 | 45 | 46 | 19 | 50 | 17 ( 15 BUFR: 4 |
| FM 13 SHIP | 23 | 3 |  | 8 | 24 | 28 | 14 | 26 | 14 ( 7 BUFR: 3 |
| FM 14 SYNOP MOBIL | 3 |  |  |  | 3 | 4 | 3 | 6 | 3 ( 1 |
| FM 15 METAR | 51 | 4 |  | 13 | 41 | 47 | 18 | 32 | 21 ( 5 BUFR: 1 |
| FM 16 SPECI | 42 | 4 |  | 9 | 37 | 42 | 16 | 30 | 17 ( 4 BUFR: 1 |
| FM 18 BUOY | 4 | 5 | 2 | 3 | 8 | 12 | 4 | 16 | 8 ( 5 BUFR: 3 |
| FM 20 RADOB | 12 |  |  | 1 | 7 | 12 | 5 | 7 | 5 ( 1 |
| FM 22 RADREP | 4 |  |  |  | 2 | 3 |  | 2 | 2 |
| FM 32 PILOT | 35 | 4 |  | 11 | 26 | 31 | 16 | 27 | 14 ( 8 BUFR: 4 |
| FM 33 PILOT SHIP | 4 | 2 |  | 2 | 7 | 8 | 4 | 13 | 7 ( 5 BUFR: 4 |
| FM 34 PILOT MOBIL | 2 |  |  |  | 3 | 5 | 2 | 7 | 4 ( 1 BUFR: 1 |
| FM 35 TEMP | 50 | 6 |  | 18 | 40 | 51 | 19 | 39 | 21 ( 11 BUFR: 4 |
| FM 36 TEMP SHIP | 10 | 2 |  | 3 | 11 | 13 | 6 | 22 | 8 ( 7 BUFR: 4 |
| FM 37 TEMP DROP |  | 1 |  | 1 | 2 | 3 | 2 | 6 | 4 ( 1 BUFR: 1 |
| FM 38 TEMP MOBIL | 4 |  |  |  | 5 | 6 | 3 | 9 | 5 ( 2 BUFR: 2 |
| FM 39 ROCOB | 3 |  |  | 1 | 2 | 3 | 2 | 4 | 3 |
| FM 40 ROCOB SHIP | 2 |  |  |  | 1 | 2 | 1 | 2 | 1 |
| FM 41 CODAR | 1 |  |  |  | 2 | 2 | 1 | 3 | 3 |
| FM 42 AMDAR | 4 | 4 |  | 2 | 5 | 7 | 5 | 13 | 5 ( 4 BUFR: 2 |
| FM 44 ICEAN | 1 |  |  |  | 1 | 2 |  | 1 | 2 |
| FM 45 IAC | 3 |  |  |  | 3 | 3 | 2 | 2 | 1 |
| FM 46 IAC FLEET | 1 | 1 |  |  | 2 | 1 |  | 2 | 1 |
| FM 47 GRID | 1 | 7 |  | 6 | 8 | 11 | 2 | 26 | 7 ( 2 |
| FM 49 GRAF |  |  |  |  |  |  |  |  |  |
| FM 50 WINTEM | 1 | 4 |  | 1 | 5 | 6 | 1 | 9 | 4 ( 1 |
| FM 51 TAF | 32 | 16 | 2 | 7 | 38 | 46 | 13 | 29 | 13 ( 5 BUFR: 1 |
| FM 53 ARFOR | 3 | 3 |  | 1 | 9 | 7 | 3 | 7 | 2 |
| FN 54 ROFOR | 7 | 5 |  | 2 | 13 | 13 | 4 | 8 | 5 |
| FM 61 MAFOR | 2 | 1 |  | 1 | 4 | 3 | 1 |  | 2 |
| FM 62 TRACKOB | 2 | 4 |  | 3 | 2 | 5 | 1 | 4 | 4 |
| FM 63 BATHY | 5 | 4 |  | 4 | 5 | 9 | 4 | 8 | 4 ( 4 BUFR: 2 |
| FM 64 TESAC | 2 | 3 |  | 3 | 3 | 7 | 2 | 7 | 3 ( 4 BUFR: 2 |
| FM 65 WAVEOB | 1 |  |  | 1 | 1 |  | 2 |  | ( 1 BUFR: 1 |
| FM 67 HYDRA | 9 | 1 |  | 1 | 5 | 6 |  | 5 | 4 ( 2 |
| FM 68 HYFOR | 4 | 1 |  | 1 | 2 | 4 |  | 3 | 2 ( 1 |
| FM 71 CLIMAT | 41 | 19 |  | 9 | 29 | 51 | 15 | 31 | 16 ( 6 |
| FM 72 CLIMAT SHIP | 3 | 1 |  |  | 2 | 5 | 3 | 5 | 4 |
| FM 73 NACLI,... |  |  |  |  | 1 | 1 |  |  |  |
| FM 75 CLIMAT TEMP | 32 | 12 |  | 10 | 22 | 38 | 11 | 23 | 12 ( 3 |
| FM 76 CLIMAT TEMP SHIP | 2 | 2 |  |  | 2 | 4 | 2 | 6 | 3 ( 1 |
| FM 81 SFAZI |  | 1 |  |  |  |  |  |  |  |
| FM 82 SFLOC |  |  |  |  | 2 |  |  | 2 |  |
| FM 83 SFAZU |  | 1 |  |  |  |  |  |  |  |
| FM 85 SAREP |  | 3 |  | 1 | 2 | 3 | 2 | 4 | 5 |
| FM 86 SATEM | 1 | 4 |  | 2 | 5 | 7 | 2 | 15 | 6 ( 4 BUFR: 3 |
| FM 87 SARAD |  |  |  |  | 2 | 5 |  | 4 | 2 |
| FM 88 SATOB | 1 | 3 |  | 2 | 6 | 8 | 3 | 16 | 5 ( 2 BUFR: 1 |
| FM 92 GRIB | 2 | 14 |  | 14 | 15 | 12 | 4 | 25 | 11 ( 1 |
| FM 94 BUFR | 7 | 10 | 1 | 12 | 12 | 10 | 5 | 11 | 8 ( 2 |
| FM 95 CREX (experimental up to April 2000 - operational in May 2000) | 2 | 2 |  | 3 | 3 | 3 |  | 3 | 2 ( 1 |

## APPENDIX B

# AUTOMATION FOR ENCODING

Indicated in front is the Number of computer systems used over the Number of countries using automation for encoding the corresponding WMO code (e.g.: 18/20).

18/20

SYNOP:	COMPAQ-PC486, MS-DOS, PASCAL 7.0*

VAX, VMS, PL/1*

DEC ALPHA, VMS, FORTRAN*

DOS, PASCAL*

SGI, UNIX, FORTRAN 77*

PC, MS-DOS, C*

DEC ALPHA, VMS 7.1, FORTRAN

RS6000, AIX, C*

SUN, UNIX, C*

IMS, QNX, MILOS 500

PC, MS-DOS, Q-BASIC *

PC, WINDOWS, C & PASCAL

WS, UNIX, C*

PENTHIUM, WINDOWS 95, DELPHI*

IBM 590H, UNIX, FORTRAN

HITACHI, UNIX, C

FUJITSU, OSIV MSP, FORTRAN 77

PENTHIUM, WINDOWS, VISUAL BASIC

5/8

SHIP		PC, MS-DOS, C

FUJITSU, OSIV MSP, FORTRAN 77

DEC ALPHA, VMS, FORTRAN

SUN, UNIX, C

PC, FORTRAN 77

12/13

METAR	SGI, UNIX, FORTRAN 77*

PC, MS-DOS, C*

COMPAQ DESKPRO 4/331, DOS 6.22

WS, UNIX, C

COMPAQ-PC486, MS-DOS, PASCAL 7.0*

PENTHIUM, WINDOWS 95, DELPHI

PC, WINDOWS NT, VISUAL BASIC

DOS, PASCAL

HITACHI, UNIX, C

DEC ALPHA, VMS, FORTRAN

SUN, UNIX, C

PC, WINDOWS, C

9/9

SPECI		PC, MS-DOS, C

COMPAQ DESKPRO 4/331, DOS 6.22

WS, UNIX, C

COMPAQ-PC486, MS-DOS, PASCAL 7.0*

PENTHIUM, WINDOWS 95, DELPHI

HITACHI, UNIX, C

DEC ALPHA, VMS, FORTRAN

SUN, UNIX, C

PENTHIUM, WINDOWS, VISUAL BASIC

3/3

BUOY		HITACHI, UNIX, C

SGI CHALLENGE, UNIX, C

SG, IRIX

1/1

RADOB	SIEMENS, RS 2000

8/11

PILOT		MICROCORA

WS, UNIX, C

DIGICORA

SGI, UNIX, FORTRAN 77*

PC, MS-DOS, C

FUJITSU, OSIV MSP, FORTRAN 77

HP, UNIX, C

PENTHIUM, WINDOWS, VISUAL BASIC

2/2

PILOT SHIP	WS, UNIX, C

FUJITSU, OSIV MSP, FORTRAN 77

10/18

TEMP		MICROCORA

WS, UNIX, C

PENTHIUM, WINDOWS 95, VAISALA SOFTWARE

SGI, UNIX, FORTRAN 77*

PC, MS-DOS, C

FUJITSU, OSIV MSP, FORTRAN 77

DIGICORA

PC, WINDOWS, FORTRAN 77

HP, UNIX, C

PENTHIUM, WINDOWS, VISUAL BASIC

4/3

TEMP SHIP	WS, UNIX, C

NEC, MS-DOS, BASIC & C

FUJITSU, OSIV MSP, FORTRAN 77

PC, WINDOWS, FORTRAN 77

1/1

TEMP DROP	WS, UNIX, C

1/1

ROCOB	NEC, MS-DOS, C

1/2

AMDAR	FUJITSU, OSIV MSP, FORTRAN 77

4/6

GRID 		SGI, UNIX, FORTRAN 77

HP, UNIX, C

HITACHI, VOS3, FORTRAN 77

FUJITSU, OSIV MSP, FORTRAN 77

1/1

WINTEM	SGI, UNIX, FORTRAN 77

6/7

TAF		PC, MS-DOS, C

WS, UNIX, C

PC, WINDOWS NT, VISUAL BASIC

HITACHI, UNIX, C

DEC ALPHA, VMS, FORTRAN

SUN, UNIX, C

1/1

ARFOR	DEC ALPHA, VMS, FORTRAN

2/2

ROFOR	PC, WINDOWS NT, VISUAL BASIC

DEC ALPHA, VMS, FORTRAN

1/1

MAFOR	WS, UNIX, C

3/3

TRACKOB	DOS, FORTRAN 77

IBM 43P, UNIX, C

FUJITSU, OSIV MSP, FORTRAN 77

5/4

BATHY	DOS, FORTRAN 77

IBM 43P, UNIX, C

PC, MS-DOS, BASIC

FUJITSU, OSIV MSP, FORTRAN 77

SGI, UNIX, FORTRAN 77

3/3

TESSAC	DOS, FORTRAN 77

IBM 43P, UNIX, C

SGI, UNIX, FORTRAN 77

1/1

WAVEOB	NEC, MS-DOS, C

1/1

HYDRA	PC, MS-DOS, PASCAL

1/1

HYFOR	PC, MS-DOS, PASCAL

11/9

CLIMAT	PC, MS-DOS, PASCAL 7.0

IBM 43P, UNIX, C

SOLARIS, UNIX, C

SGI, UNIX, FORTRAN 77

NEC, MS-DOS, C

HITACHI, VOS3, FORTRAN 77

FUJITSU, OSIV MSP, FORTRAN 77

DEC ALPHA, VMS, FORTRAN

SIEMENS, RS 2000, ASSEMBLER

HP 720, UNIX, C

IMS, QNX, MILOS 500

7/10

CLIMAT TEMP PENTHIUM, WINDOWS 95, VAISALA SOFTWARE

PC, MS-DOS

IBM 43P, UNIX, C

SGI, UNIX, FORTRAN 77

NEC, MS-DOS, C

FUJITSU, OSIV MSP, FORTRAN 77

HP, UNIX, C

1/1

SAREP	FUJITSU-SUN, SUN OS, C

2/2

SATEM	SUN, UNIX, C

FUJITSU, OSIV MSP, FORTRAN 77

1/2

SATOB	FUJITSU, OSIV MSP, FORTRAN 77

14/13

GRIB		AIX & UNIX, FORTRAN 77

SGI 2000, UNIX, C

CRAY, UNIX, C

CRAY, UNIX, FORTRAN 77

NEC-SX-4, UNIX, FORTRAN 90 AND C

VPP-HP, UNIX, FORTRAN

SUN, UNIX, C

IBM 590H, UNIX, C

HITACHI, VOS3, FORTRAN 77

HITACHI, UNIX, FORTRAN 77

FUJITSU, OSIV MSP, FORTRAN 77

SGI, IRIX, FORTRAN 77

CRAY, UNICOS, FORTRAN 90

SUN, BOLARIS, FORTRAN 77

11/12

BUFR		ALPHA, VMS, FORTRAN

SGI CHALLENGE, UNIX, C

SUN, VERSADOS, PASCAL

SUN, UNIX, C

CYBER 2000U, NOS/VE, FORTRAN & C

UNIX, FORTRAN 77

HITACHI, UNIX, C

NEC, ACOS, COBOL 85

FUJITSU, OSIV MSP, FORTRAN 77

SGI, IRIX, FORTRAN 77

VAX, FORTRAN & C

4/3

CREX		SGI 2000, UNIX, C

PC, MS-DOS, PASCAL 7.0

PC, MS-DOS, GW-BASIC

HITACHI, UNIX, C

### APPENDIX C

I.	Additional questions (number of same answers is indicated in brackets):

1.	If your processing of traditional character codes (FM 12 to FM 88) is automated:

YES  34  NO  17

a. On what computer platform(s) is your software running? (indicate  make/model):

DATA GENERAL/UMS, CDC CYBER 932, MESSIR 1

SGI ORIGIN 200 or  2000 (7)

SGI CHALLENGE XL (2)

SGI INDIGO

PC(12), PC 486(3), IBM PC/AT

IBM PC Pentium II (2)

IBM RISC 6000, HP, COMPAQ

DEC/ALPHA 1000

ICL DRS 6000

MICROVAX 3100/80

HP/T600,SUN ULTRA SPARC (2)

IBM 590H

VAX/4000, SUN/SPARC 2D

CYBER 2000 U

HITACHI S-3800/480, HITACHI 3500, HITACHI 3050RX

Mini-Computers

SUN ULTRA

PDP 11

DEC VAX 5000/240

EC 1061, CM 1420

b. With which operating system?  (e.g. UNIX, MS-DOS) :

AOS/VS, NOS/VE (2)

UNIX (17)

MS-DOS (15)

Windows (4)

VOS3, Windows NT (2), OS IV MSP

AIX, LINUX (3)

V6.22

VS

OPEN VMS (2)

HP-UX

VMS (2), SOLARIS

XENIX (2)

RT11

QNX

ULTRIX 4.3A

CBM, RSX11M4.1, WIN 32

c. What language used by the decoder? (e.g. FORTRAN 77)

FORTRAN 77 (18)

FORTRAN (3)

FORTRAN 90

FORTRAN 4

IDEAFIX/ORACLE

C (15)

BORLAND TURBO C

PL1

PC ASSEMBLER (2)

AUTOCAD

Assembler (2)

PASCAL (2)

BORLAND PASCAL 4.0

BASIC

QBASIC

DELPHI

2.	If your agency uses BUFR,

NO 38, YES 15

a.  For what types of data? Indicate: For	Encoding and/or	Decoding

Observations at automated stations		YES 			YES

Forecasts of upper air soundings

at grid points					YES			YES

TOVS/ATOVS (2)								YES

METEOSAT									YES

Acquisition of surface data from

Automated stations							YES

ERS (2)									YES

Wind profilers								YES

ACARS									YES

SYNOP,SHIP,PILOT,PILOT SHIP

TEMP (2), TEMP SHIP, IAC,

CLIMAT, CLIMAT TEMP				YES			YES

RADAR DATA (6)					YES			YES

SYNOP (2),SYNOP MOBIL,PILOT

TEMP MOBIL, SATEM,SATOB			YES			YES

ALL DATA ARCHIVING				YES			YES

RADAR-CERAD					YES			YES

Aerodrome data					YES			YES

USED FOR ARCHIVING

Most character codes				YES			YES

FM 12,13,15,16,32,33,35,36,51		YES			YES

Wind Profiler						YES			YES

Low-level wind in Typhoon vicinity		YES			YES

TOVS, HI-SATOB, ERS/URA,

METEOSAT0E, 63E, ACARS,

FOREIGN TY									YES

SYNOP,SHIP,PILOT,TEMP,AMDAR,

SATEM,AIREP,TAF,METAR,

SIGMET,SPECI								YES

For SIGWX						YES			YES

Traditional data codes				YES			YES

SSMI data									YES

Wave data									YES

b.  List the advantages of  BUFR

Compactness of data (3), manage any type of data, flexible - expandable for local or international applications (2), overall very powerful

Convenient for calculation

Fully flexible and volume efficient

Allows easy conversion into internal format

General Code Form

Save disk space

Universal form, Data compression, New codes easy to handle

Machine independent, self defined, easy to add or change observational elements

Save disk memory

Efficient for data processing and transmission

Portability and uniformity

The only possibility for composition of RADAR data

Embedded control (?)

c.  List the disadvantages of BUFR

Not human readable (4), tables to be coordinated, data source and data recipient to ensure the same interpretation

High requirement for the used computer

Requires a sophisticated ENCODER/DECODER

For transmission, it requires X25 or TCP/IP

Possible confusion within tables (2)

Tables updating and coordination (3)

Need a decoder/encoder

Binary

Complexity (2), not easily readable

Difficulty in coding and decoding

Decrease accuracy (?)

No standard encoders/decoders, various implementation of codes

Too strict rules (?)

3.	Is your agency already using CREX?  YES 3    NO  54

If no, is your agency planning to use CREX at some stage in the future? YES 23   NO 21

a.  For what types of data?  Indicate:

For Encoding	manual or	automatic and/or Decoding	manual or	automatic

OZONE		1		 3						 1

ALL			2		 2				1		 1 (planned)

SYNOP,METAR,SPECI,PILOT,

TEMP,CLIMAT,CLIMAT TEMP	 1						 1 (planned)

TOTAL OZONE			 2				2		 1 (currently)

RADIOLOGICAL SOUNDING 	 1						    (planned)

OZONE SOUNDING			 1						    (planned)

SYNOP, SYNOP MOBIL		 1						 1 (planned)

RADIOACTIVITY SOUNDINGS	 1						 1 (planned)

TYPHOON FORECAST		 1						 1

CLIMAT, OZONE, MONITORING	 1	1			1		 1 (planned) SYNOP, TEMP			 1						 1 (planned)

SYNOP,SHIP,PILOT,TEMP,AMDAR,

SATEM,AIREP,TAF,METAR,

SIGMET,SPECI							1		1(planned)

SYNOP,SHIP,PILOT,TEMP,SATOB,IOC FLEET					1(planned)

HYDROLOGY									1

SYNOP,PILOT,TEMP,CODAR,

CLIMAT				1	1					1(planned)

b.	List the advantages of CREX.

Close relationship to BUFR, good solution for simple needs, human readable (in recurring cases), flexible

Experience of using CREX will be helpful for migration to BUFR

Similarity of the concept of CREX and BUFR (flexibility, expandability)

CREX can prevent the proliferation of new various character codes (3)

CREX allows direct readability without various decoder

CREX does not require X25 nor TCP/IP for transmission

CREX allows data representation in commonly used units

General Code (universality)

Flexibility allowing to provide different data in different situation

Easy to use code

Flexibility of tables, can be used by not automated centres

c.	List the disadvantages of CREX.

Octal representation of flag tables, limitation for satellite data, less flexible than BUFR (?), not really readable when content varies, does not compress data, coordination of tables, coordination between data source and data recipient

CREX is not volume efficient

Transition of traditional character codes to CREX would require modifications of the existing software

Cost for renewal of existing software

Could be too long a message (2)

Lack experienced staff (training necessary)

4.	If you use or if you plan to use a BUFR or CREX decoder software:

a. On what computer platform(s) is (will be) your software running? (indicate  make/model):

SGI (5) ORIGIN (3)

SGI/CHALLENGE XL (2)

IBM, SUN (4)

DEC/VAX,DEC/ALPHA 1000

SGI/INDY, DEC/ALPHA

HP T600, SUN ULTRA (2) SPARC (2)

HP-UX

IBM 590H

CYBER 2000 U

HITACHI S-3800/480, HITACHI 3500, HITACHI 3050RX

PC (3), Mini-computers

Pentium

Pentium 200Mhz, SGI INDIGO

CRAY Y-MP 86

DIGITAL VAX 3100

DEC ALPHA 2100,4000, IBM/SP 2

b. With which operating system?  (e.g. UNIX, MS-DOS) :

UNIX (19)

UNICOS

DUNIX 4.0 D

LINUX for PC

VMS, OPEN VMS (2)

IRIX (2)/DIGITAL UNIX

SOLARIS (2)

NOS/VE

MS-DOS (5)

VOS3

Windows (2)

c. What language used by the decoder? (e.g. FORTRAN 77)

COBOL

FORTRAN 77 (15)

FORTRAN (6)

C (15)

C++ (3)

Visual C++

AUTOCAD

- What data types are you not able to transmit, receive, and/or process in the alphanumeric (character) WMO Code Forms?

Satellites (2), wind profilers, ACARS

Monitoring reports of regional synoptic network

High resolution products

Forecast vertical profiles

Radar

Radiological sounding

Air pollution data (use internal character code)

Agrometeorological (use internal character code)

Observations and predictions of ENSO, Developing anomalies, ITCZ data, Soil hydrological bilan

Pictorial information

None (6)

Advisories, Forecasts

Aeronautical data and information

No problems (2)

Some aircraft and radiation data

Measured data from automatic station

6.	What types of data do you think are good candidates for representation and exchange in CREX ?

OZONE (2)

ALL

In theory, most data types, but not satellite, not varying observation (not SYNOP?)

Monitoring reports of regional synoptic network, SYNOP (4)

Surface observations(2), Upper-level sounding, Hydrology, Ozone, etc..

Especially the data for which the WMO character codes do not exist, e.g. ozone data, radiological sounding data, air-pollution data, agrometeorological data

Atmospheric CO2, Tropospheric stability indeces, some GRIB parameters(?)

Automatic weather station data reporting at intervals shorter than 1 hour

Data presently being transmitted in BUFR for sometime till all GDPS Centres have the capability to receive and decode BUFR data.

Advisories, Forecasts

Automated weather station’s data (e.g. precipitation intensity)

SHIP, PILOT (2), TEMP(2), SATOB

Climatic data

Measured data from automatic sensors

7.	What codes do you think are good candidates for transition to CREX?

SYNOP (7) Easier to plot with station position as part of the code.  It must be possible to plot manually because computers can fail at critical times,

TEMP (3)

No existing codes, only new data types which cannot be put in BUFR

SHIP (2), PILOT

Ozone codes, some WMO Codes BUT NOT METAR, SPECI, TAF, SYNOP & TEMP

Common used FM Codes

ARFOR,WAVEOB,CLIMAT,SATOB

All character codes

Data from automatic measurement

All alphanumeric codes

HYDRO, CLIMAT  (2)

8.	What types of data do you think are good candidates for representation and exchange in BUFR?

All types of data. (2)

Products of numerical models

Surface observation, Upper-level sounding, Satellite sounding, Hydrology, Ozone, etc…

Data that cannot be represented in character formats (e.g. radar data), upper-air sounding data and gradually all observational data

FM codes commonly used by forecast models

Satellite data

Data with high temporal resolution

Observations, SYNOP (3), TEMP (2)

High resolution satellite derived products and automated aircraft reports.

All, especially satellite data

Automated weather station’s data (e.g. precipitation intensity)

Weather RADAR

All data observed automatically

Must be investigated thoroughly and tested with real data

Upper-air data

RADAR, Satellite data

PILOT

SHIP, HYDRO, CLIMAT

9.	What codes do you think are good candidates for transition to BUFR?

In the short term SATOB.  In the long term all types of data.  Training will be necessary to explain BUFR.  Free exchange of software.

FM 47 GRID

SYNOP (3),  SHIP, BUOY, PILOT, TEMP (3), BATHY, TESAC, SATEM (2),

SATOB (2)

All actually used character codes for representation of observational data

FM codes commonly used by forecast models

Satellite data

BUOY, AMDAR

All codes

All data observed automatically

Must be investigated thoroughly and tested with real data

All alphanumeric codes and CREX

ANNEX TO PARAGRAPH 8

PROPOSAL FOR A MIGRATION STRATEGY

1.	CBS Ext. 98 stated that: “The Commission agreed that the lack of a standard software interface for the binary data formats hampered the migration to BUFR code.  It agreed that the wider use of the table driven formats depended upon development of widely available, easy to use software.”  It is obvious that the development, the free distribution and free maintenance of integrated standard universal BUFR, CREX and GRIB encoders/decoders, for most common operating systems and languages, would have permitted an easier migration to table driven codes.  The ideas expressed below in this document are based on the assumption that the free distribution and maintenance of such packages will be planned and implemented in tandem with these proposals.

#### Preliminary analysis of requirements for observational data

2.	There are presently fifteen GDPS Centres running an operational Global Model (Sao Paolo-INPE- Brazil, Montreal- Canada, Washington-USA, Bracknell-UK, ECMWF, Toulouse-France, Offenbach-Germany, Moscow–Russia/in development, Beijing-China, Seoul-Korea, Tokyo-Japan, NCMRWF-India, Singapore, Melbourne-Australia, Pretoria-South Africa).  The required scientific expertise and the super computer power necessary to run an efficient Global Model suggests that these Centres have the means or can develop the means to process input data in binary formats.  These Centres require, in principle, all the data available (at a certain resolution) to feed their data assimilation system.  BUFR could be their input for all data types.  Climate diagnostic and prediction Centres usually work in delayed mode through INTERNET, or are within main GDPS Centres and can usually process binary data.  Centres running Numerical Weather Prediction Model normally have the capability to receive binary data, however they may also need a Regional Set of all data available in their area.

# 3.	A small National Meteorological Centre which receives products from the “so-called” advanced GDPS Centres normally does not require all the global data.  The usual requirements are only for the observations of the neighboring states.  The requirement may be different for aeronautical reports (METAR, SPECI, TAF, Etc..), where the demand can be intercontinental.

# Transition

4.	Ultimately, all observations transmission should be performed in BUFR.  Every observation transmitted in BUFR requires data communication links for the exchange of files containing BUFR data such as X.25 or TCP/IP GTS links or possibly via INTERNET.  For the majority of GTS Centres, this stage can be reached in a short time period.  Most likely, there will always be requirements for new data to be transmitted in character code for various reasons.

5.	The conversion between BUFR and alphanumeric codes (CREX or traditional Codes) by Telecommunication Centres, in order to transfer the observations to NMCs who cannot receive binary data, will be cumbersome and difficult to implement.  Decoding is not a telecommunication function and may require quality control which is more a data processing function than a telecommunication/transport function.  A better solution is a double transmission, for a certain time period by the originator/producer of the same observations in BUFR and in traditional character format.  For example, the transmission by an NMC of WMO bulletins in both BUFR and SYNOP codes,for the same set of stations during a transition period, would be the solution.  This process should be very carefully implemented with more detailed analyses of requirements for observational data to avoid overloading GTS Centres with large number of bulletins to be relayed.

6.	It is strongly desired to switch to BUFR for exchange of all data.  The CREX equivalent image of BUFR data could be used for the translation of the message back to character format.  This would still provide the advantages of a table driven format to the user unable to receive binary data.  CREX has been made as simple as possible for human readability and usability.  It is also agreed that providing a facility to make easy the conversions between BUFR and CREX, would help the transition to a world with only binary data representation forms.  This could be a positive factor for the transition to BUFR.  The change to a transmission of data only in BUFR can be done when all the recipients can receive binary data.

7.	In the transition stage, the rules for choosing a format for the transmission of observations by the producer (or NMC) should be:

(i)	BUFR shall be used for all transmission of observations whenever possible;

(ii)	if BUFR cannot be used because there is no appropriate telecommunication line or satellite link from the NMC or from the platform to the RDBC, or there is no appropriate hardware (the lack of software should no longer be an argument), or the direct user (within the Region, not in that case the RDBC) of the data cannot receive or process BUFR data, then a traditional WMO alphanumeric code shall be used;

(iii)	if there is no existing WMO alphanumeric code corresponding to the observations or there would be an expansion required to the WMO alphanumeric code for new observed parameters, the CREX code shall be used.

# Application oriented data flow analysis

8.	In fact, a better data management approach would be to find out if the producer can transmit binary data, then if all the potential users of the data are able or not to receive and process binary data.  If they are, there is no need to also transmit in traditional alphanumeric codes.  A survey, performed under the OPAG on ISS, should be able to link the migration strategy with the data flow (from producer to the end user at the application function) within the World Weather Watch, linking the production of observations to the meteorological applications.  Is the universal store and forward system really necessary for all meteorological observations?  Surely, the principle of universal access to meteorological data, within the Resolution 40 frame, has to be offered and preserved, but not necessarily by the use of the "store and forward" system.  One could design data banks (DATA BASES) by type or by region, and selective predefined transmission/concentration.  Then a limited set of files would be systematically forwarded to other Data Banks.  A real time request-reply system could be implemented to satisfy the remaining limited required data flows.

9.	An application oriented data flow analysis, tracing the data from observations to application processing, will determine if the dissemination in character codes is required by all countries for all data types presently transmitted in alphanumeric codes.  To be successful, a change of codes for data transmission has to be undertaken after a thorough data management analysis.  Why are WMO data exchanged and what for?  The old scheme of meteorological observations distributed universally, which was the principles and the purpose in the sixties, when the GTS was developed, is no more true and a serious data flow analysis has to be performed.  However, the principle of universal access to WMO data has to be maintained.  And a new system may even improve it.

10.	For example, many satellite data are already transmitted in BUFR.  It is a necessity because these data are bulky and quite new, requiring many new parameters that only the BUFR tables can accommodate.  For these data the users and the related applications related are limited and only a handful of Centres use these data.  The same logic applies to ACARS, RADAR or profiler data.  A subset of some ACARS and profiler data are also transmitted in parallel in alphanumeric AIREP and PILOT formats.

# New Scheme

11.	From those considerations emerges a pattern where traditional alphanumeric codes are required only within the same Region (or at the border across Regions for neighbor States).  The data flow for traditional alphanumeric codes should be a concentration to a Regional or Inter-Regional Data Bank, located in a main GDPS Centre.  The Regional Data Bank Centre (RDBC) would decode and perform the standard quality control and transform the data into BUFR.  Of course, such functions would have to be trusted by the other GDPS Centres, who would expect the best set of observations from the RDBC.  Then only a limited set of files containing the information of the area of responsability of the RDBC would be systematically forwarded to other RDBCs for further down systematic transmission for operational applications.  Other Centres (from the Region - it might be Centres running NWP models, or from other Regions), needing special information would send a request to the RDBC concerned.  The reply would be performed by TCP/IP file exchange.  The requesting Centre would receive a file of BUFR reports.

12.	The data flow for acquisition of observations would appear then as a set of star type regional networks, the stars being the RDBCs.  The RDBCs would be connected between each other by Very High Speed Connections via an improved GTS.  The RDBCs may also provide an INTERNET access, playing a backup-role and offering access to any NMC in the World connected on INTERNET.  Request reply would be performed on priority between RDBCs themselves, but NMCs or RSMCs could also performed request-reply via the GTS, or via INTERNET.  Data could be provided in BUFR or on demand in CREX format (for small enough data sets).  It is important to separate the mere transport functions from the application functions (the latter comprising the data decoding, the storage, the data processing, the products generation and the archiving).  It is also the applications requirements which determine the set of observations to be performed.

13.	The monitoring of the data acquisition would then be the responsibility of the RDBCs, and only over their respective Region.  There would be no more need for store and forward directories for the observations bulletins, and mistake in updating of directories.  Only a list of expected data in the RDBC.  There would be a regional concentration following the national concentrations, then a limited forwarding of files to other RDBCs, who then will send a limited set of files to RSMCs and NMCs.  With that scheme, it would be possible that within some region, e.g. RA VI all the data could be exchanged and processed in BUFR.  Every NMC being able to receive and decode BUFR data.  While in other regions traditional WMO alphanumeric Codes or CREX codes will be exchanged.  That sheme would have an impact on the GTS functions (defined in the GTS Manual) and the GDPS functions (defined in the GDPS Manual).

###### ANNEX TO PARAGRAPH 9

Procedures for amendment to the Manual on Codes

1.	General Validation and Implementation Procedures

1.1	Amendments to the Manual on Codes must be proposed in writing.  The proposal shall specify the needs, purposes and requirements and include information on a contact point for technical matters.

1.2	The ITC/DR&C*, supported by the Secretariat, shall validate the stated requirements and develop a draft recommendation to respond to the requirements as appropriate.

1.3	A draft recommendation developed by the ICT/DR&C must be endorsed by the Chairperson of OPAG/ISS prior to its consideration by CBS which subsequently submits it for approval to the Executive Council.  Draft recommendations must have followed the procedures described in the paragraph 5.4.31 of the abridged final report of CBS-Ext.(94) before being submitted to a CBS session.  These procedures are given in section 4 below.  During inter-sessional periods, the "fast track" mechanism, prescribed in the section 2 below, is used to ensure the necessary flexibility in responding to urgent requirements of users.

1.4	Updates of the Manual on Codes shall be issued as supplements only once a year in August, and include all changes implemented since the previous update and those approved for implementation on the first Wednesday following the first of November.

2.	Fast Track mechanism for Validation and Implementation

2.1	Fast track mechanism shall be used in inter-sessional periods of CBS for additions to Tables A, B, and D in BUFR or CREX, with associated code tables or flag tables, to Tables 0, 2, and 3 in GRIB Edition 1, to common tables related to character codes, e.g. radiosonde entries, and to other simple additional table entries in character codes.

2.2	Draft recommendations developed by the ICT/DR&C must follow the validation procedures described in 4.1, 4.2 and 4.3 and must be endorsed by the Chairperson of OPAG/ISS, the president of CBS on behalf of the Commission and approved by the President of WMO on behalf of the EC.  However, the filling of reserved and unused entries in the existing code and flag tables are considered editorial adjustments and will be effected by the Secretary-General in consultation with the president of CBS.

2.3	Implementation of amendments approved through the fast track shall normally be limited to one per year and the implementation date should be fixed as the first Wednesday following the first of November.  If the Chairpersons of ICT/DR&C and OPAG/ISS agree that an exceptional situation exists, a second fast track implementation can be initiated.

2.4	WMO Members shall be notified of amendments approved through the fast track timely enough to allow a period at least three months between the receipt of the notification and the date of implementation.

3.	Procedures for correction of existing entries in the BUFR and CREX tables

3.1	If an erroneous specification of an entry is found in the BUFR or CREX table, a new descriptor should normally be added to the table through the fast track procedures and used instead of the old one for encoding (especially if it concerns the data width).  An appropriate explanation shall be added to the notes of the table to clarify the practice along with the date of the change.

3.2	This situation is considered an editorial adjustment according to 2.2.

4.	Validation Procedures with respect to proposed changes to WMO codes and data representation forms

4.1	The need for, and the purpose of, the proposed changes should be fully documented;

4.2	This documentation must include the results of non-operational testing of the changes as described below;

4.3	For new or modified WMO code and data representation forms, proposed changes should be tested by the use of at least two independently developed encoders and two independently developed decoders which incorporated the proposed change.  Where the data originated from a necessarily unique source (for example the data stream from an experimental satellite), the successful testing of a single encoder with at least two independent decoders would be considered adequate.  Results should be made available to the ICT/DR&C with a view to verifying the technical specifications;

4.4	Draft recommendations to be submitted to CBS sessions must be published as pre-session documents at least three months prior to the session.

_____________

ANNEX TO PARAGRAPH 2.1.8

FM 92-XII GRIB - General Regularly-distributed Information in Binary form

CODE FORM:

SECTION 0	Indicator Section

SECTION 1	Identification Section

SECTION 2	(Local Use Section) 						}

}

SECTION 3	Grid Definition Section				}		}

}		}

SECTION 4	Product Definition Section	}		}		}

}		}		} (repeated)

SECTION 5	Data Representation Section 	}		} (repeated)	}

} (repeated)	}		}

SECTION 6	Bit-map Section			}		}		}

}		}		}

SECTION 7	Data Section			}		}		}

SECTION 8	End Section

Notes:

(1)	GRIB is the name of a data representation form for general regularly-distributed information in binary.

(2)	Data encoded in GRIB consists of a continuous bit-stream made of a sequence of octets (1 octet = 8 bits).

(3)	The octets of a GRIB message are grouped into sections:

Section	Section				Section

Number	Name				Contents

0	Indicator Section			“GRIB”, Discipline, GRIB edition number, length of message

1	Identification Section		Length of section, section number, characteristics that apply to all processed data in the GRIB message

2	Local Use Section		Length of section, section number, additional items for local use by

(optional)			originating centres

3	Grid Definition Section		Length of section, section number, geometry of values within the plane described by the two fixed coordinates

4	Product Definition Section		Length of section, section number, description of the data that follows, including the two fixed coordinates

5	Data Representation Section	Length of section, section number, description of how the data that follows is represented

6	Bit-map Section			Length of section, section number, indication of presence or absence of data at each of the grid points, as applicable

7	Data Section			Length of section, section number, data values

8	End Section			“7777"

- Sequences of GRIB sections 2 to 7, sections 3 to 7 or sections 4 to 7 may be repeated within a single GRIB message.  All sections within such repeated sequences must be present and shall appear in the numerical order noted above.  Unrepeated sections remain in effect until redefined.

- It will be noted that the GRIB code is not suitable for visual data recognition without computer interpretation.

- The representation of data by means of series of bits is independent of any particular machine representation.

- Message and section lengths are expressed in octets. Octets are numbered 1, 2, 3, etc., starting at the beginning of each section.  Therefore, octet numbers in a template refer to the respective section.

- Bit positions within octets are referred to as bit 1 to bit 8, where bit 1 is the most significant and bit 8 is the least significant.  Thus, an octet with only bit 8 set to 1 would have the integer value 1.

- As used in "GRIB",  “International Alphabet No. 5" is regarded as an 8-bit alphabet with bit 1 set to zero.

(10)	IEEE single-precision floating-point representation is:

s AAAAAAA ABBBBBBB BBBBBBBB BBBBBBBB

Where:	s is the sign bit, where 0 means positive and 1 means negative

A.... A is an 8-bit integer representing the biased exponent

B.... B is a 23-bit integer representing the significant

REGULATIONS:

92.1	General

92.1.1 	The GRIB code shall be used for the exchange and storage of general regularly-distributed information expressed in binary form.

92.1.2	The beginning and the end of the code shall be identified by 4 octets coded according to the International Alphabet No. 5 to represent the indicators "GRIB" and "7777" in Indicator Section 0 and End Section 8, respectively.  All other octets included in the code shall represent data in binary form.

92.1.3	Each section included in the code shall always end on an octet boundary.  This rule shall be applied by appending bits set to zero to the section where necessary.

92.1.4	All bits set to “1" for any value indicates that value is missing.  This rule shall not apply to packed data.

92.1.5	If applicable, negative values shall be indicated by setting the most significant bit to “1”.

92.1.6	Latitude, longitude, and angle values shall be in units of 10-6 degree.

92.1.7	The latitude values shall be limited to the range 0 to 90 degrees inclusive. Orientation shall be north latitude positive, south latitude negative.  Bit 1 is set to 1 to indicate south latitude.

92.1.8	The longitude values shall be limited to the range 0 to 360 degrees inclusive.  Orientation shall be east longitude positive, with only positive values being used.  Bit 1 is set to 1 to indicate west longitude.

92.1.9	The latitude and longitude of the first grid point and the last grid point shall always be given for regular grids.

92.1.10	Vector components at the North and South Poles shall be coded according to the following conventions.

92.1.10.1 If the resolution and component flags in section 3 (Code table 3.2) indicate that the vector components are relative to the defined grid, the vector components at the Pole shall be resolved relative to the grid.

92.1.10.2 Otherwise, for projections where there are multiple points at a given pole, the U and V components shall be resolved as if measured an infinitesimal distance from the Pole at the longitude corresponding to each grid point.  At the North Pole, the U component at a grid point with longitude L shall be resolved along the meridian 90 degrees East of L, and the V component along the meridian 180 degrees from L.  At the south Pole, the U component at a grid point with longitude L shall be resolved along the meridian 90 degrees East of L, and the V component shall be resolved along L.

92.1.10.3 Otherwise, if there is only one Pole point, either on a cylindrical projection with all but one point deleted, or on any projection (such as polar stereographic) where the Pole maps to a unique point, the U and V components shall be resolved along longitudes 90W and 0 respectively at the North Pole and along longitudes 90W and 180 respectively at the South Pole.

Note: 	(1) This differs from the treatment of the Poles in the WMO traditional alphanumeric codes.

92.1.11	The first and last grid points shall not necessarily correspond to the first and last data points, respectively, if the bit-map is used.

92.2	Section 0 - Indicator Section

92.2.1	Section 0 shall always be 16 octets long.

92.2.2	The first four octets shall always be character coded according to the International Alphabet No. 5 as "GRIB".

92.2.3	The remainder of the section shall contain reserved octets, followed by the Discipline, the GRIB edition number, and the length of the entire GRIB message (including the Indicator Section).

92.3	Section 1 - Identification Section

92.3.1	The length of the section, in units of octets, shall be expressed over the group of the first four octets, i.e., over the first 32 bits.

92.3.2	The section number shall be expressed in the fifth octet.

92.3.3	Octets beyond 21 are reserved for future use and need not be present.

92.4	Section 2 - Local Use Section

92.4.1	Regulations 92.3.1 and 92.3.2 shall apply.

92.4.2	Section 2 is optional.

92.5	Section 3 - Grid Definition Section

92.5.1	Regulations 92.3.1 and 92.3.2 shall apply.

92.6	Section 4 - Product Definition Section

92.6.1	Regulations 92.3.1 and 92.3.2 shall apply.

92.7	Section 5 - Data Representation Section

92.7.1	Regulations 92.3.1 and 92.3.2 shall apply.

92.8	Section 6 - Bit-map Section

92.8.1	Regulations 92.3.1 and 92.3.2 shall apply.

92.9	Section 7 - Data Section

92.9.1	Regulations 92.3.1 and 92.3.2 shall apply.

92.9.2	Data shall be coded using the minimum number of bits necessary to provide the accuracy required by international agreement.  This required accuracy/precision shall be achieved by scaling the data by multiplication by an appropriate power of 10 (which may be 0) after forming the non-negative differences, and then using the binary scaling to select the precision of the transmitted value.

92.9.3	The data shall be packed by the method identified in Section 5.

    - Data shall be coded in the form of non-negative scaled differences from a reference value of the whole field plus, if applicable, a local reference value.

NOTES:

(1) 	A reference value is normally the minimum value of the data set which is represented.

(2) 	The basic concept of complex packing is a splitting of the field values into groups, which share common descriptors, by removal of local reference values (such as local means).  It is intended to reduce data size, though with some overhead due to extra descriptors.

(3) 	The original data value Y (in the units of code table 4.2) can be recovered with the formula:

Y = R + ((X1+X2) * 10D * 2E)

For complex packing schemes,

E   = Binary scale factor,

D   = Decimal scale factor

R   = Reference value of the whole field,

X1 = Reference value (scaled integer) of the group the data value belongs to,

X2 = Positive increment binary value associated with the original scaled value.

For simple packing, E, D, and R are as above, but

X1 = 0,

X2 = Scaled (encoded) value.

92.10	Section 8 - End Section

92.10.1	The end section shall always be 4 octets long, character, character coded according to the International Alphabet No. 5 as "7777".

SPECIFICATION OF OCTET CONTENTS

SECTION 0 - INDICATOR SECTION

Octet No.	Contents

1-4		“GRIB” (coded according to the International Alphabet No. 5.)

5-6		Reserved

7		Discipline - GRIB Master Table Number (see Code Table 0.0)

8		GRIB Edition Number (currently 2)

9-16		Total length of GRIB message in octets (including Section 0)

SECTION 1 - IDENTIFICATION SECTION

Octet No.	Contents

1-4		Length of section in octets (21 or nn)

5		Number of section (“1”)

6-7		Identification of originating/generating centre (see Common Code Table C-1)

8-9		Identification of originating/generating sub-centre (allocated by originating/generating center)

- GRIB Master Tables Version Number (see Code Table 1.0)

- GRIB Local Tables Version Number (see Code Table 1.1)

12		Significance of Reference Time (see Code Table 1.2)

13-14		Year (4 digits)		|

15		Month			|

16		Day			| Reference time of data

17		Hour			|

18		Minute			|

19		Second			|

20		Production status of processed data in this GRIB message (see Code Table 1.3)

21		Type of processed data in this GRIB message (see Code Table 1.4)

22 - nn		Reserved: need not be present

SECTION 2 - LOCAL SECTION USE

Octet No.	Contents

1-4		Length of section in octets (nn)

5		Number of section (“2”)

6-nn		Local use

SECTION 3 - GRID DEFINITION SECTION

Octet No.	Contents

1-4		Length of section in octets (nn)

5		Number of section (“3”)

6 		Source of grid definition (see Code Table 3.0 and Note 1)

7-10		Number of data points

11-12		Grid Definition Template Number (see Code Table 3.1)

13-nn		Grid Definition Template (see Template 3.x, where x is the Grid Definition Template Number

given in 	octets 11-12)

Note:	(1) If octet 6 is not zero, octets beyond 10 may not be supplied.

SECTION 4 - PRODUCT DEFINITION SECTION

Octet No.	Contents

1-4		Length of section in octets (nn)

5		Number of section (“4”)

6-7		Product Definition Template Number (see Code Table 4.0)

8-nn		Product Definition Template (see Template 4.x, where x is the Product Definition Template

Number 	given in octets 6-7.

SECTION 5 - DATA REPRESENTATION SECTION

Octet No.	Contents

1-4		Length of section in octets (nn)

5		Number of section (“5”)

6-9		Number of actual data points where one or more values are specified in Section 7.

10-11		Data Representation Template Number (see Code Table 5.0)

12-nn		Data Representation Template (see Template 5.x, where x is the Data Representation

Template Number given in octets 10-11)

SECTION 6 - BIT-MAP SECTION

Octet No.	Contents

1-4		Length of section in octets (nn)

5		Number of section (“6”)

6		Bit-map indicator (see Code Table 6.0 and Note (1))

7-nn		Bit-map

Note:	(1) If octet 6 is not zero, the length of the Section is 6 and octets 7-nn are not present.

SECTION 7 -  DATA SECTION

Octet Number(s)	Contents

1-4		Length of section in octets (nn)

5		Number of section (“7”)

6-nn		Data in a format described by Data Template 7.x, where x is the Data Representation Template number given in octets 10-11 of Section 5.

SECTION 8 - END SECTION

Octet No.	Contents

1-4		"7777" (coded according to the International Alphabet No. 5.)

TEMPLATE DEFINITIONS

### TEMPLATE DEFINITIONS USED IN SECTION 3

Grid Definition Template 3.0: 	Latitude/longitude (or equidistant cylindrical, or Plate Carree)

Octet Number(s)		Contents

13		Shape of the earth (see Code Table 3.2)

14		Scale factor of radius of spherical earth

15-18		Scaled value of radius of spherical earth

19		Scale factor of major axis of oblate spheroid earth

20-23		Scaled value of major axis of oblate spheroid earth

24		Scale factor of minor axis of oblate spheroid earth

25-28		Scaled value of minor axis of oblate spheroid earth

29-32		Ni - number of points along a parallel

33-36		Nj - number of points along a meridian

37-40		La1 - latitude of first grid point

41-44		Lo1 - longitude of first grid point

45		Resolution and component flags (see Flag Table 3.3)

46-49		La2 - latitude of last grid point

50-53		Lo2 - longitude of last grid point

54-57		Di - i direction increment (see Note (1))

58-61		Dj - j direction increment (see Note (1))

62		Scanning mode (flags - see Flag Table 3.4)

Note:

(1) 	Direction increments are in units of 10-6 degrees.

Grid Definition Template 3.1: 	Rotated Latitude/longitude (or equidistant cylindrical, or Plate Carree)

Octet Number(s)		Contents

13-62		Same as Grid Definition Template 3.0

63-66		Latitude of the southern pole of projection

67-70		Longitude of the southern pole of projection

71-74		Angle of rotation of projection (IEEE 32-bit floating point value)

Notes:

(1) 	Direction increments are in units of 10-6 degree.

(2) 	Three parameters define a general latitude/longitude coordinate system, formed by a general rotation of the sphere.  One choice for these parameters is:

(a)  	The geographic latitude in degrees of the southern pole of the coordinate system, Thetap for example.

(b) 	The geographic longitude in degrees of the southern pole of the coordinate system, Lambdap for example.

(c)  	The angle of rotation in degrees about the new polar axis (measured clockwise when looking from the southern to the northern pole) of the coordinate system, assuming the new axis to have been obtained by first rotating the sphere through Lambdap degrees about the geographic polar axis, and then rotating through (90 = Thetap) degrees so that the southern pole moved along the (previously rotated) Greenwich meridian.

Grid Definition Template 3.2: 	Stretched Latitude/longitude (or equidistant cylindrical, or Plate Carree)

Octet Number(s)		Contents

13-62		Same as Grid Definition Template 3.0

63-66		Latitude of the pole of stretching

67-70		Longitude of the pole of stretching

71-74		Stretching factor (IEEE 32-bit floating point value)

Notes:

  - Direction increments are in units of 10-6 degree.

  - The stretching is defined by three parameters:

(a) 	The latitude in degrees (measured in the model coordinate system) of the “pole of stretching”;

- The longitude in degrees (measured in the model coordinate system) of the “pole of stretching”; and

(c)	The stretching factor C in units of 10-6 represented as an integer.

The stretching is defined by representing data uniformly in a coordinate system with longitude Y and latitude X1, where:

(1 - C2) + (1 + C2) sin X

X1 = sin-1 -----------------------------

(1 + C2) + (1 - C2) sin X

and Y and X are longitude and latitude in a coordinate system in which the “pole of stretching” is the northern pole.  C = 1 gives uniform resolution, while C > 1 give enhanced resolution around the pole of stretching.

Grid Definition Template 3.3:	Stretched and Rotated Latitude/longitude (or equidistant cylindrical, or Plate Carree)

Octet Number(s)		Contents

13-62		Same as Grid Definition Template 3.0

63-66		Latitude of the southern pole of projection

67-70		Longitude of the southern pole of projection

71-74		Angle of rotation of projection (IEEE 32-bit floating point value)

75-78		Latitude of the pole of stretching

79-82		Longitude of the pole of stretching

83-86		Stretching factor (IEEE 32-bit floating point value)

Notes:

(1) 	Direction increments are in units of 10-6 degree.

(2) 	See Note (2) under Grid Definition Template 3.1 - Rotated Latitude/longitude (or equidistant cylindrical, or Plate Carree)

(3) 	See Note (2) under Grid Definition Template 3.2 - Stretched Latitude/longitude (or equidistant cylindrical, or Plate Carree)

Grid Definition Template 3.4:	Thinned Latitude/longitude (or equidistant cylindrical, or Plate Carree)

Octet Number(s)		Contents

13-62		Same as Grid Definition Template 3.0

63-nn		List of numbers of points in each row (nn = (Ni * 2) + 46) or column (nn = (Nj * 2) + 46)

Notes:

(1)	For data on a quasi-regular grid, in which all the rows or columns do not necessarily have the same number of grid points, either Ni (octets 29-32) or Nj (Octets 33-36) and the corresponding Di (octets 54-57) or Dj (octets 58-61) shall be coded with all bits set to 1 (missing); the actual number of points along each parallel or meridian shall be coded in 2 octets of octets 47-nn.

(2) 	A quasi-regular grid is only defined for appropriate grid scanning modes.  Either rows or columns, but not both simultaneously, may have variable numbers of points.  The first point in each row (column) shall be positioned at the meridian (parallel) indicated by octets 37-44.  The grid points shall be evenly spaced in latitude (longitude).

Grid Definition Template 3.10:	Mercator

Octet Number(s)		Contents

13			Shape of the earth (see Code Table 3.2)

14			Scale factor of radius of spherical earth

15-18		Scaled value of radius of spherical earth

19			Scale factor of major axis of oblate spheroid earth

20-23		Scaled value of major axis of oblate spheroid earth

24			Scale factor of minor axis of oblate spheroid earth

25-28		Scaled value of minor axis of oblate spheroid earth

29-32		Ni - number of points along a parallel

33-36		Nj - number of points along a meridian

37-40		La1 - latitude of first grid point

41-44		Lo1 - longitude of first grid point

45			Resolution and component flags (See Flag Table 3.3)

46-49 		LaD - Latitude(s) at which the Mercator projection intersects the Earth (Latitude(s) where Di and Dj are specified)

50-53		La2 - latitude of last grid point

54-57		Lo2 - longitude of last grid point

58			Scanning mode (flags - see Flag Table 3.4)

59-62 		Orientation of the grid, angle between i direction on the map and the equator (see note (1))

63-66		Di - longitudinal direction grid length (see note (2))

67-70		Dj - latitudinal direction grid length (see note (2))

Notes:

(1) 	Limited to the range of 0 to 90 degrees; if the angle of orientation of the grid is neither 0 nor 90 degrees, Di and Dj must be equal to each other.

(2) 	Grid lengths are in units of 10-5 m, at the latitude specified by LaD.

Grid Definition Template 3.20:	Polar stereographic projection

Octet Number(s)		Contents

13			Shape of the earth (see Code Table 3.2)

14			Scale factor of radius of spherical earth

15-18		Scaled value of radius of spherical earth

19			Scale factor of major axis of oblate spheroid earth

20-23		Scaled value of major axis of oblate spheroid earth

24			Scale factor of minor axis of oblate spheroid earth

25-28		Scaled value of minor axis of oblate spheroid earth

29-32		Nx - number of points along X-axis

33-36		Ny - number of points along Y-axis

37-40		La1 - latitude of first grid point

41-44		Lo1 - longitude of first grid point

45			Resolution and component flag (See flag table 3.3 and note (1))

46-49		LaD - Latitude where Dx and Dy are specified

50-53		LoV - orientation of the grid (see note (2))

54-57		Dx - X-direction grid length (see note (3))

58-61		Dy - Y-direction grid length (see note (3))

62			Projection centre flag (See Flag Table 3.5)

63			Scanning mode (See flag table 3.4)

Notes:

(1) 	The resolution flag (bit 3-4 of Flag table 3.3) is not applicable.

(2) 	LoV is the value of the meridian which is parallel to the Y-axis (or columns of the grid) along which latitude increases as the Y-coordinate increases (the orientation longitude may or may not appear on a particular grid).

(3) 	Grid length is in units of 10-5 m at the latitude specified by LaD.

(4) 	Bit 2 of the projection flag is not applicable to the polar stereographic projection.

Grid Definition Template 3.30:	Lambert conformal

Octet Number(s)		Contents

13			Shape of the earth (see Code Table 3.2)

14			Scale factor of radius of spherical earth

15-18		Scaled value of radius of spherical earth

19			Scale factor of major axis of oblate spheroid earth

20-23		Scaled value of major axis of oblate spheroid earth

24			Scale factor of minor axis of oblate spheroid earth

25-28		Scaled value of minor axis of oblate spheroid earth

29-32		Nx - number of points along the X-axis

33-36		Ny - number of points along the Y-axis

37-40		La1 - latitude of first grid point

41-44		Lo1 - longitude of first grid point

45			Resolution and component flags (See Flag Table 3.3)

46-49		LaD - Latitude where Dx and Dy are specified

50-53 		LoV - Longitude of meridian parallel to Y-axis along which latitude increases as the Y-coordinate increases

54-57		Dx - X-direction grid length (see note (1))

58-61		Dy - Y-direction grid length (see note (1))

62			Projection centre flag (see Flag Table 3.5)

63			Scanning mode (see Flag Table 3.4)

64-67		Latin 1 - first latitude from the pole at which the secant cone cuts the sphere

68-71		Latin 2 - second latitude from the pole at which the secant cone cuts the sphere

72-75		Latitude of the southern pole of projection

76-79		Longitude of the southern pole of projection

Notes:

(1) 	Grid lengths are in units tenths of 10-5 m, at the latitude specified by LaD.

(2)	If Latin 1 = Latin 2, then the projection is on a tangent cone.

(3)	The resolution flags (bits 3-4 of Flag Table 3.3) are not applicable

(4) 	LoV is the value of the meridian which is parallel to the Y-axis (or columns of the grid) along which latitude increases as the Y-coordinate increases (the orientation longitude may or may not appear on a particular grid).

# Grid Definition Template 3.40:	Gaussian latitude/longitude

Octet Number(s)		Contents

13			Shape of the earth (see Code Table 3.2)

14			Scale factor of radius of spherical earth

15-18		Scaled value of radius of spherical earth

19			Scale factor of major axis of oblate spheroid earth

20-23		Scaled value of major axis of oblate spheroid earth

24			Scale factor of minor axis of oblate spheroid earth

25-28		Scaled value of minor axis of oblate spheroid earth

29-32		Ni - number of points along a parallel

33-36		Nj - number of points along a meridian

37-40		La1 - latitude of first grid point

41-44		Lo1 - longitude of first grid point

45			Resolution and component flags (see Flag Table 3.3)

46-49		La2 - latitude of last grid point

50-53		Lo2 - longitude of last grid point

54-57		Di - i direction increment (see note (1))

58-61		N - number of parallels between a pole and the equator (see note (2))

62			Scanning mode (flags - see Flag Table 3.4)

Notes:

(1) 	Direction increments are in units of 10-6 degree.

(2) 	The number of parallels between a pole and the equator is used to establish the variable (Gaussian) spacing of the parallels; this value must always be given.

Grid Definition Template 3.41:	Rotated Gaussian latitude/longitude

Octet Number(s)		Contents

13-62		Same as Grid Definition Template 3.40

63-66		Latitude of the southern pole of projection

67-70		Longitude of the southern pole of projection

71-74		Angle of rotation of projection (IEEE 32-bit floating point value)

Notes:

(1) 	Direction increments are in units of 10-6 degree.

(2) 	The number of parallels between a pole and the equator is used to establish the variable (Gaussian) spacing of the parallels; this value must always be given.

(3) 	See Note (2) under Grid Definition Template 3.1 - Rotated Latitude/longitude grid (or equidistant cylindrical, or Plate Carree)

# Grid Definition Template 3.42:	Stretched Gaussian latitude/longitude

Octet Number(s)		Contents

13-62		Same as Grid Definition Template 3.40

63-66		Latitude of the pole of stretching

67-70		Longitude of the pole of stretching

71-74		Stretching factor (IEEE 32-bit floating point value)

Notes:

(1) 	Direction increments are in units of 10-6 degree.

(2) 	The number of parallels between a pole and the equator is used to establish the variable (Gaussian) spacing of the parallels; this value must always be given.

(3) 	See Note (2) under Grid Definition Template 3.2 -Stretched Latitude/longitude (or equidistant cylindrical, or Plate Carree)

# Grid Definition Template 3.43:	Stretched and rotated Gaussian latitude/longitude

Octet Number(s)		Contents

13-62		Same as Grid Definition Template 3.40

63-66		Latitude of the southern pole of projection

67-70		Longitude of the southern pole of projection

71-74		Angle of rotation of projection (IEEE 32-bit floating point value)

75-78		Latitude of the pole of stretching

79-82		Longitude of the pole of stretching

83-86		Stretching factor (IEEE 32-bit floating point value)

Notes:

(1) 	Direction increments are in units of 10-6 degree.

(2) 	The number of parallels between a pole and the equator is used to establish the variable (Gaussian) spacing of the parallels; this value must always be given.

(3) 	See Note (2) under Grid Definition Template 3.1 -Rotated Latitude/longitude (or equidistant cylindrical, or Plate Carree)

(4) 	See Note (2) under Grid Definition Template 3.2 -Stretched Latitude/longitude (or equidistant cylindrical, or Plate Carree)

# Grid Definition Template 3.50:	Spherical harmonic coefficients

Octet Number(s)		Contents

13-16		J - pentagonal resolution parameter

17-20		K - pentagonal resolution parameter

21-24		M - pentagonal resolution parameter

25			Representation type indicating the method used to define the norm (see Code Table 3.6).

26 			Representation mode indicating the order of the coefficients (see Code Table 3.7)

27-30		Latitude of the southern pole of projection

31-34		Longitude of the southern pole of projection

Notes:	(1) 	The pentagonal representation of resolution is general.  Some common truncations are special cases of the pentagonal one:

Triangular	M = J = K

Rhomboidal	K = J + M

Trapezoidal	K = J, K > M

# Grid Definition Template 3.51:	Rotated spherical harmonic coefficients

Octet Number(s)		Contents

13-26		Same as Grid Definition Template 3.50

27-30 	Latitude of the southern pole of projection

31-34		Longitude of the southern pole of projection

35-38		Angle of rotation of projection (IEEE 32-bit floating point value)

Notes:

(1) 	See Note (1) under Grid Definition Template 3.50 - Spherical harmonic coefficients

- See Note (2) under Grid Definition Template 3.1 - Rotated Latitude/longitude grid (or equidistant cylindrical, or Plate Carree)

## Grid Definition Template 3.52:	Stretched spherical harmonic coefficients

Octet Number(s)		Contents

13-26		Same as Grid Definition Template 3.50

27-30		Latitude of the pole of stretching

31-34		Longitude of the pole of stretching

35-38		Stretching factor (IEEE 32-bit floating point value)

Notes:

(1) 	See Note (1) under Grid Definition Template 3.50 - Spherical harmonic coefficients

(2) 	See Note (2) under Grid Definition Template 3.20 - Stretched Latitude/longitude grid (or equidistant cylindrical, or Plate Carree)

# Grid Definition Template 3.53:	Stretched and rotated spherical harmonic coefficients

Octet Number(s)		Contents

13-26		Same as Grid Definition Template 3.50

27-30		Latitude of the southern pole of projection

31-34		Longitude of the southern pole of projection

35-38		Angle of rotation of projection (IEEE 32-bit floating point value)

39-42		Latitude of pole of stretching

43-46		Longitude of pole of stretching

47-50		Stretching factor (IEEE 32-bit floating point value)

Notes:	(1) 	See Note (1) under Grid Definition Template 3.50 - Spherical harmonic coefficients

(2) 	See Note (2) under Grid Definition Template 3.1 -Rotated Latitude/longitude (or equidistant cylindrical, or Plate Carree)

(3) 	See Note (2) under Grid Definition Template 3.2 -Stretched Latitude/longitude (or equidistant cylindrical, or Plate Carree)

Grid Definition Template 3.90:	Space view perspective or orthographic

Octet Number(s)		Contents

13			Shape of the earth (see Code Table 3.2)

14			Scale factor of radius of spherical earth

15-18		Scaled value of radius of spherical earth

19			Scale factor of major axis of oblate spheroid earth

20-23		Scaled value of major axis of oblate spheroid earth

24			Scale factor of minor axis of oblate spheroid earth

25-28		Scaled value of minor axis of oblate spheroid earth

29-32		Nx - number of points along X-axis (columns)

33-36		Ny - number of points along Y-axis (rows or lines)

37-40		Lap - latitude of sub-satellite point

41-44		Lop - longitude of sub-satellite point

45			Resolution and component flags (see Code Table 3.3)

46-49		dx - apparent diameter of Earth in grid lengths, in X-direction

50-53		dy - apparent diameter of Earth in grid lengths, in Y-direction

54-57 		Xp - X-coordinate of sub-satellite point (in units of 10-3 grid length expressed as an integer)

58-61 		Yp - Y-coordinate of sub-satellite point (in units of 10-3 grid length expressed as an integer)

62			Scanning mode (flags - see Flag Table 3.4)

63-66 		Orientation of the grid; i.e., the angle between the increasing Y-axis and the meridian of the sub-satellite point in the direction of increasing latitude (see Note (3))

67-70 		Nr - altitude of the camera from the Earth’s centre, measured in units of the Earth’s (equatorial) radius (see Notes (4) and (5))

71-74		Xo - X-coordinate of origin of sector image

75-78		Yo - Y-coordinate of origin of sector image

Notes:

(1)	It is assumed that the satellite is at its nominal position, i.e., it is looking directly at its sub-satellite point.

(2)	Octets 46-49 shall be set to all ones (missing) to indicate the orthographic view (from infinite distance)

(3) 	It is the angle between the increasing Y-axis and the meridian 180oE if the sub-satellite point is the North Pole; or the meridian 0o if the sub-satellite point is the South Pole.

(4)	The apparent angular size of the Earth will be given by 2 * Arcsin (1/Nr).

- For orthographic view from infinite distance, the value of Nr should be encoded as missing (all bits set to 1).

- The horizontal and vertical angular resolutions of the sensor (Rx and Ry), needed for navigation equation, can be calculated from the following:

Rx = 2 * Arcsin (1/Nr) / dx

Ry = 2 * Arcsin (1/Nr) / dy

Grid Definition Template 3.100: 	Triangular grid based on an icosahedron

Octet Number(s)		Contents

13			n2 - exponent of 2 for the number of intervals on main triangle sides

14			n3 - exponent of 3 for the number of intervals on main triangle sides

15-16		ni - number of intervals on main triangle sides of the icosahedron

17			nd - Number of diamonds

18-21		Latitude of the pole point of the icosahedron on the sphere

22-25		Longitude of the pole point of the icosahedron on the sphere

26-29		Longitude of the center line of the first diamond of the icosahedron on the sphere

30			Grid point position (see Code table 3.8)

31			Numbering order of diamonds (flag - see Flag table 3.9)

32			Scanning mode for one diamond (flags - see Flag table 3.10)

33-36		nt - total number of grid points

Notes:

(1) 	For more details see appendix II to the Manual of Codes, Vol. I, Part B- definition of the triangular grid based on an icosahedron

(2) 	The origin of the grid is an icosahedron with 20 triangles and 12 vertices.  The triangles are combined to nd 	quadrangles, the so-called diamonds  (e.g. if nd = 10, two of the icosahedron triangles form a diamond, and if nd = 5, 4 icosahedron triangles form a diamond).  There are two resolution values called n2 and n3 describing the division of each triangle side.  Each triangle side is divided into ni equal parts where ni = 3**n3 * 2**n2 with n3 either equal to 0 or to 1. In the example of appendix II, the numbering order of the rectangles is anti-clockwise with a view from the pole point on both hemispheres. Diamonds 1 to 5 are northern hemisphere and diamonds 6 to 10 are Southern Hemisphere.

(3) 	The exponent of 3 for the number of divisions of triangle sides is used only with a value of either 0 or 1.

(4) 	The total number of grid points for one global field depends on the grid point position. If e.g. the grid points are located at the vertices of the triangles nt = (ni + 1) * (ni + 1) * nd since grid points at diamond edges are contained in both adjacent diamonds and for the same reason the pole points are contained in each of the five adjacent diamonds.

Grid Definition Template 3.110:	Equatorial azimuthal equidistant projection

Octet Number(s)		Contents

13			Shape of the earth (see Code Table 3.2)

14			Scale factor of radius of spherical earth

15-18		Scaled value of radius of spherical earth

19			Scale factor of major axis of oblate spheroid earth

20-23		Scaled value of major axis of oblate spheroid earth

24			Scale factor of minor axis of oblate spheroid earth

25-28		Scaled value of minor axis of oblate spheroid earth

29-32		Nx - number of points along X-axis

33-36		Ny - number of points along Y-axis

37-40		La1 - latitude of tangency point (center of grid)

41-44		Lo1 - longitude of tangency point

45			Resolution and component flag (see flag table 3.3)

46-49		Dx - X-direction grid length in units of 10-5 m as measured at the point of the axis

50-53		Dy - Y-direction grid length in units of 10-5 m as measured at the point of the axis

54			Projection center flag

55			Scanning mode (see flag table 3.4)

Grid Definition Template 3.120:	Azimuth-range projection

Octet Number(s)		Contents

13-16		Nb - number of data bins along radials (see Note (1))

17-20		Nr - number of radials

21-24		La1 - latitude of center point

25-28		Lo1 - longitude of center point

29-32		Dx - spacing of bins along radials

33-36		Dstart - offset from origin to inner bound

37 - (31+4Nr)		For each of Nr radials:

(31+4(Nr-1)) - (32+4(Nr-1)) Azi - starting azimuth, degree x 10 (degrees as north)

(33+4(Nr-1)) - (34+4(Nr-1)) Adelta - azimuthal width, degrees x 100, (+ clockwise, - counterclockwise)

Note:

(1) 	A data bin is a data point representing the volume centered on it.

TEMPLATE DEFINITIONS USED IN SECTION 4

Product Definition Template 4.0:		Analysis or forecast at a horizontal level or in a horizontal layer at a point in time

Octet Number(s)		Contents

8		Parameter category (see Code Table 4.1).

9		Parameter number (see Code Table 4.2).

10		Type of generating process (see Code Table 4.3)

11		Background generating process identifier (defined by originating center)

12		Analysis or forecast generating processes identifier (defined by originating center)

13-14	Hours of observational data cutoff after reference time (See note (1))

15		Minutes of observational data cutoff after reference time

16		Indicator of unit of time range (see Code Table 4.4)

17-20	Forecast time in units defined by octet 16

21		Type of first fixed surface (see Code Table 4.5)

22		Scale factor of first fixed surface

23-26	Scaled value of first fixed surface

27		Type of second fixed surface (see Code Table 4.5)

28		Scale factor of second fixed surface

29-32	Scaled value of second fixed surface

Note:

(1) 	Hours greater than 65534 will be coded as 65534.

Product Definition Template 4.1:		Individual ensemble forecast, control and perturbed, at a horizontal level or in a horizontal layer at a point in time

Octet Number(s)		Contents

8 		Parameter category (see Code Table 4.1)

9		Parameter number (see Code Table 4.2)

10		Type of generating process (see Code Table 4.3)

11		Background generating process identifier (defined by originating center)

12	 	Forecast generating process identifier (defined by originating center)

13-14 	Hours after reference time of data cutoff  (see note (1))

15    	Minutes after reference time of data cutoff

16		Indicator of unit of time range (See Code Table 4.4)

17-20	Forecast time in units defined by octet 16

21 		Type of first fixed surface (see Code Table 4.5)

22  		Scale factor of first fixed surface

23-26 	Scaled value of first fixed surface

27		Type of second fixed surface (see Code Table 4.5)

28		Scale factor of second fixed surface

29-32	Scaled value of second fixed surface

33		Type of ensemble forecast (see Code Table 4.6)

34		Perturbation number

35		Number of forecasts in ensemble

Note:

(1) 	Hours greater than 65534 will be coded as 65534.

Product Definition Template 4.2:Derived forecast based on all ensemble members at a horizontal level or in a horizontal layer at a point in time

Octet Number(s)		Contents

8			Parameter category (see Code Table 4.1)

9			Parameter number (see Code Table 4.2)

10			Type of generating process (see Code Table 4.3)

11			Background generating process identifier (defined by originating center)

12	 		Forecast generating process identifier (defined by originating center)

13-14		Hours after reference time of data cutoff  (see note (1))

15			Minutes after reference time of data cutoff

16			Indicator of unit of time range (See Code Table 4.4)

17-20		Forecast time in units defined by octet 16

21			Type of first fixed surface (see Code Table 4.5)

22			Scale factor of first fixed surface

23-26		Scaled value of first fixed surface

27			Type of second fixed surface (see Code Table 4.5)

28			Scale factor of second fixed surface

29-32		Scaled value of second fixed surface

33			Derived forecast (see Code Table 4.7)

34			Number of forecasts in ensemble

Note:

(1) 	Hours greater than 65534 will be coded as 65534.

Product Definition Template 4.3:Derived forecasts based on a cluster of ensemble members over a rectangular area at a horizontal level or in a horizontal layer at a point in time

Octet Number(s)		Contents

8 		Parameter category (see Code Table 4.1)

9 		Parameter number (see Code Table 4.2)

10		Type of generating process (see Code Table 4.3)

11		Background generating process identifier (defined by originating center)

12		Forecast generating process identifier (defined by originating center)

13-14	Hours after reference time of data cutoff  (see note (1))

15		Minutes after reference time of data cutoff

16		Indicator of unit of time range (See Code Table 4.4)

17-20	Forecast time in units defined by octet 16

21		Type of first fixed surface (see Code Table 4.5)

22		Scale factor of first fixed surface

23-26	Scaled value of first fixed surface

27		Type of second fixed surface (see Code Table 4.5)

28		Scale factor of second fixed surface

29-32	Scaled value of second fixed surface

33		Derived forecast (see Code Table 4.7)

34		Number of forecasts in the ensemble (N)

35		Cluster identifier

36		Number of cluster to which the high resolution control belongs

37		Number of cluster to which the low resolution control belongs

38		Total number of clusters

39		Clustering method (see Code Table 4.8)

40-43	Northern latitude of cluster domain

44-47	Southern latitude of cluster domain

48-51	Eastern longitude of cluster domain

52-55	Western longitude of cluster domain

56-(55+N)	List of N ensemble forecast numbers

Note:

(1) 	Hours greater than 65534 will be coded as 65534.

Product Definition Template 4.4:	Derived forecasts based on a cluster of ensemble members over a circular area at a horizontal level or in a horizontal layer at a point in time

Octet Number(s) 		Contents

8 		Parameter category (see Code Table 4.1)

9 		Parameter number (see Code Table 4.2)

10		Type of generating process (see Code Table 4.3)

11		Background generating process identifier (defined by originating center)

12		Forecast generating process identifier (defined by originating center)

13-14	Hours after reference time of data cutoff  (see note (1))

15		Minutes after reference time of data cutoff

16		Indicator of unit of time range (See Code Table 4.4)

17-20	Forecast time in units defined by octet 16

21		Type of first fixed surface (see Code Table 4.5)

22		Scale factor of first fixed surface

23-26	Scaled value of first fixed surface

27		Type of second fixed surface (see Code Table 4.5)

28		Scale factor of second fixed surface

29-32	Scaled value of second fixed surface

33		Derived forecast (see Code Table 4.7)

34		Number of forecasts in the ensemble (N)

35		Cluster identifier

36		Number of cluster to which the high resolution control belongs

37		Number of cluster to which the low resolution control belongs

38		Total number of clusters

39		Clustering method (see Code Table 4.8)

40-43	Latitude of central point in cluster domain

44-47	Longitude of central point in cluster domain

48-51	Radius of cluster domain

52-(51+N)	List of N ensemble forecast numbers

Note:

(1) 	Hours greater than 65534 will be coded as 65534.

Product Definition Template 4.5:	Probability forecasts at a horizontal level or in a horizontal layer at a point in time

Octet Number(s) 		Contents

- Parameter category (see Code Table 4.1)

- Parameter number (see Code Table 4.2)

10		Type of generating process (see Code Table 4.3)

11		Background generating process identifier (defined by originating center)

12		Forecast generating process identifier (defined by originating center)

13-14	Hours after reference time of data cutoff  (see note (1))

15		Minutes after reference time of data cutoff

16		Indicator of unit of time range (See Code Table 4.4)

17-20	Forecast time in units defined by octet 16

21		Type of first fixed surface (see Code Table 4.5)

22		Scale factor of first fixed surface

23-26	Scaled value of first fixed surface

27		Type of second fixed surface (see Code Table 4.5)

28		Scale factor of second fixed surface

29-32	Scaled value of second fixed surface

33		Forecast probability number

34		Total number of forecast probabilities

35		Probability type (see Code Table 4.9)

36		Scale factor of lower limit

37-40	Scaled value of lower limit

41		Scale factor of upper limit

42-45	Scaled value of upper limit

Note:

(1) 	Hours greater than 65534 will be coded as 65534.

Product Definition Template 4.6:		Percentile forecasts at a horizontal level or in a horizontal layer at a point in time

Octet Number(s) 		Contents

8		Parameter category (see Code Table 4.1)

9 		Parameter number (see Code Table 4.2)

10		Type of generating process (see Code Table 4.3)

11		Background generating process identifier (defined by originating center)

12		Forecast generating process identifier (defined by originating center)

13-14	Hours after reference time of data cutoff  (see note (1))

15		Minutes after reference time of data cutoff

16		Indicator of unit of time range (See Code Table 4.4)

17-20	Forecast time in units defined by octet 16

21		Type of first fixed surface (see Code Table 4.5)

22		Scale factor of first fixed surface

23-26	Scaled value of first fixed surface

27		Type of second fixed surface (see Code Table 4.5)

28		Scale factor of second fixed surface

29-32	Scaled value of second fixed surface

33		Percentile value (from 100% to 0%)

Note:

(1) 	Hours greater than 65534 will be coded as 65534.

Product Definition Template 4.7:	Analysis or forecast error at a horizontal level or in a horizontal layer at a point in time

Octet Number(s) 		Contents

8		Parameter category (see Code Table 4.1)

9		Parameter number (see Code Table 4.2)

10		Type of generating process (see Code Table 4.3)

11		Background generating process identifier (defined by originating center)

12		Analysis or forecast generating process identifier (defined by originating center)

13-14	Hours after reference time of data cutoff  (see note (1))

15		Minutes after reference time of data cutoff

16		Indicator of unit of time range (See Code Table 4.4)

17-20	Forecast time in units defined by octet 16

21		Type of first fixed surface (see Code Table 4.5)

22		Scale factor of first fixed surface

23-26	Scaled value of first fixed surface

27		Type of second fixed surface (see Code Table 4.5)

28		Scale factor of second fixed surface

29-32	Scaled value of second fixed surface

Note:

(1) 	Hours greater than 65534 will be coded as 65534.

Product Definition Template 4.8:	Average, accumulation, and/or extreme values at a horizontal level or in a horizontal layer in a continuous or non-continuous time interval

Octet Number(s)		Contents

8 		Parameter category (see Code Table 4.1)

9 		Parameter number (see Code Table 4.2)

10		Type of generating process (see Code Table 4.3)

11		Background generating process identifier (defined by originating center)

12		Analysis or Forecast generating process identifier (defined by originating center)

13-14	Hours after reference time of data cutoff  (see note (1))

15		Minutes after reference time of data cutoff

16		Indicator of unit of time range (See Code Table 4.4)

17-20	Forecast time in units defined by octet 16 (see Note (2))

21		Type of first fixed surface (see Code Table 4.5)

22		Scale factor of first fixed surface

23-26	Scaled value of first fixed surface

27		Type of second fixed surface (see Code Table 4.5)

28		Scale factor of second fixed surface

29-32	Scaled value of second fixed surface

33-34	Year		|

35		Month		|

36		Day		|Time of end of overall time interval

37		Hour		|

38		Minute		|

39		Second

40		n - Number of time range specifications describing the time intervals used to calculate the statistically processed field

  - Total number of data values missing in statistical process.

  - Specification or the outermost (or only) time range over which statistical processing is done

45		Statistical process used to calculate the processed field from the field at each time increment during the time range (see Code Table 4.10)

46		Type of time increment between successive fields used in the statistical processing (See Code Table 4.11)

47		Indicator of unit of time for time range over which statistical processing is done (See Code Table 4.3)

48-51		Length of the time range over which statistical processing is done, in units defined by the previous octet

52		Indicator of unit of time for the increment between the successive fields used (See Code Table 4.3)

53-56		Time increment between successive fields, in units defined by the previous octet (See note 3)

57-nn		These octets are included only if n>1, where nn = 45 + 12*n

57-68		As octets 45 to 56, next innermost step of processing

69-nn		Additional time range specifications, included in accordance with the value of n.  Contents as octets 45 to 56, repeated as necessary.

Notes:

(1)	Hours greater than 65534 will be coded as 65534.

(2)	The reference time in section 1 and the forecast time together define the beginning of the overall time interval.

(3)	An increment of zero means that the statistical processing is the result of a continuous (or near continuous) process, not the processing of a number of discrete samples.  Examples of such continuous processes are the temperatures measured by analogue maximum and minimum thermometers or thermographs, and the rainfall measured by a rain gauge.

(4)	The reference and forecast times are successively set to their initial values plus or minus the increment, as defined by the type of time increment (one of octets 46, 58, 70 ...).  For all but the innermost (last) time range, the next inner range is then processed using these reference and forecast times as the initial reference and 	forecast time.

#### Product Definition Template 4.20:	Radar product

Octet Number(s)		Contents

8			Parameter category (see Code Table 4.1).

9			Parameter number (see Code Table 4.2).

10			Type of generating process (see Code Table 4.3)

11			Number of radar sites used

12			Indicator of unit of time range

13-16			Site latitude (hundredths of degree)

17-20			Site longitude (hundredths of degree)

21-22			Site elevation (meters)

23-26			Site ID (alphanumeric)

27-28			Site ID (numeric)

29			Operating mode (see Code Table 4.12)

30			Reflectivity calibration constant (tenths of dB)

31			Quality control indicator (see Code Table 4.13)

32			Clutter filter indicator (see Code Table 4.14)

33			Constant antenna elevation angle (tenths of degree true)

34-35			Accumulation interval (minutes)

36			Reference reflectivity for echo top (dB)

37-39			Range bin spacing (m)

40-41			Radial angular spacing (tenths of degree true)

Product Definition Template 4.30:		Satellite Product.

Octet Number(s)		Contents

8		Parameter category (see Code Table 4.1)

9		Parameter number (See Code Table 4.2)

10		Type of generating process (see Code Table 4.3)

11		Observation generating process identifier (defined by originating centers)

12		Number of contributing bands (NB)

Repeat the following 5 values for each contributing band (nb = 1,NB)

(13+5(nb-1))	Satellite series of band nb (code table defined by originating/generating center)

(14+5(nb-1))	Satellite numbers of band nb (code table defined by originating/generating center)

(15+5(nb-1))	Instrument types of band nb (code table defined by originating/generating center)

(16+5(nb-1))	Central wavelength number of band nb

(17+5(nb-1))	Central wavelength power of 10 of band nb

#### Product Definition Template 4.254:	CCITTIA5 character string

Octet Number(s)		Contents

8			Parameter category (see Code Table 4.1).

9			Parameter number (see Code Table 4.2).

10-13		Number of characters

TEMPLATE DEFINITIONS USED IN SECTION 5

#### Data Representation Template 5.0:	Grid point data - simple packing

Octet Number(s)		Contents

12-15		Reference value (R) (IEEE 32-bit floating-point value)

16-17		Binary scale factor (E)

18-19		Decimal scale factor (D)

20			Number of bits containing each packed value (field width)

21	Type of original field values (see Code Table 5.1)

#### Data Representation Template 5.1:	Matrix values at grid point -simple packing

Octet Number(s)		Contents

12-21		Same as Data Representation Template 5.0

22		0, no matrix bit maps present; 1 matrix bit maps present.

23-26		Number of data values encoded in Section 7

27-28		NR - first dimension (rows) of each matrix.

29-30		NC - second dimension (columns) of each matrix.

31		First dimension coordinate value definition (Code Table 5.2)

32		NC1 - number of coefficients or values used to specify first dimension coordinate function.

33		Second dimension coordinate value definition (Code Table 5.2)

34		NC2 - number of coefficients or values used to specify second dimension coordinate function

35		First dimension physical significance (Code Table 5.3)

36		Second dimension physical significance (Code Table 5.3)

37-(36+NC1*4)		Coefficients to define first dimension coordinate values in functional form, or the explicit coordinate values (IEEE 32-bit floating-point value)

(37+NC1*4)- (36+4(NC1+NC2))

Coefficients to define second dimension coordinate values in functional form, or the explicit coordinate values (IEEE 32-bit floating-point value)

Notes:

(1) 	This form of representation enables a matrix of values to be depicted at each grid point; the two dimensions of the matrix may represent coordinates expressed in terms of two elemental parameters (e.g. direction and frequency for wave spectra).  The numeric values of these coordinates, beyond that of simple subscripts, can be given in a functional form, or as a collection of explicit numbers.

(2) 	Some simple coordinate functional forms are tabulated in Code Table 5.2.  Where a more complex coordinate function applies, the coordinate values shall be explicitly denoted by the inclusion of the actual set of values rather than the coefficients.  This shall be indicated by a code figure 0 from Code Table 5.2; the number of explicit values coded shall be equal to the appropriate dimension of the matrix for which values are presented and they shall follow octet 36 in place of the coefficients.

(3) 	Matrix bit maps will be present only if indicated by octet 22. If present, there shall be one bit map for each grid point with data values, as defined by the primary bit map in Section 6, each of length (NR*NC) bits: a bit set to 1 will indicate a data element at the corresponding location within the matrix.  Bit maps shall be represented end-to-end, without regard for octet boundaries; the last bit map shall, if necessary, be followed by bits set to zero to fill any partially used octet.

(4)	Matrices restricted to scanning in the +  i direction (left to right) and in the -j direction (top to bottom).

Data Representation Template 5.2:	Grid point data - complex packing

Octet Number(s)		Contents

12-21 		Same as Data Representation Template 5.0 - Field width applying here to «group references»

22			Basic splitting method in use (see Code Table 5.4)

23			Use of explicit missing values (see Code Table 5.5)

24-27		Primary missing value substitute

28-31		Secondary missing value substitute

32-35		NG - Number of groups of data values into which field is split

36			Reference for widths of groups

37 			Field width for incremental widths of groups (after removal of reference specified at previous octet)

38-41		Reference for lengths of groups

42 			Field width for incremental lengths of groups (after removal of reference specified at previous octet)

Notes:

(1) 	Group lengths have no meaning for row by row packing, where groups are coordinate lines (so the Grid Description Section and possibly the Bit-map Section are enough); for consistency associated field width and reference should then be encoded as 0.

(2) 	For row by row packing with a bit-map, there should always be as many groups as rows. In case of rows with only missing values, all associated descriptors should be coded as zero.

(3) 	Management of widths/lengths descriptors also into a reference and increments is a way to save descriptor size, which is an issue as far as compression gains are concerned.

(4) 	Management of explicitly missing values is an alternative to bit-map use within Section 6; it is intended to reduce the whole GRIB message size.

(5) 	There may be two types of missing value(s), such as to make a distinction between static misses (for instance, due to a land/sea mask) and occasional misses.

(6) 	As an extra option, substitute value(s) for missing data may be specified. If not wished (or not applicable), all bits should be set to 1 for relevant substitute value(s).

(7) 	If substitute value(s) are specified, type of content should be consistent with original field values (floating-point -and then IEEE 32-bit encoded-, or integer).

(8) 	If primary missing values are used, such values are encoded within appropriate group with all bits set to 1 at packed data level.

- If secondary missing values are used, such values are encoded within appropriate group with all bits set to 1, except the last one set to 0, at packed data level.

(10) 	A group containing only missing values (of either type) will be encoded as a constant group (null width, no associated data) and the group reference will have all bits set to 1 for primary type, and all bits set to 1, except the last bit set to 0, for secondary type.

(11) 	If necessary, group widths and/or field width of group references may be enlarged to avoid ambiguities between missing value indicator(s) and true data.

Data Representation Template 5.3: 	Grid point data - complex packing and spatial differencing

Octet Number(s)		Contents

12- 42		Same as Data Representation Template 5.2

43			Order of spatial differencing (see Code Table 5.6)

44 			Field width of spatial differencing extra descriptors (initial values of original scaled data values -integer-, overall minimum of spatial differences)

Note:

(1) 	Spatial differencing is a preprocessing before group splitting at encoding time. It is intended for smooth enough fields to get a reduced data size when combined with a splitting scheme as described in the previous template. At order 1, f (1) is retained and scaled field values are replaced by f (2)-f (1), f (n)-f (n-1). At order 2, processing is iterated. To keep values positive in order to apply splitting scheme, the overall minimum of the resulting field is removed. At decoding time, after bit string unpacking, the original scaled values are recovered by adding the overall minimum and summing up recursively.

TEMPLATE DEFINITIONS USED IN SECTION 7

#### Data Template 7.0:	Grid point data - simple packing

Octet Number(s)		Contents

6-nn		Binary data values - binary string, with each (scaled) data value

Data Template 7.1: 	Matrix values at grid point -simple packing

Octet Number(s)		Contents

6-nn		Binary data values - binary string, with each (scaled) data value

Notes:

(1) 	Group descriptors mentioned above may not be physically present; if associated field width is 0.

(2) 	Group lengths have no meaning for row by row packing; for consistency associated field width should then be encoded as 0. So no specific test for row by row case is mandatory at decoding software level to handle encoding/decoding of group descriptors.

Data Template 7.2: 	Grid point data - complex packing

Octet Number(s)	Contents

6-xx		Reference values of groups (X1 in decoding formula)

- NG values, encoded on field width described at octet 20 of DRT

[xx+1]-yy		Widths increments of groups

- NG values, encoded on field width described at octet 37 of DRT

[yy+1]-zz		Lengths increments of groups - not present for row by row splitting

- NG values, encoded on field width described at octet 42 of DRT

[zz+1]-nn	Incremental binary data values (X2 in decoding formula) - packed binary string of groups of (deviations from group references), where field width is the group one, and so may vary from one group to another

Notes:

(1) 	Group descriptors mentioned above may not be physically present; if associated field width is 0.

(2) 	Group lengths have no meaning for row by row packing; for consistency associated field width should then be encoded as 0. So no specific test for row by row case is mandatory at decoding software level to handle encoding/decoding of group descriptors.

(3) 	For groups with a constant value, associated field width is 0, and no incremental data are physically present.

Data Template 7.3:	Grid point data - complex packing and spatial differencing

Octet Number(s)		Contents

6-ww 		First values of original (undifferenced) scaled data values, followed by the overall minimum of differences  (To be added at decoding time to unsplit values, before the sum up which reverses the differentiation) - number of values is (order of differenciation +1); field width is described at octet 43 of DRS

[ww+1]-xx		Reference values of groups (X1 in decoding formula)

- NG values, encoded on field width described at octet 20 of DRT 5.3

[xx+1]-nn		Same as for DT 7.2

Notes:

(1) 	Extra descriptors related to spatial differencing are added before the splitting descriptors, to reflect the separation between the 2 approaches. It enables to share software parts between cases with and without spatial differencing.

(2) 	The position of overall minimum after initial data values is a choice that enables less software management.

(3) 	Overall minimum will be negative in most cases. First bit should indicate the sign: 0 if positive, 1 if negative.

CODE AND FLAG TABLES

CODE TABLES USED IN SECTION 0

Code Table 0.0:		Discipline of processed data in the GRIB message, number of GRIB Master Table

Code figure	Meaning

0		Meteorological products

1		Hydrological products

2		Land surface products

3		Space products

4-9		Reserved

10		Oceanographic products

11-191		Reserved

192-254		Reserved for local use

255		Missing

CODE TABLES USED IN SECTION 1

Code Table 1.0:	GRIB Master Tables Version Number

Code figure	Meaning

0		Experimental

1		Initial operational version number

2-254 		future operational version numbers

255		local table used

Code Table 1.1:	GRIB Local Tables Version Number

Code figure	Meaning

0		Local tables not used

1-254		Number of local tables version used

255		Missing

Code Table 1.2:	Significance of Reference Time

Code figure	Meaning

0		Analysis

1		Start of forecast

2		Verifying time of forecast

3-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 1.3:	Production status of data

Code figure	Meaning

0		Operational products

1		Operational test products

2		Research products

3		Re-analysis products

4-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 1.4:	Type of data

Code figure	Meaning

0		Analysis products

1		Forecast products

2		Analysis and forecast products

3		Control forecast products

4		Perturbed forecast products

5		Control and perturbed forecast products

6		Processed satellite observations

7		Processed radar observations

8-191		Reserved

192-254		Reserved for local use

255		Missing

Note:		An initialized analysis is considered a zero-hour forecast

CODE AND FLAG TABLES USED IN SECTION 3

Code Table 3.0: 		Source of Grid Definition

Code figure	Meaning				Comments

0		Specified in Section 3.1

1		Predetermined grid definition 	Defined by originating centre

2-191		Reserved

192-254		Reserved for local use

255		A grid definition does not apply to this product

Code Table 3.1:   	Grid Definition Template Number

Code figure	Meaning				Comments

0		Latitude/longitude		Also called equidistant cylindrical, or Plate Carree.

1		Rotated latitude/longitude

2		Stretched latitude/longitude

3		Stretched and rotated latitude/longitude

4		Thinned latitude/longitude

5-9		Reserved

10		Mercator

11-19		Reserved

20		Polar stereographic		can be south or north.

21-29		Reserved

30		Lambert Conformal		can be secant or tangent, conical or bipolar.

(Also called Albers equal-area.)

31-39		Reserved

40		Gaussian latitude/longitude

41		Rotated Gaussian latitude/longitude

42		Stretched Gaussian latitude/longitude

43		Stretched and rotated Gaussian latitude/longitude

44-49		Reserved

50		Spherical harmonic coefficients

51		Rotated spherical harmonic coefficients

52		Stretched spherical harmonic coefficients

53		Stretched and rotated spherical harmonic coefficients

54-89		Reserved

90		Space view perspective orthographic.

91-99		Reserved

100		Triangular grid based on an icosahedron

101-109		Reserved

110		Equatorial azimuthal equidistant projection

111-119		Reserved

120		Azimuth-range projection

121- 32767	Reserved

32768-65534	Reserved for local use

65535		Missing

Code Table 3.2:		Shape of the Earth

Code figure	Meaning

0		Earth assumed spherical with radius = 6367.47 km

1		Earth assumed spherical with radius specified by data producer

2		Earth assumed oblate spheroid with size as determined by IAU in 1965 (major axis = 6378.160 km, minor axis = 6356.775 km, f = 1/297.0)

3		Earth assumed oblate spheroid with major and minor axes specified by data producer

4-191		Reserved

192-254		Reserved for local use

255		Missing

Flag Table 3.3:		Resolution and Component Flags

Bit

Number            Value 	Meaning

1-2			Reserved

3		0	i direction increments not given

1	i direction increments given

4		0	j direction increments not given

1	j direction increments given

5		0 	Resolved u- and v- components of vector quantities relative to easterly and northerly directions

1 	Resolved u- and v- components of vector quantities relative to the defined grid in the direction of increasing x and y (or i and j) coordinates respectively

6-8			Reserved - set to zero

Flag Table 3.4:		Scanning Mode

Bit

Number      Value		Meaning

1	         0		Points of first row or column scan in the +i (+x) direction

1		Points of first row or column scan in the -i (-x) direction

2	         0		Points of first row or column scan in the -j (-y) direction

1		Points of first row or column scan in the +j (+y) direction

3	         0		Adjacent points in i (x) direction are consecutive

1		Adjacent points in j (y) direction is consecutive

4	         0		All rows scan in the same direction

1		Adjacent rows scans in the opposite direction

5-8			Reserved

Notes:

(1)	i direction: west to east along a parallel or left to right along an X-axis

(2)	j direction: south to north along a meridian, or bottom to top along a Y-axis

Flag Table 3.5: 		Projection Centre

Bit

Number	  Value	Meaning

1              0 	North Pole is on the projection plane

1      	South Pole is on the projection plane

2              0 	Only one projection centre is used

1      	Projection is bi-polar and symmetric

Code table 3.6:		Spectral data representation type

Copy from WMO #306, Vol. I.2, part B

Code table 3.7:		Spectral data representation mode

Copy from WMO #306, Vol. I.2, part B

Code table 3.8:		Grid point position

Code

Figure		Meaning

0		Grid points at triangle vertices

1		Grid points at centres of triangles

2		Grid points at midpoints of triangle sides

3-191		Reserved

192-254		Reserved for local use

255		Missing

Flag table 3.9:		Numbering order of diamonds as seen from the corresponding pole

Bit No.	Value	Meaning

1             0	Clockwise orientation

1	Anti-clockwise (i.e., counter-clockwise) orientation

2-8		Reserved

Flag table 3.10:		Scanning mode for one diamond

Bit No.	Value	Meaning

1             0	Points scan in +i direction, i.e. from pole to equator

1	Points scan in -i direction, i.e. from equator to pole

2             0	Points scan in +j direction, i.e. from west to east

1	Points scan in -j direction, i.e. from east to west

3	    0	Adjacent points in i direction are consecutive

1	Adjacent points in j direction is consecutive

4-8		Reserved

CODE AND FLAG TABLES USED IN SECTION 4

Code Table 4.0:		Product Definition Template Number

Number		Description

0		Analysis or forecast at a horizontal level or in a horizontal layer at a point in time

1 		Individual ensemble forecast, control and perturbed, at a horizontal level or in a horizontal layer at a point in time

2 		Derived forecast based on all ensemble members at a horizontal level or in a horizontal layer at a point in time

3 		Derived forecasts based on a cluster of ensemble members over a rectangular area at a horizontal level or in a horizontal layer at a point in time

4 		Derived forecasts based on a cluster of ensemble members over a circular area at a horizontal level or in a horizontal layer at a point in time

5		Probability forecasts at a horizontal level or in a horizontal layer at a point in time

6		Percentile forecasts at a horizontal level or in a horizontal layer at a point in time

7		Analysis or forecast error at a horizontal level or in a horizontal layer at a point in time

8		Average, accumulation, extreme values or other statistically processed value at a horizontal level or in a horizontal layer in a continuous or non-continuous time interval

9-19		Reserved

20		Radar product

21-29		Reserved

30		Satellite product

31-253		Reserved

254		CCITTIA5 character string

255-32767 	Reserved

32768-65534   	Reserved for local use

65535		Missing

Code Table 4.1:		Category of parameters by product discipline

Product Discipline 0:	Meteorological products

Category	Description

0		Temperature

1		Moisture

2		Momentum

3		Mass

4		Short-wave Radiation

5		Long-wave Radiation

6		Cloud

7		Thermodynamic Stability indices

8		Kinematic Stability indices

9		Temperature Probabilities

10		Moisture Probabilities

11		Momentum Probabilities

12		Mass Probabilities

13		Aerosols

14		Trace gases (e.g., ozone, CO2)

15		Radar

16		Forecast Radar Imagery

17		Electro-dynamics

18		Nuclear/radiology

19		Physical atmospheric properties

20-189		Reserved

190		CCITTIA5 string

191		Miscellaneous

192-254		Reserved for local use

255		Missing

Product Discipline 1:	Hydrological products

Category	Description

0		Hydrology

1		Hydrology probabilities

2-192		Reserved

192-254		Reserved

255		Missing

Product Discipline 2:	Land surface products

Category	Description

0		Vegetation/Biomass

1		Agri-/aquacultural Special Products

2		Transportation-related Products

3		Soil Products

4-191		Reserved

192-254		Reserved

255		Missing

Product Discipline 3: 	Space Products

Category	Description

0		Satellite, derived imager products

1		Satellite, derived sounder products

2		Satellite, infra-red imagery

3		Satellite, visible imagery

5		Satellite, water vapor imagery

4-191		Reserved

192-254		Reserved

255		Missing

Product Discipline 10 - Oceanographic products

Category	Description

0		Waves

1		Currents

2		Ice

3		Surface Properties

4		Sub-surface Properties

5-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 4.2	Parameter number by product discipline and parameter category

Product Discipline 0:	Meteorological products, 	Parameter Category 0:	Temperature

Number		Parameter							Units

0		Temperature							K

1		Virtual temperature						K

2		Potential temperature						K

3		Pseudo-adiabatic potential temperature				K

or equivalent potential temperature

4		Maximum temperature						K

5		Minimum temperature						K

6		Dew point temperature						K

7		Dew point depression (or deficit)					K

8		Lapse rate							K m-1

9		Temperature anomaly						K

10		Latent heat net flux						W m-2

11		Sensible heat net flux						W m-2

12		Heat index							K

13		Wind chill factor							K

14		Minimum dew point depression					K

15		Virtual potential temperature					K

16-191		Reserved

192-254		Reserved for local use

255		Missing

Product Discipline 0:	Meteorological products, 	Parameter Category 1:	Moisture

Number		Parameter							Units

0		Specific humidity							kg kg-1

1		Relative humidity						%

2		Humidity mixing ratio						kg kg-1

3		Precipitable water						kg m-2

4		Vapor pressure							Pa

5		Saturation deficit							Pa

6		Evaporation							kg m-2

7		Precipitation rate							kg m-2 s-1

8		Total precipitation						kg m-2

9		Large scale precipitation (non-convective)				kg m-2

10		Convective precipitation						kg m-2

11		Snow depth							m

12		Snowfall rate water equivalent					kg m-2 s-1

13		Water equivalent of accumulated snow depth			kg m-2

14		Convective snow							kg m-2

15		Large scale snow							kg m-2

16		Snow melt							kg m-2

17		Snow age							day

18		Absolute humidity						kg m-3

19		Precipitation type							code table (4.201)

20		Integrated liquid water						kg m-2

21		Condensate							kg kg-1

22		Cloud mixing ratio						kg kg-1

23		Ice water mixing ratio						kg kg-1

24		Rain mixing ratio							kg kg-1

25		Snow mixing ratio						kg kg-1

26		Horizontal moisture convergence					kg kg-1 s-1

27		Maximum relative humidity					%

28		Maximum absolute humidity					kg m-3

29		Total snowfall							m

30		Precipitable water category					code table (4.202)

31		Hail								m

32		Graupel (snow pellets)						kg kg-1

33-191		Reserved

192-254		Reserved for local use

255		Missing

Product Discipline 0:	Meteorological products, 	Parameter Category 2:	Momentum

Number		Parameter							Units

0		Wind direction (from which blowing)				deg true

1		Wind speed							m s-1

2		u-component of wind						m s-1

3		v-component of wind						m s-1

4		Stream function							m2 s-1

5		Velocity potential						m2 s-1

6		Montgomery stream function					m2 s-2

7		Sigma coordinate vertical velocity					s-1

8		Vertical velocity (pressure)					Pa s-1

9		Vertical velocity (geometric)					m s-1

10		Absolute vorticity						s-1

11		Absolute divergence						s-1

12		Relative vorticity							s-1

13		Relative divergence						s-1

14		Potential vorticity						K m2 kg-1 s-1

15		Vertical u-component shear					s-1

16		Vertical v-component shear					s-1

17		Momentum flux, u component					N m-2

18		Momentum flux, v component					N m-2

19		Wind mixing energy						J

20		Boundary layer dissipation					W m-2

21		Maximum wind speed						m s-1

22		Wind speed (gust)						m s-1

23		u-component of wind (gust)					m s-1

24		v-component of wind (gust)					m s-1

25-191		Reserved

192-254		Reserved for local use

255		Missing

Product Discipline 0:	Meteorological products, 	Parameter Category 3:	Mass

Number		Parameter							Units

0		Pressure								Pa

1		Pressure reduced to MSL						Pa

2		Pressure tendency						Pa s-1

3		ICAO Standard Atmosphere Reference Height			m

4		Geopotential							m2 s-2

5		Geopotential height						gpm

6		Geometric height							m

7		Standard deviation of height					m

8		Pressure anomaly							Pa

9		Geopotential height anomaly					gpm

10		Density								kg m-2

11		Altimeter setting							Pa

12		Thickness							m

13		Pressure altitude							m

14		Density altitude							m

15-191		Reserved

192-254		Reserved for local use

255		Missing

Product Discipline 0:	Meteorological products, 	Parameter Category 4:	Short-wave Radiation

Number		Parameter							Units

0		Net short-wave radiation flux (surface)				W m-2

1		Net short-wave radiation flux (top of atmosphere)			W m-2

2		Short wave radiation flux						W m-2

3		Global radiation flux						W m-2

4		Brightness temperature						K

5		Radiance (with respect to wave number)				W m-1 sr-1

6		Radiance (with respect to wave length)				W m-3 sr-1

7-191		Reserved

192-254		Reserved for local use

255		Missing

Product Discipline 0:	Meteorological products, 	Parameter Category 5:	Long-wave Radiation

Number		Parameter							Units

0		Net long wave radiation flux (surface)				W m-2

1		Net long wave radiation flux (top of atmosphere)			W m-2

2		Long wave radiation flux						W m-2

3-191		Reserved

192-254		Reserved for local use

255		Missing

Product Discipline 0:	Meteorological products, 	Parameter Category 6:	Cloud

Number		Parameter							Units

0		Cloud Ice							kg m-2

1		Total cloud cover							%

2		Convective cloud cover						%

3		Low cloud cover							%

4		Medium cloud cover						%

5		High cloud cover							%

6		Cloud water							kg m-2

7		Layer cloud amount						%

8		Layer cloud type							code table (4.203)

9		Thunderstorm maximum tops					m

10		Thunderstorm coverage						code table (4.204)

11		Cloud base							m

12		Cloud top							m

13		Ceiling								m

14-191		Reserved

192-254		Reserved for local use

255		Missing

Product Discipline 0:	Meteorological products, 	Parameter Category 7:	Thermodynamic Stability Indices

Number		Parameter							Units

0		Parcel lifted index (to 500 hPa)					K

1		Best lifted index (to 500 hPa)					K

2		K index								K

3		KO index							K

4		Total totals index							K

5		Sweat index							numeric

6		Convective available potential energy				J kg-1

7		Convective inhibition						J kg-1

8		Storm relative helicity						J kg-1

9		Energy helicity index						numeric

10-191		Reserved

192-254		Reserved for local use

255		Missing

Product Discipline 0:	Meteorological products, 	Parameter Category 13:	Aerosols

Number		Parameter							Units

0		Aerosol type							code table (4.205)

1-191		Reserved

192-254		Reserved for local use

255		Missing

Product Discipline 0:	Meteorological products, 	Parameter Category 14:	Trace Gases

Number		Parameter							Units

0		Total ozone							Dobson

1-191		Reserved

192-254		Reserved for local use

255		Missing

Product Discipline 0 - Meteorological products, 		Parameter Category 15:	Radar

Number		Parameter							Units

0		Base spectrum width						m s-1

1		Base reflectivity							dB

2		Base radial velocity						m s-1

3		Vertically-integrated liquid					kg m-1

4		Layer-maximum base reflectivity					dB

5		Precipitation							kg m-2

6		Radar spectra (1)							-

7		Radar spectra (2)							-

8		Radar spectra (3)							-

9-191		Reserved

192-254		Reserved for local use

255		Missing

Product Discipline 0:	Meteorological products, 	Parameter Category 19:	Physical atmospheric properties

Number		Parameter							Units

0		Visibility							m

1		Albedo								%

2		Thunderstorm probability						%

3		mixed layer depth						m

4		Volcanic ash							code table (4.206)

5		Icing top							m

6		Icing base							m

7		Icing								code table (4.207)

8		Turbulence top							m

9		Turbulence base							m

10		Turbulence							code table (4.208)

11		Turbulent kinetic energy						J kg-1

12		Planetary boundary layer regime					code table (4.209)

13		Contrail intensity							code table (4.210)

14		Contrail engine type						code table (4.211)

15		Contrail top							m

16		Contrail base							m

17-191		Reserved

192-254		Reserved for local use

255		Missing

Product Discipline 0:	Meteorological products, 	Parameter Category 253:ASCII character string

Number		Parameter							Units

0		Arbitrary text string						CCITTIA5

1-191		Reserved

192-254		Reserved for local use

255         	Missing

Product Discipline 2:	Land surface products, 		Parameter Category 0:	Vegetation/Biomass

Number		Parameter							Units

0		Land cover (1=land, 2=sea)					Proportion

1		Surface roughness						m

2		Soil temperature							K

3		Soil moisture content						kg m-2

4		Vegetation							%

5		Water runoff							kg/m-2

6		Evapotranspiration						kg —2 s-1

7		Model terrain height						m

8		Land use							code table (4.212)

9-191		Reserved

192-254		Reserved for local use

255		Missing

Product Discipline 2:	Land surface products, 		Parameter Category 2:	Soil Products

Number		Parameter							Units

0		Soil type							code table (4.213)

1		Upper layer soil temperature					K

2		Upper layer soil moisture						kg m-3

3		Lower layer soil moisture						kg m-3

4		Bottom layer soil temperature					K

5-191		Reserved

192-254		Reserved for local use

255		Missing

Product discipline 3:	Space products, 			Parameter Category 2:	Satellite, infra-red imagery

Number		Parameter							Units

0		Scaled radiance							numeric

1		Scaled reflectance factor						numeric

2		Scaled albedo							numeric

3		Scaled brightness temperature					numeric

4		Scaled precipitable water						numeric

5		Scaled estimated precipitation					numeric

6-191		Reserved

192-254		Reserved for local use

255		Missing

Product Discipline 3:	Space products,			Parameter Category 3:	Satellite, visible imagery

Number		Parameter							Units

0		Surface albedo							-

1-191		Reserved

192-254		Reserved for local use

255		Missing

Product Discipline 10:	Oceanographic products, 	Parameter Category 0:	Waves

Number		Parameter							Units

0		Wave spectra (1)							-

1		Wave spectra (2)							-

2		Wave spectra (3)							-

3		Significant height of combined wind waves and swell			m

4		Direction of wind waves						Degree true

5		Significant height of wind waves					m

6		Mean period of wind waves					s

7		Direction of swell waves						Degree true

8		Significant height of swell waves					m

9		Mean period of swell waves					s

10		Primary wave direction						Degree true

11		Primary wave mean period					s

12		Secondary wave direction						Degree true

13		Secondary wave mean period					s

14-191 		Reserved

192-254		Reserved for local use

255		Missing

Product Discipline 10:	Oceanographic products, 	Parameter Category 1:	Currents

Number		Parameter							Units

0		Current direction							Degree true

1		Current speed							m s-1

2		u-component of current						m s-1

3		v-component of current						m s-1

4-191		Reserved

192-254		Reserved for local use

255		Missing

Product Discipline 10:	Oceanographic products, 	Parameter Category 2:	Ice

Number		Parameter							Units

0		Ice cover							Proportion

1		Ice thickness							m

2		Direction of ice drift						Degree true

3		Speed of ice drift							m s-1

4		u-component of ice drift						m s-1

5		v-component of ice drift						m s-1

6		Ice growth rate							m s-1

7		Ice divergence							s-1

8-191		Reserved

192-254		Reserved for local use

255		Missing

Product Discipline 10:	Oceanographic products, 	Parameter Category 4:	Surface Properties

Number		Parameter							Units

0		Water temperature						K

1		Deviation of sea level from mean					m

2-191		Reserved

192-254		Reserved for local use

255		Missing

Product Discipline 10:	Oceanographic products, 	Parameter Category 5:	Sub-surface Properties

Number		Parameter							Units

0		Main thermocline depth						m

1		Main thermocline anomaly					m

2		Transient thermocline depth					m

3		Salinity								kg kg-1

4-191		Reserved

192-254		Reserved for local use

255		Missing

Code table 4.3:	Type of generating process

Code figure	Meaning

0		Analysis

1		Initialization

2		Forecast

3		Bias corrected forecast

4		Ensemble forecast

5		Probability forecast

6		Forecast error

7		Analysis error

8-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 4.4: 	Indicator of unit of time range

Code figure	Meaning

0 		Minute

1		Hour

2		Day

3 		Month

4		Year

5 		Decade (10 years)

6		Normal (30 years)

7		Century (100 years)

8-9		Reserved

10		3 hours

11		6 hours

12		12 hours

13		Second

14-191		Reserved

192-254		Reserved for local use

255		Missing

Code table 4.5:	Fixed surface types and units

Code

Figure		Meaning								Units

0		Reserved

1		Ground or water surface						-

2		Cloud base level							-

3		Level of cloud tops						-

4		Level of 0o C isotherm						-

5		Level of adiabatic condensation lifted from the surface		-

6		Maximum wind level						-

7		Tropopause							-

8		Nominal top of the atmosphere					-

9		Sea bottom							-

10-19		Reserved

20		Isothermal level							K

21-99		Reserved

100		Isobaric surface							Pa

101		Mean sea level

102		Specific altitude above mean sea level				m

103		Specified height level above ground				m

104		Sigma level							“sigma” value

105		Hybrid level							-

106		Depth below land surface						m

107		Isentropic (theta) level						K

108		Level at specified pressure difference from ground to level		Pa

109		Potential vorticity surface						K m2  kg-1 s-1

110		Reserved

111		Eta* level							-

112-116		Reserved

117		Mixed layer depth						m

118-159		Reserved

160		Depth below sea level						m

161-191		Reserved

192-254		Reserved for local use

255		Missing

* 	The ETA vertical coordinate system involves normalizing the pressure at some point an a specific level by the mean sea level pressure at that point

Code Table 4.6: 	Type of ensemble forecast

Code figure	Meaning

0 		Unperturbed high-resolution control forecast

1		Unperturbed low-resolution control forecast

2		Negatively perturbed forecast

3 		Positively perturbed forecast

4-191		Reserved

192-254		Reserved for local use

255	    	Missing

Code Table 4.7:	Derived forecast

Code figure	Meaning

0		Unweighted mean of all members

1		Weighted mean of all members

2		Standard deviation with respect to cluster mean

3		Standard deviation with respect to cluster mean, normalized

4-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 4.8:	Clustering Method

Code figure	Meaning

0		Anomaly correlation

1		Root mean square

2-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 4.9:	Probability Type

Code figure	Meaning

0		Probability of event below lower limit

1		Probability of event above upper limit

2		Probability of event between lower and upper limits

3-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 4.10: Type of statistical processing

Code figure	Meaning

0		Average

1		Accumulation

2		Maximum

- Minimum

4		Difference (Value at the end of time range minus value at the beginning)

5		Root mean square

6		Standard deviation

7		Covariance (Temporal variance)

8		Difference (Value at the start of time range minus value at the end)

9-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 4.11:	Type of time intervals

Code figure	Meaning

0		Reserved

1		Successive times processed have same forecast time, start time of forecast is incremented

2		Successive times processed have same start time of forecast, forecast time is incremented

3		Successive times processed have start time of forecast incremented and forecast time decremented so that valid time remains constant

4		Successive times processed have start time of forecast decremented and forecast time incremented so that valid time remains constant

5-191		Reserved

192-254	Reserved for local use

255		Missing

Code Table 4.12:	Operating Mode

Code figure	Meaning

0		Clear

1		Precipitation

2-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 4.13:	Quality Control Indicator

Code figure	Meaning

0		No quality control applied

1		Quality control applied

2-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 4.14:	Clutter Filter Indicator

Code figure	Meaning

0		No clutter filter used

1		Clutter filter used

2-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 4.201: Precipitation Type

Code figure	Meaning

0		Reserved

1		Rain

2		Thunderstorm

3		Freezing rain

4		Mixed/ice

5		Snow

6-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 4.202: Precipitable water category

Code figure	Meaning

0-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 4.203: Layer cloud type

Code figure	Meaning

0		Clear

1		Cumulonimbus

2		Stratus

3		Stratocumulus

4		Cumulus

5		Altostratus

6		Nimbostratus

7		Altocumulus

8		Cirrostratus

9		Cirrocumulus

10		Cirrus

11		Cumulonimbus - ground based fog beneath the lowest layer

12		Stratus - ground based fog beneath the lowest layer

13		Stratocumulus - ground based fog beneath the lowest layer

14		Cumulus - ground based fog beneath the lowest layer

15		Altostratus - ground based fog beneath the lowest layer

16		Nimbostratus - ground based fog beneath the lowest layer

17		Altocumulus - ground based fog beneath the lowest layer

18		Cirrostratus - ground based fog beneath the lowest layer

19		Cirrocumulus - ground based fog beneath the lowest layer

20		Cirrus - ground based fog beneath the lowest layer

21-190		Reserved

191		Unknown

0-191		Reserved

192-254		Reserved for local use

255		Missing

Note: Code figures 11-20 indicate all four layers were used and a ground-based fog is beneath the lowest layer.

Code Table 4.204: Thunderstorm coverage

Code figure	Meaning

0		None

1		Isolated (1%  - 2%)

2		Few (3% - 15%)

3		Scattered (16% - 45%)

4		Numerous (> 45%)

5-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 4.205: Aerosol type

Code figure	Meaning

0		Aerosol not present

1		Aerosol present

2-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 4.206: Volcanic ash

Code figure	Meaning

0		Not present

1		Present

2-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 4.207: Icing

Code figure	Meaning

0		None

1		Light

2		Moderate

3		Severe

4-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 4.208: Turbulence

Code figure	Meaning

0		None (smooth)

1		Light

2		Moderate

3		Severe

4		Extreme

5-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 4.209: Planetary boundary layer regime

Code figure	Meaning

0		Reserved

1		Stable

2		Mechanically driven turbulence

3		Forced convection

4		Free convection

5-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 4.210: Contrail intensity

Code figure	Meaning

0		Contrails not present

1		Contrails present

2-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 4.211: Contrail engine type

Code figure	Meaning

0		Low bypass

1		High bypass

2		Non bypass

3-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 4.212: Land Use

Code figure	Meaning

0		Reserved

1		Urban land

2		Agriculture

3		Range land

4		Deciduous forest

5		Coniferous forest

6		Forest/wetland

7		Water

8		Wetlands

9		Desert

10		Tundra

11		Ice

12		Tropical forest

13		Savannah

14-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 4.213: Soil type

Code figure	Meaning

0		Reserved

1		Sand

2		Loamy sand

3		Sandy loam

4		Silt loam

5		Organic (redefined)

6		Sandy clay loam

7		Silt clay loam

8		Clay loam

9		Sandy clay

10		Silty clay

11		Clay

12-191		Reserved

192-254		Reserved for local use

255		Missing

CODE AND FLAG TABLES USED IN SECTION 5

Code Table 5.0: 	Data Representation Template Number

Code figure	Meaning

0		Grid point data - simple packing

1		Matrix value - simple packing

2		Grid point data - complex packing

3		Grid point data - complex packing and spatial differencing

4		Spectral data -simple packing

5 		Spectral data - complex packing

6-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 5.1:	Type of original field values

Code figure	Meaning

0		Floating point

1		Integer

2-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 5.2:	Matrix coordinate value function definition.

Code Figure	Meaning

0		explicit coordinate values set

1		Linear coordinates

f(1)=C1

f(n)=f (n-1)+C2

2		Log linear coordinates

f (1)=C1

f (n)=C2(log(base C2)+C3)

C2 defines the base of the logarithmic scale used.

3-10		Reserved

11		Geometric coordinates

f (1)=C1

f(n)=C2*f(n-1)

12-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 5.3:	Matrix coordinate parameter

Code Figure	Meaning

1		Direction Degrees true

2		Frequency (s-1)

3		Radial number (2pi/lambda) (m-1)

4-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 5.4:	Group Splitting Method

Code figure	Meaning

0		Row by row splitting

1		General group splitting

2-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 5.5	Missing Value Management for Complex Packing

Code figure	Meaning

0		No explicit missing values included within data values

1		Primary missing values included within data values

2		Primary and secondary missing values included within data values

3-191		Reserved

192-254		Reserved for local use

255		Missing

Code Table 5.4:	Order of Spatial Differencing

Code Figure	Meaning

0		Reserved

1		First-order spatial differencing

2		Second-order spatial differencing

3-191		Reserved

192-254		Reserved for local use

255		Missing

CODE AND FLAG TABLES USED IN SECTION 6

Code Table 6.0:

Code figure 	Meaning

0 		A bit map applies to this product and is specified in this Section

1 - 253		A bit map pre-determined by the originating/generating Centre applies to this product and is not specified in this Section.

254		A bit map defined previously in the same "GRIB" message applies to this product.

255		A bit map does not apply to this product.

ANNEX

LIST OF ACRONYMS

| ACARS | AirCraft Addressing and Reporting System |
| --- | --- |
| AWS | Automatic Weather Station |
| BUFR | Binary Universal Form for data Representation |
| CBS | Commission for Basic Systems |
| CBS-Ext.(98) | Extraordinary session of CBS held in 1998 |
| COST | European Co-Operation in the field of Scientific and Technical research |
| CREX | Character Representation form for data Exchange |
| DBCP | Drifting Buoy Cooperation Panel |
| DCP | Data Collection Platform |
| DIF | Directory Interchange Format |
| EC | Executive Council of the WMO |
| ECMWF | European Centre for Medium-range Weather Forecast |
| EUMETSAT | European Meteorological Satellite (or Agency) |
| ET | Expert Team |
| ET/EDF | Expert Team on Evolution of Data Formats |
| FNMOC | Fleet Numerical Meteorology and Oceanography Centre |
| FORTRAN | FORmula TRANslation |
| FTP | File Transfer Protocol |
| GDPS | Global Data Processing System |
| GIF | Graphic Interchange Format |
| GIS | Geographic Information System |
| GOS | Global Observing System |
| GRIB 1 | Processed data in the form of GRId-point values expressed in Binary form |
| GRIB 2 | General Regularly distributed Information in Binary form |
| GTS | Global Telecommunications System |
| ICAO | International Civil Aviation Organisation |
| ICT | Implementation/Coordination Team (of CBS) |
| ICT/DRC | Implementation/Coordination Team on Data Representation and Codes |
| ID | Identifier |
| IOC | International Oceanographic Commission |
| ISO | International Standards Organization |
| JCOMM | Joint WMO/IOC Technical Commission for Oceanography and Marine Meteorology |
| JPEG | Joint Photographic Experts Group format |
| LINUX | Not an acronym – name of an operating system |
| MS/DOS | /Disk Operating System |
| MSS | Message Switching System |
| MTN | Main Telecommunications Network (of the GTS) |
| NASA | National Aeronautics and Space Administration |
| NCEP | National Centre for Environment Prediction |
| NMC | National Meteorological Centre |
| NMHS | National Meteorological or Hydrological Service |
| NMS | National Meteorological Service |
| NWP | Numerical Weather Prediction |
| NWS | National Weather Service |
| OPAG | Open Programme Area Group (of CBS) |
| OPAG-ISS | Open Programme Area Group on Information Systems and Services |
| PNG | Portable Network Graphic |
| RA | Regional Association (WMO) |
| RASS | Radio Acoustic Sounding System |
| RDBC | Regional Data Bank Centre |
| RSMC | Regional Specialised Meteorological Centre |
| SGDR&C | Sub-Group on Data Representation and Codes (CBS) |
| SI | System International |
| TCP | Tropical Cyclone Programme |
| TCP/IP | Transport Control Protocol/Internet Protocol |
| TIFF | Tagged Image File Format |
| UNIX | Not an acronym – name of an operating system |
| UTC | Universal Time Coordinate |
| WGDM | Working Group on Data Management (CBS) |
| WMO | World Meteorological Organization |
| WWW | World Weather Watch |

# Footnotes

* Note:  The ICT/DR&C and the OPAG/ISS are the current bodies in 2000 dealing with Data Representation and Codes within CBS.  If they were replaced by other bodies performing the same function, the same rules would apply, by replacing the names of the entities appropriately.