|  | World Meteorological Organization Organisation météorologique mondiale Temps ● Climat ● Eau Weather ● Climate ● Water |
| --- | --- |

Commission for Aeronautical Meteorology and Commission for Basic Systems

Expert Team on the Assessment of Data Representation Systems (ET-ADRS)

Expert Team on the OPMET Data Representation (ET-ODR)

| Document for discussion by the ET-ADRS and the ET-ODR |
| --- |
| Title | Development of a WMO conceptual model of data representation - Three-level Modelling of WMO data products based on BUFR/CREX tables |
| Document name | ModelFromBUFR.doc |
| References | ET-ADRS-1/ Doc. 4.1(2) (see http://www.wmo.int/pages/prog/www/WDM/ET-ADRS-1/doc4-1_iso191xx.doc) Draft report of the first meeting of the ET-ADRS (see http://www.wmo.int/pages/prog/www/WDM/ET-ADRS-1/ET-ADRS-1_draft_report_v7.doc) Report of the first meeting of the ET-ODR (see http://www.wmo.int/pages/prog/www/WDM/ET-ODR-1/ET-ODR-1_report.doc) |
| Summary | The document presents a methodology for creating models for data product specifications based on BUFR/CREX tables. This document also presents the application of this methodology to: The development of a three-level modelling of the WMO data products; The implementation of database applications for the production, exportation, importation and storage of the WMO data products; The implementation of the WMO data products as datasets and their representation for data interchange in different data representation systems; The presentation of OPMET data product in XML. |
| Follow-up action | The ET-ADRS and ET-ODR are invited to consider the methodology for developing models for WMO data products based on BUFR/CREX tables and the possible applications of this methodology to the modelling of WMO data products and the representation of WMO data products for data interchange. The ET-ODR is in particular invited to consider applying the METAR/SPECI and TAF models for the presentation of OPMET data in XML within the framework of the pilot project for the presentation of OPMET data in XML. |

Table of the versions

The proposals for amendments should be sent to pkerherve@wmo.int

| Description | Date | Author |
| --- | --- | --- |
| Version 1 | February 2009 | WMO Secretariat - P. Kerhervé |
| Version 2 | February 2009 | WMO Secretariat - P. Kerhervé |

Contents

1.	Background information	4

2.	Terminology	4

3.	BUFR tables and their relationship	4

4. 	Methodology for creating models for data product based on BUFR/CREX tables	6

5.	Meta-model, model and data products	8

6.	Compliance with the ISO 19100 series of geographic information standards	8

7.	Implementation of database applications for the production, exportation, importation and storage of the data products	10

8.	Application of the models to the implementation of the data products and their representation for data interchange	10

9.	Application to the presentation of OPMET data product in XML	11

Annex 1	12

Application of the ISO 19100 series to the development of a pilot project for the presentation of OPMET data in XML	12

Annex 2	13

Application of the methodology to the sequence 313043	13

Annex 3	14

Application of the methodology for the creation of the tree for METAR/SPECI reports	14

Annex 4	16

Table of the tables of the tree and their relationship for the METAR/SPECI model	16

Annex 5	17

Structure of the tables of the tree for the METAR/SPECI model	17

Annex 6	23

Structure of the tables of the tree and their relationship in the METAR/SPECI model	23

Annex 7	24

Instance of a SPECI report in XML format for interchange	24

Annex 8	28

Table of the tables of the tree and their relationship for the TAF model	28

Annex 9	29

Structure of the tables of the tree for the TAF model	29

Annex 10	36

Structure of the tables of the tree and their relationship in the TAF model	36

Annex 11	37

Instance of a TAF report in XML format for interchange	37

Annex 12	41

Database applications	41

Annex 13	42

Extracts from the ISO TC 211 multilingual glossary related to terms used in the document ET-ADRS-1/ Doc. 4.1(2)	42

1.	Background information

- The ET-ADRS agreed that the application of the ISO 19100 series of geographic information standards to the development of a WMO conceptual model of data representation should be considered as a fundamental element of a CBS policy on data representation systems, in particular with a view to:

- Applying a standard approach for data representation, leading to the development of a WMO core profile of the ISO 19100 series for data and metadata, encompassing the WMO core profile of the ISO metadata standard, in line with other initiatives such as INSPIRE); the application schemata and associated tables used to represent data in BUFR, CREX, XML, NetCDF or HDF, such as the BUFR/CREX/GRIB tables, may be used to develop this WMO core profile for data and metadata, in particular to develop the relevant ISO 19100 feature catalogues, application schema(ta) and data product specification(s);

- Facilitating the interoperability and data interchange between applications based on data representations systems associated to BUFR, CREX, GRIB, XML, NetCDF and HDF.

- Noting the activities undertaken by Eurocontrol and US FAA for the presentation of OPMET data in XML, the ET-ADRS  recommended the development of a pilot project for the presentation of OPMET data in XML, possibly based on the applications of ISO 19131 – data product specification – and ISO 19118 – encoding rules - as given in Annex 1. Such a pilot project should aim at gaining practical experience in the application of the standard approach. The ET-ODR should coordinate a more detailed definition of the scope of the pilot project and its implementation, and should report to the ET-ADRS on the outcomes of the pilot project.

2.	Terminology

Extracts from the ISO TC 211 multilingual glossary related to terms used in this document as well as in the referenced document ET-ADRS-1/ Doc. 4.1(2) are given in Annex 13. In this document, a Data Representation System (DRS) is viewed as a set of rules, regulations, standards, procedures or conventions to be used to represent a data product for interchange. The application of these rules, regulations, standards, procedures or conventions fosters the interoperability required for the access and the use the data product by any users.

3.	BUFR tables and their relationship

- The BUFR/CREX tables can be grouped into four categories and therefore incorporated into four catalogues as follows:

- A catalogue of sequences (“SequencesCat”) containing the sequences listed  in Table D of the  Manual on Codes;

- A catalogue of elements (“ElementsCat”) containing the elements listed in Table B of the Manual on Codes;

- A catalogue of codes (“CodesCat”) regrouping the code tables included in Table B of the Manual on Codes;

- A catalogue of flags (“FlagsCat”) regrouping the flag tables included in Table B of the Manual on Codes.

- In common code table C-11, a type of data product is defined by a data category and a sub category. In Table D, a product is associated to a template defined by a sequence number, for example “307051” for a METAR/SPECI report. The templates can be listed in a table (TemplatesList).

- Figure 1 shows the relationship between the following catalogues/tables: CommonTableC11, TemplatesList, SequencesCat, ElementsCat, CodesCat, FlagsCat.and other tables of the common code tables.

4. 	Methodology for creating models for data product based on BUFR/CREX tables

- The methodology for creating a model is based on a sequential reading of the catalogue of sequences with a view to generating the tree of tables with their relationship, as described in Figure 2 with the following results.

Creation of the tables of the tree

  - A table is created for each sequence and each replication, except for a short delayed replication; the name of the table corresponds to the path in the tree from the table root to the table node, e.g. “M307051M307046” for the table associated to the sequence “307046” for METAR/SPECI; “Rn” (n being the number of replication for the same sequence) is added to the name of the table in case of a replication, e.g “M307051M307046R1”; “Dn” is added to the name of the table in order to avoid duplication of names;

Creation of the fields of the tables

  - Elements (see also 3.5) are included as fields in these tables with the name E”FXY”n”p” with “FXY” being the element number and “p” the number of the field in the table, e.g. “E020060n0” for the first field in the table “M307051M307046” corresponding to the element “020060”. The elements having “increments” in their name, the data repetition factors (031002 and 031012) and certain data description operators (2XY) are ignored and only those remaining elements significant for the model are included in the structure of the tables. For example, a table associated to the sequence 313043 (see Annex 2) should have only four fields: E006002n0, E005002n1, E005002, E006012 and a child table 319043R1 of raster type with n records of p fields E030001nx.

Relationship between the tables of the tree

  - A relationship is created between each pair of tables adjacent on the branches of the tree; in this respect, the two first fields of each table are a foreign key (ForeignKey) and an index (Index). For example the first field of “M307051M307046” (F0) is a foreign key used for the relationship with the table “M307051”; the second field of “M307051M307046” (F5) is an index used for the relationship with the table “M307051M307046R1”, F5 being a foreign key for “M307051M307046R1”, etc..

- The model only defines the tables, their structure and their relationship.

- An example of the application of this methodology for METAR/SPECI reports is given in Annex 3.

- The names allocated to the tables and the fields of the tables reflect the sequential reading of the catalogue of sequences, i.e. the path from the table root to the table node. This naming convention is of interest during the process of development of the tree. Alias names (e.g. sequence number such as M”n” (“n”=1,2,…) or meaningful names such as “SeaConditions”) should preferably be used in order to reduce the length of the names for example for an XML representation, or in order to facilitate their use.

- The above models are defined for a unique instance of a data product. The model for a collection of instances of a data product, e.g. a compilation of METAR/SPECI reports, can be defined as a replication of the models for an instance, adding a layer in the tree of tables. In this case, the replications are determined by the values of the unique index (F0) of the root table.

5.	Meta-model, model and data products

  - The methodology induces a three-level modelling of the data products (see Figure 3): meta-model level, model level and data products level. The results of the application of the methodology for a type of data product, defined by a category and a sub-category in Common Table C-11 or by a sequence of BUFR Table D, is a tree of tables that is the instance of two meta-models defined as follows:

  - A meta-model defining the structure of a table of the tables of the trees: names of the tables (each associated to a sequence of BUFR Table D), aliases, descriptions of the tables, foreign keys and unique indexes for each table.

  - A meta-model describing how to define the tables of the trees and their structure: names of the tables, fields (i.e. elements of BUFR Table B) and attributes of the fields (description and unit).

The methodology described in above paragraph 4 and Figure 2 is the basic reference documentation of the meta-model.

  - Each model associated to a type of data product is defined by instances of the meta-models as follows:

    - A table that is an instance of the meta-model of the table of the tables of the tree defined in above paragraph 5.1.1

    - Tables that are instances of the meta-model of the tables of the tree defined in above paragraph 5.1.2

The documents describing the structure and the contents of these tables are the basic reference documentation of the model for a data product (see examples in Annexes 4 and 5 for METAR/SPECI, and in Annexes 8 and 9 for TAF).

  - Diagrams showing the tables of the tree with their fields and their relationship can be derived from the tables mentioned in above paragraphs 5.2.1 and 5.2.2 (see examples in Annex 6 for METAR/SPECI and in Annex 10 for TAF).

6.	Compliance with the ISO 19100 series of geographic information standards

  - This three-level modelling is consistent with the Conceptual Schema Modelling Facilities (CSMF) applied in the ISO 19100 series of geographic information standards (see ET-ADRS-1/ Doc. 4.1(2)). The two tables (see above paragraph 5.2) describing the data structure and the content of the data products include the basic information to create an application schema (ISO 19109). The BUFR catalogue of elements and the BUFR catalogue of sequences include the basic information to create the catalogue of features. The WMO core profile of the ISO metadata standard (see http://www.wmo.int/pages/prog/www/WDM/Metadata/documents.html) can be use as a model for the production of the metadata associated to a data product. The use of this basic information for the creation of an application schema, a feature catalogue and a metadata schema associated to a type of data product can result in the development of a data product specification (ISO 19131) as given in Annex 1.

7.	Implementation of database applications for the production, exportation, importation and storage of the data products

  - The three-level modelling is independent from the implementation of the database applications used at centres for the production, exportation, importation and storage of the data products.

  - The application of the meta-model makes it possible to generate automatically the models for all types of data products from a database application. The models facilitate the implementation of the database applications at centres for the production, exportation, importation and storage of data products since the same type of applications or algorithms, based on these three levels, can be used to produce and receive the data products. The Access Applications developed by the Secretariat are examples of such applications based on the METAR/SPECI model to create, export and import METAR/SPECI reports presented in XML; these applications can be easily extended to create, export and import other types of data products (see Annex 12).

8.	Application of the models to the implementation of the data products and their representation for data interchange

  - The tree of the tables derived directly from the model in accordance with model documentation (see above paragraph 5.2, and examples in Annex 6 for METAR/SPECI and in Annex 10 for TAF).) is a possible example of implementation of the data product (a data set) in a database application. The model ensures that any other dataset as determined by the implementer of the database application can be matched with the dataset derived directly from the model.

  - At the model level, the format of the contents of each field of the tables of the tree is defined with reference to the catalogue of elements, in particular as regards the unit, code and flag. The model ignores any other constraints imposed by a Data Representation System (DRS), such as scale or width for BUFR.  The formats of presentation of the instances of the model are defined at the data level in particular when encoding the instances for their exchange for example in BUFR or XML.

  - The encoding rules used to present the data products for their interchange in a DRS and the decoding rules used to import a data product received (see Annex 1) are defined by the model documentation and the reference documentation specific to the DRS. The representation of the data product in the DRS is the result of the encoding of the dataset based in accordance with this documentation.

  - The model provides a framework for the implementation of decoders and encoders by decoding a data product presented in a DRS into a reference dataset, e.g. the dataset derived directly from the model, and by encoding the reference dataset into data products presented in any other DRS (see Annex 1).

Encoding and decoding rules for BUFR/CREX representation

  - The encoding and decoding rules for the interchange of a data product in WMO Traditional Alphanumerical Codes (TAC) and in Table Driven Code Forms (TDCF) (BUFR/CREX) are defined in the Manual on Codes. The implementation of the encoding and decoding rules for BUFR/CREX is facilitated by the fact that the three-level modelling derives from the BUFR tables.

Encoding and decoding rules for the XML representation

  - The implementation of the dataset in the form of a tree of tables with their relationship provides a hierarchical structure for the exportation of the dataset into XML. Therefore the dataset derived from the dataset derived directly from the model can easily be exported into XML.

  - Procedures for the presentation of the contents of the fields should be defined. A proposal is to present the contents of the fields, which are BUFR elements, in the units defined in the catalogue of elements without constraints on the scale and the width, and by selecting the appropriate values in the catalogue of codes or flags as required.

- Application to the presentation of OPMET data product in XML

  - The OPMET data products are defined by the names of the relevant Traditional Alphanumerical Code (TAC) forms METAR/SPECI and TAF. The data category and sub category In common code table C-11 is 000010 for METAR/SPECI. The sequence associated to the data products in the catalogue of sequences is “307051” for METAR/SPECI and “307056” for TAF.

  - The  model documentation for the data products includes:

- A table that is an instance of the meta-model of the table of the tables of the tree defined in above paragraph 5.1.1; the structure of the table is given in Annex 4 for METAR/SPECI and in Annex 8 for TAF;

- Tables that are instances of the meta-model of the tables of the tree defined in above paragraph 5.1.2; the contents of these tables are given in Annex 5 for METAR/SPECI and in Annex 9 for TAF.

  - Diagrams showing the tables of the tree with their fields and their relationship are given in Annex 6 for METAR/SPECI and in Annex 10 for TAF.

  - Instances of data products in XML format for interchange are given in Annex 7 for SPECI report and in Annex 11 for TAF report. These instances are those used as examples in WMO-No. 782 – aerodrome reports and forecasts – a user’s handbook to the codes.   The contents of the fields are presented in accordance with the proposal mentioned in above paragraph 8.7: to present the contents of the fields, which are BUFR elements, in the units defined in the catalogue of elements without constraints on the scale and the width, and by selecting the appropriate values in the catalogue of codes or flags as required. With a view to reducing the size of the files for their interchange, the names of the files and fields (or elements) used in the tags are the short names: Mn or Tn (fields “Alias” in Annexes 4 and 8) and (E + sequence number of the field in each table). Any other names for the tags could be defined in the model documentations as required.

  - The names of the files are defined in accordance with the general file naming convention (see Attachment II-15 to the Manual on the GTS).

  - Annex 12 includes information on  three Access applications used by the Secretariat to:

- Produce the model documentation related to a data product, i.e. to produce an instance of the meta-model;

- Create an  instance of the METAR/SPECI model and export it into XML format;

- Import a METAR/SPECI instance presented in XML and browse it with a view to testing an interchange of WMO data product presented in XML.

Annex 1

Application of the ISO 19100 series to the development of a pilot project for the presentation of OPMET data in XML

Annex 2

Application of the methodology to the sequence 313043

In the model, a table associated to the sequence 313043 should have only four fields: E006002n0, E005002n1, E005002, E006012 and a child table 319043R1 of raster type with n records of p fields E030001nx corresponding to the five elements marked hereunder. All the other elements should be ignored.

| TABLE REFERENCE | TABLE REFERENCES | ELEMENT NAME |
| --- | --- | --- |
| F | X | Y |  |  |
|  |  |  |  |  |  | (Run-length encoded picture data for Pixel value (4 bits), regular grid) |
| 3 | 13 | 043 | 0 | 06 | 002 | First longitude location minus one increment |
|  |  |  | 0 | 05 | 002 | First latitude location minus one increment |
|  |  |  | 0 | 05 | 012 | Latitude increment |
|  |  |  | 1 | 12 | 000 | Delayed replication of 12 descriptors |
|  |  |  | 0 | 31 | 001 | Replication factor |
|  |  |  | 1 | 10 | 000 | Delayed replication of 10 descriptors |
|  |  |  | 0 | 31 | 001 | Replication factor |
|  |  |  | 1 | 04 | 000 | Delayed replication of 4 descriptors |
|  |  |  | 0 | 31 | 001 | Replication factor |
|  |  |  | 0 | 06 | 012 | Longitude increment |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |
|  |  |  | 0 | 31 | 011 | Repetition factor |
|  |  |  | 0 | 30 | 001 | Pixel value (4 bits) |
|  |  |  | 0 | 06 | 012 | Longitude increment |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |
|  |  |  | 0 | 31 | 001 | Replication factor |
|  |  |  | 0 | 30 | 001 | Pixel value (4 bits) |

Annex 3

Application of the methodology for the creation of the tree for METAR/SPECI reports

Figure 2 shows the process for the sequential reading of the catalogue of sequences. For METAR/SPECI reports, the steps, which are resulting from this process in the sequential reading and corresponding to the start of the creation of the tables “M307051”, “M307051M307045”, “M307051M307045M301011”, “M307051M307046”and “M307051M307046R1”, are as follows:

- The first row read is the first one with field “FXY” = “307051”.  The table “M307051” is created. The value of the field “reference” is “307045”. This is the case FXY=”3XY”: the table “M307051M307045” is created and the next row to read is the first row with the field FXY = “307045”

- At the first row with the field FXY = “307045”, the value of the field “reference” is “001063”. This is the case FXY=”0XY”:  The element 001063 is added as a field in the table “M307051M307045” and the next row to read is the next row.

- At the next row, the value of the field “reference” is “008079”. This is the case FXY=”0XY”:  The element 009079 is added as a field in the table “M307051M307045” and the next row to read is the next row.

- At the next row, the value of the field “reference” is “002001”. This is the case FXY=”0XY”:  The element 002001 is added as a field in the table “M307051M307045” and the next row to read is the next row.

- At the next row, the value of the field “reference” is “301011”. This is the case FXY=”3XY”: the table “M307051M307045M301011” is created and the next row to read is the first row with the field FXY = “301011”

- …(cont.)

- At the first row with the field FXY = “307046”, the value of the field “reference” is “020060”. This is the case FXY=”0XY”:  The element 020060 is added as a field in the table and the next row to read is the next row.

- At the next row, the value of the field “reference” is “102000”. This is the case FXY=”1XY”: Since this is not a short delayed replication, the table “M307051M307046R1” is created and the next row to read is the current row + 2.

- At the current row + 2, the value of the field “reference” is “005021”. This is the case FXY=”0XY”:  The element 005021 is added as a field in the table “M307051M307046R1” and the next row to read is the next row.

Table 2 – Extracts from the templates for METAR/SPECI/TAF

| F X Y | Reference | Element/Sequence name | METAR/SPECI/TAF Representation |
| --- | --- | --- | --- |
| 3 07 051 | 3 07 045 | Main part of METAR/SPECI data |  |
|  | 3 07 046 | Visibility | VVVV or VVVVNDV VNVNVNVNDv |
|  | 3 07 013 | Runway visual range | RDRDR/VRVRVRVR |
|  | 3 07 014 | Weather intensity and phenomena | w’w’ |
|  | 3 07 047 | Clouds | NsNsNshshshs |
|  | 3 07 016 | Recent weather phenomena | REw’w’ |
|  | 3 07 017 | Runway shear | WS RDRDR |
|  | 3 07 049 | Sea conditions | WTsTs/SS’ |
|  | 3 07 050 | Runway state | RDRDR ERCReReRBRBR |
|  | 1 01 000 | Delayed replication of one descriptor |  |
|  | 0 31 001 | Replication count (0 to 3 normally) |  |
|  | 3 07 048 | Trend type forecast |  |

| F X Y | Reference | Element/Sequence name | METAR/SPECI/TAF Representation |
| --- | --- | --- | --- |
| 3 07 045 | 0 01 063 | ICAO location indicator | CCCC |
|  | 0 08 079 | Aviation product status (routine, special, corrected, not available) | METAR SPECI COR |
|  | 0 02 001 | Type of station | (AUTO) |
|  | 3 01 011 | Year, month, day | YY |
|  | 3 01 012 | Hour, minute | GGgg |
|  | 3 01 023 | Latitude-longitude (coarse accuracy) |  |
|  | 0 07 030 | Height of station ground above mean sea level |  |
|  | 0 07 031 | Height of barometer above mean sea level |  |

| F X Y | Reference | Element/Sequence name | METAR/SPECI/TAF Representation |
| --- | --- | --- | --- |
| 3 07 046 | 0 20 060 | Prevailing visibility | VVVV or VVVVNDV |
|  | 1 02 000 | Delayed replication of two descriptors |  |
|  | 0 31 001 | Number of replication (up to 2) |  |
|  | 0 05 021 | Bearing or azimuth (direction of minimum visibility observed) | Dv |
|  | 0 20 059 | Minimum visibility | VNVNVNVN |

Annex 4

Table of the tables of the tree and their relationship for the METAR/SPECI model

| name | alias | alias_2 (see footnote 2) | description | ForeignKey | index |
| --- | --- | --- | --- | --- | --- |
| M307051 | M1 | METAR |  |  | F0 |
| M307051M307045 | M2 | MainPart | Main part of METAR/SPECI data | F0 | F1 |
| M307051M307045M301011 | M3 | YYMMDD | Year, month, day | F1 | F2 |
| M307051M307045M301012 | M4 | HHmm | Hour, minute | F1 | F3 |
| M307051M307045M301023 | M5 | Coordinates | Latitude-longitude (coarse accuracy) | F1 | F4 |
| M307051M307046 | M6 | Visibility | Visibility | F0 | F5 |
| M307051M307046R1 | M7 | PrevailingVisibility_R |  | F5 | F6 |
| M307051M307013 | M8 | RunwayVisualRange | Runway visual range | F0 | F7 |
| M307051M307013R1 | M9 | ByRunways_1R |  | F7 | F8 |
| M307051M307014 | M10 | WeatherIntensityPhenomena_1 | Weather intensity and phenomena | F0 | F9 |
| M307051M307014R1 | M11 | ByTypes1_R |  | F9 | F10 |
| M307051M307047 | M12 | Clouds_1 | Clouds | F0 | F11 |
| M307051M307047R1 | M13 | ByLayers_1R |  | F11 | F12 |
| M307051M307016 | M14 | RecentWeatherPhenomena | Recent weather phenomena | F0 | F13 |
| M307051M307016R1 | M15 | ByPhenomena_R |  | F13 | F14 |
| M307051M307017 | M16 | RunwayShear | Runway shear | F0 | F15 |
| M307051M307017R1 | M17 | ByRunways_2R |  | F15 | F16 |
| M307051M307049 | M18 | Seaconditions | Sea conditions | F0 | F17 |
| M307051M307050 | M19 | RunwayState | Runway state | F0 | F18 |
| M307051M307050R1 | M20 | GeneralConditionByRunways_R |  | F18 | F19 |
| M307051M307050R2 | M21 | DepositsByRunways_R |  | F18 | F20 |
| M307051R1 | M22 | Trends_R |  | F0 | F21 |
| M307051R1M307048 | M23 | TrendTypeForecast | Trend type forecast | F21 | F22 |
| M307051R1M307048R1 | M24 | Changes_R |  | F22 | F23 |
| M307051R1M307048R1M301012 | M25 | TimeChange | Time of change | F23 | F24 |
| M307051R1M307048M307014 | M26 | WeatherIntensityPhenomena_2 | Weather intensity and phenomena | F22 | F25 |
| M307051R1M307048M307014R1 | M27 | ByTypes_2R |  | F25 | F26 |
| M307051R1M307048M307047 | M28 | Clouds_2 | METAR/SPECI/TAF clouds | F22 | F27 |
| M307051R1M307048M307047R1 | M29 | ByLayers_2R |  | F27 | F28 |

Annex 5

Structure of the tables of the tree for the METAR/SPECI model

(a) List of elements FXY in the order of the reading of the catalogue of sequences, as fields of the tables of the tree

| table | alias | element | FXY | name | unit |
| --- | --- | --- | --- | --- | --- |
| M307051M307045 | M2 | E001063n0 | 001063 | ICAO location indicator | Character |
| M307051M307045 | M2 | E008079n1 | 008079 | Product status | Code table |
| M307051M307045 | M2 | E002001n2 | 002001 | Type of station | Code table |
| M307051M307045M301011 | M3 | E004001n0 | 004001 | Year | Year |
| M307051M307045M301011 | M3 | E004002n1 | 004002 | Month | Month |
| M307051M307045M301011 | M3 | E004003n2 | 004003 | Day | Day |
| M307051M307045M301012 | M4 | E004004n0 | 004004 | Hour | Hour |
| M307051M307045M301012 | M4 | E004005n1 | 004005 | Minute | Minute |
| M307051M307045M301023 | M5 | E005002n0 | 005002 | Latitude (coarse accuracy) | Degree |
| M307051M307045M301023 | M5 | E006002n1 | 006002 | Longitude (coarse accuracy) | Degree |
| M307051M307045 | M2 | E007030n3 | 007030 | Height of station ground above mean sea level (see Note 3) | m |
| M307051M307045 | M2 | E007031n4 | 007031 | Height of barometer above mean sea level (see Note 4) | m |
| M307051M307045 | M2 | E007032n5 | 007032 | Height of sensor above local ground (or deck of marine platf | m |
| M307051M307045 | M2 | E011001n6 | 011001 | Wind direction | Degree true |
| M307051M307045 | M2 | E011016n7 | 011016 | Extreme counterclockwise wind direction of a variable wind | Degree true |
| M307051M307045 | M2 | E011017n8 | 011017 | Extreme clockwise wind direction of a variable wind | Degree true |
| M307051M307045 | M2 | E008054n9 | 008054 | Qualifier for wind speed or wind gusts | Code table |
| M307051M307045 | M2 | E011083n10 | 011083 | Wind speed | km h-1 |
| M307051M307045 | M2 | E011084n11 | 011084 | Wind speed | knot |
| M307051M307045 | M2 | E011002n12 | 011002 | Wind speed | m s-1 |
| M307051M307045 | M2 | E008054n13 | 008054 | Qualifier for wind speed or wind gusts | Code table |
| M307051M307045 | M2 | E011085n14 | 011085 | Maximum wind gust speed | km h-1 |
| M307051M307045 | M2 | E011086n15 | 011086 | Maximum wind gust speed | knot |
| M307051M307045 | M2 | E011041n16 | 011041 | Maximum wind gust speed | m s-1 |
| M307051M307045 | M2 | E008054n17 | 008054 | Qualifier for wind speed or wind gusts | Code table |
| M307051M307045 | M2 | E007032n18 | 007032 | Height of sensor above local ground (or deck of marine platf | m |
| M307051M307045 | M2 | E012023n19 | 012023 | Temperature | Celsius |
| M307051M307045 | M2 | E012024n20 | 012024 | Dew point temperature | Celsius |
| M307051M307045 | M2 | E007032n21 | 007032 | Height of sensor above local ground (or deck of marine platf | m |
| M307051M307045 | M2 | E010052n22 | 010052 | Altimeter setting (QNH) | Pa |
| M307051M307045 | M2 | E020009n23 | 020009 | General Weather Indicator (TAF/METAR) | Code table |
| M307051M307046 | M6 | E020060n0 | 020060 | Prevailing horizontal visibility (5) | m |
| M307051M307046R1 | M7 | E005021n0 | 005021 | Bearing or azimuth | Degree true |
| M307051M307046R1 | M7 | E020059n1 | 020059 | Minimum horizontal visibility | m |
| M307051M307013R1 | M9 | E001064n0 | 001064 | Runway designator | Character |
| M307051M307013R1 | M9 | E008014n1 | 008014 | Qualifier for runway visual range | Code table |
| M307051M307013R1 | M9 | E020061n2 | 020061 | Runway visual range (RVR) | m |
| M307051M307013R1 | M9 | E008014n3 | 008014 | Qualifier for runway visual range | Code table |
| M307051M307013R1 | M9 | E020061n4 | 020061 | Runway visual range (RVR) | m |
| M307051M307013R1 | M9 | E020018n5 | 020018 | Tendency of runway visual range | Code table |
| M307051M307014R1 | M11 | E020019n0 | 020019 | Significant present or forecast weather | Character |
| M307051M307047R1 | M13 | E008002n0 | 008002 | Vertical significance (surface observations) | Code table |
| M307051M307047R1 | M13 | E020011n1 | 020011 | Cloud amount | Code table |
| M307051M307047R1 | M13 | E020012n2 | 020012 | Cloud type | Code table |
| M307051M307047R1 | M13 | E020013n3 | 020013 | Height of base of cloud | m |
| M307051M307047R1 | M13 | E020092n4 | 020092 | Height of base of cloud | Foot |
| M307051M307047 | M12 | E020002n0 | 020002 | Vertical visibility | m |
| M307051M307047 | M12 | E020091n1 | 020091 | Vertical visibility | Foot |
| M307051M307016R1 | M15 | E020020n0 | 020020 | Significant recent weather phenomena | Character |
| M307051M307017R1 | M17 | E011070n0 | 011070 | Designator of the runway affected by wind shear (including A | Character |
| M307051M307049 | M18 | E022043n0 | 022043 | Sea/water temperature | K |
| M307051M307049 | M18 | E022021n1 | 022021 | Height of waves | m |
| M307051M307050 | M19 | E020085n0 | 020085 | General condition of runway | Code table |
| M307051M307050R1 | M20 | E001064n0 | 001064 | Runway designator | Character |
| M307051M307050R1 | M20 | E020085n1 | 020085 | General condition of runway | Code table |
| M307051M307050R2 | M21 | E001064n0 | 001064 | Runway designator | Character |
| M307051M307050R2 | M21 | E020086n1 | 020086 | Runway deposits | Code table |
| M307051M307050R2 | M21 | E020087n2 | 020087 | Runway contamination | Code table |
| M307051M307050R2 | M21 | E020088n3 | 020088 | Depth of runway deposits | m |
| M307051M307050R2 | M21 | E020089n4 | 020089 | Runway friction coefficient | Code table |
| M307051R1M307048 | M23 | E008016n0 | 008016 | Change qualifier of a trend-type forecast or an aerodrome fo | Code table |
| M307051R1M307048R1 | M24 | E008017n0 | 008017 | Qualifier of the time when the forecast change is expected | Code table |
| M307051R1M307048R1M301012 | M25 | E004004n0 | 004004 | Hour | Hour |
| M307051R1M307048R1M301012 | M25 | E004005n1 | 004005 | Minute | Minute |
| M307051R1M307048 | M23 | E007032n1 | 007032 | Height of sensor above local ground (or deck of marine platf | m |
| M307051R1M307048 | M23 | E011001n2 | 011001 | Wind direction | Degree true |
| M307051R1M307048 | M23 | E008054n3 | 008054 | Qualifier for wind speed or wind gusts | Code table |
| M307051R1M307048 | M23 | E011083n4 | 011083 | Wind speed | km h-1 |
| M307051R1M307048 | M23 | E011084n5 | 011084 | Wind speed | knot |
| M307051R1M307048 | M23 | E011002n6 | 011002 | Wind speed | m s-1 |
| M307051R1M307048 | M23 | E008054n7 | 008054 | Qualifier for wind speed or wind gusts | Code table |
| M307051R1M307048 | M23 | E011085n8 | 011085 | Maximum wind gust speed | km h-1 |
| M307051R1M307048 | M23 | E011086n9 | 011086 | Maximum wind gust speed | knot |
| M307051R1M307048 | M23 | E011041n10 | 011041 | Maximum wind gust speed | m s-1 |
| M307051R1M307048 | M23 | E008054n11 | 008054 | Qualifier for wind speed or wind gusts | Code table |
| M307051R1M307048 | M23 | E007032n12 | 007032 | Height of sensor above local ground (or deck of marine platf | m |
| M307051R1M307048 | M23 | E020009n13 | 020009 | General Weather Indicator (TAF/METAR) | Code table |
| M307051R1M307048 | M23 | E020060n14 | 020060 | Prevailing horizontal visibility (5) | m |
| M307051R1M307048M307014R1 | M27 | E020019n0 | 020019 | Significant present or forecast weather | Character |
| M307051R1M307048M307047R1 | M29 | E008002n0 | 008002 | Vertical significance (surface observations) | Code table |
| M307051R1M307048M307047R1 | M29 | E020011n1 | 020011 | Cloud amount | Code table |
| M307051R1M307048M307047R1 | M29 | E020012n2 | 020012 | Cloud type | Code table |
| M307051R1M307048M307047R1 | M29 | E020013n3 | 020013 | Height of base of cloud | m |
| M307051R1M307048M307047R1 | M29 | E020092n4 | 020092 | Height of base of cloud | Foot |
| M307051R1M307048M307047 | M28 | E020002n0 | 020002 | Vertical visibility | m |
| M307051R1M307048M307047 | M28 | E020091n1 | 020091 | Vertical visibility | Foot |

(b) List of tables of the tree ordered by field “table”

| table | alias | Field | FXY | name | unit |
| --- | --- | --- | --- | --- | --- |
| M307051M307045 | M2 | E001063n0 | 001063 | ICAO location indicator | Character |
| M307051M307045 | M2 | E008079n1 | 008079 | Product status | Code table |
| M307051M307045 | M2 | E002001n2 | 002001 | Type of station | Code table |
| M307051M307045 | M2 | E007030n3 | 007030 | Height of station ground above mean sea level (see Note 3) | m |
| M307051M307045 | M2 | E007031n4 | 007031 | Height of barometer above mean sea level (see Note 4) | m |
| M307051M307045 | M2 | E007032n5 | 007032 | Height of sensor above local ground (or deck of marine platf | m |
| M307051M307045 | M2 | E011001n6 | 011001 | Wind direction | Degree true |
| M307051M307045 | M2 | E011016n7 | 011016 | Extreme counterclockwise wind direction of a variable wind | Degree true |
| M307051M307045 | M2 | E011017n8 | 011017 | Extreme clockwise wind direction of a variable wind | Degree true |
| M307051M307045 | M2 | E008054n9 | 008054 | Qualifier for wind speed or wind gusts | Code table |
| M307051M307045 | M2 | E011083n10 | 011083 | Wind speed | km h-1 |
| M307051M307045 | M2 | E011084n11 | 011084 | Wind speed | knot |
| M307051M307045 | M2 | E011002n12 | 011002 | Wind speed | m s-1 |
| M307051M307045 | M2 | E008054n13 | 008054 | Qualifier for wind speed or wind gusts | Code table |
| M307051M307045 | M2 | E011085n14 | 011085 | Maximum wind gust speed | km h-1 |
| M307051M307045 | M2 | E011086n15 | 011086 | Maximum wind gust speed | knot |
| M307051M307045 | M2 | E011041n16 | 011041 | Maximum wind gust speed | m s-1 |
| M307051M307045 | M2 | E008054n17 | 008054 | Qualifier for wind speed or wind gusts | Code table |
| M307051M307045 | M2 | E007032n18 | 007032 | Height of sensor above local ground (or deck of marine platf | m |
| M307051M307045 | M2 | E012023n19 | 012023 | Temperature | Celsius |
| M307051M307045 | M2 | E012024n20 | 012024 | Dew point temperature | Celsius |
| M307051M307045 | M2 | E007032n21 | 007032 | Height of sensor above local ground (or deck of marine platf | m |
| M307051M307045 | M2 | E010052n22 | 010052 | Altimeter setting (QNH) | Pa |
| M307051M307045 | M2 | E020009n23 | 020009 | General Weather Indicator (TAF/METAR) | Code table |
| M307051M307045M301011 | M3 | E004001n0 | 004001 | Year | Year |
| M307051M307045M301011 | M3 | E004002n1 | 004002 | Month | Month |
| M307051M307045M301011 | M3 | E004003n2 | 004003 | Day | Day |
| M307051M307045M301012 | M4 | E004004n0 | 004004 | Hour | Hour |
| M307051M307045M301012 | M4 | E004005n1 | 004005 | Minute | Minute |
| M307051M307045M301023 | M5 | E005002n0 | 005002 | Latitude (coarse accuracy) | Degree |
| M307051M307045M301023 | M5 | E006002n1 | 006002 | Longitude (coarse accuracy) | Degree |
| M307051M307046 | M6 | E020060n0 | 020060 | Prevailing horizontal visibility (5) | m |
| M307051M307046R1 | M7 | E005021n0 | 005021 | Bearing or azimuth | Degree true |
| M307051M307046R1 | M7 | E020059n1 | 020059 | Minimum horizontal visibility | m |
| M307051M307013R1 | M9 | E001064n0 | 001064 | Runway designator | Character |
| M307051M307013R1 | M9 | E008014n1 | 008014 | Qualifier for runway visual range | Code table |
| M307051M307013R1 | M9 | E020061n2 | 020061 | Runway visual range (RVR) | m |
| M307051M307013R1 | M9 | E008014n3 | 008014 | Qualifier for runway visual range | Code table |
| M307051M307013R1 | M9 | E020061n4 | 020061 | Runway visual range (RVR) | m |
| M307051M307013R1 | M9 | E020018n5 | 020018 | Tendency of runway visual range | Code table |
| M307051M307014R1 | M11 | E020019n0 | 020019 | Significant present or forecast weather | Character |
| M307051M307047 | M12 | E020002n0 | 020002 | Vertical visibility | m |
| M307051M307047 | M12 | E020091n1 | 020091 | Vertical visibility | Foot |
| M307051M307047R1 | M13 | E008002n0 | 008002 | Vertical significance (surface observations) | Code table |
| M307051M307047R1 | M13 | E020011n1 | 020011 | Cloud amount | Code table |
| M307051M307047R1 | M13 | E020012n2 | 020012 | Cloud type | Code table |
| M307051M307047R1 | M13 | E020013n3 | 020013 | Height of base of cloud | m |
| M307051M307047R1 | M13 | E020092n4 | 020092 | Height of base of cloud | Foot |
| M307051M307016R1 | M15 | E020020n0 | 020020 | Significant recent weather phenomena | Character |
| M307051M307017R1 | M17 | E011070n0 | 011070 | Designator of the runway affected by wind shear (including A | Character |
| M307051M307049 | M18 | E022043n0 | 022043 | Sea/water temperature | K |
| M307051M307049 | M18 | E022021n1 | 022021 | Height of waves | m |
| M307051M307050 | M19 | E020085n0 | 020085 | General condition of runway | Code table |
| M307051M307050R1 | M20 | E001064n0 | 001064 | Runway designator | Character |
| M307051M307050R1 | M20 | E020085n1 | 020085 | General condition of runway | Code table |
| M307051M307050R2 | M21 | E001064n0 | 001064 | Runway designator | Character |
| M307051M307050R2 | M21 | E020086n1 | 020086 | Runway deposits | Code table |
| M307051M307050R2 | M21 | E020087n2 | 020087 | Runway contamination | Code table |
| M307051M307050R2 | M21 | E020088n3 | 020088 | Depth of runway deposits | m |
| M307051M307050R2 | M21 | E020089n4 | 020089 | Runway friction coefficient | Code table |
| M307051R1M307048 | M23 | E008016n0 | 008016 | Change qualifier of a trend-type forecast or an aerodrome fo | Code table |
| M307051R1M307048 | M23 | E007032n1 | 007032 | Height of sensor above local ground (or deck of marine platf | m |
| M307051R1M307048 | M23 | E011001n2 | 011001 | Wind direction | Degree true |
| M307051R1M307048 | M23 | E008054n3 | 008054 | Qualifier for wind speed or wind gusts | Code table |
| M307051R1M307048 | M23 | E011083n4 | 011083 | Wind speed | km h-1 |
| M307051R1M307048 | M23 | E011084n5 | 011084 | Wind speed | knot |
| M307051R1M307048 | M23 | E011002n6 | 011002 | Wind speed | m s-1 |
| M307051R1M307048 | M23 | E008054n7 | 008054 | Qualifier for wind speed or wind gusts | Code table |
| M307051R1M307048 | M23 | E011085n8 | 011085 | Maximum wind gust speed | km h-1 |
| M307051R1M307048 | M23 | E011086n9 | 011086 | Maximum wind gust speed | knot |
| M307051R1M307048 | M23 | E011041n10 | 011041 | Maximum wind gust speed | m s-1 |
| M307051R1M307048 | M23 | E008054n11 | 008054 | Qualifier for wind speed or wind gusts | Code table |
| M307051R1M307048 | M23 | E007032n12 | 007032 | Height of sensor above local ground (or deck of marine platf | m |
| M307051R1M307048 | M23 | E020009n13 | 020009 | General Weather Indicator (TAF/METAR) | Code table |
| M307051R1M307048 | M23 | E020060n14 | 020060 | Prevailing horizontal visibility (5) | m |
| M307051R1M307048R1 | M24 | E008017n0 | 008017 | Qualifier of the time when the forecast change is expected | Code table |
| M307051R1M307048R1M301012 | M25 | E004004n0 | 004004 | Hour | Hour |
| M307051R1M307048R1M301012 | M25 | E004005n1 | 004005 | Minute | Minute |
| M307051R1M307048M307014R1 | M27 | E020019n0 | 020019 | Significant present or forecast weather | Character |
| M307051R1M307048M307047 | M28 | E020002n0 | 020002 | Vertical visibility | m |
| M307051R1M307048M307047 | M28 | E020091n1 | 020091 | Vertical visibility | Foot |
| M307051R1M307048M307047R1 | M29 | E008002n0 | 008002 | Vertical significance (surface observations) | Code table |
| M307051R1M307048M307047R1 | M29 | E020011n1 | 020011 | Cloud amount | Code table |
| M307051R1M307048M307047R1 | M29 | E020012n2 | 020012 | Cloud type | Code table |
| M307051R1M307048M307047R1 | M29 | E020013n3 | 020013 | Height of base of cloud | m |
| M307051R1M307048M307047R1 | M29 | E020092n4 | 020092 | Height of base of cloud | Foot |

Annex 6

Structure of the tables of the tree and their relationship in the METAR/SPECI model

Annex 7

Instance of a SPECI report in XML format for interchange

The names of the files are of the type Mn (Alias in Annex 5) and the names of the fields are reduced to (E + sequence number of the field in the table).

<?xml version="1.0" encoding="UTF-8" ?>

- <dataroot xmlns:od="urn:schemas-microsoft-com:officedata" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xsi:noNamespaceSchemaLocation="W_xx-org-centre,SPECI,_C_LUDO_200902211025.xsd" generated="2009-02-09T13:41:04">

- <M1>

<Sequence>307051</Sequence>

<F0>1</F0>

- <M2>

<F0>1</F0>

<F1>1</F1>

<E0>LUDO</E0>

<E1>SPECI</E1>

<E2>AUTO</E2>

<E3>30</E3>

<E4>33</E4>

<E5>3</E5>

<E6>310</E6>

<E7>280</E7>

<E8>350</E8>

<E9>0</E9>

<E11>15</E11>

<E15>27</E15>

<E19>10</E19>

<E20>3</E20>

- <M3>

<F1>1</F1>

<E2>21</E2>

</M3>

- <M4>

<F1>1</F1>

<E0>10</E0>

<E1>25</E1>

</M4>

- <M5>

<F1>1</F1>

</M5>

</M2>

- <M12>

<F0>1</F0>

<F11>1</F11>

- <M13>

<F11>1</F11>

<E1>FEW</E1>

<E4>500</E4>

</M13>

- <M13>

<F11>1</F11>

<F12>2</F12>

<E1>FEW</E1>

<E2>CB</E2>

<E4>1000</E4>

</M13>

- <M13>

<F11>1</F11>

<F12>3</F12>

<E1>SCT</E1>

<E4>1800</E4>

</M13>

- <M13>

<F11>1</F11>

<F12>4</F12>

</M13>

- <M13>

<F11>1</F11>

<F12>5</F12>

</M13>

</M12>

- <M14>

<F0>1</F0>

<F13>1</F13>

- <M15>

<F13>1</F13>

<E0>RERA</E0>

</M15>

</M14>

- <M16>

<F0>1</F0>

<F15>1</F15>

- <M17>

<F15>1</F15>

<E0>R24</E0>

</M17>

</M16>

- <M18>

<F0>1</F0>

</M18>

- <M19>

<F0>1</F0>

<F18>1</F18>

- <M20>

<F18>1</F18>

<E0>R24</E0>

</M20>

- <M21>

<F18>1</F18>

<E0>R24</E0>

<E1>4</E1>

<E2>5</E2>

<E3>12</E3>

<E4>93</E4>

</M21>

</M19>

- <M22>

<F0>1</F0>

<F21>1</F21>

- <M23>

<F21>1</F21>

<F22>1</F22>

<E0>BECMG</E0>

<E2>250</E2>

<E5>35</E5>

<E8>50</E8>

<E14>6000</E14>

- <M24>

<F22>1</F22>

<F23>1</F23>

<E0>FM</E0>

- <M25>

<F23>1</F23>

<E0>11</E0>

<E1>00</E1>

</M25>

</M24>

- <M26>

<F22>1</F22>

<F25>1</F25>

- <M27>

<F25>1</F25>

<E0>NSW</E0>

</M27>

</M26>

- <M28>

<F22>1</F22>

<F27>1</F27>

- <M29>

<F27>1</F27>

</M29>

</M28>

</M23>

</M22>

- <M6>

<F0>1</F0>

<F5>1</F5>

<E0>4000</E0>

- <M7>

<F5>1</F5>

<E0>SW</E0>

<E1>1400</E1>

</M7>

</M6>

- <M8>

<F0>1</F0>

<F7>1</F7>

- <M9>

<F7>1</F7>

<E0>R24</E0>

<E2>P2000</E2>

</M9>

</M8>

- <M10>

<F0>1</F0>

<F9>1</F9>

- <M11>

<F9>1</F9>

<E0>+SHRA</E0>

</M11>

</M10>

</M1>

</dataroot>

Annex 8

Table of the tables of the tree and their relationship for the TAF model

| name | alias | alias_2 (see footnote 2) | description | ForeignKey | index |
| --- | --- | --- | --- | --- | --- |
| T307056 | T1 | TAF |  |  | F0 |
| T307056T307052 | T2 | IdentificationTimeInterval | Identification and time interval | F0 | F1 |
| T307056T307052T301011 | T3 | YYMMDD1 | Year, Month, Day | F1 | F2 |
| T307056T307052T301012 | T4 | HHmn1 | Hour, Minute | F1 | F3 |
| T307056T307052T301011D1 | T5 | YYMMDD2 | Year, Month, Day | F1 | F4 |
| T307056T307052T301012D1 | T6 | HHmn2 | Hour, Minute | F1 | F5 |
| T307056T307052T301011D2 | T7 | YYMMDD3 | Year, Month, Day | F1 | F6 |
| T307056T307052T301012D2 | T8 | HHmn3 | Hour, Minute | F1 | F7 |
| T307056T307052T301023 | T9 | Coordinates | Latitude-longitude (coarse accuracy) | F1 | F8 |
| T307056T307053 | T10 | Forecast | Forecast | F0 | F9 |
| T307056T307053T307014 | T11 | Weather1 | Weather | F9 | F10 |
| T307056T307053T307014R1 | T12 | ByTypes1_R |  | F10 | F11 |
| T307056T307053T307047 | T13 | CloudLayer(s)1 | Cloud layer(s) | F9 | F12 |
| T307056T307053T307047R1 | T14 | ByLayers_1R |  | F12 | F13 |
| T307056T307054 | T15 | ExtremeTemperaturesForecast | Extreme temperatures forecast | F0 | F14 |
| T307056R1 | T16 | SignificantChanges |  | F0 | F15 |
| T307056R1T307055 | T17 | ForecastChange | Forecast change | F15 | F16 |
| T307056R1T307055T301012 | T18 | HHmn4 | Hour, Minute | F16 | F17 |
| T307056R1T307055T301012D1 | T19 | HHmn5 | Hour, Minute | F16 | F18 |
| T307056R1T307055T307053 | T20 | ForecastConditions | Forecast conditions during or after change | F16 | F19 |
| T307056R1T307055T307053T307014 | T21 | Weather2 | Weather | F19 | F20 |
| T307056R1T307055T307053T307014R1 | T22 | ByTypes2_R |  | F20 | F21 |
| T307056R1T307055T307053T307047 | T23 | CloudLayer(s)2 | Cloud layer(s) | F19 | F22 |
| T307056R1T307055T307053T307047R1 | T24 | ByLayers_2R |  | F22 | F23 |

Annex 9

Structure of the tables of the tree for the TAF model

(a) List of elements FXY in the order of the reading of the catalogue of sequences, as fields of the tables of the tree

| table | alias | element | FXY | name | unit |
| --- | --- | --- | --- | --- | --- |
| T307056T307052 | T2 | E001063n0 | 001063 | ICAO location indicator | Character |
| T307056T307052 | T2 | E008039n1 | 008039 | Time significance (Aviation forecast) | Code table |
| T307056T307052T301011 | T3 | E004001n0 | 004001 | Year | Year |
| T307056T307052T301011 | T3 | E004002n1 | 004002 | Month | Month |
| T307056T307052T301011 | T3 | E004003n2 | 004003 | Day | Day |
| T307056T307052T301012 | T4 | E004004n0 | 004004 | Hour | Hour |
| T307056T307052T301012 | T4 | E004005n1 | 004005 | Minute | Minute |
| T307056T307052 | T2 | E008079n2 | 008079 | Product status | Code table |
| T307056T307052 | T2 | E008039n3 | 008039 | Time significance (Aviation forecast) | Code table |
| T307056T307052T301011D1 | T5 | E004001n0 | 004001 | Year | Year |
| T307056T307052T301011D1 | T5 | E004002n1 | 004002 | Month | Month |
| T307056T307052T301011D1 | T5 | E004003n2 | 004003 | Day | Day |
| T307056T307052T301012D1 | T6 | E004004n0 | 004004 | Hour | Hour |
| T307056T307052T301012D1 | T6 | E004005n1 | 004005 | Minute | Minute |
| T307056T307052 | T2 | E008039n4 | 008039 | Time significance (Aviation forecast) | Code table |
| T307056T307052T301011D2 | T7 | E004001n0 | 004001 | Year | Year |
| T307056T307052T301011D2 | T7 | E004002n1 | 004002 | Month | Month |
| T307056T307052T301011D2 | T7 | E004003n2 | 004003 | Day | Day |
| T307056T307052T301012D2 | T8 | E004004n0 | 004004 | Hour | Hour |
| T307056T307052T301012D2 | T8 | E004005n1 | 004005 | Minute | Minute |
| T307056T307052T301023 | T9 | E005002n0 | 005002 | Latitude (coarse accuracy) | Degree |
| T307056T307052T301023 | T9 | E006002n1 | 006002 | Longitude (coarse accuracy) | Degree |
| T307056T307052 | T2 | E007030n5 | 007030 | Height of station ground above mean sea level (see Note 3) | m |
| T307056T307052 | T2 | E007031n6 | 007031 | Height of barometer above mean sea level (see Note 4) | m |
| T307056T307053 | T10 | E007032n0 | 007032 | Height of sensor above local ground (or deck of marine platf | m |
| T307056T307053 | T10 | E011001n1 | 011001 | Wind direction | Degree true |
| T307056T307053 | T10 | E008054n2 | 008054 | Qualifier for wind speed or wind gusts | Code table |
| T307056T307053 | T10 | E011083n3 | 011083 | Wind speed | km h-1 |
| T307056T307053 | T10 | E011084n4 | 011084 | Wind speed | knot |
| T307056T307053 | T10 | E011002n5 | 011002 | Wind speed | m s-1 |
| T307056T307053 | T10 | E008054n6 | 008054 | Qualifier for wind speed or wind gusts | Code table |
| T307056T307053 | T10 | E011085n7 | 011085 | Maximum wind gust speed | km h-1 |
| T307056T307053 | T10 | E011086n8 | 011086 | Maximum wind gust speed | knot |
| T307056T307053 | T10 | E011041n9 | 011041 | Maximum wind gust speed | m s-1 |
| T307056T307053 | T10 | E008054n10 | 008054 | Qualifier for wind speed or wind gusts | Code table |
| T307056T307053 | T10 | E007032n11 | 007032 | Height of sensor above local ground (or deck of marine platf | m |
| T307056T307053 | T10 | E020009n12 | 020009 | General Weather Indicator (TAF/METAR) | Code table |
| T307056T307053 | T10 | E020060n13 | 020060 | Prevailing horizontal visibility (5) | m |
| T307056T307053T307014R1 | T12 | E020019n0 | 020019 | Significant present or forecast weather | Character |
| T307056T307053T307047R1 | T14 | E008002n0 | 008002 | Vertical significance (surface observations) | Code table |
| T307056T307053T307047R1 | T14 | E020011n1 | 020011 | Cloud amount | Code table |
| T307056T307053T307047R1 | T14 | E020012n2 | 020012 | Cloud type | Code table |
| T307056T307053T307047R1 | T14 | E020013n3 | 020013 | Height of base of cloud | m |
| T307056T307053T307047R1 | T14 | E020092n4 | 020092 | Height of base of cloud | Foot |
| T307056T307053T307047 | T13 | E020002n0 | 020002 | Vertical visibility | m |
| T307056T307053T307047 | T13 | E020091n1 | 020091 | Vertical visibility | Foot |
| T307056T307054 | T15 | E007032n0 | 007032 | Height of sensor above local ground (or deck of marine platf | m |
| T307056T307054 | T15 | E008039n1 | 008039 | Time significance (Aviation forecast) | Code table |
| T307056T307054 | T15 | E004003n2 | 004003 | Day | Day |
| T307056T307054 | T15 | E004004n3 | 004004 | Hour | Hour |
| T307056T307054 | T15 | E008023n4 | 008023 | First order statistics | Code table |
| T307056T307054 | T15 | E012023n5 | 012023 | Temperature | Celsius |
| T307056T307054 | T15 | E008039n6 | 008039 | Time significance (Aviation forecast) | Code table |
| T307056T307054 | T15 | E004003n7 | 004003 | Day | Day |
| T307056T307054 | T15 | E004004n8 | 004004 | Hour | Hour |
| T307056T307054 | T15 | E008023n9 | 008023 | First order statistics | Code table |
| T307056T307054 | T15 | E012023n10 | 012023 | Temperature | Celsius |
| T307056T307054 | T15 | E008023n11 | 008023 | First order statistics | Code table |
| T307056T307054 | T15 | E007032n12 | 007032 | Height of sensor above local ground (or deck of marine platf | m |
| T307056R1T307055 | T17 | E033045n0 | 033045 | Probability of following event (see Notes 1 and 3) | % |
| T307056R1T307055 | T17 | E008016n1 | 008016 | Change qualifier of a trend-type forecast or an aerodrome fo | Code table |
| T307056R1T307055 | T17 | E008039n2 | 008039 | Time significance (Aviation forecast) | Code table |
| T307056R1T307055 | T17 | E004003n3 | 004003 | Day | Day |
| T307056R1T307055T301012 | T18 | E004004n0 | 004004 | Hour | Hour |
| T307056R1T307055T301012 | T18 | E004005n1 | 004005 | Minute | Minute |
| T307056R1T307055 | T17 | E008039n4 | 008039 | Time significance (Aviation forecast) | Code table |
| T307056R1T307055 | T17 | E004003n5 | 004003 | Day | Day |
| T307056R1T307055T301012D1 | T19 | E004004n0 | 004004 | Hour | Hour |
| T307056R1T307055T301012D1 | T19 | E004005n1 | 004005 | Minute | Minute |
| T307056R1T307055T307053 | T20 | E007032n0 | 007032 | Height of sensor above local ground (or deck of marine platf | m |
| T307056R1T307055T307053 | T20 | E011001n1 | 011001 | Wind direction | Degree true |
| T307056R1T307055T307053 | T20 | E008054n2 | 008054 | Qualifier for wind speed or wind gusts | Code table |
| T307056R1T307055T307053 | T20 | E011083n3 | 011083 | Wind speed | km h-1 |
| T307056R1T307055T307053 | T20 | E011084n4 | 011084 | Wind speed | knot |
| T307056R1T307055T307053 | T20 | E011002n5 | 011002 | Wind speed | m s-1 |
| T307056R1T307055T307053 | T20 | E008054n6 | 008054 | Qualifier for wind speed or wind gusts | Code table |
| T307056R1T307055T307053 | T20 | E011085n7 | 011085 | Maximum wind gust speed | km h-1 |
| T307056R1T307055T307053 | T20 | E011086n8 | 011086 | Maximum wind gust speed | knot |
| T307056R1T307055T307053 | T20 | E011041n9 | 011041 | Maximum wind gust speed | m s-1 |
| T307056R1T307055T307053 | T20 | E008054n10 | 008054 | Qualifier for wind speed or wind gusts | Code table |
| T307056R1T307055T307053 | T20 | E007032n11 | 007032 | Height of sensor above local ground (or deck of marine platf | m |
| T307056R1T307055T307053 | T20 | E020009n12 | 020009 | General Weather Indicator (TAF/METAR) | Code table |
| T307056R1T307055T307053 | T20 | E020060n13 | 020060 | Prevailing horizontal visibility (5) | m |
| T307056R1T307055T307053T307014R1 | T22 | E020019n0 | 020019 | Significant present or forecast weather | Character |
| T307056R1T307055T307053T307047R1 | T24 | E008002n0 | 008002 | Vertical significance (surface observations) | Code table |
| T307056R1T307055T307053T307047R1 | T24 | E020011n1 | 020011 | Cloud amount | Code table |
| T307056R1T307055T307053T307047R1 | T24 | E020012n2 | 020012 | Cloud type | Code table |
| T307056R1T307055T307053T307047R1 | T24 | E020013n3 | 020013 | Height of base of cloud | m |
| T307056R1T307055T307053T307047R1 | T24 | E020092n4 | 020092 | Height of base of cloud | Foot |
| T307056R1T307055T307053T307047 | T23 | E020002n0 | 020002 | Vertical visibility | m |
| T307056R1T307055T307053T307047 | T23 | E020091n1 | 020091 | Vertical visibility | Foot |

(b) List of tables of the tree ordered by field “table”

| table | alias | Field | FXY | name | unit |
| --- | --- | --- | --- | --- | --- |
| T307056T307052 | T2 | E001063n0 | 001063 | ICAO location indicator | Character |
| T307056T307052 | T2 | E008039n1 | 008039 | Time significance (Aviation forecast) | Code table |
| T307056T307052 | T2 | E008079n2 | 008079 | Product status | Code table |
| T307056T307052 | T2 | E008039n3 | 008039 | Time significance (Aviation forecast) | Code table |
| T307056T307052 | T2 | E008039n4 | 008039 | Time significance (Aviation forecast) | Code table |
| T307056T307052 | T2 | E007030n5 | 007030 | Height of station ground above mean sea level (see Note 3) | m |
| T307056T307052 | T2 | E007031n6 | 007031 | Height of barometer above mean sea level (see Note 4) | m |
| T307056T307052T301011 | T3 | E004001n0 | 004001 | Year | Year |
| T307056T307052T301011 | T3 | E004002n1 | 004002 | Month | Month |
| T307056T307052T301011 | T3 | E004003n2 | 004003 | Day | Day |
| T307056T307052T301012 | T4 | E004004n0 | 004004 | Hour | Hour |
| T307056T307052T301012 | T4 | E004005n1 | 004005 | Minute | Minute |
| T307056T307052T301011D1 | T5 | E004001n0 | 004001 | Year | Year |
| T307056T307052T301011D1 | T5 | E004002n1 | 004002 | Month | Month |
| T307056T307052T301011D1 | T5 | E004003n2 | 004003 | Day | Day |
| T307056T307052T301012D1 | T6 | E004004n0 | 004004 | Hour | Hour |
| T307056T307052T301012D1 | T6 | E004005n1 | 004005 | Minute | Minute |
| T307056T307052T301011D2 | T7 | E004001n0 | 004001 | Year | Year |
| T307056T307052T301011D2 | T7 | E004002n1 | 004002 | Month | Month |
| T307056T307052T301011D2 | T7 | E004003n2 | 004003 | Day | Day |
| T307056T307052T301012D2 | T8 | E004004n0 | 004004 | Hour | Hour |
| T307056T307052T301012D2 | T8 | E004005n1 | 004005 | Minute | Minute |
| T307056T307052T301023 | T9 | E005002n0 | 005002 | Latitude (coarse accuracy) | Degree |
| T307056T307052T301023 | T9 | E006002n1 | 006002 | Longitude (coarse accuracy) | Degree |
| T307056T307053 | T10 | E007032n0 | 007032 | Height of sensor above local ground (or deck of marine platf | m |
| T307056T307053 | T10 | E011001n1 | 011001 | Wind direction | Degree true |
| T307056T307053 | T10 | E008054n2 | 008054 | Qualifier for wind speed or wind gusts | Code table |
| T307056T307053 | T10 | E011083n3 | 011083 | Wind speed | km h-1 |
| T307056T307053 | T10 | E011084n4 | 011084 | Wind speed | knot |
| T307056T307053 | T10 | E011002n5 | 011002 | Wind speed | m s-1 |
| T307056T307053 | T10 | E008054n6 | 008054 | Qualifier for wind speed or wind gusts | Code table |
| T307056T307053 | T10 | E011085n7 | 011085 | Maximum wind gust speed | km h-1 |
| T307056T307053 | T10 | E011086n8 | 011086 | Maximum wind gust speed | knot |
| T307056T307053 | T10 | E011041n9 | 011041 | Maximum wind gust speed | m s-1 |
| T307056T307053 | T10 | E008054n10 | 008054 | Qualifier for wind speed or wind gusts | Code table |
| T307056T307053 | T10 | E007032n11 | 007032 | Height of sensor above local ground (or deck of marine platf | m |
| T307056T307053 | T10 | E020009n12 | 020009 | General Weather Indicator (TAF/METAR) | Code table |
| T307056T307053 | T10 | E020060n13 | 020060 | Prevailing horizontal visibility (5) | m |
| T307056T307053T307014R1 | T12 | E020019n0 | 020019 | Significant present or forecast weather | Character |
| T307056T307053T307047 | T13 | E020002n0 | 020002 | Vertical visibility | m |
| T307056T307053T307047 | T13 | E020091n1 | 020091 | Vertical visibility | Foot |
| T307056T307053T307047R1 | T14 | E008002n0 | 008002 | Vertical significance (surface observations) | Code table |
| T307056T307053T307047R1 | T14 | E020011n1 | 020011 | Cloud amount | Code table |
| T307056T307053T307047R1 | T14 | E020012n2 | 020012 | Cloud type | Code table |
| T307056T307053T307047R1 | T14 | E020013n3 | 020013 | Height of base of cloud | m |
| T307056T307053T307047R1 | T14 | E020092n4 | 020092 | Height of base of cloud | Foot |
| T307056T307054 | T15 | E007032n0 | 007032 | Height of sensor above local ground (or deck of marine platf | m |
| T307056T307054 | T15 | E008039n1 | 008039 | Time significance (Aviation forecast) | Code table |
| T307056T307054 | T15 | E004003n2 | 004003 | Day | Day |
| T307056T307054 | T15 | E004004n3 | 004004 | Hour | Hour |
| T307056T307054 | T15 | E008023n4 | 008023 | First order statistics | Code table |
| T307056T307054 | T15 | E012023n5 | 012023 | Temperature | Celsius |
| T307056T307054 | T15 | E008039n6 | 008039 | Time significance (Aviation forecast) | Code table |
| T307056T307054 | T15 | E004003n7 | 004003 | Day | Day |
| T307056T307054 | T15 | E004004n8 | 004004 | Hour | Hour |
| T307056T307054 | T15 | E008023n9 | 008023 | First order statistics | Code table |
| T307056T307054 | T15 | E012023n10 | 012023 | Temperature | Celsius |
| T307056T307054 | T15 | E008023n11 | 008023 | First order statistics | Code table |
| T307056T307054 | T15 | E007032n12 | 007032 | Height of sensor above local ground (or deck of marine platf | m |
| T307056R1T307055 | T17 | E033045n0 | 033045 | Probability of following event (see Notes 1 and 3) | % |
| T307056R1T307055 | T17 | E008016n1 | 008016 | Change qualifier of a trend-type forecast or an aerodrome fo | Code table |
| T307056R1T307055 | T17 | E008039n2 | 008039 | Time significance (Aviation forecast) | Code table |
| T307056R1T307055 | T17 | E004003n3 | 004003 | Day | Day |
| T307056R1T307055 | T17 | E008039n4 | 008039 | Time significance (Aviation forecast) | Code table |
| T307056R1T307055 | T17 | E004003n5 | 004003 | Day | Day |
| T307056R1T307055T301012 | T18 | E004004n0 | 004004 | Hour | Hour |
| T307056R1T307055T301012 | T18 | E004005n1 | 004005 | Minute | Minute |
| T307056R1T307055T301012D1 | T19 | E004004n0 | 004004 | Hour | Hour |
| T307056R1T307055T301012D1 | T19 | E004005n1 | 004005 | Minute | Minute |
| T307056R1T307055T307053 | T20 | E007032n0 | 007032 | Height of sensor above local ground (or deck of marine platf | m |
| T307056R1T307055T307053 | T20 | E011001n1 | 011001 | Wind direction | Degree true |
| T307056R1T307055T307053 | T20 | E008054n2 | 008054 | Qualifier for wind speed or wind gusts | Code table |
| T307056R1T307055T307053 | T20 | E011083n3 | 011083 | Wind speed | km h-1 |
| T307056R1T307055T307053 | T20 | E011084n4 | 011084 | Wind speed | knot |
| T307056R1T307055T307053 | T20 | E011002n5 | 011002 | Wind speed | m s-1 |
| T307056R1T307055T307053 | T20 | E008054n6 | 008054 | Qualifier for wind speed or wind gusts | Code table |
| T307056R1T307055T307053 | T20 | E011085n7 | 011085 | Maximum wind gust speed | km h-1 |
| T307056R1T307055T307053 | T20 | E011086n8 | 011086 | Maximum wind gust speed | knot |
| T307056R1T307055T307053 | T20 | E011041n9 | 011041 | Maximum wind gust speed | m s-1 |
| T307056R1T307055T307053 | T20 | E008054n10 | 008054 | Qualifier for wind speed or wind gusts | Code table |
| T307056R1T307055T307053 | T20 | E007032n11 | 007032 | Height of sensor above local ground (or deck of marine platf | m |
| T307056R1T307055T307053 | T20 | E020009n12 | 020009 | General Weather Indicator (TAF/METAR) | Code table |
| T307056R1T307055T307053 | T20 | E020060n13 | 020060 | Prevailing horizontal visibility (5) | m |
| T307056R1T307055T307053T307014R1 | T22 | E020019n0 | 020019 | Significant present or forecast weather | Character |
| T307056R1T307055T307053T307047 | T23 | E020002n0 | 020002 | Vertical visibility | m |
| T307056R1T307055T307053T307047 | T23 | E020091n1 | 020091 | Vertical visibility | Foot |
| T307056R1T307055T307053T307047R1 | T24 | E008002n0 | 008002 | Vertical significance (surface observations) | Code table |
| T307056R1T307055T307053T307047R1 | T24 | E020011n1 | 020011 | Cloud amount | Code table |
| T307056R1T307055T307053T307047R1 | T24 | E020012n2 | 020012 | Cloud type | Code table |
| T307056R1T307055T307053T307047R1 | T24 | E020013n3 | 020013 | Height of base of cloud | m |
| T307056R1T307055T307053T307047R1 | T24 | E020092n4 | 020092 | Height of base of cloud | Foot |

Annex 10

Structure of the tables of the tree and their relationship in the TAF model

Annex 11

Instance of a TAF report in XML format for interchange

The names of the files are of the type Tn (Alias in Annex 9) and the names of the fields are reduced to (E + sequence number of the field in the table).

<?xml version="1.0" encoding="UTF-8" ?>

- <dataroot xmlns:od="urn:schemas-microsoft-com:officedata" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xsi:noNamespaceSchemaLocation=" W_xx-org-centre,TAF,_C_LUDO_200902130530.xsd" generated="2009-02-08T15:37:59">

- <T1>

<Sequence>307056</Sequence>

<F0>1</F0>

- <T2>

<F0>1</F0>

<F1>1</F1>

<E0>LUDO</E0>

<E2>TAF</E2>

- <T3>

<F1>1</F1>

<E2>13</E2>

</T3>

- <T4>

<F1>1</F1>

<E0>05</E0>

<E1>30</E1>

</T4>

- <T5>

<F1>1</F1>

<E2>13</E2>

</T5>

- <T6>

<F1>1</F1>

<E0>07</E0>

<E1>00</E1>

</T6>

- <T7>

<F1>1</F1>

<E2>13</E2>

</T7>

- <T8>

<F1>1</F1>

<E0>16</E0>

<E1>00</E1>

</T8>

- <T9>

<F1>1</F1>

</T9>

</T2>

- <T16>

<F0>1</F0>

<F15>1</F15>

- <T17>

<F15>1</F15>

<F16>1</F16>

<E1>TEMPO</E1>

<E3>13</E3>

<E5>13</E5>

- <T18>

<F16>1</F16>

<E0>11</E0>

<E1>00</E1>

</T18>

- <T19>

<F16>1</F16>

<E0>16</E0>

<E1>00</E1>

</T19>

- <T20>

<F16>1</F16>

<F19>1</F19>

- <T21>

<F19>1</F19>

<F20>1</F20>

- <T22>

<F20>1</F20>

<E0>+SHRA</E0>

</T22>

</T21>

</T20>

</T17>

</T16>

- <T16>

<F0>1</F0>

<F15>2</F15>

- <T17>

<F15>2</F15>

<F16>2</F16>

<E0>30</E0>

<E1>TEMPO</E1>

<E3>13</E3>

<E5>13</E5>

- <T18>

<F16>2</F16>

<E0>14</E0>

<E1>00</E1>

</T18>

- <T19>

<F16>2</F16>

<E0>16</E0>

</T19>

- <T20>

<F16>2</F16>

<F19>2</F19>

- <T21>

<F19>2</F19>

<F20>2</F20>

- <T22>

<F20>2</F20>

<E0>TSRA</E0>

</T22>

</T21>

- <T23>

<F19>2</F19>

<F22>1</F22>

- <T24>

<F22>1</F22>

<E1>SCT</E1>

<E3>500</E3>

</T24>

</T23>

- <T23>

<F19>2</F19>

<F22>2</F22>

- <T24>

<F22>2</F22>

<E1>BKN</E1>

<E2>CB</E2>

<E3>1000</E3>

</T24>

</T23>

</T20>

</T17>

</T16>

- <T10>

<F0>1</F0>

<F9>1</F9>

<E1>310</E1>

<E4>15</E4>

<E13>8000</E13>

- <T11>

<F9>1</F9>

<F10>1</F10>

- <T12>

<F10>1</F10>

<E0>SHRA</E0>

</T12>

</T11>

- <T13>

<F9>1</F9>

<F12>1</F12>

- <T14>

<F12>1</F12>

<E1>FEW</E1>

<E4>500</E4>

</T14>

</T13>

- <T13>

<F9>1</F9>

<F12>2</F12>

- <T14>

<F12>2</F12>

<F13>2</F13>

<E1>FEW</E1>

<E2>CB</E2>

<E4>1000</E4>

</T14>

</T13>

- <T13>

<F9>1</F9>

<F12>3</F12>

- <T14>

<F12>3</F12>

<F13>3</F13>

<E1>SCT</E1>

<E4>1800</E4>

</T14>

</T13>

- <T13>

<F9>1</F9>

<F12>4</F12>

- <T14>

<F12>4</F12>

<F13>4</F13>

<E1>BKN</E1>

<E4>2500</E4>

</T14>

</T13>

</T10>

</T1>

</dataroot>

Annex 12

Database applications

Three Access applications are used by the Secretariat as follows:

Annex 13

Extracts from the ISO TC 211 multilingual glossary related to terms used in the document ET-ADRS-1/ Doc. 4.1(2)

| TERM-ID | TERM | Definition |
| --- | --- | --- |
| 14 | application | manipulation and processing of data in support of user requirements |
| 15 | application schema | conceptual schema for data required by one or more applications |
| 67 | conceptual formalism | set of modelling concepts used to describe a conceptual model |
| 68 | conceptual model | model that defines concepts of a universe of discourse |
| 69 | conceptual schema | formal description of a conceptual model |
| 70 | conceptual schema language | formal language based on a conceptual formalism for the purpose of representing conceptual schemas |
| 104 | data | reinterpretable representation of information in a formalised manner suitable for communication, interpretation, or processing |
| 110 | data product | dataset or dataset series that conforms to a data product specification |
| 107 | data interchange | delivery, receipt and interpretation of data |
| 111 | data product specification | detailed description of a dataset or dataset series together with additional information that will enable it to be created, supplied to and used by another party |
| 123 | data type | specification of a value domain with operations allowed on values in this domain |
| 124 | dataset | identifiable collection of data |
| 125 | dataset series | collection of datasets sharing the same product specification |
| 168 | feature | abstraction of real world phenomena |
| 169 | feature association | relationship that links instances of one feature type with instances of the same or a different feature type |
| 170 | feature attribute | characteristic of a feature |
| 854 | feature catalogue | catalogue containing definitions and descriptions of the feature types, feature attributes, and feature relationships occurring in one or more sets of geographic data, together with any feature operations that may be applied |
| 177 | feature operation | operation that every instance of a feature type may perform |
| 205 | geographic information | information concerning phenomena implicitly or explicitly associated with a location relative to the Earth |
| 255 | interoperability | capability to communicate, execute programs, or transfer data among various functional units in a manner that requires the user to have little or no knowledge of the unique characteristics of those units |
| 289 | metadata | data about data |
| 290 | metadata element | discrete unit of metadata |
| 291 | metadata entity | set of metadata elements describing the same aspect of data |
| 292 | metadata schema | conceptual schema describing metadata |
| 293 | metadata section | subset of metadata which consists of a collection of related metadata entities and metadata elements |
| 299 | model | abstraction of some aspects of reality |
| 355 | product specification | description of the universe of discourse and a specification for mapping the universe of discourse to a dataset |
| 371 | register | set of files containing identifiers assigned to items with descriptions of the associated items |
| 508 | register manager | organization to which management of a register has been delegated by the register owner |
| 372 | register owner | organization that establishes a register |
| 373 | registration | assignment of a permanent, unique, and unambiguous identifier to an item |
| 375 | registry | information system on which a register is maintained |
| 395 | schema | formal description of a model |
| 405 | service | distinct part of the functionality that is provided by an entity through interfaces |
| 408 | service metadata | metadata describing the operations and geographic information available at a server |
| 486 | universe of discourse | view of the real or hypothetical world that includes everything of interest |

# Footnotes

A short delayed replication is used to indicate that a sequence of elements is or is not included in a BUFR report; if there had been an interest in grouping the elements concerned by the short delayed replication, a new sequence in Table D should have been created in this respect. Since this is not the case, this means that there is no interest in grouping the element in a new table; for the elaboration of the model, there is therefore no need to create a table for a short delayed replication; the elements can be inserted directly in the current table. The

The contents of the column alias_2 of the tables in Annexes 4 and 8 are derived from the column description when available and were entered manually.

See http://www.wmo.int/pages/prog/www/WMOCodes/SampleTemplates/NEWMETARSPECITAFTEMPLATES.doc

# Text boxes

TemplatesList (fromTable D)

- FXY

- Name

Common Tables

- FXY

FlagCat (from Table B)

- FXY

- Name

- BitNo

- Description

CodesCat (from Table B)

- FXY

- Name

- CodeFigure

- Description_1

- Description_2

ElementsCat (fromTable B)

- FXY

- Name

- Unit

Figure 2 – Sequential reading of the catalogue of sequences and creation of the tables of the tree

SequencesCat (fromTable D)

- FXY

- Element (in the format FXY)

- Name

CommonTableC11

- DataCategory

- DataSubCategory

1

1..*

0..1

1

1

0..*

Data level

1..* m

Model level

1

1

0..1

Dataset encoded in DRS No.1

Encoding rules for DRS No. 1 (ISO 19118)

Dataset encoded in DRS No.2

Yes

No

Other schemas

Temporal schema

- Read the reference FXY in the field “reference” and take action as described in the second column of Table A

- Go to the next row to read as specified in the third column of Table 1

Row part of the sequences of the template

Spatial schema

End

Metadata schema

WMO Feature catalogue

Application schema

Implemented as

0..1

Described byas

Table 1

| FXY | Action | Next row to read (see 3) (See Note 1) |
| --- | --- | --- |
| 0XY | Add the element (see Note 2) as a field in the current table. In case of the end of a replication, add the element in the table directly associated to the replication | Next row |
| 1XY | Create a table linked to the current table | Current row + 2 |
|  | Exception: ignore a short delayed replication | Current row + 2 |
| 3XY | Create a table linked to the current table | First row with the field FXY = 3XY |

Note 1: if the next row belongs to another sequence than that of the associated current table, the next row should correspond to the next row of the table associated to the last previous sequence not yet completely read in the order of the possible nested sequences.

Note 2: the elements having “increments” in their name, the data repetition factors (031002 and 031012) and certain data description operators (2XY) have to be ignored and only those remaining significant elements are included in the structure of the tables.

- Create a table corresponding to the sequence number of the template.

- Start reading the catalogue of sequences at the first row with the field FXY = sequence number of the template

- Read FXY in the field “reference” and take action as described in the second column of Table A

- Go to the next row to read as specified in the third column of Table 1

Metadata

Figure 1 - Relationship between BUFR/CREX Tables

Dataset

Data product

Data product specification (ISO 19131)

Encoding rules for DRS No. 2

specifies

A data product is an instance of the model for a type of data product

SequencesCat (fromTable D)

- FXY

- Element (in the format FXY)

- Name

1

1

The model for a type of data product is an instance of the meta-model associated to a type of data product

1..*

1

1

Common Tables

- FXY

FlagsCat (from Table B)

- FXY

- Name

- BitNo

- Description

CodesCat (from Table B)

- FXY

- Name

- CodeFigure

- Description_1

- Description_2

ElementsCat (fromTable B)

- FXY

- Name

- Unit

1..*

0..1

1

1

Model level

Data product level

TreeTables

- TableNames

- Fields/Elements

- Unit

TableList

- Names

- Aliases

- Description

- ForeignKey

- Index

Meta-model level

A meta-model describing how to define the tables of the trees and their structure: names of the tables, fields (i.e. elements of BUFR Table B) and attributes of the fields (description and unit)

A meta-model defining the structure of a table of the tables of the trees: names of the tables (each associated to a sequence of BUFR Table D), aliases, descriptions of the tables, foreign keys and unique indexes for each table.

Figure 3 – Meta-model, model and data products

Dataset encoded in DRS No.1

Dataset encoded in DRS No.2

Decoding rules for DRS No. 1 (ISO 19118)

Decoding rules for DRS No. 2

Model documentation for METAR/SPECI :

- Table of tables of the tree

- Structure of each table of the tree

Instance of observations Catalogue of BUFR codes

Catalogue of BUFR flags

Instance of the METAR/SPECI model:

- Tree of tables

- XML representation (files *.xsd, *.xml)

(see example in Annex 7)

Application to create an instance of the METAR/SPECI model and export it into XML

- Application to create an  instance of the METAR/SPECI model and export it into XML forma

- Application to produce the model documentation (instance of the meta-model)

Methodology for creating models for data product specifications based on BUFR/CREX tables

Model documentation

- Table of tables of the tree (see examples in Annexes 4  and 8 for METAR/SPECI and TAF)

- Structure of each table of the tree (see examples in Annexes 5 and 9 for METAR/SPECI and TAF)

Model documentation for METAR/SPECI:

- Table of tables of the tree

- Structure of each table of the tree

Catalogue of BUFR sequences

Catalogue of BUFR elements

Instance of the METAR/SPECI model in the form of a tree of tables; aliases for the names of the trees and the fields can be used in order to facilitate the reading

Instance of the METAR/SPECI model presented in XML (files*.xsd, *.xml)

(see example in Annex 7)

Application to import METAR/SPECI instances presented in XML and to browse them

Application to produce the model documentation for a data product defined by a sequence

- Application to import METAR/SPECI instances presented in XML and to browse them