| WORLD METEOROLOGICAL ORGANIZATION ________ CBS INTER-PROGRAMME EXPERT TEAM ON METADATA IMPLEMENTATION FIRST MEETING (Beijing, China, 26 and 30 September 2005) |  | IPET-MI-I/Doc. 2(2) (19.IX.2005) ____ ITEM: 2 ENGLISH ONLY |
| --- | --- | --- |

###### Metadata Standards

###### for all Automatic Weather Station Installations

Submitted by Igor Zahumenský

(Representative of CIMO)

________________________________________________________________

Summary and Purpose of Document

The document contains a proposed standard set of metadata elements for all Automatic Weather Station Installations as an example of specific metadata from the aspect of WMO CBS and IMOP Programmes.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to consider metadata issue from the aspect of measured data and siting criteria to meet data users’ requirements and take it into account in the development of metadata standards.

References:

- Final Report, CIMO ET on Surface Technology and Measurement Techniques, First Session, Geneva, Switzerland, 13 – 16 October 2004, http://www.wmo.int/web/www/IMOP/reports/2003-2007/ET-STMT1_Geneva2004.pdf

- Guide to Meteorological Instruments and Methods of Observation, WMO-No. 8

- Manual on GOS, WMO-No. 544

- Guidelines on Climate Metadata and Homogenization, (WMO-TD No. 1186),  www.wmo.ch/web/wcp/wcdmp/html/WCDMP-53.pdf

- International Meteorological Vocabulary, WMO-No. 182

Metadata Standards for all Automatic Weather Station Installations

I. BACKGROUND

Metadata (data about data), as applied to measurement and observation, describe the location, instrument and method of observation, quality, and other characteristics of data. Metadata are important for data users, as they need to know the circumstances of the observations/ measurements and understand the origins of the meteorological values themselves. Metadata are especially important for the elements that are particularly sensitive to exposure, such as precipitation, wind and temperature.

Metadata can be considered as an extended version of the station administrative record, containing all possible information related to the station and instruments installed, type and time of changes that occurred during the history of an observing system. The expanded metadata information can include digital images, a wide range of instrument specifications, calibration and maintenance records, and many other pieces of information.

Metadata are dynamic. Station location, ground cover, instruments, observation/ measurement practices, processing algorithms, data formats etc. change over time. The system has to track all these changes. Therefore, metadata should be as complete as possible, as up to date as possible, and as readily available as possible. Basic metadata should be available together with the observational data.

A sound quality management system entails the availability of detailed information on the observing system itself and on all changes that occur during the time of its observation. Such information on data, known as metadata, enables the operator of an observing system to take the most appropriate preventive, corrective, and adaptive actions to maintain or to enhance data quality.

As computer data management systems gradually become an important component of the data delivery systems, it is desirable that metadata are available as a computer database enabling computerized composition, updating, and use. The metadata files have to be organized in such a way to be both easily maintained and accessible. The development of a metadata system requires considerable interdisciplinary organization, and its operation, particularly the scrupulous and accurately-dated record of changes in the metadata base, requires constant attention.

Metadata presented in a uniform format is an essential requirement for the interpretation of measured data and siting criteria and metadata standards should be developed for that purpose.

II. ELEMENTS OF A METADATA DATABASE RELATED TO AN AUTOMATIC WEATHER   STATION

The proposed standard set of metadata elements

A metadata database should provide detailed information necessary for users to gain adequate background knowledge about the station and observational data, together with updates due to changes that occur.

Major database elements include the following:

- Network information (beyond a scope of this document);

- Station information;

- Individual instrument information;

- Data processing information;

- Data handling information;

- Data transmission information.

#### 2.1 Station information

There is a great deal of information related to a station's location, local topography and others. Basic station metadata include:

| Type of metadata | Explanation | Examples |
| --- | --- | --- |
| Station name | Official name of the station | Prievidza |
| Station index number(s) | Number used by the National Meteorological Service to identify a station | 11867 |
| Purpose of the station | Application and main users of data | synoptic |
| Geographical co-ordinates | Latitude and longitude of the station reference point | 18.7697 18.5939 |
| Elevation above mean sea level | Vertical distance of a reference point of the station measured from mean sea level | 260.25 m |
| Types of soil, physical constants and profile of soil | Description of soil type below the station, its characteristics | clay |
| Types of vegetation and condition, date of entry | Description of the station’s environment land | natural; grass, 7 Dec 2004 |
| Local topography description | Description of the station’s surroundings, with emphasis on topographic features that may influence the weather at the station (major terrain features) | valley station |
| Type of AWS, manufacturer, model, serial number, software version, and module detail where applicable (model, serial number, software version) | Basic information on the AWS installed | AWS: Model Vaisala MILOS 500 Hardware v1.2, Operating system v1.2.3, Application program v1.0.2. Modem: Model ABCD, Hardware v2.3, Software v3.4.5. Power supply: Model XYZ, Hardware v4.5. |
| Observing programme of the station: | Information on types of observation made, variables measured | 1-hour synoptic obs. |
| parameters measured | List of variables measured | T, P, U, DF, … |
| reference time | Reference time of observations | UTC |
| Message codes and reporting times (offset and interval). | Actual time of observations | METAR: Start 00:00 UTC, interval 1 hour. SYNOP: Start 01:00 UTC, interval 3 hours. Other: Start 00:00, interval 1 minute. |
| The datum level to which atmospheric pressure data of the station refer | MSL or geopotential of the datum levels to which the atmospheric pressure is reduced | MSL; 925 hPa; 850 hPa; |

2.2 Individual instrument information

Relevant metadata should be:

| Type of metadata | Explanation | Examples |
| --- | --- | --- |
| Variable / parameter | Variables / Parameters measured at AWS | Temperature, relative humidity |
| Sensor type: | Technical information on the sensor used for the measurement of the variable | Temperature; humidity; pressure … |
| manufacturer |  | Vaisala, Campbell, … |
| model |  | HMP45C, PTU-2000 |
| serial number |  | 12345… |
| hardware version |  | v1.2.3 |
| software version |  | v2.3.4 |
| Principle of operation: | Description of method or system used |  |
| method of measurement / observation | Type of operation principle describing method of measurement/observation used | constant current principle, polymer capacitance |
| type of detection system | Complete set of measuring instruments and other equipment assembled to carry out specified measurements | optical scatter system combined with precipitation occurrence sensing system |
| Performance characteristics | Operating range of sensors | -50 - +60 ºC, 0 - 100 % |
| Unit of measurement | SI unit in which the variable is measured | K, Pa, m s-1 |
| Measuring range | Interval between upper and lower value limits for which a variable is reported | -50 - +60 ºC, 0 – 75 m s-1 |
| Resolution | The smallest change in a physical variable which will cause a variation in the response of a measurement system. | 0.01 K, |
| Uncertainty | Variable associated with the result of a measurement that characterizes the dispersion of the values that could be reasonably attributed to the measurand; the interval in which the “the value” of the variable at the time of measurement is expected to lie. | ±0.1 K |
| Instrument time constant | Time required for an instrument to indicate a given percentage (63.2 %) of the final reading resulting from an input signal | 20 s; |
| Interface time constant | Time required for the interface electronics to indicate a given percentage (63.2 %) of the final reading resulting from an input signal | 5 s; |
| Time resolution | Frequency of sampling | 3 s, 10 s |
| Output averaging time | Time period used for the purpose of determining of reported value | 1 min.; 2 min; 10min. |
| Siting and exposure: |  |  |
| free-standing | influence of surroundings | yes / no |
| distance from main obstacle(s) | how far is it from main obstacle(s) with main influence on it | 10 m |
| degree of interference from other instruments or object | (influence of masts, ventilators, sensors …) | yes / no |
| surrounding terrain roughness | Terrain classification from Davenport (to the north, east, south, west) | N: class 1; E: class 2 |
| location |  | screen, mast, tower |
| shielding |  | screen, naturally aspirated |
| shielding time constant | Time required for the instrument exposure method (solar radiation screen, or vent etc.) to indicate a given percentage (63.2 %) of the final reading resulting from an input signal | 10 s; |
| height above ground (or level of depth) |  | 1.75 m, -0.1 m |
| height above building (roof) |  | 1.25 m |
| Data acquisition: |  |  |
| sampling interval | Time between successive observations | 3 s, 10s, 30s |
| averaging interval | Time interval from which samples are used | 1, 2, 10, 30 minutes |
| type of averaging | Method used for the calculation of the average | arithmetic; exponential; harmonic |
| Correction procedures | Corrections applied to the data | for temperature, for gravity, for wind speed |
| Calibration data |  |  |
| correction | Value to be added to or subtracted from the reading of an instrument to obtain the correct value | C = R (1+0.6R) |
| time of calibration | Date when the last calibration was made | 12 Dec 2003 |
| Preventive and corrective maintenance: |  |  |
| recommended / scheduled maintenance | Frequency of preventive maintenance | one per 3 months |
| calibration procedures | Type of method/procedure used | static/dynamic calibration |
| calibration frequency | Recommended frequency | 12 months |
| procedure description |  |  |
| Results of comparison with traveling standard | Result of the field tests of the sensor immediately after installation | 98% |
| Results of comparison with traveling standard | Result of the field tests of the sensor immediately prior to removal | 103% |

# 2.3 Data processing information

For each individual meteorological parameter, metadata related to processing procedures should include:

| Type of metadata | Explanation | Example |
| --- | --- | --- |
| Measuring / observing programme: |  |  |
| time of observation |  | 10th, …,60th min. |
| reporting frequency |  | 10 min. |
| data output | Quantity that is delivered by an instrument or system | 2-min. average value |
| processing interval | Time interval from which the samples are taken | 2, 10 min. (wind) |
| reported resolution | Resolution of variable reported | 0.1 ms-1 |
| Data-processing method, procedure, algorithm | Method used | running 10-min. average |
| Formula to calculate the element |  | VIS=N/(1/V1+1/V2+ … +1/Vn) |
| Mode of observation / measurement | Type of data being reported | instantaneous, total, mean value, variability, |
| Input source (instrument, element, etc.) | Measured or derived variable | WAA 151 |
| Constants and parameter values | Constants, parameters used in computation of derived parameter | g=9.806 65ms-2 |

### 2.4 Data handling information

Metadata elements of interest include:

| Type of metadata | Explanation | Example |
| --- | --- | --- |
| Quality control procedures, algorithms | Type of QC procedures | plausible value check; time consistency check, internal consistency check |
| QC flags definition | Description of QC flags | 1 good, 2 inconsistent, 3 doubtful 4 erroneous, 5 not checked, 6 changed |
| Processing and storage procedures | Different procedures used in the process of data reduction and data conversion | computation of visibility from extinction coefficient |
| Constants and parameter values |  |  |

#### 2.5 Data transmission information

The transmission-related metadata of interest are:

| Type of metadata | Explanation | Example |
| --- | --- | --- |
| Method of transmission | Means of transmission | GSM/GPRS, OrbComm; radio |
| Data format | Type of message used for data transmission | BUFR; SYNOP |
| Transmission time | Time of regular transmission of data | 11th minute; 60th minute |
| Transmission frequency | Frequency of data transmission | 10 minute; 1 hour |

#### 2.6 Data update information

The update-related metadata of interest are:

| Type of metadata | Explanation | Example |
| --- | --- | --- |
| Time of the last update |  | 13 January 2005 |
| Version of the tables |  | XYZ |
| Person responsible for update |  | John Smith |

III. RESPONSIBILITIES

  - Maintenance of metadata

Meteorological data producers should take responsibility for maintenance of up-to-date metadata files.

  - Exchange of metadata

Metadata should be disseminated jointly with the AWS data. BUFR templates for AWS data after an appropriate adjustment would be the suitable tools for this purpose.

  - Publication of guidelines

Guidelines for maintenance of accurate metadata for all automatic weather station installations should be published in Manual on GOS, WMO-No. 544 and Guide to Meteorological Instruments and Methods of Observation, WMO-No. 8 to ensure complete and correct information about data.