## Slide 1
RA II WIGOS Workshop
6-8 November 2018, Beijing, China
Japan
Submitted by
Yoshihiko TAHARA

## Slide 2: Outline
Introduction of Japan and JMA
National requirements for observations
Summary of national observing capabilities
Status of national implementation of WIGOS

## Slide 3: Introduction of Japan
Population: ~126,000,000
Physical context: 378,000 km2
  Four main islands, more than 6,000 small islands
  About three-fourths of Japan is covered by mountains
  111 active volcanoes
Climate:
  Four distinct seasons with a climate ranging from subarctic in the north to subtropical in the south.
  The rainy season “Baiu” in Early summer
  Tropical cyclones “Typhoon” approaching Japan from Aug. to Oct
  Heavy snow on the Sea of Japan side in winter

## Slide 4: Intro. of JMA
Staff: ~5000
Mascot “Harerun”

## Slide 5: National Requirements for Observations
Prevention and mitigation
of natural disasters
International cooperation
Development and prosperity of industry
Safety of transportation
In compliance with “the Meteorological Service Act”, JMA implements its services with the following ultimate goals (Article 1).
Provide daily/monthly forecasts and warnings/Advisories for
- Preparation for disasters
- Evacuation
- Risk management
Provide weather forecasts and climatological data to
- Energy companies
- Agriculture
- Other industries
Provide meteorological information to
- Pilot and airline companies
- Road administrators
- Train companies
Article 3 The Director-General of JMA shall, … , endeavor to carry out the following:
Establishing and maintaining observation networks concerning meteorological phenomena, earthquakes, and volcanic phenomena;
Article 4 JMA shall, when performing observations of meteorological phenomena, …, and hydrological phenomena, do so in compliance with the methods specified by Ordinance of the Ministry of Land, Infrastructure, Transport and Tourism.
- International data exchange
- Technical support
- Sharing disaster information
- Collaboration to develop technics

## Slide 6: National Requirements for Observations
Diversity of Disasters in Japan
Japan is exposed to the risk of various disasters.
Even recently, there are still many disasters that cause serious damages.
The possibility of increase in frequency and intensity of extreme precipitation is indicated in mid-latitudes because of global warming.
Multi-hazard
in Japan
Heavy Rain
Flood
Lightning
Tornado
Typhoon
Landslide
Heavy Snow
Earthquake
Tsunami
Volcano
Storm Surge
High Wave

## Slide 7: Summary of National Observing Capabilities
Observation for Civil Aviation
Weather Radar Observation
Surface Observation
at Observatories and Automated Weather Stations
Upper-air Observation
using Radiosondes and Wind Profilers
Geostationary Satellite Observation
Weather Observation Systems of JMA

## Slide 8
Nationwide Rain-gauge Network
□ Approx. 1,300 JMA
□ Approx. 3,500 MLIT (Ministry of Land, Infrastructure, Transport and Tourism)
□ Approx. 5,800 Local Government
400 km
JMA actively exchanges observational data with relevant central governmental and local authorities on a real-time basis.
Notes: JMA collect rain gauge data from Government, and local government.
MLIT is one of the Ministries of government. The initial of Ministry of Land , Infrastructure, Transport and Tourism.
MLIT has about 3500 rain gauge station.
Local Governments have about 5800 rain gauge stations totally.

## Slide 9: Summary of National Observing Capabilities
Yomiuri Shimbun Newspaper (9 September 2010)
Date
The daily highest temperature
Difference from regional average
Ave. 0.32
Ave. 1.68
Gradient: Large
Breakpoint
Gradient: Small
Before
After
rain-gauge examination
Total rainfall at reference station
Total rainfall at examined station
Ivied thermometer
Rain-gauges covered with weed

## Slide 10: Summary of National Observing Capabilities
Trouble shooting !
DATA
AWS（Instruments）
Center Systems（Servers）
AQC
HQC
USERS
OPERATORS
Basic AQC
Advanced AQC
DATA
QC information
OPERATION
QC information
(House Keeping information)

## Slide 11: Summary of National Observing Capabilities
JMA Headquarter
Regional Headquarters
Local Meteorological Offices (LMO)
Project overall strategy
Develop and improve AQC/HQC system
Give guidance to Regional Headquarters
Partner organizations
HK (House Keeping) information: operational status of instrument
Evaluate results of AQC/HQC by LMOs
Give guidance to LMOs
Organizational frameworks of Quality Control (QC) in JMA
Give guidance to partner organizations
Conduct HQC
Trouble-shoot based on AQC, HQC and HK results
Conduct periodical maintenance
Maintain observation environment

## Slide 12: Status of National Implementation of WIGOS
Regular maintenance at manned meteorological observatory
Interval | Check Items for manned station
Daily | checking data quality inspecting the condition of observation fields and instruments
Weekly | checking hardware clocks cleaning the glass shield of pyranometer
Monthly | checking silica gel (desiccant) of pyranometer
Three months | cleaning sensors and the covers of instruments checking DC power supplies checking silica gel (desiccant) of sunshine recorder
Six months | changing precipitation gauge, changing the filters of humidity sensors checking snow cover meter, checking inverter batteries
Annual | calibration for barometers and visibility sensors changing the sensors of wind vane and propeller anemometers checking for cables and anti-icing system
Five years | changing the motors and the rubber packings of shelter changing the lightning arresters changing the batteries

## Slide 13: Status of National Implementation of WIGOS
Management of observation metadata
OSCAR/Surface
GAWSIS
WMO Radar Database
Weather Radars
Radiosondes
Wind Profilers
Meteorological
Satellites
OSCAR/Space
Observatories &
Special AWSs
GAW Stations
WMO
JMA
Marine Observation
JCOMMOPS

## Slide 14
Thank you
y-tahara@met.kishou.go.jp

## Slide 15: Summary of National Observing Capabilities
■ Observatories, Special AWS 156
〇 rainfall, temperature, wind, sunshine 686
〇 rainfall, temperature, wind 87
〇 rainfall 371
＋ snowfall 323
average interval (rain gauges): 17 km
TCP/IP
AMeDAS Center System
Main System
(System Op. Center, Kiyose)
Backup System
(Osaka)
About 1300
rain gauges
Automated Weather Station
Observatory
Each observatory and station link AMeDAS center system on TCP/IP network.
Data is collected on real-time, and quality controlled.
AMeDAS Center System
(System Op. Center, Kiyose)
Backup System
(Osaka)
0
300km
100
Rain gauges monitored by JMA:
Approx. 1,300 JMA
Approx. 3,500 MLIT (Ministry of Land, Infrastructure, Transport and Tourism)
Approx. 5,800 Local Governments
Automated Weather Station “AMeDAS” AMeDAS (Automated Meteorological Data Acquisition System)

## Slide 16: Summary of national observing capabilities
Precipitation and Wind
Observation
Every 5 min.
Operation Center
(HQ, Tokyo)
Backup System
(Osaka)
Radar Coverage
Doppler Radars (20)
Kushiro
Sapporo
Hakodate
Nagano
Fukui
Matsue
Akita
Hiroshima
Fukuoka
Okinawa
Ishigakijima
Naze
Tanegashima
Murotomisaki
Osaka
Nagoya
Shizuoka
Tokyo
Niigata
Sendai
Tokyo Radar
Domestic Core Network
(TCP/IP)
C-band Radars
● JMA C-Band: 20
△ MLIT C-Band: 26
C-band Radar echo data (JMA, MLIT) are collected to the center system and integrated into a nationwide echo intensity composite map ( every 5 minutes )
Weather Radar Network

## Slide 17: Summary of national observing capabilities
■Wakamatsu
■Sendai
L-band Wind Profiler Radar Every 10 min.
Automatic Balloon Launcher (8)
■ Radiosonde Station 16
Temperature, Humidity, Wind, Pressure observation twice a day.
Average interval: 350 km
Half of them are ABL (Automatic Balloon Launcher) stations
■ Wind Profiler 33
Automated upper-level wind observation every 10 min.
Average interval: 110 km
Matsue
Kushiro
■
Radiosonde
0
300km
100
Upper-air Observation Network

## Slide 18
Temperature
Wind
Sunshine duration
Precipitation
Real-time Data Browse via JMA Website
Tokyo
(JMA Website)
http://www.jma.go.jp/en/amedas
0
20
40
60
80
100km

## Slide 19
Weather Radar Observation
Niigata
Hakodate
Kushiro
Matsue
Fukui
Sapporo
Hiroshima
Fukuoka
Naze
Sendai
Akita
Ishigakijima
Osaka
Nagoya
Nagano
Tanegashima
Murotomisaki
Shizuoka
Okinawa
Tokyo

## Slide 20: Nationwide Radar Composite Maps
for Monitoring / Nowcasting
Quantitative Precipitation
Estimation / Forecast (QPE/QPF) etc.
MLIT: Ministry of Land, Infrastructure, Transport and Tourism
C-band Radars
● JMA C-Band: 20
△ MLIT C-Band: 26
C-band Radar echo data (JMA, MLIT) are collected to the center system and integrated into a nationwide echo intensity composite map ( every 5 minutes )

## Slide 21
High Resolution Precipitation Nowcasts
short-range precipitation intensity predictions with a spatial resolution of 250 m
derived from weather radar data and other types of meteorological information
Rain gauges:
Approx. 1,300 JMA
Approx. 3,500 MLIT (Ministry of Land, Infrastructure, Transport and Tourism)
Approx. 5,800 Local Governments
(JMA Web page)
http://www.jma.go.jp/en/highresorad/
Provision of effective information for disaster prevention
JMA radars replaced with units featuring a 250-m radial resolution (offering twice as much detail as before) until 2014 for improved observation of local downpours
Involves the use of data such as rain gauges, wind profilers, radiosondes and MLIT-XRAIN radars
Forecasts of precipitation intensity distribution with a spatial resolution of 250 m covering the period up to 30 minutes ahead
Rain gauges
High Resolution Precipitation Nowcasts
MLIT: Ministry of Land, Infrastructure, Transport and Tourism
20 JMA Radars (C-band)
38 MLIT-XRAIN Radars (X-band)

## Slide 22
Approaching winds
Receding winds
tornadoes
Potentially tornado-generating vortex
(meso-cyclones)
Doppler Weather Radar
Provision of effective information on the risk of tornado outbreaks
Detection of the potential outbreak area of tornadoes/gusts using radar observation data and numerical prediction results
Radial-wind component
2013/09/02 14:20JST Tokyo-radar
Detection of meso-cyclones
A strongly-localized pair of
receding winds (warm color) and approaching winds (cold color)
Echo intensity
2013/09/02 14:20JST Tokyo-radar
Detection of “meso-cyclones” using Doppler Radars
(JMA Web page)
http://www.jma.go.jp/en/highresorad/
“Hook”-shaped echo

## Slide 23
ABL (Automatic Balloon Launcher)
JMA’s Radiosonde Stations
Kushiro
Matsue
Sapporo
Fukuoka
Naze
Ishigakijima
Akita
Wakkanai
Kagoshima
Shionomisaki
Wajima
Hachijojima
Minamidaitojima
Chichijima
Minamitorishima
Aerological
Observatory
MBL (Manned Balloon Launching)
MBL (Manned Balloon Launching)

## Slide 24: Observation by Radar Wind Profilers
Antenna
L-band(1.3GHz) Transceiver
Antenna with snow dome
Operation Center
(JMA Headquarters)
Upper Air Wind
Scattered Electric Wave
Doppler shifted
Radiated Electric Wave
Radiated Electric wave is scattered by turbulent density of atmosphere.
Air Flow
1.3 GHz Electric wave (5 beams) radiated from Radar Wind Profiler is scattered by turbulent density of atmosphere.
Air flow (velocity) is calculated from Doppler shifted reflective wave.
Kumagaya (36.15N, 139.38E) alt.30m
Local Time
Altitude (km)
N
E
S
W
Vertical velocity
(upward)
(downward)

## Slide 25: WINDAS (Wind Profiler Network and Data Acquisition System)
Rumoi
Obihiro
Muroran
Miyako
Sakata
Kumagaya
Mito
Katsuura
Takada
Kawaguchiko
Shizuoka
Nagoya
Owase
Fukui
Hamada
Takamatsu
Kouchi
Shimizu
Kumamoto
Ohita
Nobeoka
Izuhara
Hirado
Yakushima
Yonagunijima
Hachijojima
Ichiki
Tottori
Mihama
Minamidaitojima
Naze
Operation Center
Sendai
Wakamatsu

## Slide 26
Observation by JMA : 81 Airports
Observation by JSDF/USFJ: 8 Airports
Weather Observation for Civil Aviation
Wind, Temp, Humidity Pressure, Ceiling, RVR, MOR, Rain Intensity etc. are reported as METAR/SPECI and 6sec. real-time data
JMA provides users
(Airlines, ATC, ATM etc)
with observation data
from 89 airports
on the Internet.
This Map is issued by Japan Civil Aviation Bureau.
Observation by
Person and Instruments

## Slide 27
Yonaguni
Miyako
Kumejima
Naha
Minamidaitou
Amami
Tanegashima
Kagoshima
Miyazaki
Iki
Fukuoka
Yamaguchi-Ube
Tottori
Toyama
Niigata
Akita
Aomori
Okushiri
Wakkanai
Memanbetsu
Kushiro
Shin-Chitose
Hanamaki
Fukushima
Narita
Oshima
Tokyo Haneda
Cyubu
Matsumoto
Kansai
Osaka
Kouchi
Nanki Shirahama
Takamatsu
DRAW: Doppler Radar for Airport Weather (TDWR)
LIDAR: Light Detection and Ranging
LIDEN: Lightning Detection Network System
Main Center (Kiyose, Tokyo)
Kiyose
C-band Transceiver
For Wind and Precipitation
VHF, LF Reciever
For Lightning
Near Infrared Transceiver
For Wind
DRAW+LIDAR 3
DRAW only 6
LIDEN 30
Data Centers
Oshima
Aviation Weather Observation Integrated Processing System
(DRAW, LIDAR & LIDEN)
Backup Center (Osaka)
Monitoring Center (H.Q., Tokyo)
Notes: Finally, let me talk about aviation weather observation integrated processing system.
The system consists of Doppler radars for aviation weather, Doppler lidars, and a lightning detection network.
3 major airports in Japan are equipped with a Doppler radar and a lidar.
Other 6 important airports are equipped with a Doppler radar.
Lightning detection stations are located at 30 airports.
(office)
All these observation stations are controlled from here.
(LIDARの説明）
LIDAR is basically the same as normal weather radars.
But the wavelength is different.
Normal radars use the approximately 5 cm wavelength, while lidars use the approximately 2 μm.
It means that the target is different.
Rader’s taget is water particle, while lidar’s target is aerosol such as dust in the air.
We use the radar when it’s rainy, and we use the lidar when it‘s sunny.

## Slide 28
Wind Shear Observation in All Weather Conditions
JMA provides low-level wind shear
and microburst alerts
in all weather conditions.
Normal Landing Path
ATC Tower
Active Convection
Cloud
Microburst
If the airplane could not avoid the microburst,
it would be smashed into the ground
due to the sudden decrease of lifting power.
DRAW: Doppler Radar for Airport Weather (a Japanese version of a TDWR)
DRAW (TDWR) detects low-level wind shears
in Rainy condition.
Shear Line
convergence
Microburst
divergence
LIDAR: Light Detection and Ranging
Doppler LIDAR detects
low-level wind shears
in Sunny or Cloudy condition.
All Weather
Observation
Cancel Landing
Crash
Pilots receive Low-level Wind Shear Alerts
from ATC
and cancel Landing
0837 34LA MBA 39kt- 1nm FNL
0837 34LA SLA 25kt+ 3nm FNL
Notes: A Doppler radar for aviation weather can detect microbursts and sheer lines.
When it detects such phenomena in arrival or departure areas, it automatically issues an alert message.
The message appears on the display of the air traffic controllers, who immediately the message to the pilots.
A Doppler lidar can detect low-level wind sheer in non-precipitating conditions, while a radar is useful in precipitating area.