| World Meteorological Organization |  | ICG-WIGOS/TT-WMD-1/Doc.7 |
| --- | --- | --- |
| INTER-COMMISSION COORDINATION GROUP ON WIGOS (ICG-WIGOS) TASK TEAM ON WIGOS MATADATA (TT-WMD) FIRST SESSION |  | Submitted by: | WMO Secretariat |
|  |  | Date: | 27.II.2013 |
| GENEVA, SWITZERLAND 11 – 15 MARCH 2013 |  | Original Language: | English |
|  |  | Agenda Item: | 7 |

CIMO Observational Metadata Specification

(B. Howe, Canada; M. Otsuka, Japan)

Summary and purpose of document This document provides information on CIMO’s development work on a catalogue of metadata for stations, instruments and methods of observation.

Action proposed

The Meeting is invited to agree on a level of details of WIGOS metadata to be collected, and draft a general specification for WIGOS core observational metadata; it will also consider and propose a model for the treatment of additional observational metadata - that required by one programme or another, but not by all - for submission to ICG-WIGOS.

Appendices:	 I	Draft Metadata Catalogue

References: 	1. WMO 2008: Final Report, CIMO expert team on surface technology and measurement techniques, second session, Geneva, Switzerland, 22-26 September 2008

2.  WMO 2010: AWS metadata catalogue, CBS expert team on requirements and implementation AWS platforms, sixth session, Geneva, Switzerland, 22-25 June 2010.

Draft Metadata Standard Related to Observing Stations, Instruments, and Observing Technologies

Objectives

- The assigned task is to continue development of metadata catalogue (for sensors, observing technologies and stations) using terminology used in CIMO Guide and the Guide to GOS (ref. CIMO-ET work plans 2011-2014).

- The metadata catalogue had been discussed in the previous expert team on surface technology and measurement technique (ET-ST&MT) before CIMO-XV 2010 (WMO 2008). While standardization on metadata has been addressed by different groups such as WIS, CBS ET-AWS, or more broadly by the WIGOS Task Team on Metadata, CIMO A1 ET on Standardization should focus on the metadata in the aspects of instruments and observing methods.

- According to the WIGOS framework Implementation Plan (WIP ver.1.0), the information on surface-based networks and instrumentation details currently recorded in Volume A will be available in the WIGOS Operational Database and to be accessible via the WIGOS Portal together with additional metadata. It is desirable that those elements of metadata that will be stored in the Database should agree with metadata standard that will be set in the future.

Review existing material

- The standard and recommended sets of metadata for AWS stated in the Manual on GOS and the Guide to GOS (Table 1) seem to be suitable for a starting point of the task of drafting metadata standard. They can also be expanded to manned stations, since observations for major meteorological parameters are made automatically and the observing data are transmitted to the data center in real-time regardless of manned or unmanned stations. In these GOS materials, the metadata are listed according to the major elements such as station information, individual instrument information, data-processing information, data handling information, and data transmission information. From the view point of CIMO, the first two elements including the metadata related to instruments, observing methods, siting and exposure should be focused.

- Reviewing the previous work done by ET-ST&MT (WMO 2008), it was recommended to prepare a list of observing techniques and fill in the tables of Appendix III in Guide to GOS by using the terminologies appeared in CIMO Guide or the catalogues developed by CBS ET- AWS (WMO 2010). Thus, the first draft metadata catalogue (Appendix I) was developed by supplementing the necessary items to these tables by referring to them. Information about observing techniques and types of instruments for each parameter was extracted mostly from the text of CIMO Guide. However, the information was not enough to appropriately categorize the observing techniques and the type of instruments and include all the necessary information regarding both new and old types of instruments. When it comes to the metadata for climate users, information about old analogue type of instruments and their observing methods makes a critical part of station histories.

- In addition to the metadata of observing techniques, information about siting and exposure of instruments are important as they can have a great impact on data quality. CIMO Guide and the Guidelines on climate metadata and homogenization (WMO/TD No. 1186) give thorough instructions about what kind of metadata should be collected to record local environment of station in topographical or micro scale, horizon obstructions and the enclosure of sensors (Table 1). Thus the tables in the Guide to GOS were supplemented with those metadata elements, based on experience in the JMA operational surface observing network as well.

Draft Metadata Catalogue

(Assessment of Table 1.2 - Table 2.2 of Appendix III in the Guide to GOS, WMO-No. 488)

- The first draft (shown in Appendix 1) was developed to add a list of observing methods and instruments for each meteorological parameter and metadata elements related to local environment around station, siting and exposure of instruments to the tables of Appendix III in the Guide to GOS. The draft list of observing methods and instruments is still incomplete and needs examination by the experts in instrument to be finalized.

Table 1: Existing materials related to metadata

| Material | Description for metadata |
| --- | --- |
| Manual on the Global Observing System. WMO-No. 544. | Standard set of metadata elements for automatic weather station installations. Attachment III.1 |
|  | 2.8.4 (a) – (h). (Metadata for climatological stations) |
|  | 2.11.3 (a) – (i). (Metadata for agricultural meteorological stations) |
| Guide to the Global Observing System. WMO-No. 488. | Automatic weather station metadata. Appendix III.3 |
| Guide to Meteorological instruments and methods of observation. WMO-No. 8 | 1.1.3 Metadata. General, Chapter1 in Part I |
|  | Siting classifications for surface observing stations on land. Annex 1 B, Chapter 1 in Part I |
|  | Station exposure description. Annex 1.C, Chapter 1 in Part I |
|  | 1.9.2 Elements of a metadata database. Chapter 1 in Part III |
| Guidelines on climate metadata and homogenization. WCDMP No. 53, WMO/TD No. 1186. | 2. Metadata |
| The work done by ET-ST&MT (WMO 2008) and CBS ET-AWS(WMO 2010) | - |

Future work

- There are such a wide range of metadata elements that can possibly affect data quality that they need to be prioritized in order to be exchanged internationally in operation as standard metadata.

- The list of observing methods and type of instruments in the draft metadata catalogue still needs improvement to cover a wide range of observing practices both in the present and the past. It might be helpful both to NMSs and users if a database of widely used commercialized instruments is available, whereby the specifications of the instruments are retrieved by putting the name of the manufacture and the model of the instruments.

- The metadata elements listed in the draft catalogue or the tables in the Guide to GOS are basically the expansion of administrative record originally collected for the convenience of operational observation practices at NMSs. Such information may have been scattered over different offices of different responsibilities in the operations over the years. In addition, the past metadata sometimes have not been kept in good order nor fully digitized. How to archive and deliver them to users are left to the efforts of each NMS. Some examples of practices such as how to establish a metadata database or how to prioritize the elements among all of the recommended sets of metadata according to user’s needs would be helpful to guide NMS in storing and delivering the metadata effectively or restoring their station histories.

- There has been very little common knowledge about how to evaluate the effects on data quality even if users have all the metadata in hand. There should be more communication between observers and users in understanding and interpreting the metadata data as a key indicator to data quality so that any necessary information is not neglected and properly recorded.

_________________

APPENDIX I:

Draft Metadata Catalogue (Assessment of Table 1.2, Table 2.1 and Table 2.2, Appendix III in the Guide to GOS)

1. Assessment of “Table 1.2 Individual Instrument Information (required for operational purposes)”

1.1 Type of metadata

| Parameters measured | Proposed |
| --- | --- |
| Principle of operation |  |
| Siting and exposure |  |

1.1.1 Parameters measured (proposed)

| Parameters | Variables measured |
| --- | --- |
| Temperature | Maximum temperature |
|  | Minimum temperature |
|  | (Ordinary) temperature |
|  | Soil temperature |
| Atmospheric Pressure | Pressure |
|  | Pressure tendency |
| Humidity | Mixing ratio |
|  | Dewpoint temperature |
|  | Specific humidity |
|  | Relative humidity |
|  | Vapor pressure |
|  | Saturation vapor pressure |
| Wind | Averaged wind speed/direction |
|  | Peak Gust |
| Precipitation | Amount |
|  | Duration |
|  | Intensity |
|  | Type |
|  | Snowfall |
|  | Snow depth |
| Radiation | Direct solar radiation |
|  | Global (solar) radiation |
|  | Diffuse sky (solar) radiation |
|  | Reflected solar radiation |
|  | Upward long-wave radiation (downward-looking) |
|  | Downward long-wave radiation (upward-looking) |
|  | Total radiation |
| Sunshine duration | - |
| Present/past weather | - |
| Evaporation | - |
| Soil moisture | - |
| Visibility | - |
| Clouds | Amount |
|  | Height of cloud base |
|  | Type of cloud |

1.1.2 Principle of operation

| Method of measurement/observation |  |
| --- | --- |
| Type of instrument | Proposed |
| Configuration | Proposed |
| Type of detection system |  |

1.1.2.1. Principle of operation for each parameter (proposed)

1.1.2.1.1. Temperature

| Method of measurement/observation | Type of instrument |
| --- | --- |
| Liquid-in-glass thermometers | Mercury-in-glass thermometers |
|  | Ethyl alcohol-in-glass thermometers |
|  | Others |
| Mechanical thermographs | Bimetallic thermograph |
|  | Bourdon-tube thermograph |
|  | Others |
| Electrical thermometers | Electrical resistance thermometers | Pure platinum |
|  |  | Platinum alloys |
|  |  | Nickel |
|  |  | Tungsten |
|  |  | Others |
|  | Semiconductor thermometers | Disc thermistor |
|  |  | Rod thermistor |
|  |  | Spherical thermistor |
|  |  | Others |
|  | Thermo couples |
|  | Others |
| Others | - |

Configuration

| Radiation shield or screen | Yes/no |
| --- | --- |
| Type of shield or screen |  |
| Size of shield or screen |  |
| Artificially ventilated | Yes/no |
| Degree of ventilation | [s] |

1.1.2.1.2 Atmospheric pressure

| Method of measurement/observation | Type of instrument |
| --- | --- |
| Barometers | Mercury barometers |
|  | Aneroid barometers |
|  | Bourdon-tube barometers |
|  | Others |
| Electronic barometers | Aneroid displacement transducers |
|  | Digital piezoresistive barometers |
|  | Cylindrical resonator barometers |
|  | Others |
| Bareographs | Aneroid bareographs |
|  | Others |
| Others | - |

Configuration

| Installed indoors or sheltered | Yes/no |
| --- | --- |
| Venting device | Yes/no |

1.1.2.1.3 Humidity

| Method of measurement/observation | Type of instrument |
| --- | --- |
| Psychrometers | Assmann aspirated psychrometers |
|  | Screen psychrometers |
|  | Sling/whirling psycrometers |
|  | Others |
| Hygrometers | Hair hygrometers |
|  | Chilled-mirror dewpoint hygrometers |
|  | Lithium chloride heated condensation hygrometers (dew cells) |
|  | Others |
| Electrical hygrometers | Electrical resistance hygrometers |
|  | Electrical capacitance hygrometers |
|  | Electromagnetic radiation absorption hygrometers |
|  | Others |
| Others | - |

Configuration

| Radiation shield or screen | Yes/no |
| --- | --- |
| Type of shield or screen |  |
| Size of shield or screen |  |
| Artificially ventilated | Yes/no |
| Degree of ventilation | [s] |

1.1.2.1.4 Surface wind

| Method of measurement/observation | Type of instrument |
| --- | --- |
| Rotating anemometers | Cup anemometers |
|  | Propeller anemometers |
|  | Others |
| Wind-direction vanes | Wind vanes |
|  | Others |
| Other anemometers | Pitot tube anemometers |
|  | Sonic/ultrasonic anemometers |
|  | Hot-disc anemometers |
|  | Hot-wire anemometers |
|  | Others |
| Estimation (without instrument) | Beaufort scale number |
|  | Others |
| Others | - |

Configuration

| The height of mast or tower | [m] |
| --- | --- |
| Heating device (to prevent icing) | Yes/no |

1.1.2.1.5 Precipitation

| Method of measurement/observation | Type of instrument |
| --- | --- |
| Rain gauge | Ordinary gauges |
|  | Weighing gauges |
|  | Tipping-bucket gauges |
|  | Siphoning gauges |
|  | Float gauges |
|  | Others |
| Optical method | Optical disdrometers |
|  | Others |
| Drop counter method | Drop counters |
| Impact method | Impact disdrometers |
| Capacitive method | Capacitive disdromenters |
| Ultrasonic/laser method (measurement of snow depth ) | Sonic ranging depth sensors |
|  | Laser sensors |
|  | Others |
| Manual observation for snowfall and snow depth | Rulers |
|  | Others |
| Others | - |

Configuration

| Gauge rim diameter | [cm] |
| --- | --- |
| Heating device (to prevent icing) | Yes/no |
| Wind Shield | Yes/no |
| Type of wind shield | Single Alter wind shield |
|  | Double Alter wind shield |
|  | Nipher wind shield |
|  | Tretyakov wind shield |
|  | WMO DFIR |
|  | Others |

.1.1.2.1.6 Radiation

| Method of measurement/observation | Type of instrument |
| --- | --- |
| Pyrheliometric method | Thermoelectric pyrheliometers |
|  | Thermoelectric Spectral pyrheliometers |
|  | Silver disk pyheliometers |
|  | Others |
| Pyranometric method | Thermoelectric pyranometers |
|  | Photovoltaic pyranometers |
|  | Bimetallic pyranographs |
|  | Others |
| Pyrradiometers | Pyrradiometers |
|  | Net pyrradiometer |
| Pyrgeometers | Pyrgeometers |
| Others |  |

1.1.2.1.7 Sunshine duration

| Method of measurement/observation | Type of instrument |
| --- | --- |
| Pyrheliometric method | Pyrheliometers (combined with an threshold discriminator and a time-counting device) |
| Pyranometric method | Pyranometers (the same as above) |
| Burn method | Campbell-Stokes sunshine recorders |
|  | Jordan sunshine recorders |
|  | Others |
| Contrast method | Solar-cell-type sunshine recorders |
|  | Others |
| Scanning method | Rotating mirror sunshine recorders |
|  | Others |
| Others | - |

1.1.2.1.8 Other surface variables

Present and past weather

| Method of measurement/observation | Type of instrument |
| --- | --- |
| Manual observations | - |
| Automated detection systems | Forwardscatter/backscatter present weather sensors |
|  | Optical disdrometers |
|  | Video Cameras |
|  | Others |

Visibility

| Method of measurement/observation | Type of instrument |
| --- | --- |
| Manual observations | - |
| Automated detection systems | Transmissometers |
|  | Forwardscatter sensors |
|  | Lidars |
|  | Video Cameras |
|  | Others |

Clouds

| Method of measurement/observation | Type of instrument |
| --- | --- |
| Manual observations | - |
| Automated detection systems | Ceilometers |
|  | Video Cameras |
|  | Others |

2. Assessment of “Table 2.1 Station information (required for near-real time and non-real time purposes)”

| Type of metadata |  |
| --- | --- |
| Station name |  |
| Station index number or identifier |  |
| WMO block and station numbers |  |
| Geographical coordinates |  |
| Local land-use (Agriculture, housing, industrial and commercial areas, … ) | Proposed (ref. WMO/TD No.1186) |
| Category of the station Definitions of stations as described in GOS Manual (Surface synoptic station, reference climatological station, …) | Proposed (ref. GOS Manual) |
| Postal Address of the station or the contact person (in case of unmanned stations) | Proposed |
| The name of supervising organization or institution | Proposed (ref. GOS Manual) |
| Manned station or unmanned station | Proposed |
| ……. |  |
| Local topography description |  |
| Topo-scale map with a scale of 1:20,000 – 1: 50,000 showing contours of elevation differences and local land use/land cover | Proposed (ref. CIMO Guide and WMO/TD No.1186) |
| Micro-scale map with a scale of 1:2,500 – 1:5,000 showing the locations of buildings and trees (with height) | Proposed (ref. CIMO Guide and WMO/TD No.1186) |
| Layout of the observation field showing the installation of instruments, the area covered by short grass or lawn ([m2]), and the distances between installations or from nearby buildings or trees | Proposed (ref. CIMO Guide and WMO/TD No.1186) |
| Date of latest maintenance for the surface of the field such as cutting grass or mowing, renewing or patching the lawn | Proposed (ref. WMO/TD No.1186) |
| Radiation horizon mapping including marked obstacles with their heights in the neighbourhood | Proposed (ref. CIMO Guide, WMO/TD No.1186) |
| …… |  |

When a station with a certain station number has different observing sites for different measured parameters, the station information for each of the sites should be recorded (e.g. Tokyo (47662) has a remote site 800 m away from the original location for the purpose of observing wind, radiation and sunshine duration in order to avoid the obstructions caused by nearby high story buildings. All the other parameters such as temperature, humidity or precipitation are observed at the original site).

3. Assessment of “Table 2.2 Individual instrument information (required for near-real time and non-real time purposes)”

Siting and exposure

| Type of metadata |  |
| --- | --- |
| Location |  |
| ……. |  |
| Horizon mapping (using a clinometer and compass survey in a circle around the sensor and a fisheye lens photograph looking at the zenith) | Proposed (ref. WMO/TD No.1186) |
| Photographs in the cardinal directions taken from the instrument enclosure | Proposed (ref. WMO/TD No.1186) |
| Micro-scale sketch of the instrument enclosure | Proposed (ref. WMO/TD No.1186) |
| ……. |  |

Calibration data

| Type of metadata |  |
| --- | --- |
| … |  |
| Latest date of maintenance | Proposed |
| Maintenance procedure description | Proposed |
| … |  |
| Is traceability to the international standards guaranteed? (yes/no) | Proposed |
| … |  |

__________