MANUAL ON CODES

National Coding Procedures with regard to international Code Forms.

Notification from USA (effective immediately):

Please include the text and associated code tables after “51.7 CAVOK shall not be used.” on page II-4-D-12 of WMO No. 306 Volume II (1998 Edition, Suppl. 1 (II.2002)).

In addition, the USA may optionally include the following groups immediately preceding the PROBC2C2 group:

(6IchihihitL) (5BhBhBhBtL)

(6IchihihitL)	Forecast icing group, used to forecast icing not associated with thunderstorms (thunderstorm forecasts imply moderate or greater icing).  Repeat as necessary to indicate multiple icing layers.  Omit when no icing is forecast.  Format icing groups as:

6	Icing group indicator.

Ic	Type of icing from Table 1.5.  When more than one type is expected within the same layer, encode the highest code figure.

hihihi	Height of base of icing layer in hundreds of feet above surface (see Note 1 under h).  (Table 1.4).

tL	Thickness of the icing layer in thousands of feet from Table 1.6.  When a layer is forecast to be thicker than 9,000 feet, repeat the icing group so that the base of the layer expressed by the second group coincides with the top layer given by the first group (See Note).

(5BhBhBhBtL)	Forecast turbulence group, used only to forecast turbulence not associated with a thunderstorm (thunderstorms already imply severe or extreme turbulence).  Turbulence forecasts apply to category II (CAT II) aircraft.  Omit when no turbulence is forecast.  Format turbulence groups as:

5	Turbulence group indicator.

B	Turbulence type and intensity from Table 1.7.

hBhBhB	Forecast height of the turbulence layer in hundreds of feet above surface (see Note 1 under h).  (Table 1.4).

tL	Thickness of the turbulence layer in thousands of feet from Table 1.6.

When a layer is forecast to be thicker than 9,000 feet, repeat the turbulence group so that the base of the layer expressed by the second group coincides with the top layer given by the first group (See Note).

Note:  Icing and turbulence forecasts are for phenomena not associated with thunderstorm activity, from surface to 10,000 feet above surface.

Table 1.4 Height of Lowest Level of Turbulence (hBhBhB)/Icing (hihihi)

| Code Figure | Meters | Feet |
| --- | --- | --- |
| 000 | <30 | <100 |
| 001 | 30 | 100 |
| 002 | 60 | 200 |
| 003 | 90 | 300 |
| 004 | 120 | 400 |
| 005 | 150 | 500 |
| 006 | 180 | 600 |
| 007 | 210 | 700 |
| 008 | 240 | 800 |
| 009 | 270 | 900 |
| 010 | 300 | 1,000 |
| 011 | 330 | 1,100 |
| Etc. | Etc. | Etc. |
| 099 | 2,970 | 9,900 |
| 100 | 3,000 | 10,000 |
| 110 | 3,300 | 11,000 |
| 120 | 3,600 | 12,000 |
| Etc. | Etc. | Etc. |
| 990 | 29,700 | 99,000 |
| 999 | 30,000 or more | 100,000 or more |

Table 1.5 Icing Type (Ic)

| Code Figure | Type of Icing |
| --- | --- |
| 0 | Trace icing |
| 1 | Light icing (mixed) |
| 2 | Light icing in cloud (rime) |
| 3 | Light icing in precipitation (clear) |
| 4 | Moderate icing (mixed) |
| 5 | Moderate icing in cloud (rime) |
| 6 | Moderate icing in precipitation (clear) |
| 7 | Severe icing (mixed) |
| 8 | Severe icing in cloud (rime) |
| 9 | Severe icing in precipitation (clear) |

Table 1.6 Thickness of Turbulence/Icing Layers (tL)

| Code Figure | Thickness |
| --- | --- |
| 1 | 1,000 feet |
| 2 | 2,000 feet |
| 3 | 3,000 feet |
| 4 | 4,000 feet |
| 5 | 5,000 feet |
| 6 | 6,000 feet |
| 7 | 7,000 feet |
| 8 | 8,000 feet |
| 9 | 9,000 feet |

Table 1.7  Turbulence Type/Intensity (B)

| Code Figure | Turbulence Type and Intensity |
| --- | --- |
| 0 | None |
| 1 | Light Turbulence |
| 2 | Moderate Turbulence in clear air, occasional. |
| 3 | Moderate Turbulence in clear air, frequent. |
| 4 | Moderate Turbulence in cloud, occasional. |
| 5 | Moderate Turbulence in cloud, frequent. |
| 6 | Severe Turbulence in clear air, occasional. |
| 7 | Severe Turbulence in clear air, frequent. |
| 8 | Severe Turbulence in cloud, occasional. |
| 9 | Severe Turbulence in cloud, frequent. |
| X | Extreme Turbulence |

NOTE: “occasional” is defined to occur less than 1/3 of the time.