### NEW ZEALAND

## National Deviations

15.1

The criteria covering the issue of SPECI reports are described in the following table.

15.5

Wind speed will be reported in knots

15.5.2

At all wind speeds and with any amount of variation in direction, wind direction will only be reported as variable “VRB” when it is impossible to determine a single wind direction.

15.5.3

The variation in wind direction group is reported if the total variation is 60 degrees or more and the mean wind speed is greater than 3 knots.

15.5.6

For wind speeds of 100 knots or more, the exact number of wind speed units (knots) shall be coded in lieu of the two figure code ff or fmfm.

15.6.2

When the horizontal visibility is not the same in all directions and the minimum visibility is less than 5000 m and the difference between the minimum and maximum is 50% or more of the minimum, the minimum visibility shall be given for VVVV followed, without a space, by DV consisting of one or two letters to indicate the general direction of the visibility in relation to the site of the aeronautical meteorological station reported as one of the eight points of the compass (N, NE, etc.).  If the lowest visibility is observed in more than one direction, then DV shall represent the most operationally significant direction.

When minimum visibility is less than 1500 metres while visibility in another direction is more than 5000 metres, the group VXVXVXVXDV shall also be used to report the value and direction of the maximum visibility.  If the highest visibility is observed in more than one direction, then DV shall represent the most operationally significant direction.

15.6.3

When the horizontal visibility is 10 kilometres or more, it will be coded in whole kilometres followed immediately by the letters KM.

15.6.4 and 15.10

CAVOK is not used.

15.7

Runway visual range is not reported.

15.8.10

The qualifier VC is used to indicate all weather phenomena observed within eight kilometres of the aerodrome perimeter but not at the aerodrome.

15.9

NSC is not used.

15.9.2

Vertical Visibility is not available.

15.14

The criteria governing the issue of Trend forecasts are described in the following table.

| ELEMENT | SPECI | Trend | TAF |
| --- | --- | --- | --- |
| WIND DIRECTION |  |  |  |
| A change of 60 degrees or more provided mean speed is 10 knots or more before and/or after the change: | yes | yes | yes |
| MEAN WIND SPEED |  |  |  |
| (a) A change by 10 knots or more since the last report: | yes | no | no |
| (b) An expected change of 10 knots or more: | no | yes | yes |
| GUSTINESS |  |  |  |
| An increase of 10 knots or more provided mean wind speed is 15 knots or more before and/or after the change: | yes | no | no |
| VISIBILITY |  |  |  |
| Value changes to or passes through: | 8000 m 5000 m 3000 m 1500 m 800 m | 8000 m 5000 m 3000 m 1500 m 800 m | 8000 m 5000 m 3000 m 1500 m 800 m |
| CLOUD |  |  |  |
| Provided cloud amount is BKN or OVC before and/or after the change, when the height changes to or passes through: | 1500 ft 1000 ft 500 ft 200 ft* | 1500 ft 1000 ft 500 ft 200 ft* | 1500 ft 1000 ft 500 ft 200 ft* |
| Provided the height of base is at or below 1500 ft: | When the amount has changed from SKC, FEW, or SCT to BKN or OVC, or vice versa |
| When CB are forecast to develop or dissipate | no | yes | yes |

*Auckland (NZAA) and Christchurch (NZCH) only.

| ELEMENT | SPECI | Trend | TAF |
| --- | --- | --- | --- |
| WEATHER PHENOMENA When onset or cessation of any of the following occurs | moderate or heavy precipitation (including showers thereof) thunderstorm (with or without precipitation) freezing precipitation freezing fog funnel cloud (tornado or waterspout) blowing dust, sand or snow (including snowstorm) sandstorm duststorm squall drifting dust, sand or snow ice crystals |
| When a change in intensity of any of the following occurs | moderate or heavy precipitation (including showers thereof) freezing precipitation sandstorm duststorm |