WMO No. 386 - Manual on Codes

Volume II - Regional Codes and National Coding Practices

# Notification from the Netherlands

D - NATIONAL CODING PROCEDURES WITH REGARD TO INTERNATIONAL CODE FORMS The Netherlands FM 12 SYNOP: All Dutch SYNOP observations will be generated fully automatic. There are 3 types of stations, using the SYNOP code form, if appropriate, with the code tables 4680 and 4531 for wawa and Wa1Wa2: Automated only wind stations Automated weather stations without a present weather sensor Automated weather stations with a present weather sensor Additional or different national encoding procedures when included: Section 1 6RRRtR When reported, this group is included in section 1 7wawaWa1Wa2 When included, the code tables 4680 and 4531, for wawa and Wa1Wa2, are used. 8NhCLCMCH When included, the encoded form 8//// is used Section 3 1snTxTxTx When reported, this group is included at 1800 UTC. 2snTnTnTn When reported, this group is included at 0600 UTC. 3/snTgTg When reported, this group is included at 0600 UTC, wherein TgTg is given in whole degrees Celsius. 7R24R24R24R24 When reported, this group is included at 0600 UTC 8NsChshs When included, the symbolic form 8Ns/hshs is used 9SpSpspsp This group is used in the following forms: 910ff These 3 groups are always included in reports of land stations as well as in reports of fixed sea stations 911ff 912ff Section 5 2snTnTnTn Minimum temperature in tenths of degrees Celsius, occurred during the preceding 14 hours 4snTgTgTg Minimum ground temperature in tenths of degrees Celsius, occurred at 10 cm above the ground, during the preceding 14 hours. Note: The groups are included at 0800 UTC, during the period of October to March. 511ff Highest gust during the preceding hour 512ff Maximum 10 minutes mean wind speed during the preceding hour Note 1: These 2 groups are always included in reports of land stations as well as in reports of fixed sea stations, regardless the wind speed. Note 2: These 2 groups are only in-cluded at intermediate - and main hours, to report the highest hourly gust and the highest 10 minutes mean. 51722 Snow grains during the preceding hour. 518 wawa The precipitation reported with wawa in the groups 7wawaWa1Wa2 and 518wawa is very light. 53QhQhQh Global radiation, wherein QhQhQh is reported in Joules per cm2 5975Vm Visibility in tens of meters, included when visibility, reported in the group iRixhVV, is less than 100 m.