NOTIFICATION FROM THE NETHERLANDS

### FM 15 METAR and FM 16 SPECI

National deviations from the global regulations:

Both CIVIL and MILITARY STATIONS:

15.4	With reference to fully automated observations:

If any element cannot be observed, the group in which it would have been encoded shall be replaced by the appropriate number of solidi, in accordance with the table below:

| Encoding of missing values in rapports of AUTO METAR/SPECI – 02Nov2005 |
| --- |
| Code group | Reporting practice | Total number of solidi - remarks |
| 1. Wind | ///12KT | 3 – wind direction information not available |
| 2. | 230//KT | 2 – wind speed information not available |
| 3. | /////KT | 5 – wind speed and wind direction not available |
| 4. Visibility | //// | 4 – visibility information not available; 1 group //// will replace all possible visibility groups |
| 5. RVR | R//////// | 8 – RVR information not available; 1 group R//////// will replace all possible RVR groups |
| 6. | R13///// | 5 – RVR information not available for given touchdown zone; to be used when at least 1 other RVR value is available (in such case, R//////// cannot be used) |
| 7. Present weather | // | 2 – no PW sensor available or sensor defect; 1 group // will replace all possible present weather groups |
| 8. Recent weather | RE// | 2 – information on recent weather phenomena not available; 1 group RE// will replace all possible recent weather groups |
| 9. Clouds | ///////// | 9 – no information on cloud amount, height and type; 1 group ///////// will replace all possible cloud groups |
| 10. | BKN020/// | 3 – cloud type not available for given layer |
| 11. *) | ////// (//////CB) *) | 6 – cloud amount and height not available; system is capable of detecting cloud type; 1 group ////// will replace all possible cloud groups |
| 12. | BKN////// | 6 – cloud height and type not available for given amount |
| 13. | BKN/// (BKN///CB) | 3 – cloud height not available; system is capable of detecting cloud type for the given cloud amount |
| 14. | ///020/// | 6 – cloud amount and type not available for given cloud height |
| 15. | ///020 (///020CB) | 3 – cloud amount not available; system is capable of detecting cloud type for the given cloud height |
| 16. | NCD | no clouds detected and the system is not able to detect cloud type |
| 17. | NSC | no clouds detected and no CB and/or TCU detected; system is capable of detecting cloud type |
| 18. Air temperature and dewpunt temperature | ///// | 5 – air temperature and dewpunt temperature not available; replaced by 4 //// |
| 19. | 14/// | 3 – dewpunt temperature not available; replaced by 2 // |
| 20. | ///12 | 3 – air temperature not available; replaced by 2 // |
| 21. Atmospheric pressure | Q//// or A//// | 4 – QNH information not available |
| 22. Water temperature and sea state (North Sea platforms) | W///// | 5 – water temperatuur not available; replaced by 2 // and sea state not available; replaced by 2 // |
| 23. | W///S3 | 3 – water temperatuur not available; replaced by 2 // |
| 24. | W17/// | 3 – sea state not available; replaced by 2 // |

*) – Additional remark with reference to the table, point 11:

If the system is capable of detecting cloud type, but not to associate this type to a given cloud layer, two cases are possible:

1.	If the system has not detected CB or TCU, cloud type is nevertheless considered as available for all cloud layers (the group of 3 /// is not added, as information about the absence of CB and TCU is available);

2.	If the system has detected CB or TCU, an additional cloud group (//////CB or //////TCU) is included.

15.8.1

1.	The letter abbreviations SHPL and TSPL shall not be used.

2.	The letter abbreviations SHUP or TSUP or FZUP, whatever applicable, shall be used.

3.	The precipitation form UP shall, if applicable, be combined with other forms of precipitation, such as RA, DZ, SN, GS, etc.

15.8.9

1.	Freezing fog (FZFG) shall always be reported if the wet bulb temperature (Tw) is below 0° C and the horizontal visibility is determined to be less than 1000 metres.

2.	The abbreviation BCFG, MIFG or PRFG, whatever applicable (where an automated observing system is used, it is dependent on its capability), shall be reported when the wet bulb temperature (Tw) is below 0° C and the horizontal visibility is 1000 metres or more, unless rime ice is actually deposited and observed. In such case, FZFG shall be reported.

NOTE:  with reference to visibility in fog, 15.8.16 and 15.8.18 shall apply.

15.8.12	IC shall be reported when visibility is less than 10 km.

15.8.13	FU or HZ or DU or SA shall be reported when visibility is less than 10 km.

15.8.14	BR shall be reported when visibility is less than 10 km but 1000 metres or more.

15.9.2	In case of fog, the maximum reported value for hshshs shall be 500 ft.
	In case of precipitation, the maximum reported value for hshshs shall be 1000 ft.

15.13.2.1

1.	The letter abbreviations RESHPL and RETSPL shall not be used.

2.	The letter abbreviations RESHUP or RETSUP or REFZUP, whatever applicable, shall be used.

3.	The abbreviation REUP shall, if applicable, be combined with other forms of precipitation, such as RA, DZ, SN, GS, etc.

CIVIL STATIONS only:

NOTES:

(1)	Observation station Vlissingen (EHFS) is not an aeronautical station.   It produces METAR's only (no SPECI and no TREND).

15.6.2	One extra criterium shall be added to the 50% rule for reporting the minimum visibility group VnVnVnVnDv:

"When the horizontal visibility is not the same in different directions and when the lowest visibility is different from the prevailing visibility and 1) less than 1500 metres or 2) less than 50% of the prevailing visibility and less than 5000 metres, the group VnVnVnVnDv  shall also be used ..........".

15.14	Trend forecasts:

1.	Visibility: an extra criterium of 8 kms for the horizontal visibility shall be used.

2.	Wind: a deviated criterium for the mean surface wind is: if the mean surface wind direction has changed by 30° or more and the mean speed before and/or after the change is 10 kts or more.

STATIONS of the ROYAL AIR FORCE and the ROYAL NAVY only:

15.6.1	In case of observations made by human observers, the group VVVV shall only be used to report the lowest visibility.

15.6.2	The group VnVnVnVnDv shall not be used.

15.7	The group RDRDR/VRVRVRVRVVRVRVRVRi shall not be used.

15.7.1	During periods when either the horizontal visibility is observed to be less than 3700 metres or the runway visual range for one or more runways available for 	anding is observed to be less than 3000 metres, group RDRDR/VRVRVRVRi shall be included in the report.

15.7.6	When the RVR is assessed to be more than 3000 metres, it shall be reported as P3000.

15.9.1.1	The abbreviation NSC shall not be used.

15.9.1.5	The height of the base of the cloud layer (mass) shall be reported in steps of 100 ft (30 metres) up to 5000 ft (1500 metres). Above 5000 ft steps of 1000 ft (300 metres) shall be used.

15.10	The code word CAVOK shall not be used.

15.13.3	The wind shear groups WS RWYDRDR  and WS ALL RWY shall not be used.

15.13.6	The state of the runway group RRRRERCReReRBRBR shall not be used.

15.14Trend forecasts:

The stations of the Royal Air Force and the Royal Navy shall use the 2-ATAF weather colour code, together with the change groups without a time group.

| 2-ATAF WEATHER COLOUR CODE |
| --- |
| Colour code | Visibility | Cloud base |
| Blue BLU | 8 km of more | 2500 ft or more |
| White WHT | 5 km - 8 km | 1500 ft - 2500 ft |
| Green GRN | 3.7 km - 5 km | 700 ft - 1500 ft |
| Yellow YLO | 1.6 km - 3.7 km | 300 ft - 700 ft |
| Amber AMB | 0.8 km - 1.6 km | 200 ft - 300 ft |
| Red RED | Less than 0.8 km | Less than 200 ft |
| BLACK | Aerodrome not in use due to other reasons than visibility and cloud base |

FM 51 TAF

National deviations from the global regulations:

Both CIVIL and MILITARY STATIONS:

51.5.1

1.	The letter abbreviations SHPL and TSPL shall not be used.

2.	BR or IC or FU or HZ or DU or SA, whatever applicable, shall be included when visibility is forecast to be less than 10 km.

51.6.2	In case of fog, the maximum value forecast for hshshs shall be 500 ft.
	In case of precipitation, the maximum value forecast for hshshs shall be 1000 ft.

51.10	The group (TXTFTF/GFGFZ   TNTFTF/GFGFZ) shall not be included in the report.

CIVIL STATIONS only:

51.8	Change groups

If modified conditions are forecast for horizontal visibility and/or mean surface wind, the following additional criteria values shall apply:

1.	Visibility: an extra criterium of 8 kilometres

2.	Wind: f the wind direction is forecast to change by 30° or more and the wind speed before and/or after the change is expected to be 10 kts or more.

STATIONS of the ROYAL AIR FORCE and the ROYAL NAVY only::

51.4.1	The group VVVV shall only be used to forecast the lowest visibility.

51.6.1.5	The height of the forecast cloud layer (mass) shall be given in steps of 100 ft (30 metres) up to 5000 ft (1500 metres).  Above 5000 ft steps of 1000 ft (300 metres) shall be used.

51.6.3	The abbreviation NSC shall not be used.

51.7	The code word CAVOK shall not be used.

51.8	Change groups

If modified conditions are forecast for horizontal visibility and/or cloud height, the associated criteria values used are derived from the 2-ATAF weather colour code.