WMO Publication No. 386

Manual on the Global Telecommunication System

Volume I - Global Aspects

PART II — Operational procedures for the GTS

Amendments

The amendments to the Manual on the GTS recommended by CBS-Ext.(06) and endorsed by EC-LIX enter into force as from 7 November 2007. The amendments are available at: http://www.wmo.int/pages/prog/www/ois/Operational_Information/ManOnGTS.html

The following paragraph 2.7 of the Manual on the GTS, Volume I, Part II, includes changes concerning the length of meteorological messages. These changes, which also enter into force as from 7 November 2007, were approved by CBS-XIII and endorsed by EC-VIII.

# Text boxes

Extracts from the Manual on the GTS, Volume I, Part II

2.7 	Length of meteorological messages

2.7.1 	The length of meteorological bulletins shall be determined according to the following:

2.7.1.1 	Prior to 7 November 2007:

(a) 	Any meteorological bulletin not segmented for transmission on the GTS should not exceed 15 000 octets;

(b) 	Any meteorological bulletin segmented into a series of meteorological bulletins for transmission on the GTS should not exceed 250 000 octets in its original form or when reassembled.

2.7.1.2 	On or after 7 November 2007:

(a) 	Meteorological bulletins for alphanumeric data representation transmitted on the GTS should not exceed 15 000 octets;

(b) 	The limit for meteorological bulletins for binary data representation or pictorial form shall be increased from 15 000 to 500 000 octets;

(c) 	Meteorological bulletins shall no longer be segmented for transmission on the GTS.

NOTE: Meteorological information may be exchanged using the file transfer technique described in Attachment II-15, particularly when the information exceeds 250 000 octets.