RECOMMENDATION 7 (CBS-XIV)

THE COMMISSION FOR BASIC SYSTEMS,

Noting:

(1)	Resolution 1 (Cg-XV) – Technical Regulations of the World Meteorological Organization,

(2)	Resolution 2 (Cg-XV) – World Weather Watch Programme for 2008–2011,

(3)	The Manual on Codes (WMO-No. 306), Volume I.2,

Considering the various requirements:

(1)	In GRIB Edition 2 for:

– New templates for chemicals

– New data representation template for run length packing with level values

(2)	In BUFR and CREX for:

– GHRSST data

– SBUV/2 ozone data

– Descriptors for encoding JASON2 OGDR data

– Entries for GOME Experiment

– Template for METOP GOME-2

– SMOS satellite data

– Encoding all sky radiance data

– Template for SYNOP data manually encoded in CREX

– Templates for METAR/SPECI and TAF coded in BUFR or CREX

– Template for surface observations from one-hour period

– Template for representation of SYNOP data with supplementary information on one hour observations

– Template for synoptic reports from fixed land stations suitable for SYNOP data and for maritime data from coastal and island stations

– A new sequence for locust data

– Modified descriptors for reporting correctly radiation

– Air chemistry

– New descriptors for GFA (Graphical Forecast AIRMET) data

– Wind reporting at pole

– New descriptors for intensity of precipitation

– Addition of code figure (cloud observation)

Recommends that the following amendments be adopted for operational use as from 4 November 2009:

(1)	Additions to FM 92-XIII Ext. GRIB defined in Annex 1 to this recommendation;

(2)	Additions to FM 94-XIII Ext. BUFR, FM 95-XIII Ext. CREX and to common code tables defined in Annex 2 to this recommendation;

Requests the Secretary-General to arrange for the inclusion of these amendments in the Manual on Codes (WMO-No. 306);

Authorizes the Secretary-General to make any consequent purely editorial amendments to the Manual on Codes, Volume I.2.

_____________________________________________________________________________

Annex 1 to Recommendation 7 (CBS-XIV) – Amendments to the

Manual on Codes, Volume I.2, for FM 92-XIII Ext. GRIB

NEW TEMPLATES FOR CHEMICALS

Addition of:

- a new category to Product Discipline 0 in Code Table 4.1

- a set of new parameters in Code Table 4.2

- a new Section 4 Code Table occupying 2 octets: Code Table 4.230, referring to a new Common Code Table C-14: Atmospheric chemical or physical constituent type

- new Product Definition Templates which include the new Code Table 4.230: 4.40 to 4.43

In Code Table 4.1 proposed new entry:

| Product Discipline 0: | Meteorological products |
| --- | --- |
| Category Description |  |
| 20 | Atmospheric chemical constituents |
| 21-189 | Reserved |

In Code Table 4.2 the following addition:

Product Discipline 0: Meteorological products, Parameter Category 20: Atmospheric chemical constituents

| Number | Parameter | Units |
| --- | --- | --- |
| 0 | Mass density (concentration) | kg m-3 |
| 1 | Column-integrated mass density (see Note) | kg m-2 |
| 2 | Mass mixing ratio (mass fraction in air) | kg kg-1 |
| 3 | Atmosphere emission mass flux | kg m-2 s-1 |
| 4 | Atmosphere net production mass flux | kg m-2 s-1 |
| 5 | Atmosphere net production and emission mass flux | kg m-2 s-1 |
| 6 | Surface dry deposition mass flux | kg m-2 s-1 |
| 7 | Surface wet deposition mass flux | kg m-2 s-1 |
| 8 | Atmosphere re-emission mass flux | kg m-2 s-1 |
| 9-49 | Reserved |  |
| 50 | Amount in atmosphere | mol |
| 51 | Concentration in air | mol m-3 |
| 52 | Volume mixing ratio (fraction in air) | mol mol-1 |
| 53 | Chemical gross production rate of concentration | mol m-3 s-1 |
| 54 | Chemical gross destruction rate of concentration | mol m-3 s-1 |
| 55 | Surface flux | mol m-2 s-1 |
| 56 | Changes of amount in atmosphere (see Note 1) | mol s-1 |
| 57 | Total yearly average burden of the atmosphere | mol |
| 58 | Total yearly averaged atmospheric loss (see Note 1) | mol s-1 |
| 59-99 | Reserved |  |
| 100 | Surface area density (aerosol) | m-1 |
| 101 | Atmosphere optical thickness | m |
| 102-191 | Reserved |  |
| 192-254 | Reserved for local use |  |
| 255 | Missing |  |

Code Table 4.230: Atmospheric chemical constituent type

(see Common Code Table C-14)

Proposed new Product Definition Templates

The following proposed Product Definition Templates are based on existing templates with the inclusion of the new proposed Code Table 4.230.

Product Definition Template 4.40: Analysis or forecast at a horizontal level or in a horizontal layer at a point in time for atmospheric chemical constituents

| Octet Number(s) | Contents |
| --- | --- |
| 10 | Parameter category (see Code Table 4.1) |
| 11 | Parameter number (see Code Table 4.2) |
| 12-13 | Atmospheric chemical constituent type (see Code Table 4.230) |
| 14 | Type of generating process (see Code Table 4.3) |
| 15 | Background generating process identifier (defined by originating centre) |
| 16 | Analysis or forecast generating process identifier (defined by originating centre) |
| 17-18 | Hours of observational data cutoff after reference time (see Note 1) |
| 19 | Minutes of observational data cutoff after reference time |
| 20 | Indicator of unit of time range (see Code Table 4.4) |
| 21-24 | Forecast time in units defined by octet 20 |
| 25 | Type of first fixed surface (see Code Table 4.5) |
| 26 | Scale factor of first fixed surface |
| 27-30 | Scaled value of first fixed surface |
| 31 | Type of second fixed surface (see Code Table 4.5) |
| 32 | Scale factor of second fixed surface |
| 33-36 | Scaled value of second fixed surface |

Note:

- Hours greater than 65534 will be coded as 65534.

Product Definition Template 4.41: Individual ensemble forecast, control and perturbed, at a horizontal level or in a horizontal layer at a point in time for atmospheric chemical constituents

| Octet Number(s) | Contents |
| --- | --- |
| 10 | Parameter category (see Code Table 4.1) |
| 11 | Parameter number (see Code Table 4.2) |
| 12-13 | Atmospheric chemical constituent type (see Code Table 4.230) |
| 14 | Type of generating process (see Code Table 4.3) |
| 15 | Background generating process identifier (defined by originating centre) |
| 16 | Forecast generating process identifier (defined by originating centre) |
| 17-18 | Hours after reference time of data cutoff (see Note 1) |
| 19 | Minutes after reference time of data cutoff |
| 20 | Indicator of unit of time range (see Code Table 4.4) |
| 21-24 | Forecast time in units defined by octet 20 |
| 25 | Type of first fixed surface (see Code Table 4.5) |
| 26 | Scale factor of first fixed surface |
| 27-30 | Scaled value of first fixed surface |
| 31 | Type of second fixed surface (see Code Table 4.5) |
| 32 | Scale factor of second fixed surface |
| 33-36 | Scaled value of second fixed surface |
| 37 | Type of ensemble forecast (see Code Table 4.6) |
| 38 | Perturbation number |
| 39 | Number of forecasts in ensemble |

Note:

- Hours greater than 65534 will be coded as 65534.

Product Definition Template 4.42: Average, accumulation, and/or extreme values or other statistically processed values at a horizontal level or in a horizontal layer in a continuous or non-continuous time interval for atmospheric chemical constituents

| Octet Number(s) | Contents |
| --- | --- |
| 10 | Parameter category (see Code Table 4.1) |
| 11 | Parameter number (see Code Table 4.2) |
| 12-13 | Atmospheric chemical constituent type (see Code Table 4.230) |
| 14 | Type of generating process (see Code Table 4.3) |
| 15 | Background generating process identifier (defined by originating centre) |
| 16 | Analysis or forecast generating process identifier (defined by originating centre) |
| 17-18 | Hours after reference time of data cutoff (see Note 1) |
| 19 | Minutes after reference time of data cutoff |
| 20 | Indicator of unit of time range (see Code Table 4.4) |
| 21-24 | Forecast time in units defined by octet 20 (see Note 2) |
| 25 | Type of first fixed surface (see Code Table 4.5) |
| 26 | Scale factor of first fixed surface |
| 27-30 | Scaled value of first fixed surface |
| 31 | Type of second fixed surface (see Code Table 4.5) |
| 32 | Scale factor of second fixed surface |
| 33-36 | Scaled value of second fixed surface |
| 37-38 | Year |
| 39 | Month |
| 40 | Day |
| 41 | Hour |
| 42 | Minute |
| 43 | Second |
| 44 | n - Number of time range specifications describing the time intervals used to calculate the statistically processed field |
| 45-48 | Total number of data values missing in statistical process |
|  | 49-60 Specification of the outermost (or only) time range over which statistical processing is done |
| 49 | Statistical process used to calculate the processed field from the field at each time increment during the time range (see Code Table 4.10) |
| 50 | Type of time increment between successive fields used in the statistical processing (see Code Table 4.11) |
| 51 | Indicator of unit of time for time range over which statistical processing is done (see Code Table 4.4) |
| 52-55 | Length of the time range over which statistical processing is done, in units defined by the previous octet |
| 56 | Indicator of unit of time for the increment between the successive fields used (see Code Table 4.4) |
| 57-60 | Time increment between successive fields, in units defined by the previous octet (see Notes 3 and 4) |
|  | 61-nn These octets are included only if n>1, where nn = 48 + 12 * n |
| 61-72 | As octets 49 to 60, next innermost step of processing |
| 73-nn | Additional time range specifications, included in accordance with the value of n. Contents as octets 49 to 60, repeated as necessary. |

Notes:

- Hours greater than 65534 will be coded as 65534.

- The reference time in section 1 and the forecast time together define the beginning of the overall time interval.

- An increment of zero means that the statistical processing is the result of a continuous (or near continuous) process, not the processing of a number of discrete samples. Examples of such continuous processes are the temperatures measured by analogue maximum and minimum thermometers or thermographs, and the rainfall measured by a rain gauge.

- The reference and forecast times are successively set to their initial values plus or minus the increment, as defined by the type of time increment (one of octets 50, 62, 74 …). For all but the innermost (last) time range, the next inner range is then processed using these references and forecast times as the initial reference and forecast time.

Product Definition Template 4.43: Individual ensemble forecast, control and perturbed, at a horizontal level or in a horizontal layer in a continuous or non-continuous time interval for atmospheric chemical constituents

| Octet Number(s) | Contents |
| --- | --- |
| 10 | Parameter category (see Code Table 4.1) |
| 11 | Parameter number (see Code Table 4.2) |
| 12-13 | Atmospheric chemical constituent type (see Code Table 4.230) |
| 14 | Type of generating process (see Code Table 4.3) |
| 15 | Background generating process identifier (defined by originating centre) |
| 16 | Forecast generating process identifier (defined by originating centre) |
| 17-18 | Hours after reference time of data cutoff (see Note 1) |
| 19 | Minutes after reference time of data cutoff |
| 20 | Indicator of unit of time range (see Code Table 4.4) |
| 21-24 | Forecast time in units defined by octet 20 (see Note 2) |
| 25 | Type of first fixed surface (see Code Table 4.5) |
| 26 | Scale factor of first fixed surface |
| 27-30 | Scaled value of first fixed surface |
| 31 | Type of second fixed surface (see Code Table 4.5) |
| 32 | Scale factor of second fixed surface |
| 33-36 | Scaled value of second fixed surface |
| 37 | Type of ensemble forecast (see Code Table 4.6) |
| 38 | Perturbation number |
| 39 | Number of forecasts in ensemble |
| 40-41 | Year of end of overall time interval |
| 42 | Month of end of overall time interval |
| 43 | Day of end of overall time interval |
| 44 | Hour of end of overall time interval |
| 45 | Minute of end of overall time interval |
| 46 | Second of end of overall time interval |
| 47 | n - Number of time range specifications describing the time intervals used to calculate the statistically processed field |
| 48-51 | Total number of data values missing in statistical process |
|  | 52-63 Specification of the outermost (or only) time range over which statistical processing is done |
| 52 | Statistical process used to calculate the processed field from the field at each time increment during the time range (see Code Table 4.10) |
| 53 | Type of time increment between successive fields used in the statistical processing (see Code Table 4.11) |
| 54 | Indicator of unit of time for time range over which statistical processing is done (see Code Table 4.4) |
| 55-58 | Length of the time range over which statistical processing is done, in units defined by the previous octet |
| 59 | Indicator of unit of time for the increment between the successive fields used (see Code Table 4.4) |
| 60-63 | Time increment between successive fields, in units defined by the previous octet (see Notes 3 and 4) |
|  | 64-nn These octets are included only if n>1, where nn = 51 + 12 * n |
| 64-75 | As octets 52 to 63, next innermost step of processing |
| 76-nn | Additional time range specifications, included in accordance with the value of n. Contents as octets 52 to 63, repeated as necessary. |

Notes:

- Hours greater than 65534 will be coded as 65534.

- The reference time in section 1 and the forecast time together define the beginning of the overall time interval.

- An increment of zero means that the statistical processing is the result of a continuous (or near continuous) process, not the processing of a number of discrete samples. Examples of such continuous processes are the temperatures measured by analogue maximum and minimum thermometers or thermographs, and the rainfall measured by a rain gauge.

- The reference and forecast times are successively set to their initial values plus or minus the increment, as defined by the type of time increment (one of octets 53, 65, 77 …). For all but the innermost (last) time range, the next inner range is then processed using these reference and forecast times as the initial reference and forecast time.

NEW COMMON CODE TABLE C-14:

Atmospheric chemical or physical constituent type

| Code figure | Meaning | Chemical formula |
| --- | --- | --- |
| 0 | Ozone | O3 |
| 1 | Water vapour | H2O |
| 2 | Methane | CH4 |
| 3 | Carbon dioxide | CO2 |
| 4 | Carbon monoxide | CO |
| 5 | Nitrogen dioxide | NO2 |
| 6 | Nitrous oxide | N2O |
| 7 | Formaldehyde | HCHO |
| 8 | Sulphur dioxide | SO2 |
| 9 | Ammonia | NH3 |
| 10 | Ammonium | NH4+ |
| 11 | Nitrogen monoxide | NO |
| 12 | Atomic oxygen | O |
| 13 | Nitrate radical | NO3 |
| 14 | Hydroperoxyl radical | HO2 |
| 15 | Dinitrogen pentoxide | N2O5 |
| 16 | Nitrous acid | HONO |
| 17 | Nitric acid | HNO3 |
| 18 | Peroxynitric acid | HO2NO2 |
| 19 | Hydrogen peroxide | H2O2 |
| 20 | Molecular hydrogen | H |
| 21 | Atomic nitrogen | N |
| 22 | Sulphate | SO42- |
| 23 | Radon | Rn |
| 24 | Elemental mercury | Hg(0) |
| 25 | Divalent mercury | Hg2+ |
| 26 | Atomic chlorine | Cl |
| 27 | Chlorine monoxide | ClO |
| 28 | Dichlorine peroxide | Cl2O2 |
| 29 | Hypochlorous acid | HClO |
| 30 | Chlorine nitrate | ClONO2 |
| 31 | Chlorine dioxide | ClO2 |
| 32 | Atomic bromine | Br |
| 33 | Bromine monoxide | BrO |
| 34 | Bromine chloride | BrCl |
| 35 | Hydrogen bromide | HBr |
| 36 | Hypobromous acid | HBrO |
| 37 | Bromine nitrate | BrONO2 |
| 38-9999 | Reserved |  |
| 10000 | Hydroxyl radical | OH |
| 10001 | Methyl peroxy radical | CH3O2 |
| 10002 | Methyl hydroperoxide | CH3O2H |
| 10004 | Methanol | CH3OH |
| 10005 | Formic acid | CH3OOH |
| 10006 | Hydrogen Cyanide | HCN |
| 10007 | Aceto nitrile | CH3CN |
| 10008 | Ethane | C2H6 |
| 10009 | Ethene (= Ethylene) | C2H4 |
| 10010 | Ethyne (= Acetylene) | C2H2 |
| 10011 | Ethanol | C2H5OH |
| 10012 | Acetic acid | C2H5OOH |
| 10013 | Peroxyacetyl nitrate | CH3C(O)OONO2 |
| 10014 | Propane | C3H8 |
| 10015 | Propene | C3H6 |
| 10016 | Butanes | C4H10 |
| 10017 | Isoprene | C5H10 |
| 10018 | Alpha pinene | C10H16 |
| 10019 | Beta pinene | C10H16 |
| 10020 | Limonene | C10H16 |
| 10021 | Benzene | C6H6 |
| 10022 | Toluene | C7H8 |
| 10023 | Xylene | C8H10 |
| 10024-10499 | reserved for other simple organic molecules (e.g. higher aldehydes, alcohols, peroxides,…) |  |
| 10500 | Dimethyl sulphide | CH3SCH3 (DMS) |
| 10501-20000 | Reserved |  |
| 20001 | Hydrogen chloride |  |
| 20002 | CFC-11 |  |
| 20003 | CFC-12 |  |
| 20004 | CFC-113 |  |
| 20005 | CFC-113a |  |
| 20006 | CFC-114 |  |
| 20007 | CFC-115 |  |
| 20008 | HCFC-22 |  |
| 20009 | HCFC-141b |  |
| 20010 | HCFC-142b |  |
| 20011 | Halon-1202 |  |
| 20012 | Halon-1211 |  |
| 20013 | Halon-1301 |  |
| 20014 | Halon-2402 |  |
| 20015 | Methyl chloride (HCC-40) |  |
| 20016 | Carbon tetrachloride (HCC-10) |  |
| 20017 | HCC-140a | CH3CCl3 |
| 20018 | Methyl bromide (HBC-40B1) |  |
| 20019 | Hexachlorocyclohexane (HCH) |  |
| 20020 | Alpha hexachlorocyclohexane |  |
| 20021 | Hexachlorobiphenyl (PCB-153) |  |
| 20022-29999 | Reserved |  |
| 30000-59999 | Reserved |  |
| 60000 | HOx radical (OH+HO2) |  |
| 60001 | Total inorganic and organic peroxy radicals (HO2 + RO2) | RO2 |
| 60002 | Passive Ozone |  |
| 60003 | NOx expressed as nitrogen | NOx |
| 60004 | All nitrogen oxides (NOy) expressed as nitrogen | NOy |
| 60005 | Total inorganic chlorine | Clx |
| 60006 | Total inorganic bromine | Brx |
| 60007 | Total inorganic chlorine except HCl, ClONO2: ClOx |  |
| 60008 | Total inorganic bromine except HBr, BrONO2: BrOx |  |
| 60009 | Lumped Alkanes |  |
| 60010 | Lumped Alkenes |  |
| 60011 | Lumped Aromatic Compounds |  |
| 60012 | Lumped Terpenes |  |
| 60013 | Non-methane volatile organic compounds expressed as carbon | NMVOC |
| 60014 | Anthropogenic non-methane volatile organic compounds expressed as carbon | aNMVOC |
| 60015 | Biogenic non-methane volatile organic compounds expressed as carbon | bNMVOC |
| 60016 | Lumped oxygenated hydrocarbons | OVOC |
| 60017-61999 | Reserved |  |
| 62000 | Total aerosol |  |
| 62001 | Dust dry |  |
| 62002 | Water in ambient |  |
| 62003 | Ammonium dry |  |
| 62004 | Nitrate dry |  |
| 62005 | Nitric acid trihydrate |  |
| 62006 | Sulphate dry |  |
| 62007 | Mercury dry |  |
| 62008 | Sea salt dry |  |
| 62009 | Black carbon dry |  |
| 62010 | Particulate organic matter dry |  |
| 62011 | Primary particulate organic matter dry |  |
| 62012 | Secondary particulate organic matter dry |  |
| 62013-65534 | Reserved |  |
| 65535 | Missing |  |

Update Code Table 4.0:

Code Table 4.0:		Product Definition Template Number

Number		Description

0		Analysis or forecast at a horizontal level or in a horizontal layer at a point in time

1 		Individual ensemble forecast, control and perturbed, at a horizontal level or in a horizontal layer at a point in time

2 		Derived forecast based on all ensemble members at a horizontal level or in a horizontal layer at a point in time

3 		Derived forecasts based on a cluster of ensemble members over a rectangular area at a horizontal level or in a horizontal layer at a point in time

4 		Derived forecasts based on a cluster of ensemble members over a circular area at a horizontal level or in a horizontal layer at a point in time

5		Probability forecasts at a horizontal level or in a horizontal layer at a point in time

6		Percentile forecasts at a horizontal level or in a horizontal layer at a point in time

7		Analysis or forecast error at a horizontal level or in a horizontal layer at a point in time

8		Average, accumulation, extreme values or other statistically processed values at a horizontal level or in a horizontal layer in a continuous or non-continuous time interval

- Probability forecasts at a horizontal level or in a horizontal layer in a continuous or non-continuous time interval

- Percentile forecasts at a horizontal level or in a horizontal layer in a continuous or non-continuous time interval

- Individual ensemble forecast, control and perturbed, at a horizontal level or in a horizontal layer, in a continuous or non-continuous interval

- Derived forecasts based in all ensemble members at a horizontal level or in a horizontal layer, in a continuous or non-continuous interval

- Derived forecasts based on a cluster of ensemble members over a rectangular area, at a horizontal level or in a horizontal layer, in a continuous or non-continuous interval

- Derived forecasts based on a cluster of ensemble members over a circular area, at a horizontal level or in a horizontal layer, in a continuous or non-continuous interval

15-19	Reserved

20		Radar product

21-29		Reserved

30		Satellite product (deprecated)

31		Satellite product

32-39		Reserved

40		Analysis or forecast at a horizontal level or in a horizontal layer at a point in time for atmospheric chemical constituents

41		Individual ensemble forecast, control and perturbed, at a horizontal level or in a horizontal layer at a point in time for atmospheric chemical constituents

42		Average, accumulation, and/or extreme values or other statistically processed values at a horizontal level or in a horizontal layer in a continuous or non-continuous time interval for atmospheric chemical constituents

43		Individual ensemble forecast, control and perturbed, at a horizontal level or in a horizontal layer in a continuous or non-continuous time interval for atmospheric chemical constituents

44-253		Reserved

254		CCITT IA5 character string

255-999	Reserved

1000		Cross section of analysis and forecast at a point in time

1001		Cross section of averaged or otherwise statistically processed analysis or forecast over a range of time

1002		Cross-section of analysis and forecast, averaged or otherwise statistically processed

1003-1099	Reserved

1100		Hovmöller-type grid with no averaging or other statistical processing

1101		Hovmöller-type grid with averaging or other statistical processing

1102-32767 	Reserved

32768-65534   	Reserved for local use

65535		Missing

NEW DATA REPRESENTATION TEMPLATE FOR RUN LENGTH PACKING WITH LEVEL VALUES

New entry to the Code Table 5.0

200	Run length packing with level values

New Data Representation Template

5.200	Grid point data - Run length packing with level values

12	Number of bits used for each packed value in the run length packing with level values

13-14	MV - Maximum value within the levels that are used in the packing

15-16	MVL - Maximum value of level (Predefined)

17	Decimal scale factor of representative value of each level

18-19+2*(lv-1)   List of MVL scaled representative values of each level from lv=1 to MVL

##### Annex 2 to Recommendation 7 (CBS-XIV) - Amendments to the Manual on Codes, Volume I.2, for FM 94-XIII Ext. BUFR and FM 95-XIII Ext. CREX

CONTENT

Page

DESCRIPTORS FOR ATMOSPHERIC CHEMISTRY

DESCRIPTORS TO BE USED WHEN EXCHANGING GLOBAL OCEAN DATA ASSIMILATION EXPERIMENT (GODAE) HIGH RESOLUTION SEA SURFACE TEMPERATURE (GHRSST) DATA

TEMPLATE FOR SYNOPTIC REPORTS FROM FIXED LAND STATIONS SUITABLE FOR SYNOP DATA MANUALLY ENCODED IN CREX

NEW PROPOSED BUFR/CREX METAR/SPECI AND TAF TEMPLATES

FOR SBUV/2 OZONE DATA

FOR SATELLITE DATA EXCHANGES

MODIFIED DESCRIPTORS FOR REPRESENTATION OF RADIATION DATA

NATIONAL AND WMO STATION IDENTIFICATION AND THE AWS BUFR TEMPLATES

NEW DESCRIPTORS FOR GFA (GRAPHICAL FORECAST AIRMET) DATA

FOR THE ENCODING OF THE JASON2 OGDR DATA

FOR SMOS SATELLITE DATA

FOR GOME EXPERIMENT DATA

METOP GOME-2 BUFR TEMPLATE

BUFR TABLE D AND CODE TABLE ENTRIES FOR ENCODING OF ALL SKY RADIANCE DATA

BUFR template for representation of SYNOP data with supplementary information on one-hour observations

BUFR TEMPLATE FOR SYNOPTIC REPORTS FROM FIXED LAND STATIONS SUITABLE FOR SYNOP DATA AND FOR MARITIME DATA FROM COASTAL AND ISLAND STATIONS

TEMPLATE FOR PASSING LOCUST INFORMATION

WIND REPORTING AT POLES

NEW DESCRIPTOR FOR INTENSITY OF PRECIPITATION

ADDITION OF A CODE FIGURE (CLOUD OBSERVATIONS)

DESCRIPTORS FOR ATMOSPHERIC CHEMISTRY

| Element Descriptor | Element name | Unit | Scale | Reference Value | Data Width |
| --- | --- | --- | --- | --- | --- |
| 0-02-071 | Spectrographic wavelength | m | 13 | 0 | 30 |
| 0-08-026 | Matrix significance | Code Table | 0 | 0 | 6 |
| 0-08-043 | Atmospheric chemical or physical constituent type | Code Table | 0 | 0 | 8 |
| 0-08-090 | Decimal scale of following significands | Numeric | 0 | -127 | 8 |
| 0-15-008 | Significand of volumetric mixing ratio | Numeric | 0 | 0 | 10 |
| 0 15 021 | Integrated mass density | kg/m**2 | 11 | 0 | 31 |
| 0-15-024 | Optical depth | Numeric | 4 | 0 | 24 |
| 0-25-143 | Linear coefficient | Numeric | 6 | -5000000 | 24 |

Note 1:

Descriptor 0 08 090 is to be used to establish the decimal scale of one or more subsequent numerical element descriptors requiring a large dynamic range of values.  The numerical element descriptor(s) will contain the scaled value of the measurement(s) with the required number of significant digits.  The actual value will be obtained, at the application level, by multiplying the scaled value by the given decimal scale: (scaled value * 10decimal scale).

Note 2:

When descriptor 0 08 043 is used to specify particulate matter (PM) under a given size threshold, descriptor 0 08 045 may also be used to further specify a subset of the PM population on the basis of ion composition.

Note 3:

Descriptor 0 25 143 is intended for numerical, non-dimensional values to be used as coefficients in statistical or linear processing.  Each instance of 0 25 143 should be characterized by using an appropriate significance qualifier, such as 0 08 026.

Code Tables

0 08 026 - Matrix significance

| Code figure | Meaning |
| --- | --- |
| 0 | Averaging kernel matrix |
| 1 | Correlation matrix (C) |
| 2 | Lower triangular correlation matrix square root (L from C=LLT) |
| 3 | Inverse of lower triangular correlation matrix square root (L-1) |
| 4-42 | Reserved |
| 43-62 | Reserved for local use |
| 63 | Missing or undefined significance |

0 08 043 - Amospheric chemical or physical constituent type

Note: The last column in the table contains the associated registry number from the Chemical Abstracts Service (CAS) of the American Chemical Society.

| Code figure | Meaning |
| --- | --- |
|  | Name | Formula | CAS Number (if applicable) |
| 0 | Ozone | O3 | 10028-15-6 |
| 1 | Water vapour | H2O | 7732-18-5 |
| 2 | Methane | CH4 | 74-82-8 |
| 3 | Carbon dioxide | CO2 | 124-38-9 |
| 4 | Carbon monoxide | CO | 630-08-0 |
| 5 | Nitrogen dioxide | NO2 | 10102-44-0 |
| 6 | Nitrous oxide | N2O | 10024-97-2 |
| 7 | Formaldehyde | HCHO | 50-00-0 |
| 8 | Sulfur dioxide | SO2 | 7446-09-5 |
| 09-24 | reserved |  |  |
| 25 | Particulate Matter < 1.0 microns |  |  |
| 26 | Particulate Matter < 2.5 microns |  |  |
| 27 | Particulate Matter < 10 microns |  |  |
| 28 | Aerosols (generic) |  |  |
| 29 | Smoke (generic) |  |  |
| 30 | Crustal Material (generic dust) |  |  |
| 31 | Volcanic Ash |  |  |
| 32-200 | reserved |  |  |
| 201-254 | reserved for local use |  |  |
| 255 | missing |  |  |

DESCRIPTORS TO BE USED WHEN EXCHANGING GLOBAL OCEAN DATA ASSIMILATION EXPERIMENT (GODAE) HIGH RESOLUTION SEA SURFACE TEMPERATURE (GHRSST) DATA:

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | Unit | Scale | Ref. value | Data width (bits) | Unit | Scale | Data width (chars) |
| 0 25 037 | SST bias | K | 2 | -127 | 8 | K | 2 | 3 |
| 0 14 035 | Solar Radiation Flux | W m-2 | 1 | 0 | 14 | W m-2 | 1 | 5 |
| 0 25 022 | GHRSST Rejection Flag | Flag table | 0 | 0 | 9 | Flag table | 0 | 3 |
| 0 25 023 | GHRSST Confidence Flag | Flag table | 0 | 0 | 9 | Flag table | 0 | 3 |
| 0 25 024 | GHRSST data quality | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 01 028 | Aerosol optical Depth (AOD) source | Code table | 0 | 0 | 5 | Code table | 0 | 2 |
| 0 01 024 | Wind Speed source | Code Table | 0 | 0 | 5 | Code Table | 0 | 2 |
| 0 01 029 | SSI Source | Code Table | 0 | 0 | 5 | Code Table | 0 | 2 |
| 0 01 038 | Source of Sea Ice Fraction | Code Table | 0 | 0 | 5 | Code Table | 0 | 2 |
| 0 25 038 | Difference between SST and analysis | K | 1 | -127 | 8 | K | 1 | 3 |
| 0 22 046 | Sea Ice Fraction | Numeric | 2 | 0 | 7 | Numeric | 2 | 3 |

Flag tables:

0 25 022 - GHRSST Rejection Flag

| Bit No. |  |
| --- | --- |
| 1 | Unprocessed |
| 2 | Land suspected. |
| 3 | Wind speed too large |
| 4 | Ice detected. |
| 5 | Rain detected (Microwave retrievals only) |
| 6 | Cloudy detected (Infra-red retrievals only) |
| 7 | Cosmetic value |
| 8 | SST out of range |
| All 9 | Missing value |

0 25 023 - GHRSST Confidence Flag

| Bit No. |  |
| --- | --- |
| 1 | Default confidence value has been used |
| 2 | Default bias and standard deviation has been used |
| 3 | Sun glint suspected |
| 4 | Sea ice retrieval for microwave data |
| 5 | High wind speed retrieval |
| 6 | Inaccurate SST due to low SST (< 285K) (Only applies to the TMI instrument) |
| 7 | Relaxed rain contamination suspected |
| 8 | Potential side lobe contamination |
| All 9 | Missing value |

Codes Tables

0 25 024 – GHRSST proximity confidence.

| Code figure |  |
| --- | --- |
| 0 | Unprocessed infrared retrieval |
| 1 | Cloudy retrievals |
| 2 | Bad: Data that are probably contaminated by cloud |
| 3 | Suspect data |
| 4 | Acceptable data |
| 5 | Excellent data |
| 6 | Cool skin suspected |
| 7-9 | Reserved |
| 10 | Unprocessed microwave retrieval |
| 11 | Questionable microwave retrieval that may be contaminated |
| 12 | Acceptable microwave retrieval |
| 13 | High probability of diurnal variability |
| 14 | Reserved |
| 15 | Missing value |

0 01 028 - Aerosol optical Depth (AOD) source

| Code figure |  |
| --- | --- |
| 0 | No AOD data available |
| 1 | NESDIS |
| 2 | NAVOCEANO |
| 3 | NAAPS |
| 4 | MERIS |
| 5 | AATSR |
| 6-30 | Reserved for future use |
| 31 | Missing value |

0 01 024 - Wind Speed source

| Code figure |  |
| --- | --- |
| 0 | No wind speed data available |
| 1 | AMSR-E data |
| 2 | TMI data |
| 3 | NWP: ECMWF |
| 4 | NWP: UK Met Office |
| 5 | NWP: NCEP |
| 6 | Reference climatology |
| 7 | ERS_Scatterometer |
| 8-30 | Reserved for future use |
| 31 | Missing value |

0 01 029 - SSI Source

| Code figure |  |
| --- | --- |
| 0 | No SSI data available |
| 1 | MSG_SEVIRI |
| 2 | GOES East |
| 3 | GOES West |
| 4 | ECMWF |
| 5 | NCEP |
| 6 | UK Met Office |
| 7-30 | Reserved for future use |
| 31 | Missing value |

0 01 038 - Source of Sea Ice Fraction

| Code figure |  |
| --- | --- |
| 0 | No sea ice set |
| 1 | NSIDC SSM/I Cavalieri et al (1992) |
| 2 | AMSR-E |
| 3 | ECMWF |
| 4 | CMS (France) cloud mask used by Medspiration |
| 5 | EUMETSAT OSI-SAF |
| 6-30 | Reserved for future use |
| 31 | Missing value |

Table of Acronyms

| Acronym | Expansion |
| --- | --- |
| AATSR | Advanced Along-Track Scanning Radiometer. |
| AMSR-E | Advanced Microwave Scanning Radiometer. |
| AOD | Aerosol optical depth. |
| CMS | Centre de Meteorologie Spatiale (Lannion, France). |
| ERS | European Remote-sensing Satellite. |
| EUMETSAT | European organization for the exploitation of meteorological satellites. |
| GHRSST-PP | GODAE High Resolution Sea Surface Temperature Pilot Project. |
| GODAE | Global Ocean Data Assimilation Experiment. |
| GOES | Geostationary Operational Environment Satellite. |
| IR | Infra-red. |
| MERIS | Medium Resolution Imaging Spectrometer. |
| MSG | Meteosat Second Generation. |
| MW | Microwave. |
| NAAPS | Navy Aerosol Analysis and Prediction System. |
| NAVOCEANO | Naval Oceanographic Office (United States of America). |
| NCEP | National Centers for Environmental Prediction. |
| NESDIS | National Environmental Satellite, Data, and Information Service. (United States of America). |
| NWP | Numerical weather prediction. |
| OSI-SAF | Ocean and Sea Ice Satellite Applications Facility. |
| RF | Radio frequency. |
| SEVIRI | Spinning Enhanced Visible and Infrared Imager |
| SSI | Surface Solar Irradiance. |
| TMI | Tropical Rainfall Measuring Mission (TRMM) Microwave Imager. |

TM D07089 - TEMPLATE FOR SYNOPTIC REPORTS FROM FIXED LAND STATIONS SUITABLE FOR SYNOP DATA MANUALLY ENCODED IN CREX

| D 07 089 |  | Sequence for representation of synoptic reports from a fixed land station suitable for SYNOP data manually encoded in CREX |
| --- | --- | --- |
|  | D 07 087 | “Instantaneous” parameters of sequence D07089 |
|  | D 07 088 | “Period” parameters of sequence D07089 |

Notes:

- “Instantaneous” parameter is a parameter that is not coupled to a time period descriptor, e.g. B04024.

- “Period” parameter is a parameter that is coupled to a time period descriptor, e.g. B04024.

This CREX template for synoptic reports from fixed land stations further expands as follows:

| D 07 087 |  |  | “Instantaneous” parameters of sequence D07089 |  |
| --- | --- | --- | --- | --- |
|  |  |  | Surface station identification, time, horizontal and vertical coordinates | in CREX |
|  | D 01 001 | B 01 001 | WMO block number II | Numeric, 0, 2 |
|  |  | B 01 002 | WMO station number iii | Numeric, 0, 3 |
|  | B 02 001 |  | Type of station (ix) | Code table, 0, 1 |
|  | D 01 011 | B 04 001 | Year | Year, 0, 4 |
|  |  | B 04 002 | Month | Month, 0, 2 |
|  |  | B 04 003 | Day YY | Day, 0, 2 |
|  | D 01 012 | B 04 004 | Hour GG | Hour, 0, 2 |
|  |  | B 04 005 | Minute gg | Minute, 0, 2 |
|  | D 01 023 | B 05 002 | Latitude (course accuracy) | Degree, 2, 4 |
|  |  | B 06 002 | Longitude (course accuracy) | Degree, 2, 5 |
|  | B 07 030 |  | Height of station ground above msl | m, 1, 5 |
|  | B 07 031 |  | Height of barometer above msl | m, 1, 5 |
|  |  |  | Pressure data |  |
|  | D 02 001 | B 10 004 | Pressure PoPoPoPo | Pa, –1, 5 |
|  |  | B 10 051 | Pressure reduced to mean sea level PPPP | Pa, –1, 5 |
|  |  | B 10 061 | 3-hour pressure change ppp | Pa, –1, 4 |
|  |  | B 10 063 | Characteristic of pressure tendency a | Code table, 0, 2 |
|  | B 10 062 |  | 24-hour pressure change p24p24p24 | Pa, –1, 4 |
|  | B 07 004 |  | Pressure (standard level) a3 = 925, 850, 700, ..hPa = missing for lowland stations | Pa, –1, 5 |
|  | B 10 009 |  | Geopotential height of the standard level hhh = missing for lowland stations | gpm, 0, 5 |
|  |  |  | Temperature and humidity |  |
|  | B 07 032 |  | Height of sensor above local ground (for temperature measurement) | m, 2, 5 |
|  | B 12 101 |  | Temperature/dry-bulb temperature (sc. 2) snTTT | °C, 2, 4 |
|  | B 12 103 |  | Dew-point temperature (sc. 2) snTdTdTd | °C, 2, 4 |
|  | B 13 003 |  | Relative humidity | %, 0, 3 |
|  | B 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2, 5 |
|  |  |  | Visibility |  |
|  | B 20 001 |  | Horizontal visibility VV | m, –1, 4 |
|  |  |  | Cloud data |  |
|  | D 02 004 | B 20 010 | Cloud cover (total) N If N = 9, then B 20 010 = 113 %, if N = /, then B 20 010 = missing. | %, 0, 3 |
|  |  | B 08 002 | Vertical significance if CL are observed, then B 08 002 = 7 (low cloud), if CL are not observed and CM are observed, then B 08 002 = 8 (middle cloud), if only CH are observed, B 08 002 = 0, if N = 9, then B 08 002 = 5, if N = 0, then B 08 002 = 62, if N = /, then B 08 002 = missing. | Code table, 0, 2 |
|  |  | B 20 011 | Cloud amount (of low or middle clouds) Nh If N = 0, then B 20 011 = 0, if N = 9, then B 20 011 = 9, if N = /, then B 20 011 = missing. | Code table, 0, 2 |
|  |  | B 20 013 | Height of base of cloud h If N = 0 or /, then B 20 013 = missing. | m, –1, 4 |
|  |  | B 20 012 | Cloud type (low clouds) CL B 20 012 = CL + 30, if N = 0, then B 20 012 = 30, if N = 9 or /, then B 20 012 = 62. | Code table, 0, 2 |
|  |  | B 20 012 | Cloud type (middle clouds) CM B 20 012 = CM + 20, if N = 0, then B 20 012 = 20, if N = 9 or / or CM = /, then B 20 012 = 61. | Code table, 0, 2 |
|  |  | B 20 012 | Cloud type (high clouds) CH 0 20 012 = CH + 10, if N = 0, then B 20 012 = 10, if N = 9 or / or CH = /, then B 20 012 = 60. | Code table, 0, 2 |
|  | R 01 000 |  | Delayed replication of the next 1 descriptor |  |
|  | D 02 005 | B 08 002 | Vertical significance In any Cb layer, B 08 002 = 4 , else: in the first replication: if N = 9, then B 08 002 = 5, if N = /, then B 08 002 = missing, else B 08 002 = 1; in the other replications B 08 002 = 2, 3, 4. | Code table, 0, 2 |
|  |  | B 20 011 | Cloud amount Ns In the first replication: If N = /, then B 20 011 = missing, else B 20 011 = Ns; in the other replications B 20 011 = Ns. | Code table, 0, 2 |
|  |  | B 20 012 | Cloud type C if N = 9 or /, then B 20 012 = missing, else B 20 012 = C. | Code table, 0, 2 |
|  |  | B 20 013 | Height of base of cloud hshs | m, -1, 4 |
| D 07 088 |  |  | “Period” parameters of sequence D 07 089 |  |
|  |  |  | Present and past weather |  |
|  | B 20 003 |  | Present weather ww | Code table, 0, 3 |
|  | B 04 024 |  | Time period At 00, 06, 12, 18 UTC = - 6. At 03, 09,15, 21 UTC = - 3. | Hour, 0, 4 |
|  | B 20 004 |  | Past weather (1) W1 | Code table, 0, 2 |
|  | B 20 005 |  | Past weather (2) W2 | Code table, 0, 2 |
|  |  |  | Evaporation |  |
|  | B 04 024 |  | Time period in hours = - 24 | Hour, 0, 4 |
|  | B 02 004 |  | Type of instrument for evaporation or iE crop type for evapotranspiration | Code table, 0, 2 |
|  | B 13 033 |  | Evaporation /evapotranspiration EEE | kg m-2, 1, 4 |
|  |  |  | Sunshine |  |
|  | R 02 002 |  | Replicate next 2 descriptors 2 times |  |
|  | B 04 024 |  | Time period in hours In the first replication = - 24, in the second replication = - 1. | Hour, 0, 4 |
|  | B 14 031 |  | Total sunshine in minutes In the first replication SSS in the second replication SS | Minute, 0, 4 |
|  |  |  | Precipitation |  |
|  | R 02 002 |  | Replicate next 2 descriptors 2 times |  |
|  | B 04 024 |  | Time period in hours tR | Hour, 0, 4 |
|  | B 13 011 |  | Total precipitation RRR no precipitation = 0 trace = - 0.1 | kg m-2, 1, 5 Encoded as: -00001 |
|  |  |  | Extreme temperatures |  |
|  | B 07 032 |  | Height of sensor above local ground (for temperature measurement) | m, 2, 5 |
|  | B 04 024 |  | Time period in hours = - 12 | Hour, 0, 4 |
|  | B 12 111 |  | Maximum temperature at height and over period specified snTxTxTx | °C, 2, 4 |
|  | B 04 024 |  | Time period in hours = - 12 | Hour, 0, 4 |
|  | B 12 112 |  | Minimum temperature at height and over period specified snTnTnTn | °C, 2, 4 |
|  |  |  | Wind data |  |
|  | B 07 032 |  | Height of sensor above local ground (for wind measurement) | m, 2, 5 |
|  | B 02 002 |  | Type for instrumentation for wind measurement iw | Flag table, 0, 2 |
|  | B 08 021 |  | Time significance = 2 (time averaged) | Code table, 0, 2 |
|  | B 04 025 |  | Time period = - 10 (or number of minutes after a significant change of wind, if any) | Minute, 0, 4 |
|  | B 11 001 |  | Wind direction dd If dd = 00 (calm) or dd = 99 (variable), B 11 001 = 0. | Degree true, 0, 3 |
|  | B 11 002 |  | Wind speed ff | m s-1, 1, 4 |
|  | B 08 021 |  | Time significance (set to missing to cancel the previous value) | Code table, 0, 2 |

Notes:

- CREX Edition 1 is recommended for manual encoding of data.

- If the addition of another “instantaneous” parameter is required, the sequence descriptor D07089 shall be replaced by D07087 D07088, and the B-descriptor for this parameter shall be placed between D07087 and D07088.

- If the addition of another “period” parameter is required, the sequence D 07 089 shall be supplemented by the relevant B-descriptor provided no additional “instantaneous” parameter is needed.

Example

CREX++

T000103 A000 D07089++

63 894 1 2006 02 22 06 00 -0687 03920 00552 00564 10062 10122 //// // 0000 ///// ///// 00125  2900 2320 071 ///// 2500 038 07 03 0073 31 20 10 0001 01 03 08 0073 005 -0006 00 00 -0024 01 0085 -0024 0690 -0001 0060 -0024 00000 //// ///// 00125 //// //// -0012 2210 01000 14 02 -0010 060 0025 //++
7777

Example with optional check digits:

CREX++

T000103 A000 D07089 E++

063 1894 21 32006 402 522 606 700 8-0687 903920 000552 100564 210062 310122 4//// 5// 60000 7///// 8///// 900125 02900 12320 2071 3///// 42500 5038 607 703 80073 931 020 110 20001 301 403 508 60073 7005 8-0006 900 000 1-0024 201 30085 4-0024 50690

6-0001 70060 8-0024 900000 0//// 1///// 200125 3//// 4////  5-0012 62210 701000 814 902

0-0010 1060 20025 3//++
7777

NEW PROPOSED METAR/SPECI AND TAF TEMPLATES

Proposal for modification of B-descriptors for representation of visibility

Newly proposed B-descriptors for prevailing and minimum horizontal visibility with a Note to be added under Class 20:

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 20 060 | Prevailing horizontal visibility (5) | m | -1 | 0 | 10 | m | -1 | 4 |
| 0 20 059 | Minimum horizontal visibility | m | -1 | 0 | 9 | m | -1 | 3 |

- A prevailing visibility value of 10000 m before scaling (after scaling 1000) shall be used to report prevailing visibility 10 km or more.

Unambiguous conversion from TDCF data to TAC data

Unambiguous conversion from TDCF data to TAC data is requested by ICAO as well as by many end users, it is proposed to add two notes under the BUFR Table D, Category 7:

Notes:

- Within 3 07 045, 3 07 048 and 3 07 053, wind speed shall be reported in the same units as in the original TAC data  and:

0 11 083 shall be set to missing, if wind speed is reported in knots or m s-1 in TAC data,

0 11 084 shall be set to missing, if wind speed is reported in km h-1 or m s-1 in TAC data.

- Within 3 07 045, 3 07 048 and 3 07 053, maximum wind speed (gusts) shall be reported in the same units as in the original TAC data and:

0 11 085 shall be set to missing, if maximum wind speed is reported in knots or m s-1 in

TAC data,

0 11 086 shall be set to missing, if maximum wind speed is reported in km h-1 or m s-1 in

TAC data.

Following the Notes (x) an (y), the wind speed (and the maximum wind speed) will be reported only in meters per second in the BUFR message if these parameters are reported in meters per second in the original TAC data.

Below are the METAR/SPECI/TAF templates and BUFR/CREX B and D descriptors with the proposed modifications, corrections and additions written in blue.  It should replace the current file in the WMO Server.

Proposed additions to BUFR Table D

| F X Y | Reference | Element/Sequence name | METAR/SPECI/TAF Representation |
| --- | --- | --- | --- |
|  |  | (Main part of METAR/SPECI), replacing 3 07 011 |  |
| 3 07 045 | 0 01 063 | ICAO location indicator | CCCC |
|  | 0 08 079 | Aviation product status (routine, special, corrected, not available) | METAR SPECI COR |
|  | 0 02 001 | Type of station | (AUTO) |
|  | 3 01 011 | Year, month, day | YY |
|  | 3 01 012 | Hour, minute | GGgg |
|  | 3 01 023 | Latitude-longitude (coarse accuracy) |  |
|  | 0 07 030 | Height of station ground above mean sea level |  |
|  | 0 07 031 | Height of barometer above mean sea level |  |
|  | 0 07 032 | Height of sensor above local ground = 10m (if the actual value is not available) |  |
|  | 0 11 001 | Wind direction | ddd |
|  | 0 11 016 | Extreme counterclockwise wind direction of a variable wind | dndndn |
|  | 0 11 017 | Extreme clockwise wind direction of a variable wind | dxdxdx |
|  | 0 08 054 | Qualifier for wind speed or wind gusts | P |
|  | 0 11 083 | Wind speed (km/h) (see Note (x)) | ff |
|  | 0 11 084 | Wind speed (knots) (see Note (x)) | ff |
|  | 0 11 002 | Wind speed (m/s) (see Note (x)) | ff |
|  | 0 08 054 | Qualifier for wind speed or wind gusts | P |
|  | 0 11 085 | Maximum wind speed (gusts) (km/h) (see Note (y)) | fmfm |
|  | 0 11 086 | Maximum wind speed (gusts) (knots) (see Note (y)) | fmfm |
|  | 0 11 041 | Maximum wind speed (gusts) (m/s) (see Note (y)) | fmfm |
|  | 0 08 054 | Qualifier for wind speed or wind gusts = missing (to cancel the previous value) |  |
|  | 0 07 032 | Height of sensor above local ground = 2m (if the actual value is not available) |  |
|  | 0 12 023 | Temperature (Celsius) | T´T´ |
|  | 0 12 024 | Dew point (Celsius) | T´dT´d |
|  | 0 07 032 | Height of sensor above local ground = missing (to cancel the previous value) |  |
|  | 0 10 052 | Altimeter setting (QNH) | QPHPHPHPH |
|  | 0 20 009 | General Weather Indicator TAF/METAR | CAVOK |
|  |  | (METAR/SPECI visibility) |  |
| 3 07 046 | 0 20 060 | Prevailing visibility | VVVV or VVVVNDV |
|  | 1 02 000 | Delayed replication of two descriptors |  |
|  | 0 31 001 | Number of replication (up to 2) |  |
|  | 0 05 021 | Bearing or azimuth (direction of minimum visibility observed) | Dv |
|  | 0 20 059 | Minimum visibility | VNVNVNVN |
|  |  | (METAR/SPECI/TAF clouds), replacing 3 07 015 |  |
| 3 07 047 | 1 05 000 | Delayed replication of 5 descriptor |  |
|  | 0 31 001 | Number of replications |  |
|  | 0 08 002 | Vertical significance |  |
|  | 0 20 011 | Cloud amount | NsNsNs |
|  | 0 20 012 | Cloud type | CC |
|  | 0 20 013 | Height of base of cloud (m) | hshshs |
|  | 0 20 092 | Height of base of cloud (feet) | hshshs |
|  | 0 20 002 | Vertical visibility (m) | VVhshshs |
|  | 0 20 091 | Vertical visibility (feet) | VVhshshs |
|  |  | (Trend type forecast), replacing 3 07 018 |  |
| 3 07 048 | 0 08 016 | Change qualifier for trend type forecast | TTTTT NOSIG |
|  | 1 02 000 | Delayed replication of two descriptors |  |
|  | 0 31 001 | Number of replications (0, 1 or 2) |  |
|  | 0 08 017 | Qualifier for time of forecast change | TT |
|  | 3 01 012 | Time of change | GGgg |
|  | 1 12 000 | Delayed replication of twelve descriptors |  |
|  | 0 31 000 | Short delayed replication count (0 or 1) |  |
|  | 0 07 032 | Height of sensor above local ground = 10m (if the actual value is not available) |  |
|  | 0 11 001 | Wind direction | ddd |
|  | 0 08 054 | Qualifier for wind speed or wind gusts | P |
|  | 0 11 083 | Wind speed (km/h) (see Note (x)) | ff |
|  | 0 11 084 | Wind speed (knots) (see Note (x)) | ff |
|  | 0 11 002 | Wind speed (m/s) (see Note (x)) | ff |
|  | 0 08 054 | Qualifier for wind speed or wind gusts | P |
|  | 0 11 085 | Maximum wind speed (gusts) (km/h) (see Note (y)) | fmfm |
|  | 0 11 086 | Maximum wind speed (gusts) (knots) (see Note (y)) | fmfm |
|  | 0 11 041 | Maximum wind speed (gusts) (m/s) (see Note (y)) | fmfm |
|  | 0 08 054 | Qualifier for wind speed or wind gusts = missing (to cancel the previous value) |  |
|  | 0 07 032 | Height of sensor above local ground = missing (to cancel the previous value) |  |
|  | 0 20 009 | General weather indicator | CAVOK NSW NSC |
|  | 1 01 000 | Delayed replication of one descriptor |  |
|  | 0 31 000 | Short delayed replication count (0 or 1) |  |
|  | 0 20 060 | Prevailing visibility | VVVV |
|  | 3 07 014 | Weather intensity and phenomena | w’w’ |
|  | 3 07 047 | METAR/SPECI/TAF clouds | NsNsNshshshs |
|  |  | (Sea conditions WTsTs/SS’) |  |
| 3 07 049 | 1 02 000 | Delayed replication of 2 descriptors |  |
|  | 0 31 000 | Short delayed replication factor (0 or 1) |  |
|  | 0 22 043 | Sea/water temperature | TsTs |
|  | 0 22 021 | Height of waves | S’ |
|  |  | (Runway state RRRRERERCReReRBRBR) |  |
| 3 07 050 | 1 01 000 | Delayed replication of one descriptor |  |
|  | 0 31 000 | Short delayed replication factor (0 or 1) |  |
|  | 0 20 085 | General condition of runway | SNOCLO |
|  | 1 02 000 | Delayed replication of two descriptors |  |
|  | 0 31 001 | Number of replications |  |
|  | 0 01 064 | Runway designator | DRDR |
|  | 0 20 085 | General condition of runway | CLRD// |
|  | 1 05 000 | Delayed replication of 5 descriptors |  |
|  | 0 31 001 | Number of replications |  |
|  | 0 01 064 | Runway designator | DRDR |
|  | 0 20 086 | Runway deposits | ER |
|  | 0 20 087 | Runway contamination | CR |
|  | 0 20 088 | Depth of runway deposits | eReR |
|  | 0 20 089 | Runway friction coefficient | BRBR |
|  |  | (Full METAR/SPECI), replacing 3 07 021 |  |
| 3 07 051 | 3 07 045 | Main part of METAR/SPECI data |  |
|  | 3 07 046 | Visibility | VVVV or VVVVNDV VNVNVNVNDv |
|  | 3 07 013 | Runway visual range | RDRDR/VRVRVRVR |
|  | 3 07 014 | Weather intensity and phenomena | w’w’ |
|  | 3 07 047 | Clouds | NsNsNshshshs |
|  | 3 07 016 | Recent weather phenomena | REw’w’ |
|  | 3 07 017 | Runway shear | WS RDRDR |
|  | 3 07 049 | Sea conditions | WTsTs/SS’ |
|  | 3 07 050 | Runway state | RDRDR ERCReReRBRBR |
|  | 1 01 000 | Delayed replication of one descriptor |  |
|  | 0 31 001 | Replication count (0 to 3 normally) |  |
|  | 3 07 048 | Trend type forecast |  |
|  |  | (Aerodrome forecast identification and time interval) |  |
| 3 07 052 | 0 01 063 | ICAO location identifier | CCCC |
|  | 0 08 039 | Time significance = 0 (Issue time of forecast) |  |
|  | 3 01 011 | Year, Month, Day | YY |
|  | 3 01 012 | Hour, Minute | GGgg |
|  | 0 08 079 | Aviation product status | COR CNL AMD NIL |
|  | 0 08 039 | Time significance = 1 (Time of commencement of period of the forecast) |  |
|  | 3 01 011 | Year, Month, Day | Y1Y1 |
|  | 3 01 012 | Hour, Minute | G1G1 |
|  | 0 08 039 | Time significance = 2 (Time of ending of period of the forecast) |  |
|  | 3 01 011 | Year, Month, Day | Y2Y2 |
|  | 3 01 012 | Hour, Minute | G2G2 |
|  | 3 01 023 | Latitude-longitude (coarse accuracy) |  |
|  | 0 07 030 | Height of station ground above mean sea level |  |
|  | 0 07 031 | Height of barometer above mean sea level |  |
|  |  | (Forecast weather at an aerodrome) |  |
| 3 07 053 | 0 07 032 | Height of sensor above local ground = 10m (if the actual value is not available) |  |
|  | 0 11 001 | Wind direction | ddd |
|  | 0 08 054 | Qualifier for wind speed or wind gusts | P |
|  | 0 11 083 | Wind speed (km/h) (see Note (x)) | ff |
|  | 0 11 084 | Wind speed (knots) (see Note (x)) | ff |
|  | 0 11 002 | Wind speed (m/s) (see Note (x)) | ff |
|  | 0 08 054 | Qualifier for wind speed or wind gusts | P |
|  | 0 11 085 | Maximum wind speed (gusts) (km/h) (see Note (y)) | fmfm |
|  | 0 11 086 | Maximum wind speed (gusts) (knots) (see Note (y)) | fmfm |
|  | 0 11 041 | Maximum wind speed (gusts) (m/s) (see Note (y)) | fmfm |
|  | 0 08 054 | Qualifier for wind speed or wind gusts = missing (to cancel the previous value) |  |
|  | 0 07 032 | Height of sensor above local ground = missing (to cancel the previous value) |  |
|  | 0 20 009 | General weather indicator | CAVOK NSW NSC |
|  | 0 20 060 | Prevailing visibility | VVVV |
|  | 3 07 014 | Weather | w’w’ |
|  | 3 07 047 | Cloud layer(s) | NsNsNshshshs |
|  |  | (Forecast of extreme temperatures) |  |
| 3 07 054 | 0 07 032 | Height of sensor above local ground = 2m (if the actual value is not available) |  |
|  | 0 08 039 | Time significance = 3 (Forecast time of maximum temperature) |  |
|  | 0 04 003 | Day |  |
|  | 0 04 004 | Hour | GFGF |
|  | 0 08 023 | First order statistics = 3 (Minimum) |  |
|  | 0 12 023 | Temperature (Celsius) | TFTF |
|  | 0 08 039 | Time significance = 4 (Forecast time of minimum temperature) |  |
|  | 0 04 003 | Day |  |
|  | 0 04 004 | Hour | GFGF |
|  | 0 08 023 | First order statistics = 2 (Maximum) |  |
|  | 0 12 023 | Temperature (Celsius) | TFTF |
|  | 0 08 023 | First order statistics = missing (to cancel the previous value) |  |
|  | 0 07 032 | Height of sensor above local ground = missing (to cancel the previous value) |  |
|  |  | (Change indicator and forecast changes) |  |
| 3 07 055 | 0 33 045 | Probability of following event | C2C2 |
|  | 0 08 016 | Change qualifier for an aerodrome forecast | TTTTTT |
|  | 0 08 039 | Time significance = 5 (Time of beginning of the forecast change) |  |
|  | 0 04 003 | Day |  |
|  | 3 01 012 | Hour, Minute | GGgg |
|  | 0 08 039 | Time significance = 6 (Time of ending of the forecast change) |  |
|  | 0 04 003 | Day |  |
|  | 3 01 012 | Hour, Minute | GeGe |
|  | 3 07 053 | Forecast conditions during or after change |  |
|  |  | (Aerodrome forecast – full TAF) |  |
| 3 07 056 | 3 07 052 | Identification and time interval |  |
|  | 3 07 053 | Forecast |  |
|  | 3 07 054 | Extreme temperatures forecast |  |
|  | 1 01 000 | Delayed replication of one descriptor |  |
|  | 0 31 001 | Replication factor |  |
|  | 3 07 055 | Forecast change |  |

The following notes are proposed to be included under BUFR Table D, Category 7.

Notes:

- Within 3 07 045, 3 07 048 and 3 07 053, wind speed shall be reported in the same units as in the original TAC data  and:

0 11 083 shall be set to missing, if wind speed is reported in knots or m s-1 in TAC data,

0 11 084 shall be set to missing, if wind speed is reported in km h-1 or m s-1 in TAC data.

- Within 3 07 045, 3 07 048 and 3 07 053, maximum wind speed (gusts) shall be reported in the same units as in the original TAC data  and:

0 11 085 shall be set to missing, if maximum wind speed is reported in knots or m s-1 in TAC data,

0 11 086 shall be set to missing, if maximum wind speed is reported in km h-1 or m s-1 in TAC data.

Proposed additions to BUFR/CREX table B.

| Table reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | Unit | Scale | Reference | Width | Unit | Scale | Width |
| 0 08 039 | Time significance (Aviation forecast) | Code table | 0 | 0 | 6 | Code table | 0 | 2 |
| 0 08 054 | Qualifier for wind speed or wind gusts | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 11 083 | Wind speed | km h-1 | 0 | 0 | 9 | km h-1 | 0 | 3 |
| 0 11 084 | Wind speed | knot | 0 | 0 | 8 | knot | 0 | 3 |
| 0 11 085 | Maximum wind gust speed | km h-1 | 0 | 0 | 9 | km h-1 | 0 | 3 |
| 0 11 086 | Maximum wind gust speed | knot | 0 | 0 | 8 | knot | 0 | 3 |
| 0 12 023 | Temperature | Celsius | 0 | -99 | 8 | Celsius | 0 | 2 |
| 0 12 024 | Dew point temperature | Celsius | 0 | -99 | 8 | Celsius | 0 | 2 |
| 0 20 059 | Minimum horizontal visibility | m | -1 | 0 | 9 | m | -1 | 3 |
| 0 20 060 | Prevailing horizontal visibility (5) | m | -1 | 0 | 10 | m | -1 | 4 |
| 0 20 085 | General condition of runway | Code table | 0 | 0 | 4 | Code table | 0 | 1 |
| 0 20 086 | Runway deposits | Code table | 0 | 0 | 4 | Code table | 0 | 1 |
| 0 20 087 | Runway contamination | Code table | 0 | 0 | 4 | Code table | 0 | 1 |
| 0 20 088 | Depth of runway deposits | m | 3 | 0 | 12 | m | 0 | 4 |
| 0 20 089 | Runway friction coefficient | Code table | 0 | 0 | 7 | Code table | 0 | 2 |
| 0 20 092 | Height of base of cloud | Foot | -2 | 0 | 10 | Foot | -2 | 3 |
| 0 20 091 | Vertical visibility | Foot | -2 | 0 | 10 | Foot | -2 | 3 |

The following Note (5) is proposed to be included under Class 20:

- A prevailing visibility value of 10000 m before scaling (after scaling 1000) shall be used to report prevailing visibility 10 km or more.

Proposed additions to BUFR Code/Flag tables

| 0 08 039 |
| --- |
| Time significance (Aviation forecast) |
| Code figure |  |
| 0 | Issue time of forecast |
| 1 | Time of commencement of period of the forecast |
| 2 | Time of ending of period of the forecast |
| 3 | Forecast time of maximum temperature |
| 4 | Forecast time of minimum temperature |
| 5 | Time of beginning of the forecast change |
| 6 | Time of ending of the forecast change |
| 7…62 | Reserved |
| 63 | Missing |
| 0 08 054 |
| Qualification of wind speed or wind gusts |
| 0 | Wind speed or gust is as reported |
| 1 | Wind speed is greater than that reported (P in METAR/TAF/SPECI) |
| 2-6 | Reserved |
| 7 | Missing |
| 0 20 085 |
| General condition of runway |
| 0 | Cleared (CLRD//) |
| 1 | All runways closed (SNOCLO) |
| 2-14 | Reserved |
| 15 | Missing |

| 0 20 086 |
| --- |
| Runway deposits |
| Code figure |  |
| 0 | Clear and dry |
| 1 | Damp |
| 2 | Wet with water patches |
| 3 | Rime and frost covered (depth normally less than 1 mm) |
| 4 | Dry snow |
| 5 | Wet snow |
| 6 | Slush |
| 7 | Ice |
| 8 | Compacted or rolled snow |
| 9 | Frozen ruts or ridges |
| 10-14 | Reserved |
| 15 | Missing or not reported (e.g. due to runway clearance in progress) |

| 0 20 087 |
| --- |
| Runway contamination |
| Code figure |  |
| 0 | Reserved |
| 1 | Less than 10% of runway covered |
| 2 | 11% to 25% of runway covered |
| 3-4 | Reserved |
| 5 | 25% to 50% of runway covered |
| 6-8 | Reserved |
| 9 | 51% to 100% of runway covered |
| 10-14 | Reserved |
| 15 | Missing or not reported (e.g. due to runway clearance in progress) |

| 0 20 089 |
| --- |
| Runway friction coefficient |
| 0 | 0.00 |
| 1 | 0.01 |
| 2…88 | 0.02…0.88 |
| 89 | 0.89 |
| 90 | 0.90 |
| 91 | Braking action poor |
| 92 | Braking action medium to poor |
| 93 | Braking action medium |
| 94 | Braking action medium to good |
| 95 | Braking action good |
| 96-98 | Reserved |
| 99 | Unreliable |
| 100-126 | Reserved |
| 127 | Missing, not reported and/or runway not operational. |

Proposed additions to BUFR Code table 0 08 079

| 0 08 079 |
| --- |
| Aviation product status |
| Code figure |  |
| 0 | Normal issue |
| 1 | Correction to a previously issued product (COR) |
| 2 | Amendment to a previously issued product (AMD) |
| 3 | Correction to a previously issued amended product (COR AMD) |
| 4 | Cancellation of a previously issued product (CNL) |
| 5 | No product available (NIL) |
| 6 | Special report (SPECI) |
| 7 | Corrected special report (SPECI COR) |
| 8…14 | Reserved |
| 15 | Missing or not applicable |

FOR SBUV/2 OZONE DATA

New Table D sequence

|  |  | (Ozone data) |
| --- | --- | --- |
| 3 10 019 | 0 01 007 | Satellite identifier |
|  | 0 02 019 | Satellite instruments (“624” = SBUV/2) |
|  | 3 01 011 | Date |
|  | 3 01 013 | Time |
|  | 3 01 023 | Lat/Long |
|  | 0 07 025 | Solar zenith angle |
|  | 0 08 021 | Time significance (“28” = Start of scan) |
|  | 0 07 025 | Solar zenith angle |
|  | 0 08 021 | Time significance (“29” = End of scan) |
|  | 0 07 025 | Solar zenith angle |
|  | 0 08 021 | Time significance (“Missing” = Cancel) |
|  | 0 08 029 | Remotely-sensed surface type |
|  | 0 05 040 | Orbit number |
|  | 0 08 075 | Ascending/descending orbit qualifier |
|  | 0 08 003 | Vertical significance (“0” = Surface) |
|  | 0 10 004 | Pressure (terrain) |
|  | 0 08 003 | Vertical significance (“Missing” = Cancel) |
|  | 2 07 002 | Increase scale, reference value and data width |
|  | 0 15 001 | Total ozone |
|  | 2 07 000 | Cancel increase scale, reference value and data width |
|  | 0 33 070 | Total ozone quality |
|  | 0 15 030 | Aerosol contamination index |
|  | 2 07 002 | Increase scale, reference value and data width |
|  | 0 20 081 | Cloud amount in segment (cloud fraction) |
|  | 2 07 000 | Cancel increase scale, reference value and data width |
|  | 0 08 003 | Vertical significance (“2” = Cloud top) |
|  | 0 33 042 | Type of limit represented by following value (“0” = Exclusive lower limit) |
|  | 0 07 004 | Pressure |
|  | 2 07 002 | Increase scale, reference value and data width |
|  | 0 15 001 | Total ozone (below cloud top pressure) |
|  | 2 07 000 | Cancel increase scale, reference value and data width |
|  | 0 08 003 | Vertical significance (“Missing” = Cancel) |
|  | 1 13 021 | Repeat next 13 descriptors 21 times |
|  | 0 07 004 | Pressure (at bottom of layer) |
|  | 0 07 004 | Pressure (at top of layer) |
|  | 2 07 002 | Increase scale, reference value and data width |
|  | 0 08 021 | Time significance (“27” = First guess) |
|  | 0 15 005 | Ozone p |
|  | 0 08 021 | Time significance (“Missing” = Cancel) |
|  | 0 15 005 | Ozone p |
|  | 0 33 007 | % confidence |
|  | 2 07 000 | Cancel increase scale, reference value and data width |
|  | 0 08 026 | Matrix significance (“4” = Row of averaging kernel matrix) |
|  | 1 01 020 | Repeat next descriptor 20 times |
|  | 0 25 143 | Linear coefficient |
|  | 0 08 026 | Matrix significance (“Missing” = Cancel) |
|  | 0 08 043 | Atmospheric chemical type (“0” = Ozone) |
|  | 1 09 015 | Repeat next 9 descriptors 15 times |
|  | 0 07 004 | Pressure |
|  | 0 08 090 | Decimal scale of following Table B values |
|  | 2 07 006 | Increase scale, reference value and data width |
|  | 0 15 008 | Scaled mixing ratio (volumetric) |
|  | 2 07 000 | Cancel increase scale, reference value and data width |
|  | 0 08 090 | Decimal scale of following Table B values (“Missing” = Cancel) |
|  | 2 07 002 | Increase scale, reference value and data width |
|  | 0 33 007 | % confidence |
|  | 2 07 000 | Cancel increase scale, reference value and data width |
|  | 0 08 043 | Atmospheric chemical type (“Missing” = Cancel) |
|  | 0 33 071 | Profile ozone quality |
|  | 1 08 008 | Repeat next 8 descriptors 8 times |
|  | 2 02 124 | Change scale |
|  | 2 01 107 | Change data width |
|  | 0 02 071 | Spectrographic wavelength |
|  | 2 01 000 | Cancel change data width |
|  | 2 02 000 | Cancel change scale |
|  | 2 07 002 | Increase scale, reference value and data width |
|  | 0 20 081 | Cloud amount in segment (cloud fraction) |
|  | 2 07 000 | Cancel increase scale, reference value and data width |

New Table B descriptors

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | Unit | Scale | Ref. value | Data width | Unit | Scale | Data width |
| 0 15 030 | Aerosol contamination index (see Note 6) | Numeric | 2 | -1000 | 12 | Numeric | 2 | 4 |
| 0 33 070 | Total ozone quality | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 33 071 | Profile ozone quality | Code table | 0 | 0 | 4 | Code table | 0 | 2 |

# BUFR Code Tables for SBUV/2 Data:

0-33-070	Total ozone quality

| 0 | Good retrieval |
| --- | --- |
| 1 | Bad aerosol information flag or NOAA-16 radiance anomaly |
| 2 | Solar zenith angle greater than 84 degrees |
| 3 | 380nm residue greater than limit |
| 4 | Ozone inconsistency |
| 5 | Difference between profile ozone and step 3 total ozone exceeds threshold (set to 25 DU) |
| 6 | Step 1 ozone iteration did not converge |
| 7 | Any channel residue greater than 16 or bad radiance |
| 8-14 | Reserved |
| 15 | Missing |

0-33-071 	Profile ozone quality

| 0 | Good retrieval |
| --- | --- |
| 1 | Solar zenith angle greater than 84 degrees |
| 2 | Difference between step 3 and profile total ozone greater than limit (25 DU) |
| 3 | Average final residue for wavelengths used in retrieval greater than threshold |
| 4 | Final residue greater than 3 times a priori error |
| 5 | Difference between retrieved and a priori greater than 3 times a priori error |
| 6 | Non-convergent solution |
| 7 | Upper level profile anomaly or stray light anomaly |
| 8 | Initial residue greater than 18.0 N-value units |
| 9-14 | Reserved |
| 15 | Missing |

Add the following note to BUFR/CREX Class 15:

- For this descriptor, numbers less than -1 indicate a predominance of scattering aerosols, increasing in concentration as the number becomes more negative.  Numbers greater than +1 indicate a predominance of absorptive aerosols, increasing in concentration as the number becomes more positive.  Numbers between -1 and +1 indicate clouds or noise.

Add the following entries to the existing code table for

0-08-029 	Remotely-sensed surface type

| 4 | Low inland (below sea level) |
| --- | --- |
| 5 | Mix of land and water |
| 6 | Mix of land and low inland |
| 7-254 | Reserved |

FOR SATELLITE DATA EXCHANGES

Addition of the following entries to Common Code Table C-13:

Category 003 - Vertical soundings (satellite)

Please add:

002 - ATOVS

003 - AMSU-A

004 - AMSU-B

005 - HIRS

006 - MHS

007 - IASI

Category 012 - Surface data (satellite)

Please add

007 - ASCAT

The acronyms have the following meanings:

ATOVS = Advanced TIROS Operational Vertical Sounder (TIROS = Television and Infrared Observation Satellite)

AMSU-A = Advanced Microwave Sounding Unit-A

AMSU-B = Advanced Microwave Sounding Unit-B

HIRS = High Resolution Infrared Radiation Sounder

MHS = Microwave Humidity Sounder

IASI = Infrared Atmospheric Sounding Interferometer

ASCAT = Advanced Wind Scatterometer

MODIFIED DESCRIPTORS FOR REPRESENTATION OF RADIATION DATA

The modified descriptors for representation of radiation data and Notes (1) and (2) under Class 14 are proposed to be introduced in Version 14 of WMO FM 94 BUFR tables.

- Insufficient range of values

It is proposed to modify data widths and reference values of descriptors for representation of radiation data to become:

| Table reference | Element name | Unit | Scale | Refer. value | Data width | kJ m-2 | J cm-2 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | max upward | max downward | max upward | max downward |
| 0 14 001 | Long-wave radiation, integrated over 24 hours | J m-2 | –3 | –65536 | 17 | -65536 | 65534 | -6553.6 | 6553.4 |
| 0 14 002 | Long-wave radiation, integrated over period specified | J m-2 | –3 | –65536 | 17 | -65536 | 65534 | -6553.6 | 6553.4 |
| 0 14 003 | Short-wave radiation, integrated over 24 hours | J m-2 | –3 | –65536 | 17 | -65536 | 65534 | -6553.6 | 6553.4 |
| 0 14 004 | Short-wave radiation, integrated over period specified | J m-2 | –3 | –65536 | 17 | -65536 | 65534 | -6553.6 | 6553.4 |
| 0 14 011 | Net long-wave radiation, integrated over 24 hours | J m-2 | –3 | –65536 | 17 | -65536 | 65534 | -6553.6 | 6553.4 |
| 0 14 012 | Net long-wave radiation, integrated over period specified | J m-2 | –3 | –65536 | 17 | -65536 | 65534 | -6553.6 | 6553.4 |
| 0 14 013 | Net short-wave radiation, integrated over 24 hours | J m-2 | –3 | –65536 | 17 | -65536 | 65534 | -6553.6 | 6553.4 |
| 0 14 014 | Net short-wave radiation, integrated over period specified | J m-2 | –3 | –65536 | 17 | -65536 | 65534 | -6553.6 | 6553.4 |
|  |  |  |  |  |  | min | max | min | max |
| 0 14 028 | Global solar radiation (high accuracy), integrated over period specified | J m-2 | -2 | 0 | 20 | 0 | 104857.4 | 0 | 10485.74 |
| 0 14 029 | Diffuse solar radiation (high accuracy), integrated over period specified | J m-2 | -2 | 0 | 20 | 0 | 104857.4 | 0 | 10485.74 |
| 0 14 030 | Direct solar radiation (high accuracy), integrated over period specified | J m-2 | -2 | 0 | 20 | 0 | 104857.4 | 0 | 10485.74 |

b)  	Sign of downward and upward radiation

It is proposed to modify the Notes (1) and (2) under Class 14 to read:

- Downward radiation shall be assigned positive values.

- Upward radiation shall be assigned negative values.

c)  	Correction of 0 14 017 and 0 14 018

The existing descriptors 0 14 017 and 014 018 are proposed to be modified in Version 14 of WMO FM 94 BUFR tables to read:

| Table reference | Element name | Unit | Scale | Reference value | Data width |
| --- | --- | --- | --- | --- | --- |
| 0 14 017 | Instantaneous long-wave radiation | W m-2 | 0 | -512 | 10 |
| 0 14 018 | Instantaneous short-wave radiation | W m-2 | 0 | -2048 | 12 |

NATIONAL AND WMO STATION IDENTIFICATION AND THE AWS BUFR TEMPLATES

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 01 101 | State identifier | Code table | 0 | 0 | 10 | Code table | 0 | 3 |
| 0 01 102 | National station number | Numeric | 0 | 0 | 30 | Numeric | 0 | 9 |

| Table reference | Table reference | Element name |
| --- | --- | --- |
| 3 01 089 |  | National station identification |
|  | 0 01 101 | State identifier |
|  | 0 01 102 | National station number |

| Table reference | Element name |
| --- | --- |
| 3 07 091 | BUFR template for surface observations from one-hour period with national and WMO station identification |

Code Table 0 01 101: State identifier

| Code figure |  |
| --- | --- |
| 0-99 | Reserved |
| 100 101 102 103 104 105 106 107 108 109 110 111 112 113 114 115 116 117 118 119 120 121 122 123 124 125 126 127 128 129 130 131 132 133 134 135 136 137 138 139 140 141 142 143 144 145 146 147 148 149 150 151 152 153 154 155 156 -199 | Algeria Angola Benin Botswana Burkina Faso Burundi Cameroon Cape Verde Central African Republic Chad Comoros Congo Cote d'Ivoire Democratic Republic of the Congo Djibouti Egypt Eritrea Ethiopia France (RA I) Gabon Gambia Ghana Guinea Guinea-Bissau Kenya Lesotho Liberia Libyan Arab Jamahiriya Madagascar Malawi Mali Mauritania Mauritius Morocco Mozambique Namibia Niger Nigeria Portugal (RA I) Rwanda Sao Tom and Prince Senegal Seychelles Sierra Leone Somalia South Africa Spain Sudan Swaziland Togo Tunisia Uganda United Kingdom of Great Britain and Northern Ireland (RA I) United Republic of Tanzania Zambia Zimbabwe Reserved for Region I (Africa) |
| 200 201 202 203 204 205 206 207 208 209 210 211 212 213 214 215 216 217 218 219 220 221 222 223 224 225 226 227 228 229 230 231 232 233 234 235 -299 | Afghanistan Bahrain Bangladesh Bhutan Cambodia China Democratic People's Republic of Korea Hong Kong, China India Iran, Islamic Republic of Iraq Japan Kazakhstan Kuwait Kyrgyz Republic Lao People's Democratic Republic Macao, China Maldives Mongolia Myanmar Nepal Oman Pakistan Qatar Republic of Korea Republic of Yemen Russian Federation (RA II) Saudi Arabia Sri Lanka Tajikistan Thailand Turkmenistan United Arab Emirates Uzbekistan Viet Nam, Socialist Republic of Reserved for Region II (Asia) |
| 300 301 302 303 304 305 306 307 308 309 310 311 312 313 -399 | Argentina Bolivia Brazil Chile Colombia Ecuador France Guyana Paraguay Peru Suriname Uruguay Venezuela Reserved for Region III (South America) |
| 400 401 402 403 404 405 406 407 408 409 410 411 412 413 414 415 416 417 418 419 420 421 422 423 424 425 426 - 499 | Antigua and Barbuda Bahamas Barbados Belize British Caribbean Territories Canada Colombia Costa Rica Cuba Dominica Dominican Republic El Salvador France (RA IV) Guatemala Haiti Honduras Jamaica Mexico Netherlands Antilles and Aruba Nicaragua Panama Saint Lucia Trinidad and Tobago United Kingdom of Great Britain and Northern Ireland (RA IV) United States of America (RA IV) Venezuela Reserved for Region IV (North America, Central America and the Caribbean) |
| 500 501 502 503 504 505 506 507 508 509 510 511 512 513 514 515 516 517 518 519 520 521 – 599 | Australia Brunei Darussalam Cook Islands Fiji French Polynesia Indonesia Kiribati Malaysia Micronesia, Federated States of New Caledonia New Zealand Niue Papua New Guinea Philippines Samoa Singapore Solomon Islands Tonga United Kingdom of Great Britain and Northern Ireland (RA V) United States of America (RA V) Vanuatu Reserved for Region V (South-West Pacific) |
| 600 601 602 603 604 605 606 607 608 609 610 611 612 613 614 615 616 617 618 619 620 621 622 623 624 625 626 627 628 629 630 631 632 633 634 635 636 637 638 639 640 641 642 643 644 645 646 647 648 649 650 - 699 | Albania Armenia Austria Azerbaijan Belarus Belgium Bosnia and Herzegovina Bulgaria Croatia Cyprus Czech Republic Denmark Estonia Finland France (RA VI) Georgia Germany Greece Hungary Iceland Ireland Israel Italy Jordan Kazakhstan Latvia Lebanon Lithuania Luxembourg Malta Monaco Montenegro Netherlands Norway Poland Portugal (RA VI) Republic of Moldova Romania Russian Federation (RA VI) Serbia Slovakia Slovenia Spain Sweden Switzerland Syrian Arab Republic The Former Yugoslav Republic of Macedonia Turkey Ukraine United Kingdom of Great Britain and Northern Ireland (RA VI) Reserved for Region VI (Europe) |
| 700 – 999 1000 – 1022 1023 | Reserved Not used Missing value |

BUFR template for surface observations from one-hour period

TM 307091

|  |  |  | Unit, scale |
| --- | --- | --- | --- |
| 3 01 089 |  | National station identification |  |
|  | 0 01 101 | State identifier (1) | Code table, 0 |
|  | 0 01 102 | National station number (1) | Numeric, 0 |
| 3 01 090 |  | Fixed surface station identification; time, horizontal and vertical co-ordinates |  |
|  | 3 01 004 | Surface station identification |  |
|  |  | WMO block number(1) | Numeric, 0 |
|  |  | WMO station number(1) | Numeric, 0 |
|  |  | Station or site name | CCITT IA5, 0 |
|  |  | Type of station | Code table, 0 |
|  | 3 01 011 | Year(2) | Year, 0 |
|  |  | Month(2) | Month, 0 |
|  |  | Day(2) | Day, 0 |
|  | 3 01 012 | Hour(2) | Hour, 0 |
|  |  | Minute(2) | Minute, 0 |
|  | 3 01 021 | Latitude (high accuracy) | Degree, 5 |
|  |  | Longitude (high accuracy) | Degree, 5 |
|  | 0 07 030 | Height of station ground above mean sea level | m, 1 |
|  | 0 07 031 | Height of barometer above mean sea level | m, 1 |
| 0 08 010 |  | Surface qualifier (for temperature data) | Code table, 0 |
| 3 01 091 |  | Surface station instrumentation |  |
|  | 0 02 180 | Main present weather detecting system | Code table, 0 |
|  | 0 02 181 | Supplementary present weather sensor | Flag table, 0 |
|  | 0 02 182 | Visibility measurement system | Code table, 0 |
|  | 0 02 183 | Cloud detection system | Code table, 0 |
|  | 0 02 184 | Type of lightning detection sensor | Code table, 0 |
|  | 0 02 179 | Type of sky condition algorithm | Code table, 0 |
|  | 0 02 186 | Capability to detect precipitation phenomena | Flag table, 0 |
|  | 0 02 187 | Capability to detect other weather phenomena | Flag table, 0 |
|  | 0 02 188 | Capability to detect obscuration | Flag table, 0 |
|  | 0 02 189 | Capability to discriminate lightning strikes | Flag table, 0 |
| 3 02 001 | 0 10 004 | Pressure | Pa, –1 |
|  | 0 10 051 | Pressure reduced to mean sea level | Pa, –1 |
|  | 0 10 061 | 3-hour pressure change(3) | Pa, –1 |
|  | 0 10 063 | Characteristic of pressure tendency(3) | Code table, 0 |
| 0 07 004 |  | Pressure (standard level) | Pa, –1 |
| 0 10 009 |  | Geopotential height of the standard level | gpm, 0 |
| 3 02 072 |  | Temperature and humidity data |  |
|  | 0 07 032 | Height of sensor above local ground | m, 2 |
|  | 0 07 033 | Height of sensor above water surface | m, 1 |
|  | 0 12 101 | Temperature/dry-bulb temperature (scale 2) | K, 2 |
|  | 0 12 103 | Dew-point temperature (scale 2) | K, 2 |
|  | 0 13 003 | Relative humidity | %, 0 |
| 1 03 000 |  | Delayed replication of 3 descriptors |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 1 01 005 |  | Replicate 1 descriptor five times |  |
| 3 07 063 | 0 07 061 | Depth below land surface | m, 2 |
|  | 0 12 130 | Soil temperature (scale 2) | K, 2 |
| 0 07 061 |  | Depth below land surface (set to missing to cancel the previous value) | m, 2 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 069 |  | Visibility data |  |
|  | 0 07 032 | Height of sensor above local ground | m, 2 |
|  | 0 07 033 | Height of sensor above water surface | m, 1 |
|  | 0 33 041 | Attribute of following value | Code table, 0 |
|  | 0 20 001 | Horizontal visibility | m, –1 |
| 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
| 0 07 033 |  | Height of sensor above water surface (set to missing to cancel the previous value) | m, 1 |
| 1 05 000 |  | Delayed replication of 5 descriptors |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 0 20 031 |  | Ice deposit (thickness) | m, 2 |
| 0 20 032 |  | Rate of ice accretion | Code table, 0 |
| 0 02 038 |  | Method of sea surface temperature measurement | Code table, 0 |
| 0 22 043 |  | Sea/water temperature (scale 2) | K, 2 |
| 3 02 021 | 0 22 001 | Direction of waves | Degree true, 0 |
|  | 0 22 011 | Period of waves | s, 0 |
|  | 0 22 021 | Height of waves | m, 1 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 078 |  | State of ground and snow depth measurement |  |
|  | 0 02 176 | Method of state of ground measurement | Code table, 0 |
|  | 0 20 062 | State of ground (with or without snow) | Code table, 0 |
|  | 0 02 177 | Method of snow depth measurement | Code table, 0 |
|  | 0 13 013 | Total snow depth | m, 2 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 073 |  | Cloud data |  |
|  | 0 20 010 | Cloud cover (total) | %, 0 |
|  | 1 05 004 | Replicate 5 descriptors four times |  |
|  | 0 08 002 | Vertical significance | Code table, 0 |
|  | 0 20 011 | Cloud amount | Code table, 0 |
|  | 0 20 012 | Cloud type | Code table, 0 |
|  | 0 33 041 | Attribute of following value | Code table, 0 |
|  | 0 20 013 | Height of base of cloud | m, -1 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 074 |  | Present and past weather |  |
|  | 0 20 003 | Present weather(4) | Code table, 0 |
|  | 0 04 025 | Time period (= - 60 minutes) | Minute, 0 |
|  | 0 20 004 | Past weather (1) (4) | Code table, 0 |
|  | 0 20 005 | Past weather (2) (4) | Code table, 0 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 075 |  | Intensity of precipitation, size of precipitation element |  |
|  | 0 08 021 | Time significance (= 2 (time averaged)) | Code table, 0 |
|  | 0 04 025 | Time period (= - 10 minutes) | Minute, 0 |
|  | 0 13 055 | Intensity of precipitation | Kg m-2 s-1, 4 |
|  | 0 13 058 | Size of precipitation element | m, 4 |
|  | 0 08 021 | Time significance (= missing value) | Code table, 0 |
| 1 02 000 |  | Delayed replication of 2 descriptors |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 0 04 025 |  | Time period (= - 10 minutes) | Minute, 0 |
| 3 02 076 |  | Precipitation, obscuration and other phenomena |  |
|  | 0 20 021 | Type of precipitation | Flag table, 0 |
|  | 0 20 022 | Character of precipitation | Code table, 0 |
|  | 0 26 020 | Duration of precipitation (5) | Minute, 0 |
|  | 0 20 023 | Other weather phenomena | Flag table, 0 |
|  | 0 20 024 | Intensity of phenomena | Code table, 0 |
|  | 0 20 025 | Obscuration | Flag table, 0 |
|  | 0 20 026 | Character of obscuration | Code table, 0 |
| 3 02 071 |  | Wind data from one-hour period |  |
|  | 0 07 032 | Height of sensor above local ground | m, 2 |
|  | 0 07 033 | Height of sensor above water surface | m, 1 |
|  | 0 08 021 | Time significance (= 2 (time averaged)) | Code table, 0 |
|  | 0 04 025 | Time period (= - 10 minutes, or number of minutes after a significant change of wind, if any) | Minute, 0 |
|  | 0 11 001 | Wind direction | Degree true, 0 |
|  | 0 11 002 | Wind speed | m s-1, 1 |
|  | 0 08 021 | Time significance (= missing value) | Code table, 0 |
|  | 1 03 002 | Replicate next 3 descriptors 2 times |  |
|  | 0 04 025 | Time period (= - 10 minutes in the first replication, = - 60 minutes in the second replication) | Minute, 0 |
|  | 0 11 043 | Maximum wind gust direction | Degree true, 0 |
|  | 0 11 041 | Maximum wind gust speed | m s-1, 1 |
|  | 0 04 025 | Time period (= - 10 minutes) | Minute, 0 |
|  | 0 11 016 | Extreme counterclockwise wind direction of a variable wind | Degree true, 0 |
|  | 0 11 017 | Extreme clockwise wind direction of a variable wind | Degree true, 0 |
| 3 02 077 |  | Extreme temperature data |  |
|  | 0 07 032 | Height of sensor above local ground | m, 2 |
|  | 0 07 033 | Height of sensor above water surface | m, 1 |
|  | 0 04 025 | Time period (= - 60 minutes) | Minute, 0 |
|  | 0 12 111 | Maximum temperature (scale 2) at height and over period specified | K, 2 |
|  | 0 12 112 | Minimum temperature (scale 2) at height and over period specified | K, 2 |
|  | 0 07 032 | Height of sensor above local ground (for ground temperature) | m, 2 |
|  | 0 04 025 | Time period (= - 60 minutes) | Minute, 0 |
|  | 0 12 112 | Minimum temperature (scale 2) at height and over period specified (for ground temperature) | K, 2 |
| 0 07 033 |  | Height of sensor above water surface (set to missing to cancel the previous value) | m, 1 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 079 |  | Precipitation measurement |  |
|  | 0 07 032 | Height of sensor above local ground | m, 2 |
|  | 0 02 175 | Method of precipitation measurement | Code table, 0 |
|  | 0 02 178 | Method of liquid water content measurement of precipitation | Code table, 0 |
|  | 0 04 025 | Time period (= - 60 minutes) | Minute, 0 |
|  | 0 13 011 | Total precipitation / total water equivalent of snow | kg m-2, 1 |
| 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 080 |  | Evaporation measurement |  |
|  | 0 02 185 | Method of evaporation measurement | Code table, 0 |
|  | 0 04 025 | Time period ( = - 60 minutes) | Minute, 0 |
|  | 0 13 033 | Evaporation /evapotranspiration | kg m-2, 1 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 081 |  | Total sunshine data |  |
|  | 0 04 025 | Time period (= - 60 minutes) | Minute, 0 |
|  | 0 14 031 | Total sunshine | Minute, 0 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 082 |  | Radiation data |  |
|  | 0 04 025 | Time period (= - 60 minutes) | Minute, 0 |
|  | 0 14 002 | Long-wave radiation, integrated over period specified | J m-2, -3 |
|  | 0 14 004 | Short-wave radiation, integrated over period specified | J m-2, -3 |
|  | 0 14 016 | Net radiation, integrated over period specified | J m-2, -4 |
|  | 0 14 028 | Global solar radiation (high accuracy), integrated over period specified | J m-2, -2 |
|  | 0 14 029 | Diffuse solar radiation (high accuracy), integrated over period specified | J m-2, -2 |
|  | 0 14 030 | Direct solar radiation (high accuracy), integrated over period specified | J m-2, -2 |
| 1 02 000 |  | Delayed replication of 2 descriptors |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 0 04 025 |  | Time period (= - 10 minutes) | Minute, 0 |
| 0 13 059 |  | Number of flashes | Numeric, 0 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 083 |  | First order statistics of P, W, T, U data |  |
|  | 0 04 025 | Time period (= -10 minutes ) | Minute, 0 |
|  | 0 08 023 | First order statistics (= 9 (best estimate of standard deviation)) (6) | Code table, 0 |
|  | 0 10 004 | Pressure | Pa, –1 |
|  | 0 11 001 | Wind direction | Degree true, 0 |
|  | 0 11 002 | Wind speed | m s-1, 1 |
|  | 0 12 101 | Temperature/dry-bulb temperature (scale 2) | K, 2 |
|  | 0 13 003 | Relative humidity | %, 0 |
|  | 0 08 023 | First order statistics (= missing value) | Code table, 0 |
| 0 33 005 |  | Quality information (AWS data) | Flag table, 0 |
| 0 33 006 |  | Internal measurement status information (AWS) | Code table, 0 |

Notes:

- 0 01 101 (WMO Member State identifier) and 0 01 102 (National AWS number) shall be used to identify a station within the national numbering system that is completely independent of the WMO international numbering system. The WMO international identification 0 01 001 (WMO block number) and 0 01 002 (WMO station number) shall be reported if available for the particular station.

- The time identification refers to the end of the one-hour period.

- 0 10 061 (3-hour pressure change) and 0 10 063 (Characteristic of pressure tendency) are included in this template, although they refer to 3-hour period preceding the time of observation.

- Present weather may be represented only by 0 20 003, especially if reported from a manned non-automated station. When encoding present weather reported from an automatic weather station, the sequence of descriptors (proposed under 3 02 076) should be used, if applicable.

- Duration of precipitation (in minutes) represents number of minutes in which any precipitation was registered.

- Best estimate of standard deviation is counted out of a set of samples (signal measurements) recorded within the period specified; it should be reported as a missing value, if the measurements of the relevant element are not available from a part of the period specified by 0 04 025.

- If reporting nominal values is required, the template shall be supplemented with 3 07 093.

NEW DESCRIPTORS FOR GFA (GRAPHICAL FORECAST AIRMET) DATA

#### Proposed Table B entries

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |

| F X Y |  | Unit | Scale | Ref. value | Data width | Unit | Scale | Data width |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 01 039 | Graphical Area Forecast (GFA) sequence identifier | CCITT IA5 | 0 | 0 | 40 | Character | 0 | 5 |
| 0 20 006 | Flight Rules | Code Table | 0 | 0 | 3 | Code Table | 0 | 1 |

Add the following new code/flag table values for BUFR/CREX Table B descriptors:

0 08 040

34	Freezing level base

35	Freezing level top

36	Flight level base

37	Flight level top

0 08 041

8	IFR Ceiling and Visibility

9	Mountain obscuration

10	Strong surface wind

11	Freezing level

12	Multiple freezing level

0 20 023

13	Wind shear

0 20 025

14	Cloud

15 	Precipitation

Code tables for proposed new Table B descriptors:

| Code Figure | 0 20 006 Flight Rules |
| --- | --- |
| 0 | Low Instrument Flight Rules - Ceiling < 500 feet and/or Visibility < 1 mile |
| 1 | Instrument Flight Rules - Ceiling < 1000 feet and/or Visibility < 3 miles |
| 2 | Marginal Visual Flight Rules – 1000 feet <= Ceiling < 3000 feet and/or 3 miles <= Visibility < 5 miles |
| 3 | Visual Flight Rules - Ceiling >= 3000 feet and/or Visibility >= 5 miles |
| 4-6 | Reserved |
| 7 | Missing value |

New Table D descriptors:

|  |  | (Graphical AIRMET Sierra) |
| --- | --- | --- |
| 3 16 071 | 3 01 014 | Time period (for which AIRMET is valid) |
|  | 1 01 000 | Delayed replication |
|  | 0 31 002 | Replication Factor |
|  | 3 16 075 | GFA IFR Ceiling and Visibility |
|  | 1 01 000 | Delayed replication |
|  | 0 31 002 | Replication Factor |
|  | 3 16 076 | GFA Mountain Obscuration |
|  |  | (Graphical AIRMET Tango) |
| 3 16 072 | 3 01 014 | Time period (for which AIRMET is valid) |
|  | 1 01 000 | Delayed replication |
|  | 0 31 002 | Replication Factor |
|  | 3 16 077 | GFA Turbulence |
|  | 1 01 000 | Delayed replication |
|  | 0 31 002 | Replication Factor |
|  | 3 16 078 | GFA Strong Surface Wind |
|  | 1 01 000 | Delayed replication |
|  | 0 31 002 | Replication Factor |
|  | 3 16 079 | GFA Low-Level Wind Shear |
|  |  | (Graphical AIRMET Zulu) |
| 3 16 073 | 3 01 014 | Time period (for which AIRMET is valid) |
|  | 1 01 000 | Delayed replication |
|  | 0 31 002 | Replication Factor |
|  | 3 16 080 | GFA Icing |
|  | 1 01 000 | Delayed replication |
|  | 0 31 002 | Replication Factor |
|  | 3 16 081 | GFA Freezing Level |

|  |  | (GFA Identifier and Observed/Forecast Location) |
| --- | --- | --- |
| 3 16 074 | 0 01 039 | GFA sequence identifier |
|  | 0 08 021 | Time significance, 4=Forecast, 16=Analysis |
|  | 3 01 014 | Time period (for which hazard is being observed/forecast) |
|  | 3 01 027 | Description of Feature |
|  | 0 08 021 | Time Significance, Missing=Cancel |

|  |  | (GFA IFR Ceiling and Visibility) |
| --- | --- | --- |
| 3 16 075 | 0 08 079 | Product Status, 0=Normal, 1=COR, 2=AMD, 3=COR AMD, 4=CNL |
|  | 0 08 041 | Data significance, 8=IFR Ceiling and Visibility |
|  | 3 16 074 | GFA Identifier and Observed/Forecast Location |
|  | 0 20 006 | Flight rules, 1=IFR |
|  | 0 33 042 | Type of limit represented by following (cloud base) value, 2=Exclusive upper limit, 7=Missing |
|  | 0 20 013 | Height of base of cloud |
|  | 0 33 042 | Type of limit represented by following (visibility) value, 2=Exclusive upper limit, 7=Missing |
|  | 0 20 001 | Horizontal visibility |
|  | 0 20 025 | Obscuration |
|  | 0 20 026 | Character of obscuration, 6=Blowing, 15=Missing |
|  | 0 08 041 | Data significance, Missing=Cancel |
|  | 0 08 079 | Product Status, Missing=Cancel |
|  |  | (GFA Mountain Obscuration) |
| 3 16 076 | 0 08 079 | Product Status, 0=Normal, 1=COR, 2=AMD, 3=COR AMD, 4=CNL |
|  | 0 08 041 | Data significance, 9=Mountain obscuration |
|  | 3 16 074 | GFA Identifier and Observed/Forecast Location |
|  | 0 20 006 | Flight rules, 1=IFR |
|  | 0 20 025 | Obscuration |
|  | 0 20 026 | Character of obscuration, 6=Blowing, 15=Missing |
|  | 0 08 041 | Data significance, Missing=Cancel |
|  | 0 08 079 | Product Status, Missing=Cancel |
|  |  | (GFA Turbulence) |
| 3 16 077 | 0 08 079 | Product Status, 0=Normal, 1=COR, 2=AMD, 3=COR AMD, 4=CNL |
|  | 0 08 011 | Meteorological feature, 13=Turbulence |
|  | 3 16 074 | GFA Identifier and Observed/Forecast Location |
|  | 0 11 031 | Degree of turbulence, 6=Moderate |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  | 0 08 079 | Product Status, Missing=Cancel |
|  |  | (GFA Strong Surface Wind) |
| 3 16 078 | 0 08 079 | Product Status, 0=Normal, 1=COR, 2=AMD, 3=COR AMD, 4=CNL |
|  | 0 08 041 | Data significance, 10=Strong surface wind |
|  | 3 16 074 | GFA Identifier and Observed/Forecast Location |
|  | 0 33 042 | Type of limit represented by following (wind speed) value, 0=Exclusive lower limit |
|  | 0 11 012 | Wind speed at 10 m |
|  | 0 08 041 | Data significance, Missing=Cancel |
|  | 0 08 079 | Product Status, Missing=Cancel |

|  |  | (GFA Low-Level Wind Shear) |
| --- | --- | --- |
| 3 16 079 | 0 08 079 | Product Status, 0=Normal, 1=COR, 2=AMD, 3=COR AMD, 4=CNL |
|  | 0 08 011 | Meteorological feature, 16=Phenomenon |
|  | 3 16 074 | GFA Identifier and Observed/Forecast Location |
|  | 0 20 023 | Other weather phenomena, bit 12=Wind shear |
|  | 0 20 024 | Intensity of phenomena |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  | 0 08 079 | Product Status, Missing=Cancel |

|  |  | (GFA Icing) |
| --- | --- | --- |
| 3 16 080 | 0 08 079 | Product Status, 0=Normal, 1=COR, 2=AMD, 3=COR AMD, 4=CNL |
|  | 0 08 011 | Meteorological feature, 15=Airframe Icing |
|  | 3 16 074 | GFA Identifier and Observed/Forecast Location |
|  | 0 20 041 | Airframe icing, 4=Moderate Icing |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  | 0 08 079 | Product Status, Missing=Cancel |
|  |  | (GFA Freezing Level) |
| 3 16 081 | 0 08 079 | Product Status, 0=Normal, 1=COR, 2=AMD, 3=COR AMD, 4=CNL |
|  | 0 08 041 | Data significance, 11=Freezing level, 12=Multiple freezing level |
|  | 3 16 074 | GFA Identifier and Observed/Forecast Location |
|  | 0 08 041 | Data significance, Missing=Cancel |
|  | 0 08 079 | Product Status, Missing=Cancel |

# FOR THE ENCODING OF THE JASON2 OGDR DATA

It is proposed to use the following sequence of entries for the encoding of the JASON2 OGDR data (new entries are in italicized and underlined):

| BUFR | Description | Unit | Scale | Reference | Width |
| --- | --- | --- | --- | --- | --- |
| F X Y | Satellite |  |  |  |  |
| 0 01 007 | SATELLITE IDENTIFIER |  |  |  |  |
| 0 02 019 | SATELLITE INSTRUMENTS |  |  |  |  |
| 0 01 096 | ACQUISITION STATION IDENTIFIER |  |  |  |  |
| 0 25 061 | SOFTWARE IDENTIFICATION |  |  |  |  |
| 0 05 044 | SATELLITE CYCLE NUMBER |  |  |  |  |
| 0 05 040 | ORBIT NUMBER |  |  |  |  |
| 0 01 030 | NUMERICAL MODEL IDENTIFIER |  |  |  |  |
|  | Datation |  |  |  |  |
| 0 04 001 | YEAR |  |  |  |  |
| 0 04 002 | MONTH |  |  |  |  |
| 0 04 003 | DAY |  |  |  |  |
| 0 04 004 | HOUR |  |  |  |  |
| 0 04 005 | MINUTE |  |  |  |  |
| 0 04 007 | SECONDS WITHIN A MINUTE |  |  |  |  |
|  | Location and Surface Type |  |  |  |  |
| 0 05 001 | LATITUDE (HIGH ACCURACY) |  |  |  |  |
| 0 06 001 | LONGITUDE (HIGH ACCURACY) |  |  |  |  |
| 0 08 029 | REMOTELY SENSED SURFACE TYPE |  |  |  |  |
| 0 08 074 | ALTIMETER ECHO TYPE |  |  |  |  |
| 0 08 077 | RADIOMETER SENSED SURFACE TYPE | CODE TABLE | 0 | 0 | 7 |
|  | Flags |  |  |  |  |
| 0 40 011 | INTERPOLATION FLAG | FLAG TABLE | 0 | 0 | 8 |
| 0 25 090 | ORBIT STATE FLAG | CODE TABLE | 0 | 0 | 4 |
| 0 25 095 | ALTIMETER STATE FLAG | CODE TABLE |  |  |  |
| 0 25 098 | ALTIMETER DATA QUALITY FLAG | FLAG TABLE | 0 | 0 | 9 |
| 0 25 099 | ALTIMETER CORRECTION QUALITY FLAG | FLAG TABLE | 0 | 0 | 9 |
| 0 21 144 | ALTIMETER RAIN FLAG |  |  |  |  |
| 0 25 096 | RADIOMETER STATE FLAG |  |  |  |  |
| 0 40 012 | RADIOMETER DATA QUALITY FLAG | FLAG TABLE | 0 | 0 | 8 |
| 0 40 013 | RADIOMETER BRIGHTNESS TEMPERATURE INTERPRETATION FLAG | CODE TABLE | 0 | 0 | 3 |
| 0 21 169 | ICE PRESENCE INDICATOR | CODE TABLE | 0 | 0 | 2 |
|  | Altimeter: Ku Band |  |  |  |  |
| 0 22 151 | KU BAND OCEAN RANGE |  |  |  |  |
| 0 22 162 | RMS OF 20 Hz KU BAND OCEAN RANGE | M | 3 | 0 | 16 |
| 0 22 163 | NUMBER OF 20Hz VALID POINTS FOR KU BAND | NUMERIC | 0 | 0 | 10 |
| 0 25 160 | KU BAND NET INSTRUMENTAL CORRECTION | M | 4 | -120000 | 18 |
| 0 25 133 | SEA STATE BIAS CORRECTION ON KU BAND |  |  |  |  |
| 0 22 156 | KU BAND SIGNIFICANT WAVE HEIGHT |  |  |  |  |
| 0 22 164 | RMS 20 HZ KU BAND SIGNIFICANT WAVE HEIGHT | M | 3 | 0 | 16 |
| 0 22 165 | NUMBER OF 20HZ VALID POINTS FOR KU BAND SIGNIFICANT WAVE HEIGHT | NUMERIC | 0 | 0 | 10 |
| 0 22 166 | KU BAND NET INSTRUMENTAL CORRECTION FOR SIGNIFICANT WAVE HEIGHT | M | 3 | -1000 | 11 |
| 0 21 137 | KU BAND CORRECTED OCEAN BACKSCATTER COEFFICIENT |  |  |  |  |
| 0 21 138 | STD KU BAND CORRECTED OCEAN BACKSCATTER COEFFICIENT |  |  |  |  |
| 0 22 167 | NUMBER OF VALID POINTS FOR KU BAND BACKSCATTER | NUMERIC | 0 | 0 | 10 |
| 0 21 139 | KU BAND NET INSTRUMENTAL CORRECTION FOR AGC |  |  |  |  |
| 0 21 118 | ATTENUATION CORRECTION ON SIGMA-0 |  |  |  |  |
| 0 21 145 | KU BAND AUTOMATIC GAIN CONTROL | DB | 2 | 0 | 13 |
| 0 21 146 | RMS KU BAND AUTOMATIC GAIN CONTROL | DB | 2 | 0 | 8 |
| 0 21 147 | NUMBER OF VALID POINTS FOR KU BAND AUTOMATIC GAIN CONTROL | NUMERIC | 0 | 0 | 5 |
|  | Altimeter: C band |  |  |  |  |
| 0 22 168 | C BAND OCEAN RANGE | M | 3 | 0 | 31 |
| 0 22 169 | RMS OF C BAND OCEAN RANGE | M | 3 | 0 | 16 |
| 0 22 170 | NUMBER OF 20Hz VALID POINTS FOR C BAND | NUMERIC | 0 | 0 | 10 |
| 0 25 161 | C BAND NET INSTRUMENTAL CORRECTION | M | 4 | -120000 | 18 |
| 0 25 162 | SEA STATE BIAS CORRECTION ON C BAND | M | 4 | -6000 | 13 |
| 0 22 171 | C BAND SIGNIFICANT WAVE HEIGHT | M | 3 | 0 | 16 |
| 0 22 172 | RMS 20HZ C BAND SIGNIFICANT WAVE HEIGHT | M | 3 | 0 | 16 |
| 0 22 173 | NUMBER OF 20HZ VALID POINTS FOR C BAND SIGNIFICANT WAVE HEIGHT | NUMERIC | 0 | 0 | 10 |
| 0 22 174 | C BAND NET INSTRUMENTAL CORRECTION FOR SIGNIFICANT WAVE HEIGHT | M | 3 | -1000 | 11 |
| 0 21 170 | C BAND CORRECTED OCEAN BACKSCATTER COEFFICIENT | DB | 2 | -32768 | 16 |
| 0 21 171 | RMS C BAND CORRECTED OCEAN BACKSCATTER COEFFICIENT | DB | 2 | -32768 | 16 |
| 0 22 175 | NUMBER OF VALID POINTS FOR C BAND BACKSCATTER | NUMERIC | 0 | 0 | 10 |
| 0 21 172 | C BAND NET INSTRUMENTAL CORRECTION FOR AGC | DB | 2 | -2048 | 12 |
| 0 21 118 | ATTENUATION CORRECTION ON SIGMA-0 |  |  |  |  |
| 0 21 173 | C BAND AUTOMATIC GAIN CONTROL | DB | 2 | 0 | 13 |
| 0 21 174 | RMS C BAND AUTOMATIC GAIN CONTROL | DB | 2 | 0 | 9 |
| 0 21 175 | NUMBER OF VALID POINTS FOR C BAND AUTOMATIC GAIN CONTROL | NUMERIC | 0 | 0 | 10 |
|  | Radiometer |  |  |  |  |
| 0 02 153 | SATELLITE CHANNEL CENTRE FREQUENCY |  |  |  |  |
| 0 12 063 | BRIGHTNESS TEMPERATURE |  |  |  |  |
| 0 02 153 | SATELLITE CHANNEL CENTRE FREQUENCY |  |  |  |  |
| 0 12 063 | BRIGHTNESS TEMPERATURE |  |  |  |  |
| 0 02 153 | SATELLITE CHANNEL CENTRE FREQUENCY |  |  |  |  |
| 0 12 063 | BRIGHTNESS TEMPERATURE |  |  |  |  |
| 0 13 090 | RADIOMETER WATER VAPOR CONTENT |  |  |  |  |
| 0 13 091 | RADIOMETER LIQUID CONTENT |  |  |  |  |
|  | Wind |  |  |  |  |
| 0 07 002 | HEIGHT OR ALTITUDE |  |  |  |  |
| 0 11 097 | WIND SPEED FROM ALTIMETER | M/S | 2 | 0 | 12 |
| 0 11 098 | WIND SPEED FROM RADIOMETER | M/S | 2 | 0 | 12 |
| 0 07 002 | HEIGHT OR ALTITUDE |  |  |  |  |
| 0 11 095 | U COMPONENT OF THE MODEL WIND VECTOR |  |  |  |  |
| 0 11 096 | V COMPONENT OF THE MODEL WIND VECTOR |  |  |  |  |
|  | Dynamic Topography |  |  |  |  |
| 0 10 096 | MEAN DYNAMIC TOPOGRAPHY | M | 3 | -131072 | 18 |
| 0 10 081 | ALTITUDE OF COG ABOVE REFERENCE ELLIPSOID |  |  |  |  |
| 0 10 082 | INSTANTANEOUS ALTITUDE RATE |  |  |  |  |
| 0 10 083 | OFF NADIR ANGLE OF THE SATELLITE FROM PLATFORM DATA |  |  |  |  |
| 0 10 101 | SQUARED OFF NADIR ANGLE OF THE SATELLITE FROM WAVEFORM DATA | DEGREES^2 | 2 | -32768 | 16 |
| 0 25 132 | IONOSPHERIC CORRECTION FROM MODEL ON KU BAND |  |  |  |  |
| 0 25 163 | ALTIMETER IONOSPHERIC CORRECTION ON KU BAND | M | 3 | -32768 | 16 |
| 025 126 | MODEL DRY TROPOSPHERIC CORRECTION |  |  |  |  |
| 0 25 128 | MODEL WET TROPOSPHERIC CORRECTION |  |  |  |  |
| 0 25 164 | RADIOMETER WET TROPOSPHERIC CORRECTION | M | 4 | -5000 | 13 |
| 0 10 085 | MEAN SEA SURFACE HEIGHT |  |  |  |  |
| 0 10 097 | MEAN SEA SURFACE HEIGHT FROM ALTIMETER ONLY | M | 3 | -131072 | 18 |
| 0 10 086 | GEOID'S HEIGHT |  |  |  |  |
| 0 10 087 | OCEAN DEPTH/LAND ELEVATION |  |  |  |  |
| 0 10 092 | SOLID EARTH TIDE HEIGHT |  |  |  |  |
| 0 10 088 | GEOCENTRIC OCEAN TIDE HEIGHT SOLUTION 1 |  |  |  |  |
| 0 10 089 | GEOCENTRIC OCEAN TIDE HEIGHT SOLUTION 2 |  |  |  |  |
| 0 10 098 | LOADING TIDE HEIGHT GEOCENTRIC OCEAN TIDE SOLUTION 1 | M | 4 | -2000 | 12 |
| 0 10 099 | LOADING TIDE HEIGHT GEOCENTRIC OCEAN TIDE SOLUTION 2 | M | 4 | -2000 | 12 |
| 0 10 090 | LONG PERIOD TIDE HEIGHT |  |  |  |  |
| 0 10 100 | N0N-EQUILIBRIUM LONG PERIOD TIDE HEIGHT | M | 4 | -2000 | 12 |
| 0 10 093 | GEOCENTRIC POLE TIDE HEIGHT |  |  |  |  |
| 0 25 127 | SEA SURFACE HEIGHT CORRECTION DUE TO PRESSURE LOADING |  |  |  |  |
| 0 40 014 | HIGH FREQUENCY FLUCTUATIONS OF THE SEA SURFACE TOPOGRAPHY CORRECTION | M | 4 | -3000 | 13 |

It is proposed to allocate the Table D entry 3 40 005 for the above sequence.

Proposal for code and flag tables

0 08 077

# Radiometer sensed surface type

| Code figure |  |
| --- | --- |
| 0 | Land |
| 1 | Sea |
| 2 | Coastal |
| 3 | Open ocean or semi-enclosed sea |
| 4 | Enclosed sea or lake |
| 5 | Continental ice |
| 6-126 | Reserved |
| 127 | Missing value |

0 40 011

# Interpolation flag

| Bit number |  |
| --- | --- |
| 1 | Mean sea surface (MSS) interpolation flag |
| 2 | Ocean tide solution 1 interpolation flag (0=4 points over ocean, 1=less than 4 points) |
| 3 | Ocean tide solution 2 interpolation flag (0=4 points over ocean, 1=less than 4 points) |
| 4 | Meteorological data interpolation flag (0=4 points over ocean, 1=less than 4 points) |
| 5 | Spare |
| 6 | Spare |
| 7 | Spare |
| All 8 bits | Missing |

# 0 25 090

# Orbit state flag

| Code figure |  |
| --- | --- |
| 0 | Orbit computed during a manoeuvre |
| 1 | Adjusted mission operations orbit |
| 2 | Extrapolated mission operations orbit |
| 3 | Adjusted (preliminary/precise) orbit |
| 4 | (preliminary/precise) orbit is estimated during a manoeuvre period |
| 5 | (preliminary/precise) orbit is interpolated over a tracking data gap |
| 6 | (preliminary/precise) orbit is extrapolated for a duration less than 1 day |
| 7 | (preliminary/precise) orbit is extrapolated for a duration that ranges from 1 day to 2 days |
| 8 | (preliminary/precise) orbit is extrapolated for a duration larger than 2 days, or that the orbit is extrapolated just after a manoeuvre |
| 9 | DORIS† DIODE‡ navigator orbit |
| 10 - 14 | Reserved |
| 15 | Missing value |

† DORIS stands for “Doppler Orbitography and Radio-positioning Integrated by Satellite”.

‡ DIODE means "Détermination Immédiate d'Orbite par Doris Embarqué" or immediate onboard orbit determination by DORIS. It is part of the DORIS instrument, which calculates the satellite's

position and velocity.

0 25 097

# Three dimensional error estimate of the navigator orbit

| Code figure |  |
| --- | --- |
| 0 | Ranges between 0 and 30 cm |
| 1 | Ranges between 30 and 60 cm |
| 2 | Ranges between 60 and 90 cm |
| 3 | Ranges between 90 and 120 cm |
| 4 | Ranges between 120 and 150 cm |
| 5 | Ranges between 150 and 180 cm |
| 6 | Ranges between 180 and 210 cm |
| 7 | Ranges between 210 and 240 cm |
| 8 | Ranges between 240 and 270 cm |
| 9 | Ranges larger than 270 cm |
| 10 - 14 | Reserved |
| 15 | Missing value |

0 25 098

# Altimeter data quality flag

| Bit number | (0 is good, 1 is bad) |
| --- | --- |
| 1 | Ku band range |
| 2 | C band range |
| 3 | Ku band SWH* |
| 4 | C band SWH* |
| 5 | Ku band backscatter coefficient |
| 6 | C band backscatter coefficient |
| 7 | Off nadir angle from Ku band waveform parameters |
| 8 | Off nadir angle from platform |
| All 9 bits | Missing |

* SWH stands for “Significant wave height”

0 25 099

# Altimeter correction quality flag

| Bit number | (0 is good, 1 is bad) |
| --- | --- |
| 1 | Ku band range instrumental correction |
| 2 | C band range instrumental correction |
| 3 | Ku band SWH* instrumental correction |
| 4 | C band SWH* instrumental correction |
| 5 | Ku band backscatter coefficient instrumental correction |
| 6 | C band backscatter coefficient instrumental correction |
| 7 | Spare |
| 8 | Spare |
| All 9 bits | Missing |

* SWH stands for “Significant wave height”

0 40 012

# Radiometer data quality flag

| Bit number | (0 is good, 1 is bad) |
| --- | --- |
| 1 | 18.7 GHz brightness temperature |
| 2 | 23.8 GHz brightness temperature |
| 3 | 34 GHz brightness temperature |
| 4 | Spare |
| 5 | Spare |
| 6 | Spare |
| 7 | Spare |
| All 8 bits | Missing |

0 40 013

# Radiometer brightness temperature interpretation flag

| Code figure |  |
| --- | --- |
| 0 | Interpolation with no gap between JMR§ data |
| 1 | Interpolation with gaps between JMR§ data |
| 2 | Extrapolation of JMR§ data |
| 3 | Failure of extrapolation and interpolation |
| 4 - 6 | Reserved |
| 7 | Missing |

§ JMR stands for “JASON-1 Microwave Radiometer”

0 21 169

# Ice presence indicator

| Code figure |  |
| --- | --- |
| 0 | No ice present |
| 1 | Ice present |
| 2 | Reserved |
| 3 | Missing |

FOR SMOS SATELLITE DATA

# Proposed new Table B entries

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | Unit | Scale | Ref. value | Data width | Unit | Scale | Data width |
| 001144 | Snapshot identifier | Numeric | 0 | 0 | 31 | Numeric | 0 | 10 |
| 015012 | Total electron count per square metre | 1/M**2 | -16 | 0 | 6 | 1/M**2 | -16 | 2 |
| 012165 | Direct sun brightness temperature | K | 0 | 0 | 23 | K | 0 | 7 |
| 012166 | Snapshot accuracy | K | 1 | -4000 | 13 | K | 1 | 4 |
| 012167 | Radiometric accuracy ( pure polarisation) | K | 1 | 0 | 9 | K | 1 | 3 |
| 012168 | Radiometric accuracy ( cross polarisation) | K | 1 | 0 | 9 | K | 1 | 3 |
| 030010 | Number of grid points | Numeric | 0 | 0 | 13 | Numeric | 0 | 4 |
| 001124 | Grid point identifier | Numeric | 0 | 0 | 24 | Numeric | 0 | 8 |
| 007012 | Grid point altitude | M | 2 | -50000 | 20 | M | 2 | 7 |
| 013048 | Water fraction | % | 1 | 0 | 10 | % | 1 | 4 |
| 012080 | Brightness temperature real part | K | 2 | -10000 | 16 | K | 2 | 5 |
| 012081 | Brightness temperature imaginary part | K | 2 | -10000 | 16 | K | 2 | 5 |
| 012082 | Pixel radiometric accuracy | K | 2 | 0 | 12 | K | 2 | 4 |
| 025081 | Incidence angle | Degree | 3 | 0 | 17 | Degree | 3 | 6 |
| 025082 | Azimuth angle | Degree | 3 | 0 | 19 | Degree | 3 | 6 |
| 025083 | Faraday rotational angle | Degree | 3 | 0 | 19 | Degree | 3 | 6 |
| 025084 | Geometric rotational angle | Degree | 5 | 0 | 26 | Degree | 5 | 8 |
| 027010 | Footprint axis 1 | M | -1 | 0 | 14 | M | -1 | 5 |
| 028010 | Footprint axis 2 | M | -1 | 0 | 14 | M | -1 | 5 |
| 025174 | SMOS information flag | Flag table | 0 | 0 | 14 | Flag table | 0 | 5 |
| 002099 | Polarisation | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 033028 | Snapshot overall quality | Code table | 0 | 0 | 3 | Code table | 0 | 1 |

Note: In full polarisation the Level1c SMOS brightness temperature (BT) is complex number.  The components of the complex BT are related to the Stokes parameters which are harmonic components of the brightness temperature.  Third and fourth Stoke parameters can be negative, leading to negative values of the complex BT.

# Proposed new BUFR Table D sequence for SMOS data

312070    001007

002019

001144

001124

030010

301011

301013

301021

007012

015012

012165

012166

012167

012168

027010

028010

002099

013048

025081

025082

025083

025084

012080

012081

012082

025174

033028

# Add new Code tables:

# 0 33 028 - Snapshot overall quality

# Code           Meaning

# 1                Nominal

# 2               Degraded by SW error; any error reported by the algorithms

# 3                Degraded by instrument error

# 4               Degraded by corrupted /missing ADF

# 5-6             Reserved

# 7               Missing value

0 02 099  Polarisation

Code         Meaning

0		HH polarisation

1		VV polarisation

2	            HV polarisation real valued component

3		HV polarisation imaginary valued component

4-6		Reserved

7                Missing value

Add new Flag table:

0 25 174 - SMOS information flag

Bit number     Meaning

1               Pixel is affected by RFI effects

2               Pixel is located in the hexagonal Alias direction centred on Sun alias

3               Pixel is close to the border delimiting the extended Alias free zone

4               Pixel is inside the extended Alias free zone

5               Pixel is inside the exclusive of Alias free zone

6               Pixel is located in a zone where a Moon Alias was reconstructed

7               Pixel is located in a zone where Sun reflection has been detected

8               Pixel is located in a zone where Sun Alias was reconstructed

9               Flat target transformation has been performed during image reconstruction                                         			of this pixel

10               Scene has been combined with an adjustment scene in opposite

polarisation during image reconstruction to account for cross-polarisation

leakage

11                Direct Moon correction has been performed during image reconstruction

of this pixel

12                Reflected Sun correction has been performed during image reconstruction

of this pixel

13                Direct Sun correction has been performed during image reconstruction of

this image

All 14           Missing value

# Add the following new Sub category in Common Code Table C-13:

Data category			International sub-category

101 Image data (satellite)		007 SMOS data

# Add the following new satellite identifier in Common Code Table C-5:

46   SMOS

# Add the following new satellite instrument in Common Code Table C-8:

176            ESA           Radiometer        MIRAS         Microwave Imaging Radiometer Using Aperture Synthesis

FOR GOME EXPERIMENT DATA

3–10–018     Ozone data

001007 – Satellite identifier

005040 – Orbit number

004001 – Year

004043 – Day of year

004004 – Hour

004005 – Minute

004006 – Second

207002 – Increase scale, reference value and data width

026030 – Measurement integration time

207000 – Cancel increase scale, reference value and data width

005002 – Latitude

006002 – Longitude

033072 – Ozone error

007025 – Solar zenith angle

005022 – Solar azimuth angle

207002 – Increase scale, reference value and data width

015001 – Total ozone

207000 – Cancel increase scale, reference value and data width

008003 - Vertical significance (“0” = surface)

207001 – Increase scale, reference value and data width

010004 – Pressure (terrain)

207000 - Cancel increase scale, reference value and data width

008003 - Vertical significance (“Missing” = Cancel)

008003 - Vertical significance (“2” = Cloud top)

033042 - Type of limit represented by following value (“0” = Exclusive lower limit)

207001 - Increase scale, reference value and data width

007004 – Pressure

207000 – Cancel increase scale, reference value and data width

207002 – Increase scale, reference value and data width

015001 – Total ozone (below cloud top pressure)

207000 – Cancel increase scale, reference value and data width

008003 – Vertical significance (“Missing” = Cancel)

207002 – Increase scale, reference value and data width

020081 – Cloud amount in segment (cloud fraction)

207000 – Cancel increase scale, reference value and data width

020065 – Snow cover

008029 – Remotely-sensed surface type

207004 – Increase scale, reference value and data width

015030 – Aerosol contamination index

207000 – Cancel increase scale, reference value and data width

008075 – Ascending/descending orbit qualifier

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | Unit | Scale | Ref. value | Data width | Unit | Scale | Data width |
| 0 26 030 | Measurement integration time | Second | 2 | 0 | 8 | Second | 2 | 3 |
| 0 33 072 | Ozone error | Code table | 0 | 0 | 5 | Code table | 0 | 2 |

0-33-072   Ozone error

| 0 | Good retrieval |
| --- | --- |
| 1 | Reflectivity out of range |
| 2 | Larger Pixels (Number of cross-track pixels less than 32) or backward scans Error |
| 3 | Solar zenith angle greater than 88 |
| 4 | Latitude/longitude out of range |
| 5 | Viewing zenith angle or solar zenith angle out of range |
| 6 | Step-one process failed in general |
| 7 | First guess ozone out of range |
| 8 | Too many iterations (exceed 8) |
| 9 | Step-one residue calculation failed |
| 10 | Step-two process failed in general |
| 11 | First guess ozone profile out of range |
| 12 | Step-two ozone value out of range |
| 13 | Step-two residue calculation failed |
| 14 | Step-three process failed in general |
| 15 | Polarization Correction Accuracy Alert |
| 16 | Radiance or irradiance less or equal to zero |
| 17-30 | Reserved |
| 31 | Missing |

# METOP GOME-2 BUFR TEMPLATE

3 22 028

ELEMENT NAME

1  001007  SATELLITE IDENTIFIER

2  002019  SATELLITE INSTRUMENTS

3  004001  YEAR

4  004002  MONTH

5  004003  DAY

6  004004  HOUR

7  004005  MINUTE

8  004006  SECOND

9  005001  LATITUDE (HIGH ACCURACY)

10  006001  LONGITUDE (HIGH ACCURACY)

11  027001  LATITUDE (HIGH ACCURACY)

12  028001  LONGITUDE (HIGH ACCURACY)

13  027001  LATITUDE (HIGH ACCURACY)

14  028001  LONGITUDE (HIGH ACCURACY)

15  027001  LATITUDE (HIGH ACCURACY)

16  028001  LONGITUDE (HIGH ACCURACY)

17  027001  LATITUDE (HIGH ACCURACY)

18  028001  LONGITUDE (HIGH ACCURACY)

19  010001  HEIGHT OF LAND SURFACE

20  014019  SURFACE ALBEDO

21  007025  SOLAR ZENITH ANGLE

22  010080  VIEWING ZENITH ANGLE

23  005023  SUN TO SATELLITE AZIMUTH DIFFERENCE

24  020010  CLOUD COVER (TOTAL)

25  008003  VERTICAL SIGNIFICANCE (SATELLITE OBSERVATIONS)

26  007004  PRESSURE

27  014026  ALBEDO AT THE TOP OF CLOUDS

28  020014  HEIGHT OF TOP OF CLOUD

29  013093  CLOUD OPTICAL THICKNESS

30  105000  DELAYED REPLICATION OF FIVE DESCRIPTORS

31  031001  DELAYED DESCRIPTOR REPLICATION FACTOR

32  007004  PRESSURE

33  007004  PRESSURE

34  008043  ATMOSPHERIC CHEMICAL OR PHISICAL CONSTITUENT TYPE

35  008044  CAS REGISTRY NUMBER

36  015021  INTEGRATED MASS DENSITY

A new category 22 for Chemical and Aerosol sequences is proposed to be used.

BUFR TABLE D AND CODE TABLE ENTRIES FOR ENCODING OF ALL SKY RADIANCE DATA

# New code table entries

In order to describe the type of clouds from which cloudy radiances are associated, it is necessary to add three new entries to the code table 0-08-003, “Vertical significance (satellite observations)”, highlighted in grey as follows:

“Vertical significance (satellite observations)”, 0-08-003

Code		Meaning

0 		Surface

1 		Base of Satellite sounding

2 		Cloud Top

3 		Tropopause

4 		Precipitable water

5 		Sounding Radiances

6 		Mean Temperatures

7 		Ozone

8 		Low cloud

9 		Med Cloud

10 		High cloud

11-62 		Reserved

63 		Missing value

# New sequence descriptors

It is proposed to add three new sequence descriptors to Table D for the encoding of all sky radiance data.  These are described below:

Sequence 		Number of descriptors 	Descriptors / sub-sequences

All sky radiance product main sequence

310027 		12 				301071 Product information

301011 Date

301013 Time

301021 Latitude / longitude

030021 Number of pixels per row

030022 Number of pixels per column

010002 Orbit height

304036 All sky radiance cloud coverage

002152 Satellite instrument used

002167 Radiance computational method

101011 Replication operator

304035 All sky radiance data

Cloud coverage

304036 		12 				020082 Amount of segment cloud free

008012 Land-Sea Qualifier: Sea

020082 Amount of segment cloud free (sea)

008012 Cancel qualifier

020081 Cloud amount in segment

008003 Vertical significance: Low cloud

020081 Cloud amount in segment (low cloud)

008003 Vertical significance: Mid cloud

020081 Cloud amount in segment (mid cloud)

008003 Vertical significance: High cloud

020081 Cloud amount in segment (high cloud)

008003 Cancel significance

All sky radiance data

304035  		15 				002153 Satellite channel centre frequency

002154 Satellite channel band width

012063 Brightness temperature

008001 Pixel type: clear

012063 Brightness temperature (clear)

008001 Pixel type: cloudy

012063 Brightness temperature (cloudy)

008001 Cancel type

008003 Vertical significance: low cloud

012063 Brightness temperature (low cloud)

008003 Vertical_significance: mid cloud

012063 Brightness temperature (mid cloud)

008003 Vertical_significance: high cloud

012063 Brightness temperature (high cloud)

008003 Cancel_significance

BUFR TEMPLATE FOR REPRESENTATION OF SYNOP DATA WITH SUPPLEMENTARY INFORMATION ON ONE-HOUR OBSERVATIONS

This template is proposed to be used for representation of surface observation data from both automatic stations and manned stations.  This template is also suitable for SYNOP observation data, by including parameters covering periods longer than one hour.

Entries from the SYNOP BUFR template TM 307080 are indicated by an asterisk * in the column S. Entries from the AWS BUFR template TM 307091 are indicated by an asterisk * in the column A.

Entries used by both templates are not marked.

The very recent modifications and additions are written in blue and bold.

TM 307096 -	BUFR template for representation of SYNOP data with supplementary information on one-hour observations

| 3 07 096 |  | Sequence for representation of SYNOP data with supplementary information on one-hour observations |
| --- | --- | --- |
|  | 3 01 090 | Fixed surface station identification, time, horizontal and vertical coordinates |
|  | 3 01 089 | National station identification |
|  | 0 08 010 | Surface qualifier (for temperature data) |
|  | 3 01 091 | Surface station instrumentation |
|  | 3 02 084 | “Instantaneous” data of sequence 307096 |
|  | 3 02 085 | “Period” data of sequence 307096 |
|  | 0 33 005 | Quality information (AWS data) |
|  | 0 33 006 | Internal measurement status information (AWS) |

This BUFR template further expands as follows:

|  |  |  |  | S | A |  | Unit, scale |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 3 01 090 |  |  |  |  |  | Surface station identification; time, horizontal and vertical co-ordinates |  |
|  | 3 01 004 |  |  |  |  | Surface station identification |  |
|  |  | 0 01 001 |  |  |  | WMO block number | Numeric, 0 |
|  |  | 0 01 002 |  |  |  | WMO station number | Numeric, 0 |
|  |  | 0 01 015 |  |  |  | Station or site name | CCITT IA5, 0 |
|  |  | 0 02 001 |  |  |  | Type of station | Code table, 0 |
|  | 3 01 011 | 0 04 001 |  |  |  | Year | Year, 0 |
|  |  | 0 04 002 |  |  |  | Month | Month, 0 |
|  |  | 0 04 003 |  |  |  | Day | Day, 0 |
|  | 3 01 012 | 0 04 004 |  |  |  | Hour | Hour, 0 |
|  |  | 0 04 005 |  |  |  | Minute | Minute, 0 |
|  | 3 01 021 | 0 05 001 |  |  |  | Latitude (high accuracy) | Degree, 5 |
|  |  | 0 06 001 |  |  |  | Longitude (high accuracy) | Degree, 5 |
|  | 0 07 030 |  |  |  |  | Height of station ground above mean sea level | m, 1 |
|  | 0 07 031 |  |  |  |  | Height of barometer above mean sea level | m, 1 |
| 3 01 089 |  |  |  |  | * | National station identification |  |
|  | 0 01 101 |  |  |  | * | State identifier (see Note 1) | Code table, 0 |
|  | 0 01 102 |  |  |  | * | National station number (see Note 1) | Numeric, 0 |
| 0 08 010 |  |  |  |  | * | Surface qualifier (for temperature data) | Code table, 0 |
| 3 01 091 |  |  |  |  | * | Surface station instrumentation |  |
|  | 0 02 180 |  |  |  | * | Main present weather detecting system | Code table, 0 |
|  | 0 02 181 |  |  |  | * | Supplementary present weather sensor | Flag table, 0 |
|  | 0 02 182 |  |  |  | * | Visibility measurement system | Code table, 0 |
|  | 0 02 183 |  |  |  | * | Cloud detection system | Code table, 0 |
|  | 0 02 184 |  |  |  | * | Type of lightning detection sensor | Code table, 0 |
|  | 0 02 179 |  |  |  | * | Type of sky condition algorithm | Code table, 0 |
|  | 0 02 186 |  |  |  | * | Capability to detect precipitation phenomena | Flag table, 0 |
|  | 0 02 187 |  |  |  | * | Capability to detect other weather phenomena | Flag table, 0 |
|  | 0 02 188 |  |  |  | * | Capability to detect obscuration | Flag table, 0 |
|  | 0 02 189 |  |  |  | * | Capability to discriminate lightning strikes | Flag table, 0 |
| 3 02 084 |  |  |  |  |  | “Instantaneous” data of sequence 307096 |  |
|  | 3 02 031 |  |  |  |  | Pressure data |  |
|  |  | 3 02 001 | 0 10 004 |  |  | Pressure | Pa, –1 |
|  |  |  | 0 10 051 |  |  | Pressure reduced to mean sea level | Pa, –1 |
|  |  |  | 0 10 061 |  |  | 3-hour pressure change | Pa, –1 |
|  |  |  | 0 10 063 |  |  | Characteristic of pressure tendency | Code table, 0 |
|  |  | 0 10 062 |  | * |  | 24-hour pressure change p24p24p24 | Pa, –1 |
|  |  | 0 07 004 |  |  |  | Pressure (standard level) | Pa, –1 |
|  |  | 0 10 009 |  |  |  | Geopotential height of the standard level | gpm, 0 |
|  | 3 02 072 |  |  |  |  | Temperature and humidity data |  |
|  |  | 0 07 032 |  |  |  | Height of sensor above local ground | m, 2 |
|  |  | 0 07 033 |  |  | * | Height of sensor above water surface | m, 1 |
|  |  | 0 12 101 |  |  |  | Temperature/dry-bulb temperature (scale 2) | K, 2 |
|  |  | 0 12 103 |  |  |  | Dew-point temperature (scale 2) | K, 2 |
|  |  | 0 13 003 |  |  |  | Relative humidity | %, 0 |
|  | 1 03 000 |  |  |  |  | Delayed replication of 3 descriptors |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 1 01 005 |  |  |  | * | Replicate one descriptor five times |  |
|  | 3 07 063 | 0 07 061 |  |  | * | Depth below land surface | m, 2 |
|  |  | 0 12 130 |  |  | * | Soil temperature (scale 2) | K, 2 |
|  | 0 07 061 |  |  |  | * | Depth below land surface (set to missing to cancel the previous value) | m, 2 |
|  |  |  |  |  |  | Visibility data |  |
|  | 1 01 000 |  |  |  |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 069 | 0 07 032 |  |  |  | Height of sensor above local ground | m, 2 |
|  |  | 0 07 033 |  |  | * | Height of sensor above water surface | m, 1 |
|  |  | 0 33 041 |  |  | * | Attribute of following value | Code table, 0 |
|  |  | 0 20 001 |  |  |  | Horizontal visibility | m, –1 |
|  | 0 07 032 |  |  |  | * | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
|  | 0 07 033 |  |  |  | * | Height of sensor above water surface (set to missing to cancel the previous value) | m, 1 |
|  |  |  |  |  |  | Marine data |  |
|  | 1 05 000 |  |  |  |  | Delayed replication of 5 descriptors |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 0 20 031 |  |  |  | * | Ice deposit (thickness) | m, 2 |
|  | 0 20 032 |  |  |  | * | Rate of ice accretion | Code table, 0 |
|  | 0 02 038 |  |  |  | * | Method of sea surface temperature measurement | Code table, 0 |
|  | 0 22 043 |  |  |  | * | Sea/water temperature (scale 2) | K, 2 |
|  | 3 02 021 | 0 22 001 |  |  | * | Direction of waves | Degree true, 0 |
|  |  | 0 22 011 |  |  | * | Period of waves | s, 0 |
|  |  | 0 22 021 |  |  | * | Height of waves | m, 1 |
|  |  |  |  |  |  | State of ground and snow depth measurement |  |
|  | 1 01 000 |  |  |  |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 078 | 0 02 176 |  |  | * | Method of state of ground measurement | Code table, 0 |
|  |  | 0 20 062 |  |  |  | State of ground (with or without snow) | Code table, 0 |
|  |  | 0 02 177 |  |  | * | Method of snow depth measurement | Code table, 0 |
|  |  | 0 13 013 |  |  |  | Total snow depth | m, 2 |
|  | 0 12 113 |  |  | * |  | Ground minimum temperature (scale 2), past 12 hours snTgTg | K, 2 |
|  |  |  |  |  |  | Cloud data |  |
|  | 1 01 000 |  |  |  |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 004 | 0 20 010 |  |  |  | Cloud cover (total) | %, 0 |
|  |  | 0 08 002 |  | * |  | Vertical significance | Code table, 0 |
|  |  | 0 20 011 |  | * |  | Cloud amount (of low or middle clouds) Nh | Code table, 0 |
|  |  | 0 20 013 |  | * |  | Height of base of cloud h | m, –1 |
|  |  | 0 20 012 |  | * |  | Cloud type (low clouds CL) CL | Code table, 0 |
|  |  | 0 20 012 |  | * |  | Cloud type (middle clouds CM) CM | Code table, 0 |
|  |  | 0 20 012 |  | * |  | Cloud type (high clouds CH) CH | Code table, 0 |
|  | 1 05 000 |  |  |  |  | Delayed replication of 5 descriptors |  |
|  | 0 31 001 |  |  | * |  | Delayed descriptor replication factor | Numeric, 0 |
|  | 0 08 002 |  |  |  |  | Vertical significance | Code table, 0 |
|  | 0 20 011 |  |  |  |  | Cloud amount | Code table, 0 |
|  | 0 20 012 |  |  |  |  | Cloud type | Code table, 0 |
|  | 0 33 041 |  |  |  | * | Attribute of following value | Code table, 0 |
|  | 0 20 013 |  |  |  |  | Height of base of cloud | m, -1 |
|  |  |  |  |  |  | Clouds with bases below station level |  |
|  | 3 02 036 | 1 05 000 |  | * |  | Delayed replication of 5 descriptors |  |
|  |  | 0 31 001 |  | * |  | Delayed descriptor replication factor | Numeric, 0 |
|  |  | 0 08 002 |  | * |  | Vertical significance | Code table, 0 |
|  |  | 0 20 011 |  | * |  | Cloud amount N’ | Code table, 0 |
|  |  | 0 20 012 |  | * |  | Cloud type C’ | Code table, 0 |
|  |  | 0 20 014 |  | * |  | Height of top of cloud H’H’ | m, -1 |
|  |  | 0 20 017 |  | * |  | Cloud top description Ct | Code table, 0 |
|  | 1 01 000 |  |  |  |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  |  |  |  | Short delayed descriptor replication factor | Numeric, 0 |
|  |  |  |  | * |  | Direction of cloud drift 6DLDMDH |  |
|  | 3 02 047 | 1 02 003 |  | * |  | Replicate 2 descriptors 3 times |  |
|  |  | 0 08 002 |  | * |  | Vertical significance (7= low cloud, 8= middle cloud, 9 = high cloud) | Code table, 0 |
|  |  | 0 20 054 |  | * |  | True direction from which clouds are moving DLDMDH | Degree true, 0 |
|  | 0 08 002 |  |  | * |  | Vertical significance (set to missing to cancel the previous value) | Code table, 0 |
|  |  |  |  | * |  | Direction and elevation of cloud 57CDaeC |  |
|  | 1 01 000 |  |  |  |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  |  |  |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 048 | 0 05 021 |  | * |  | Bearing or azimuth Da | Degree true, 2 |
|  |  | 0 07 021 |  | * |  | Elevation angle eC | Degree, 2 |
|  |  | 0 20 012 |  | * |  | Cloud type C | Code table, 0 |
|  |  | 0 05 021 |  | * |  | Bearing or azimuth (set to missing to cancel the previous value) | Degree true, 2 |
|  |  | 0 07 021 |  | * |  | Elevation angle (set to missing to cancel the previous value) | Degree, 2 |
| 3 02 085 |  |  |  |  |  | “Period” data of sequence 307096 |  |
|  |  |  |  |  |  | Present and past weather data |  |
|  | 1 05 000 |  |  |  |  | Delayed replication of 5 descriptors |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 0 20 003 |  |  |  |  | Present weather (see Note 2) | Code table, 0 |
|  | 1 03 002 |  |  |  |  | Replicate 3 descriptors 2 times |  |
|  | 0 04 024 |  |  |  |  | Time period (= -1 hour in 1. replication, -x hours in 2. replication, x corresponding to the time period of W1W2 in the SYNOP report) | Hour, 0 |
|  | 0 20 004 |  |  |  |  | Past weather (1) | Code table, 0 |
|  | 0 20 005 |  |  |  |  | Past weather (2) | Code table, 0 |
|  |  |  |  |  | * | Intensity of precipitation, size of precipitation element |  |
|  | 1 01 000 |  |  |  |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 075 | 0 08 021 |  |  | * | Time significance (= 2 (time averaged)) | Code table, 0 |
|  |  | 0 04 025 |  |  | * | Time period (= - 10 minutes) | Minute, 0 |
|  |  | 0 13 055 |  |  | * | Intensity of precipitation | kg m-2s-1, 4 |
|  |  | 0 13 058 |  |  | * | Size of precipitation element | m, 4 |
|  |  | 0 08 021 |  |  | * | Time significance (= missing value) | Code table, 0 |
|  |  |  |  |  |  | Precipitation, obscuration and other phenomena |  |
|  | 1 02 000 |  |  |  |  | Delayed replication of 2 descriptors |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 0 04 025 |  |  |  | * | Time period (= - 10 minutes) | Minute, 0 |
|  | 3 02 076 |  |  |  | * | Precipitation, obscuration and other phenomena |  |
|  |  | 0 20 021 |  |  | * | Type of precipitation | Flag table, 0 |
|  |  | 0 20 022 |  |  | * | Character of precipitation | Code table, 0 |
|  |  | 0 26 020 |  |  | * | Duration of precipitation (see Note 3) | Minute, 0 |
|  |  | 0 20 023 |  |  | * | Other weather phenomena | Flag table, 0 |
|  |  | 0 20 024 |  |  | * | Intensity of phenomena | Code table, 0 |
|  |  | 0 20 025 |  |  | * | Obscuration | Flag table, 0 |
|  |  | 0 20 026 |  |  | * | Character of obscuration | Code table, 0 |
|  |  |  |  |  |  | Lightning data |  |
|  | 1 02 000 |  |  |  |  | Delayed replication of 2 descriptors |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 0 04 025 |  |  |  | * | Time period (= - 10 minutes) | Minute, 0 |
|  | 0 13 059 |  |  |  | * | Number of flashes | Numeric, 0 |
|  |  |  |  |  |  | Wind data |  |
|  | 0 07 032 |  |  |  |  | Height of sensor above local ground | m, 2 |
|  | 0 07 033 |  |  |  | * | Height of sensor above water surface | m, 1 |
|  | 0 08 021 |  |  |  |  | Time significance (= 2 (time averaged)) | Code table, 0 |
|  | 0 04 025 |  |  |  |  | Time period (= - 10 minutes, or number of minutes after a significant change of wind) | Minute, 0 |
|  | 0 11 001 |  |  |  |  | Wind direction | Degree true, 0 |
|  | 0 11 002 |  |  |  |  | Wind speed | m s-1, 1 |
|  | 0 08 021 |  |  |  |  | Time significance (= missing value) | Code table, 0 |
|  | 1 03 003 |  |  |  |  | Replicate next 3 descriptors 3 times |  |
|  | 0 04 025 |  |  |  |  | Time period (= -10 minutes in 1. replication, = - 60 minutes in 2. replication, = - 60*3 or 60*6 minutes in 3. replication) | Minute, 0 |
|  | 0 11 043 |  |  |  |  | Maximum wind gust direction | Degree true, 0 |
|  | 0 11 041 |  |  |  |  | Maximum wind gust speed | m s-1, 1 |
|  | 0 04 025 |  |  |  | * | Time period (= - 10 minutes) | Minute, 0 |
|  | 0 11 016 |  |  |  | * | Extreme counterclockwise wind direction of a variable wind | Degree true, 0 |
|  | 0 11 017 |  |  |  | * | Extreme clockwise wind direction of a variable wind | Degree true, 0 |
|  |  |  |  |  |  | Extreme temperature data |  |
|  | 3 02 077 | 0 07 032 |  |  | * | Height of sensor above local ground | m, 2 |
|  |  | 0 07 033 |  |  | * | Height of sensor above water surface | m, 1 |
|  |  | 0 04 025 |  |  | * | Time period (= - 60 minutes) | Minute, 0 |
|  |  | 0 12 111 |  |  | * | Maximum temperature (scale 2) at height and over period specified | K, 2 |
|  |  | 0 12 112 |  |  | * | Minimum temperature (scale 2) at height and over period specified | K, 2 |
|  |  | 0 07 032 |  |  | * | Height of sensor above local ground (for ground temperature) | m, 2 |
|  |  | 0 04 025 |  |  | * | Time period (= - 60 minutes) | Minute, 0 |
|  |  | 0 12 112 |  |  | * | Minimum temperature (scale 2) at height and over period specified (for ground temperature) | K, 2 |
|  | 0 07 033 |  |  |  | * | Height of sensor above water surface (set to missing to cancel the previous value) | m, 1 |
|  | 3 02 041 | 0 07 032 |  | * |  | Height of sensor above local ground (for temperature measurement) | m, 2 |
|  |  | 0 04 024 |  | * |  | Time period | Hour, 0 |
|  |  | 0 04 024 |  | * |  | Time period (see Notes 4 and 5) | Hour, 0 |
|  |  | 0 12 111 |  | * |  | Maximum temperature (scale 2) at height and over period specified snTxTxTx | K, 2 |
|  |  | 0 04 024 |  | * |  | Time period | Hour, 0 |
|  |  | 0 04 024 |  | * |  | Time period (see Note 5) | Hour, 0 |
|  |  | 0 12 112 |  | * |  | Minimum temperature (scale 2) at height and over period specified snTnTnTn | K, 2 |
|  |  |  |  |  |  | Precipitation measurement |  |
|  | 1 06 000 |  |  |  |  | Delayed replication of 6 descriptors |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 0 07 032 |  |  |  |  | Height of sensor above local ground | m, 2 |
|  | 0 02 175 |  |  |  | * | Method of precipitation measurement | Code table, 0 |
|  | 0 02 178 |  |  |  | * | Method of liquid water content measurement of precipitation | Code table, 0 |
|  | 1 02 005 |  |  |  |  | Replicate 2 descriptors 5 times |  |
|  | 0 04 024 |  |  |  |  | Time period in hours tR (= - 1 hour in the first replication, = - 3, -6, -12 and - 24 hours in the other replications) | Hour, 0 |
|  | 0 13 011 |  |  |  |  | Total precipitation / total water equivalent of snow | kg m-2, 1 |
|  | 0 07 032 |  |  |  | * | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
|  |  |  |  |  |  | Evaporation data |  |
|  | 1 03 000 |  |  |  |  | Delayed replication of 3 descriptors |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 0 02 185 |  |  |  | * | Method of evaporation measurement | Code table, 0 |
|  | 1 01 002 |  |  |  |  | Replicate 1 descriptor 2 times |  |
|  | 3 02 044 | 0 04 024 |  | * |  | Time period in hours (= -1 hour in 1. replication, = -24 hours in 2. replication) | Hour, 0 |
|  |  | 0 02 004 |  | * |  | Type of instrument for evaporation measurement or type of crop | Code table, 0 |
|  |  | 0 13 033 |  |  |  | Evaporation /evapotranspiration | kg m-2, 1 |
|  |  |  |  |  |  | Total sunshine data |  |
|  | 1 02 000 |  |  |  |  | Delayed replication of 2 descriptors |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 1 01 002 |  |  | * |  | Replicate 1 descriptor 2 times |  |
|  | 3 02 039 | 0 04 024 |  | * |  | Time period in hours (= -1 hour in 1. replication, = -24 hours in 2. replication) | Hour, 0 |
|  |  | 0 14 031 |  |  |  | Total sunshine | Minute, 0 |
|  |  |  |  |  |  | Radiation data |  |
|  | 1 02 000 |  |  |  |  | Delayed replication of 2 descriptors |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 1 01 002 |  |  | * |  | Replicate 1 descriptor 2 times |  |
|  | 3 02 045 | 0 04 024 |  | * |  | Time period in hours (= -1 hour in 1. replication, = -24 hours in 2. replication) | Hour, 0 |
|  |  | 0 14 002 |  |  |  | Long-wave radiation, integrated over period specified | J m-2, -3 |
|  |  | 0 14 004 |  |  |  | Short-wave radiation, integrated over period specified | J m-2, -3 |
|  |  | 0 14 016 |  |  |  | Net radiation, integrated over period specified | J m-2, -4 |
|  |  | 0 14 028 |  |  |  | Global solar radiation (high accuracy), integrated over period specified | J m-2, -2 |
|  |  | 0 14 029 |  |  |  | Diffuse solar radiation (high accuracy), integrated over period specified | J m-2, -2 |
|  |  | 0 14 030 |  |  |  | Direct solar radiation (high accuracy), integrated over period specified | J m-2, -2 |
|  |  |  |  | * |  | Temperature change gr. 54g0sndT |  |
|  | 1 01 000 |  |  |  |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  |  |  |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 046 | 0 04 024 |  | * |  | Time period or displacement | Hour, 0 |
|  |  | 0 04 024 |  | * |  | Time period or displacement (see Note 6) | Hour, 0 |
|  |  | 0 12 049 |  | * |  | Temperature change over period specified sndT | K, 0 |
|  |  |  |  |  | * | First order statistics of P, W, T, U data |  |
|  | 1 01 000 |  |  |  |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  |  |  | * | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 083 | 0 04 025 |  |  | * | Time period (= -10 minutes ) | Minute, 0 |
|  |  | 0 08 023 |  |  | * | First order statistics (see Note 7) (= 9 (best estimate of standard deviation)) | Code table, 0 |
|  |  | 0 10 004 |  |  | * | Pressure | Pa, –1 |
|  |  | 0 11 001 |  |  | * | Wind direction | Degree true, 0 |
|  |  | 0 11 002 |  |  | * | Wind speed | m s-1, 1 |
|  |  | 0 12 101 |  |  | * | Temperature/dry-bulb temperature (scale 2) | K, 2 |
|  |  | 0 13 003 |  |  | * | Relative humidity | %, 0 |
|  |  | 0 08 023 |  |  | * | First order statistics (= missing value) | Code table, 0 |
| 0 33 005 |  |  |  |  | * | Quality information (AWS data) | Flag table, 0 |
| 0 33 006 |  |  |  |  | * | Internal measurement status information (AWS) | Code table, 0 |

Notes:

- The WMO international identification 0 01 001 (WMO block number) and 0 01 002 (WMO station number) shall be reported as mandatory if available for the particular station. 0 01 101 (WMO Member State identifier) and 0 01 102 (National AWS number) may be used to identify a station within the national numbering system. If the WMO station identification is not available for the particular station, the National station identification shall be used.

- When reported, present weather shall be always represented by 0 20 003. When encoding present weather reported from an automatic weather station, the sequence of descriptors (proposed under 3 02 076) should also be used, if applicable.

- Duration of precipitation represents number of minutes in which precipitation was registered.

- Within RA IV, the maximum temperature at 1200 UTC is reported for the previous calendar day (i.e. the ending time of the period is not equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

- Within RA III, the maximum day-time temperature and the minimum night-time temperature is reported (i.e. the ending time of the period may not be equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

- To construct the required time range, descriptor 004024 has to be included two times.

- Best estimate of standard deviation is counted out of a set of samples (signal measurements) recorded within the period specified; it should be reported as a missing value, if the measurements of the relevant element are not available from a part of the period specified by 0 04 025.

(8)	   Additional parameters required by regional or national reporting practices shall be accommodated in a similar way as recommended in Regulations B/C 1.9 and B/C 1.14 – Regulations for reporting SYNOP data in TDCF.

# BUFR TEMPLATE FOR SYNOPTIC REPORTS FROM FIXED LAND STATIONS SUITABLE FOR SYNOP DATA AND FOR MARITIME DATA FROM COASTAL AND ISLAND STATIONS

Proposals

a)  A new descriptor 0 20 058 (Visibility seawards from a coastal station) is proposed:

|  |  | BUFR | CREX |
| --- | --- | --- | --- |
| Table reference | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 20 058 | Visibility seawards from a coastal station | m | -1 | 0 | 13 | m | -1 | 4 |

b) TM 307079 as included in the ANNEX is proposed for pre-operational usage, provided that testing of the template takes place by the end of 2008.

TM 307079 - BUFR template for synoptic reports from fixed land stations suitable for SYNOP data and for maritime data from coastal and island stations

| 3 07 079 |  | Sequence for representation of synoptic reports from fixed land stations suitable for SYNOP data and for maritime data from coastal stations |
| --- | --- | --- |
|  | 3 01 090 | Fixed surface station identification, time, horizontal and vertical coordinates |
|  | 3 02 031 | Pressure data |
|  | 3 02 035 | Basic synoptic “instantaneous” data |
|  | 3 02 036 | Clouds with bases below station level |
|  | 1 01 000 | Delayed replication of 1 descriptor |
|  | 0 31 000 | Short delayed descriptor replication factor |
|  | 3 02 047 | Direction of cloud drift |
|  | 0 08 002 | Vertical significance |
|  | 1 01 000 | Delayed replication of 1 descriptor |
|  | 0 31 000 | Short delayed descriptor replication factor |
|  | 3 02 048 | Direction and elevation of cloud |
|  | 3 02 037 | State of ground, snow depth, ground minimum temperature |
|  | 1 02 000 | Delayed replication of 2 descriptors |
|  | 0 31 000 | Short delayed descriptor replication factor |
|  | 0 22 061 | State of the sea |
|  | 0 20 058 | Visibility seawards from a coastal station |
|  | 1 01 000 | Delayed replication of 1 descriptor |
|  | 0 31 000 | Short delayed descriptor replication factor |
|  | 3 02 056 | Sea/water surface temperature, method of measurement, depth below water surface |
|  | 1 01 000 | Delayed replication of 1 descriptor |
|  | 0 31 000 | Short delayed descriptor replication factor |
|  | 3 02 055 | Icing and ice |
|  | 3 02 043 | Basic synoptic “period” data |
|  | 3 02 044 | Evaporation data |
|  | 1 01 000 | Delayed replication of 1 descriptor |
|  | 0 31 001 | Delayed descriptor replication factor |
|  | 3 02 045 | Radiation data |
|  | 1 01 000 | Delayed replication of 1 descriptor |
|  | 0 31 000 | Short delayed descriptor replication factor |
|  | 3 02 046 | Temperature change |

TM 307079 (BUFR template for synoptic reports from fixed land stations suitable for SYNOP data and for maritime data from coastal and island stations) further expands as follows:

|  |  |  |  | Unit, scale |
| --- | --- | --- | --- | --- |
| 3 01 090 |  |  | Fixed surface station identification, time, horizontal and vertical coordinates |  |
|  | 3 01 004 | 0 01 001 | WMO block number II | Numeric, 0 |
|  |  | 0 01 002 | WMO station number iii | Numeric, 0 |
|  |  | 0 01 015 | Station or site name | CCITT IA5, 0 |
|  |  | 0 02 001 | Type of station (ix) | Code table, 0 |
|  | 3 01 011 | 0 04 001 | Year | Year, 0 |
|  |  | 0 04 002 | Month | Month, 0 |
|  |  | 0 04 003 | Day YY | Day, 0 |
|  | 3 01 012 | 0 04 004 | Hour GG | Hour, 0 |
|  |  | 0 04 005 | Minute gg | Minute, 0 |
|  | 3 01 021 | 0 05 001 | Latitude (high accuracy) | Degree, 5 |
|  |  | 0 06 001 | Longitude (high accuracy) | Degree, 5 |
|  | 0 07 030 |  | Height of station ground above mean sea level | m, 1 |
|  | 0 07 031 |  | Height of barometer above mean sea level | m, 1 |
| 3 02 031 |  |  | Pressure data |  |
|  | 3 02 001 | 0 10 004 | Pressure P0P0P0P0 | Pa, –1 |
|  |  | 0 10 051 | Pressure reduced to mean sea level PPPP | Pa, –1 |
|  |  | 0 10 061 | 3-hour pressure change ppp | Pa, –1 |
|  |  | 0 10 063 | Characteristic of pressure tendency a | Code table, 0 |
|  | 0 10 062 |  | 24-hour pressure change p24p24p24 | Pa, –1 |
|  | 0 07 004 |  | Pressure (standard level) a3 | Pa, –1 |
|  | 0 10 009 |  | Geopotential height of the standard level hhh | gpm, 0 |
| 3 02 035 |  |  | Basic synoptic “instantaneous” data |  |
|  |  |  | Temperature and humidity data |  |
|  | 3 02 032 | 0 07 032 | Height of sensor above local ground (for temperature and humidity measurement) | m, 2 |
|  |  | 0 12 101 | Temperature/dry-bulb temperature(sc.2) snTTT | K, 2 |
|  |  | 0 12 103 | Dew-point temperature (scale 2) snTdTdTd | K, 2 |
|  |  | 0 13 003 | Relative humidity | %, 0 |
|  |  |  | Visibility data |  |
|  | 3 02 033 | 0 07 032 | Height of sensor above local ground (for visibility measurement) | m, 2 |
|  |  | 0 20 001 | Horizontal visibility VV | m, –1 |
|  |  |  | Precipitation past 24 hours |  |
|  | 3 02 034 | 0 07 032 | Height of sensor above local ground (for precipitation measurement) | m, 2 |
|  |  | 0 13 023 | Total precipitation past 24 hours R24R24R24R24 | kg m-2, 1 |
|  | 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
|  |  |  | Cloud data |  |
|  | 3 02 004 | 0 20 010 | Cloud cover (total) N | %, 0 |
|  |  | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (of low or middle clouds) Nh | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud h | m, –1 |
|  |  | 0 20 012 | Cloud type (low clouds CL) CL | Code table, 0 |
|  |  | 0 20 012 | Cloud type (middle clouds CM) CM | Code table, 0 |
|  |  | 0 20 012 | Cloud type (high clouds CH) CH | Code table, 0 |
|  |  |  | Individual cloud layers or masses |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 001 |  | Delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 005 | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (Ns) Ns | Code table, 0 |
|  |  | 0 20 012 | Cloud type (C) C | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud (hshs) hshs | m, -1 |
|  |  |  | Clouds with bases below station level |  |
| 3 02 036 | 1 05 000 |  | Delayed replication of 5 descriptors |  |
|  | 0 31 001 |  | Delayed descriptor replication factor | Numeric, 0 |
|  | 0 08 002 |  | Vertical significance | Code table, 0 |
|  | 0 20 011 |  | Cloud amount N’ | Code table, 0 |
|  | 0 20 012 |  | Cloud type C’ | Code table, 0 |
|  | 0 20 014 |  | Height of top of cloud H’H’ | m, -1 |
|  | 0 20 017 |  | Cloud top description Ct | Code table, 0 |
|  |  |  | Direction of cloud drift gr. 56DLDMDH |  |
| 1 01 000 |  |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 047 | 1 02 003 |  | Replicate 2 descriptors 3 times |  |
|  | 0 08 002 |  | Vertical significance = 7 (low cloud) = 8 (middle cloud) = 9 (high cloud) | Code table, 0 |
|  | 0 20 054 |  | True direction from which clouds are moving DL, DM, DH | Degree true, 0 |
| 0 08 002 |  |  | Vertical significance (set to missing to cancel the previous value) | Code table, 0 |
|  |  |  | Direction and elevation of cloud gr. 57CDaeC |  |
| 1 01 000 |  |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 048 | 0 05 021 |  | Bearing or azimuth Da | Degree true, 2 |
|  | 0 07 021 |  | Elevation angle eC | Degree, 2 |
|  | 0 20 012 |  | Cloud type C | Code table, 0 |
|  | 0 05 021 |  | Bearing or azimuth (set to missing to cancel the previous value) | Degree true, 2 |
|  | 0 07 021 |  | Elevation angle (set to missing to cancel the previous value) | Degree, 2 |
|  |  |  | State of ground, snow depth, ground minimum temperature |  |
| 3 02 037 | 0 20 062 |  | State of ground (with or without snow) E or E’ | Code table, 0 |
|  | 0 13 013 |  | Total snow depth sss | m, 2 |
|  | 0 12 113 |  | Ground minimum temperature (scale2), past 12 hours snTgTg | K, 2 |
|  |  |  | State of the sea |  |
| 1 02 000 |  |  | Delayed replication of 2 descriptors |  |
| 0 31 000 |  |  | Short delayed descriptor replication factor | Numeric, 0 |
| 0 22 061 |  |  | State of the sea S | Code table, 0 |
| 0 20 058 |  |  | Visibility seawards from a coastal station VS | m, -1 |
|  |  |  | Sea/water surface temperature, method of measurement, and depth below sea surface |  |
| 1 01 000 |  |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 056 | 0 02 038 |  | Method of sea/water temperature measurement | Code table, 0 |
|  | 0 07 063 |  | Depth below sea/water surface (for sea surface temperature measurement) | m, 2 |
|  | 0 22 043 |  | Sea/water temperature ssTwTwTw or 925TwTw | K, 2 |
|  | 0 07 063 |  | Depth below sea/water surface (set to missing to cancel the previous value) | m, 2 |
|  |  |  | Icing and ice |  |
| 1 01 000 |  |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 055 | 0 20 031 |  | Ice deposit (thickness) EsEs | m, 2 |
|  | 0 20 032 |  | Rate of ice accretion Rs | Code table, 0 |
|  | 0 20 033 |  | Cause of ice accretion Is | Flag table, 0 |
|  | 0 20 034 |  | Sea ice concentration ci | Code table, 0 |
|  | 0 20 035 |  | Amount and type of ice bi | Code table, 0 |
|  | 0 20 036 |  | Ice situation zi | Code table, 0 |
|  | 0 20 037 |  | Ice development Si | Code table, 0 |
|  | 0 20 038 |  | Bearing of ice edge Di | Degree true, 0 |
| 3 02 043 |  |  | Basic synoptic “period” data |  |
|  |  |  | Present and past weather |  |
|  | 3 02 038 | 0 20 003 | Present weather ww | Code table, 0 |
|  |  | 0 04 024 | Time period in hours | Hour, 0 |
|  |  | 0 20 004 | Past weather (1) W1 | Code table, 0 |
|  |  | 0 20 005 | Past weather (2) W2 | Code table, 0 |
|  |  |  | Sunshine data (from 1 hour and 24 hour period) |  |
|  | 1 01 002 |  | Replicate 1 descriptors 2 times |  |
|  | 3 02 039 | 0 04 024 | Time period in hours | Hour, 0 |
|  |  | 0 14 031 | Total sunshine SS and SSS | Minute, 0 |
|  |  |  | Precipitation measurement |  |
|  | 3 02 040 | 0 07 032 | Height of sensor above local ground (for precipitation measurement) | m, 2 |
|  |  | 1 02 002 | Replicate next 2 descriptors 2 times |  |
|  |  | 0 04 024 | Time period in hours tR | Hour, 0 |
|  |  | 0 13 011 | Total precipitation / total water equivalent of snow RRR | kg m-2, 1 |
|  |  |  | Extreme temperature data |  |
|  | 3 02 041 | 0 07 032 | Height of sensor above local ground (for temperature measurement) | m, 2 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  | 0 04 024 | Time period or displacement (see Notes 1 and 2) | Hour, 0 |
|  |  | 0 12 111 | Maximum temperature (scale 2) at height and over period specified snTxTxTx | K, 2 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  | 0 04 024 | Time period or displacement (see Note 2) | Hour, 0 |
|  |  | 0 12 112 | Minimum temperature (scale 2) at height and over period specified snTnTnTn | K, 2 |
|  |  |  | Wind data |  |
|  | 3 02 042 | 0 07 032 | Height of sensor above local ground (for wind measurement) | m, 2 |
|  |  | 0 02 002 | Type of instrumentation for wind measurement iw | Flag table, 0 |
|  |  | 0 08 021 | Time significance (= 2 (time averaged)) | Code table, 0 |
|  |  | 0 04 025 | Time period (= - 10 minutes, or number of minutes after a significant change of wind) | Minute, 0 |
|  |  | 0 11 001 | Wind direction dd | Degree true, 0 |
|  |  | 0 11 002 | Wind speed ff | m s-1, 1 |
|  |  | 0 08 021 | Time significance (= missing value) | Code table, 0 |
|  |  | 1 03 002 | Replicate next 3 descriptors 2 times |  |
|  |  | 0 04 025 | Time period in minutes | Minute, 0 |
|  |  | 0 11 043 | Maximum wind gust direction | Degree true, 0 |
|  |  | 0 11 041 | Maximum wind gust speed 910fmfm, 911fxfx | m s-1, 1 |
|  | 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
|  |  |  | Evaporation data |  |
| 3 02 044 | 0 04 024 |  | Time period in hours | Hour, 0 |
|  | 0 02 004 |  | Type of instrument for evaporation or crop type for evapotranspiration iE | Code table, 0 |
|  | 0 13 033 |  | Evaporation /evapotranspiration EEE | kg m-2, 1 |
|  |  |  | Radiation data (from 1 and/or 24 hour period) |  |
| 1 01 000 |  |  | Delayed replication of 1 descriptor |  |
| 0 31 001 |  |  | Delayed descriptor replication factor | Numeric, 0 |
| 3 02 045 | 0 04 024 |  | Time period in hours | Hour, 0 |
|  | 0 14 002 |  | Long-wave radiation, integrated over period specified 553SS 4FFFF or 553SS 5FFFF, 55SSS 4F24F24F24F24 or 55SSS 5F24F24F24F24 | J m-2, -3 |
|  | 0 14 004 |  | Short-wave radiation, integrated over period specified 553SS 6FFFF, 55SSS 6F24F24F24F24 | J m-2, -3 |
|  | 0 14 016 |  | Net radiation, integrated over period specified 553SS 0FFFF or 553SS 1FFFF, 55SSS 0F24F24F24F24 or 55SSS 1F24F24F24F24 | J m-2, -4 |
|  | 0 14 028 |  | Global solar radiation (high accuracy), integrated over period specified 553SS 2FFFF, 55SSS 2F24F24F24F24 | J m-2, -2 |
|  | 0 14 029 |  | Diffuse solar radiation (high accuracy), integrated over period specified 553SS 3FFFF, 55SSS 3F24F24F24F24 | J m-2, -2 |
|  | 0 14 030 |  | Direct solar radiation (high accuracy), integrated over period specified 55408 4FFFF, 55508 5F24F24F24F24 | J m-2, -2 |
|  |  |  | Temperature change group 54g0sndT |  |
| 1 01 000 |  |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 046 | 0 04 024 |  | Time period or displacement | Hour, 0 |
|  | 0 04 024 |  | Time period or displacement (see Note 3) | Hour, 0 |
|  | 0 12 049 |  | Temperature change over period specified sndT | K, 0 |

Notes:

1)	Within RA IV, the maximum temperature at 1200 UTC is reported for the previous calendar day (i.e. the ending time of the period is not equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

2)	Within RA III, the maximum day-time temperature and the minimum night-time temperature is reported (i.e. the ending time of the period may not be equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

3)	To construct the required time range, descriptor 004024 has to be included two times.

TEMPLATE FOR PASSING LOCUST INFORMATION

3 02 089 (LOCUST INFORMATION)

| 3 02 089 |  | Locust information |
| --- | --- | --- |
|  | 0 20 101 | Locust (acridian) name Ln |
|  | 0 20 102 | Locust (maturity) color Lc |
|  | 0 20 103 | Stage of development of locusts Ld |
|  | 0 20 104 | Organization state of swarm or band of locusts Lg |
|  | 0 20 105 | Size of swarm or band of locusts and duration of passage of swarm sL |
|  | 0 20 106 | Locust population density dL |
|  | 0 20 107 | Direction of movements of locust swarm DL |
|  | 0 20 108 | Extent of vegetation ve |

Extract of regulations:

B/C 1.9.1.3 Locust control-related observations

Following data shall be reported by all Members capable of doing so:

- Locust (acridian) name (Code table 0 20 101),

- Locust (maturity) color (Code table 0 20 102),

- Stage of development of locusts (Code table 0 20 103),

- Organization state of swarm or band of locusts (Code table 0 20 104),

- Size of swarm or band of locusts and duration of passage of swarm (Code table 0 20 105),

- Locust population density (Code table 0 20 106),

- Direction of movements of locust swarm (Code table 0 20 107),

- Extent of vegetation (Code table 0 20 108). [1/12.14.1]

WIND REPORTING AT POLES

To add the following note (7) to the Class 11 of the BUFR/CREX Table B

“(7) Surface wind direction measured at a station within 1° of the North Pole or within 1° of the South Pole shall be reported in such a way that the azimuth ring shall be aligned with its zero coinciding with the Greenwich 0° meridian."

NEW DESCRIPTOR FOR INTENSITY OF PRECIPITATION

To introduce a new Table B descriptor 0 13 155

| Table Ref. | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| FXY |  | Unit | Scale | Ref. value | Data width (bits) | Unit | Scale | Data width (chars) |
| 0 13 155 | Intensity of precipitation (high accuracy) | kg m-2 s-1 | 5 | -1 | 16 | mm h-1 | 1 | 5 |

To introduce a new Table D-descriptor 3 02 175

3 02 175 = 0 08 021

0 04 025

0 13 155

0 13 058

0 08 021

To replace 0 13 055 by 0 13 155 in 3 07 091 and 3 07 096.

To replace 3 02 075 by 3 02 175 in 3 07 091 and 3 07 096.

ADDITION OF A CODE FIGURE

To add the following code figure to the BUFR/CREX Code Table 0 08 002

| Code figure |  |
| --- | --- |
| 20 | No clouds detected by the cloud detection system |

# Footnotes

FirstFixedSurface and SecondFixedSurface of Code Table 4.5 (Fixed surface types and units) to define the vertical extent, i.e. FirstFixedSurface can be set to 1 (Ground or water surface) and SecondFixedSurface set to 7 (Tropopause) for a restriction to the troposphere.