## Slide 1: Overview of Timeseries and TimeseriesML
Note: These slides were adapted from presentation by James Tomkins (UK Met Office) at the June 2015 OGC TC

## Slide 2: Overview
Background
Introducing the Candidate Standard
Conceptual Model Overview
Implementation Model Overview
Possible Future Work

## Slide 3: WaterML2.0 > TimeSeriesML
– 2012 –
WaterML 2.0
Part 1 - Timeseries Adopted
– 2013 –
RFC 13-123 requests migration out of hydrology domain to TimeseriesML
– Sept 2014 –
Intention to form SWG for TimeseriesML
– Dec 2014 –
SWG Charter approved at Tokyo TC
IPET-MDRD-1
March 2014

## Slide 4: Charter for TimeseriesML
WaterML2.0 Timeseries model as a starting point
Make the model 'domain agnostic'
  Make extension points available
Limit scope to simple timeseries observations
  Future scope may cover more complex cases

## Slide 5: Two standards: Conceptual & Implementation
Timeseries Profile
TimeseriesML 1.0
Timeseries Profile of Observations and Measurements
XML Encoding of the Timeseries Profile of Observations and Measurements

## Slide 6: Conceptual Model – Definition of Timeseries
  A sequence of data values which are ordered in time. The sequence typically records (or predicts) the value of a property of a feature over a time interval, with interim values at times within the interval. These times are monotonic and are often, but not always, at regular intervals (e.g. an hourly timeseries).
  Timeseries (noun)

## Slide 7: Conceptual Model – Definition of Timeseries
“.. a time series in the context of observational data can be seen as a discrete coverage as defined by ISO 19123*, where the domain is a spatiotemporal axis and the range is all the possible values of the observed property.”
Timeseries Profile of Observations and Measurements
[DRAFT]
*ISO 19123, Geographic Information – coverage schema
Note this is not the same thing as the ESRI coverage model (format)

## Slide 8: Conceptual Model - based on O&M
Timeseries is the 'result' of an Observation
Notes: Profile of O&M: result = Timeseries

## Slide 9: Conceptual Model – Profiling O&M
Timeseries Profile components | O & M 2.0 concepts
Timeseries and metadata about timeseries | Result
Observation specialisations | Observation
Procedures used in measurement/analysis/processing | Procedure
Monitoring Features | Sampling features
Collections | -

## Slide 10: Conceptual Model – Timeseries Observation
Single Observed Property
Time, Value Pair or Domain/Range Structures
Context Metadata
Multiple properties are therefore captured as discrete timeseries observation
2 different structures for efficiency and intuitiveness
TimeseriesObservation provides the exchange context for the timeseries e.g. process, feature, discovery etc

## Slide 11: Conceptual Model – Timeseries Observation
2 Value Types
Result Specific Metadata
Standalone Timeseries
Measures and Categories
Covers interpretation of the timeseries itself e.g. spacing, temporal extent etc
Timeseries class available for use without TimeseriesObservation

## Slide 12: Conceptual Model - Timeseries
The core of the model is the precise description of a timeseries.

## Slide 13: Conceptual Model - Timeseries
Anchor Points
Gap Periods

## Slide 14: Conceptual Model - Timeseries
Accumulations
Interpolation
Types

## Slide 15: Conceptual Model - Timeseries
Timeseries Metadata
baseTime
spacing
sampledMedium
intendedObservationSpacing
startAnchorPoint/endAnchorPoint
maxGapPeriod
...
accumulationIntervalLength/AnchorTime

## Slide 16: Conceptual Model - Timeseries
Point Metadata
quality
qualifier
processing
interpolationType
…

## Slide 17: Conceptual Model – Monitoring Feature

## Slide 18: Conceptual Model - Process
The Timeseries Profile defines an ObservationProcess feature type. This is a generic class to describe processes related to the creation of results.
The standard also permits use of other process definitions derived from
OM_Process
or
SWE AbstractProcess

## Slide 19: Conceptual Model - Collection

## Slide 20: Conceptual Model - Codelists
DataQuality
Good, Suspect, Estimate, Poor, Unchecked, Missing
InterpolationType
Continuous, Discontinuous, InstantTotal, AveragePrec, MaxPrec, MinPrec, PrecTotal, AverageSucc, TotalSucc, MinSucc, MaxSucc, ConstPrec, ConstSucc
ProcessType
Algorithm, Manual Method, Sensor, Simulation, Unknown

## Slide 21: Implementation Model (XML)
Separate UML Model supporting auto-generated XML Schema
  Follows UML to GML encoding rules including GML 3.3 rules for reference types (codelists).
Principles are:
  Support all aspects of the conceptual model
  Follow UML to GML encoding rules
  Make pragmatic encoding choices – this is a physical data model.
    Reduce number of classes in order to simplify XML encoding as much as possible
    Build on existing OGC encoding standards

## Slide 22: Implementation Model - Mapping to Concepts
Collection/Metadata
OM Observation
Time Value Pair Encoding
Domain Range Encoding
Point Metadata
Specialised data types
Process
Monitoring feature

## Slide 23: Implementation – Time, Value Pair encoding

## Slide 24: Implementation – Time, Value Pairs
    Simple interleaved time, value pair encodings.
<tsml:point>
<tsml:MeasurementTVP>
<tsml:time>2012-06-13T00:30:00.000+12:00</tsml:time>
<tsml:value>2.04</tsml:value>
</tsml:MeasurementTVP>
</tsml:point>
    Metadata e.g. quality measures, comments, etc. may be may set to a default for every value in the series
    Individual time, value pairs may override the default

## Slide 25: Imlementation – Domain Range encoding
  Uses GMLCov
  Defines a 'Timeseries metadata extension' to GML Cov
    Embeds the timeseries metadata in regular GMLCov Coverage
    Also supports Annotation Coverages
      Not tightly defined.
    See example:
    https://svn.opengeospatial.org/ogc-projects/sp/timeSeriesML.swg/trunk/xsd/examples/measurement-timeseries-soilmoisture-avg-dr.xml

## Slide 26: Possible (OGC) Future work?
?
Encodings
JSON, NetCDF etc
Multi Parameter
Result Types
Vector, Coverage etc
Harmonisation
Coverages, IOT etc

## Slide 27: Appendix: TimeseriesML is fully model-driven
Model contains:
Definitions
Diagrams
Requirements
Conformance classes
Specifications were auto-generated from UML model using EA and RTF (rich text format) templates
Provides consistency throughout model, spec and schemas.
RTF
Templates
Specification!
Fully Documented Model
XSD Schemas

## Slide 28: Thank you for your attention
Dominic Lowe
Australian Bureau of Meteorology
d.lowe@bom.gov.au