## Slide 1: Use of metadata in the development of long-term climate data sets
Blair Trewin, Australian Bureau of Meteorology

## Slide 2: What underlies climate information of this type?

## Slide 3: The Australian ACORN-SAT station network
Largely based on 2001 daily network
10 stations with recently digitised data added (black dots) – 1 station removed due to poor quality
More stations may be considered for addition later once pre-1957 data digitised
Urbanised stations are part of network but not used for climate change reporting

## Slide 4: Why do we need a homogenised data set?
Pre-1948 site at
Post Office –
near ocean
Post-1948 site at airport –
several km inland
Homogeneous data give us confidence that changes in the observations reflect real changes in the climate
Temperature (°C)

## Slide 5: Some things which can lead to inhomogeneities in a data set
Site moves
Changes in instruments
Changes in local site environment
Observing practice changes (e.g. observation time)

## Slide 6: Use of metadata in the homogenisation process
Determining that a change which may lead to an inhomogeneity has happened
Finding possible explanations for an inhomogeneity detected by statistical methods

## Slide 7: Metadata used to confirm an inhomogeneity
2011
2003
Statistical testing found an inhomogeneity (0.6°C annual, 1.0°C dry season) in maximum temperature in 2007 – station photos show that watering of site stopped then

## Slide 8: Australia has numerous sources of metadata
Station-specific
SitesDB (digital database) – since 1997 (with very limited pre-1997 information)
Hard-copy station files – both national (mostly scanned) and regional (state)
Instrument registers (mostly pre-1920)
General
Observer instructions/guides/procedures
Instrument test reports
Organisation annual reports and similar documents

## Slide 9: Some examples of material from SitesDB

## Slide 10: Material from hard-copy station files
In more recent times (1980s onwards) typically inspection reports at least every 2-3 years
Some aspects well documented (e.g. instrument changes), others less well (e.g. site environment)
Files usually contain large amounts of irrelevant material (e.g. financial records)
Metadata of all kinds becomes sparser further back in time

## Slide 11: Rutherglen – a case study of the challenges in metadata
Minimum temperatures at Rutherglen clearly cooler in later years relative to other sites
Statistical tests found inhomogeneities in 1966 and 1974

## Slide 12: What evidence do we have for site moves at Rutherglen?
Site photos from December 2012 (left) and February 1975 (right) show no significant site move since at least 1975

## Slide 13: 1958 inspection report
Woolshed 150 feet to west and no road nearby (left) and site ¼ mile from office (right) – do not match current site

## Slide 14: Other inconsistencies with current site
Hill rises 300 yards south of site (1953) – no hills for several kilometres south of current site
'Station flat but country falls slightly to north' (1939) – current site has hill rising to north

## Slide 15: Other useful information
Information on new enclosure layout (January 1966 (?), left); new co-ordinates (November 1974, right)

## Slide 16: Likely former site location

## Slide 17: Summary
Metadata are highly important in developing long-term climate data sets
Metadata cannot be assumed to be complete, especially for older data
Metadata often require considerable interpretation
Many forms of metadata are not amenable to being summarised in a database entry

## Slide 18
Blair Trewin
b.trewin@bom.gov.au
Thank you…