## Slide 1
EUMETNET preliminary positions on WRC-19 agenda Submitted by: Philippe Tristant (Eumetnet) (Doc 06.1)
Steering Group on Radio Frequency Coordination (SG-RFC)
WMO, Geneva.
24-27 January 2017

## Slide 2: Agenda Items of interest for EUMETNET
A.I. | Issue | Resolution | CPG group
1.1 | Amateur service in the 50-54 MHz band | 658 | PTD
1.2 | Satellite hard limits at 400 MHz | 765 | PTA
1.3 | METSAT and EESS at 460-470 MHz | 766 | PTA
1.6 | Non GSO FSS at 37.5-51.4 GHz | 159 | PTB
1.7 | Small satellites | 659 | PTA
1.13 | IMT 5G | 238 | ECC/PT1
1.14 | HAPS | 160 | PTA
1.15 | FS/MS above 275 GHz | 767 | PTA
1.16 | RLAN 5 GHz | 239 | PTD
9.1.5 | RLAN 5 GHz (radars) | 764 | PTD
9.1.6 | Wireless Power Transmission (WPT) | 958 | PTD
9.1.9 | FSS at 51.4-52.4 GHz | 162 | PTB

## Slide 3
Agenda item 1.1 : to consider an allocation of the frequency band 50-54 MHz to the amateur service in Region 1, in accordance with Resolution 658 (WRC-15)
Studies required
  Sharing between Amateur service and radiolocation limited to Wind Profilers in the 50-54 MHz band
Difficulties foreseen
  Primary status for amateur service against secondary status for radiolocation
  Potential willingness to also include amateur-satellite service
CPG responsible group
  CPG/PTD
EUMETNET position
  No opposition to an allocation to amateur service in the 50-54 MHz under the condition of protection of radiolocation service and provided it is made at equal status with radiolocation
  Opposition to any amateur-satellite service in the band

## Slide 4
Agenda item 1.2 : to consider in-band power limits for earth stations operating in the mobile-satellite service, meteorological-satellite service and Earth exploration-satellite service in the frequency bands 401-403 MHz and 399.9-400.05 MHz, in accordance with Resolution 765 (WRC-15)
Studies required
  Sharing between telecommand links using these allocations and the current systems operating in this band for data collection within the METSAT (A-DCS) and the EESS (ARGOS) to ensure the proper continuation of their operations
Difficulties foreseen
  Cross-linkage with AI 1.7 on SOS allocation for small satellites for the band 401-403 MHz.
CPG responsible group
  CPG/PTA
EUMETNET position
  Support the establishment of in band power limits to ensure the proper continuation of METSAT and EESS (Earth-to-space) operations in the 401-403 MHz

## Slide 5
Agenda item 1.3 : to consider possible upgrading of the secondary allocation to the meteorological satellite service (space-to-Earth) to primary status and a possible primary allocation to the Earth exploration-satellite service (space-to-Earth) in the frequency band 460-470 MHz, in accordance with Resolution 766 (WRC-15)
Studies required
  Sharing of EESS (s-E) and METSAT (s-E) with FS and MS
  Sharing between EESS (s-E) and METSAT (s-E)
Difficulties foreseen
  The use of the 460-470 MHz band is already primary in some countries as per 5.290 subject to agreement obtained under 9.21, without any pfd limit. This includes China, Japan, Russia. Potential conflict for systems using this band and not respecting the -152 dBW/m²/4 kHz limit.
  Possibility of results of studies giving an even lower pfd value difficult to meet.
  Band identified for IMT
CPG responsible group
  CPG/PTA
EUMETNET position
  Support the upgrading to primary of the METSAT (space-to-Earth) allocation in the frequency band 460-470 MHz
  Support a primary allocation to the EESS (space-to-Earth) in the frequency band 460-470 MHz provided the priority of METSAT is maintained.

## Slide 6
Agenda item 1.6 : to consider the development of a regulatory framework for non-GSO FSS satellite systems that may operate in the frequency bands 37.5-39.5 GHz (space-to-Earth), 39.5-42.5 GHz (space-to-Earth), 47.2-50.2 GHz (Earth-to-space) and 50.4-51.4 GHz (Earth-to-space), in accordance with Resolution 159 (WRC-15)
Studies required
  Compatibility between non GSO FSS (s-E) in the band 37.5-42.5 GHz and EESS (passive) in the band 36-37 GHz.
  Compatibility between non GSO FSS (E-s) in the bands 47.2-50.2 GHz and 50.4-51.4 GHz and EESS (passive) in the band 50.2-50.4 GHz.
  Sharing between non GSO FSS (s-E) and EESS (E-s) in the band 40-40.5 GHz.
Difficulties foreseen
  Availability of the FSS earth stations deployment model.
  There is no guard band available around the passive band 50.2-50.4 GHz.
  Problem of compatibility with ground-based radiometers in 50.4-51.4 GHz band in relation with the low status of radiometers
CPG responsible group
  CPG/PTB
EUMETNET position
  No opposition to the development of a regulatory framework for non-GSO FSS satellite systems in the 37.5-51.4 GHz range provided that protection of EESS (Earth-to-space), EESS (passive) and ground-based radiometers is ensured.

## Slide 7
Agenda item 1.7 : to study the spectrum needs for telemetry, tracking and command in the space operation service for non-GSO satellites with short duration missions, to assess the suitability of existing allocations to the space operation service and, if necessary, to consider new allocations, in accordance with Resolution 659 (WRC-15)
Studies required
  Suitability of existing SOS allocation below 1 GHz
  If no SOS existing allocation below 1 GHz is suitable, sharing of SOS with METAIDS, METSAT (E-s) and EESS (E-s) in the 400.15-406 MHz band
Difficulties foreseen
  Double interest for scientific community, protection of METAIDS, EESS and METSAT and possible development of pico and nano satellites
  Risk of focus on the 400 MHz band
CPG responsible group
  CPG/PTA
EUMETNET position
  Support to specific SOS allocations for non-GSO satellites with short duration missions provided it does not impair the current and future use of METAIDS, METSAT and EESS (Earth-to-space) services in the 400.15-406 MHz band

## Slide 8
Agenda item 1.13 : to consider identification of frequency bands for the future development of International Mobile Telecommunications (IMT), including possible additional allocations to the mobile service on a primary basis, in accordance with Resolution 238 (WRC-15)
Studies required
  Sharing with ISS and EESS (s-E) in the band 25.25 – 27.5 GHz
  Sharing with EESS (E-s) in the band 40-40.5 GHz
  Compatibility between IMT and EESS (passive) in the bands 31.5-31.8 GHz, 36-37 GHz, 50.2-50.4 GHz, 52.6 - 54.25 GHz and 86-92 GHz
Difficulties foreseen
  Availability of the IMT characteristics not available before the 31st March 2017
  Footnotes in the band 25.5-27 GHz mentioning that EESS earth stations shall not claim protection from MS, and de facto, from IMT.
  Nothing guarantees that the Administrations will still accept to give licensees in the future to deploy new, or even continue to operate current transmitting or receiving earth stations.
  No guard band available around the passive band 50.2-50.4 GHz.
  Problem of compatibility with ground-based radiometers in relation with the low status of radiometers
CPG responsible group
  ECC/PT1
EUMETNET position
  No opposition to new IMT 5G identification/allocations provided that protection of ISS, EESS (Earth-to-space and space-to-Earth), EESS (passive) and ground based radiometers is ensured and that guarantees is given on the long-term usage of transmitting or receiving EESS earth stations (in particular in the 25.5-27 GHz band)

## Slide 9
Agenda item 1.14 : to consider, on the basis of ITU-R studies in accordance with Resolution 160 (WRC-15), appropriate regulatory actions for high-altitude platform stations (HAPS), within existing fixed-service allocations
Studies required
  Compatibility between HAPS in the band 21.4-22 GHz and EESS (passive) and radiometers in the band 21.2-21.4 GHz
  Sharing with ISS, EESS (s-E) and ground-based radiometers in the band 25.25 – 27.5 GHz
Difficulties foreseen
  The frequency band 24.25-27.5 GHz is also considered for IMT. It is therefore likely that either one or the other will enter into the band 25.25-27.5 GHz used by scientific services.
  HAPS donwlinks will have a more severe impact in EESS receiving earth stations than HAPS uplinks or IMT.
  Problem of compatibility with ground-based radiometers in relation with the low status of radiometers
CPG responsible group
  CPG/PTA
EUMETNET position
  No opposition to new HAPS identification provided that protection of ISS, EESS (space-to-Earth), EESS (passive) and ground-based radiometers is ensured and that guarantees is given on the long-term usage of transmitting or receiving EESS earth stations (in particular in the 25.5-27 GHz band)

## Slide 10
Agenda item 1.15 : to consider identification of frequency bands for use by administrations for the land mobile and fixed services applications operating in the frequency range 275-450 GHz, in accordance with Resolution 767 (WRC-15)
Studies required
  Sharing and compatibility studies between the land-mobile, fixed and passive services operating in the frequency range 275-450 GHz depending on the exact bands targeted.
Difficulties foreseen
  Radio-astronomy has identified in 5.565 bands which are not identical to EESS (passive) ones, leaving no empty band in this frequency range for FS or MS, and therefore requiring sharing.
CPG responsible group
  CPG/PTA
EUMETNET position
  No opposition to FS/MS identification in the 275-450 GHz band provided that protection of EESS (passive) is ensured

## Slide 11
Agenda item 1.16 : to consider issues related to wireless access systems, including radio local area networks (WAS/RLAN), in the frequency bands between 5 150 MHz and 5 925 MHz, and take the appropriate regulatory actions, including additional spectrum allocations to the mobile service, in accordance with Resolution 239 (WRC-15)
Studies required
  Participate in the RLAN requirements studies in order to verify the consistency of spectrum requirements with real needs as well as deployment scenarios.
  Studies to counter the rationales provided by the RLAN industry with regard to the applicability, efficiency and enforcement possibility of the proposed mitigation techniques.
  Additional studies on the compatibility between RLANs and altimeters/scatterometers (including revisiting studies performed prior WRC-03).
  Compatibility with meteorological radars in the 5350-5470 MHz, including assessment of DFS requirements
Difficulties foreseen
  Same as for WRC-15 (high pressure from RLAN industry, conflict with EC Mandate, …).
  Ambiguity for altimeters also covering the band 5470-5570 MHz
CPG responsible group
  CPG/PTD
EUMETNET position
  Opposition to new RLAN identification/allocation in the 5350-5470 MHz band
  Opposition to the outdoor usage of RLAN in the 5250-5350 MHz band

## Slide 12
Agenda item 9.1.5 : consideration of the technical and regulatory impacts of referencing Recommendations ITU-R M.1638-1 and ITU-R M.1849-1 in Nos. 5.447F and 5.450A of the Radio Regulations (Resolution 764 (WRC-15))
Studies required
  To show that reference to Recommendation ITU-R M.1849-1 will have no impact on the conditions of use of the 5600-5650 MHz band for RLAN and meteorological radars
Difficulties foreseen
  May have an impact on the decisions related to agenda item 1.16.
CPG responsible group
  CPG/PTD
EUMETNET position
  Support referencing Recommendation ITU-R M.1849-1 in No 5.450A of the Radio Regulations

## Slide 13
Agenda item 9.1.6 : Studies concerning Wireless Power Transmission (WPT) for electric vehicles
Studies required
  To better understand the WPT principles and related propagation conditions
  To confirm the frequency range under considerations for WPT (i.e. 20 to 6800 kHz range)
  To assess the potential impact of WPT on lightning detection networks
Difficulties foreseen
  WPT characteristics are currently not known
CPG responsible group
  CPG/PTD
EUMETNET position
  No opposition to study suitable harmonized frequency ranges for WPT provided that it does not impact operation of lightning detection networks operating in the 20-300 kHz range.

## Slide 14
Agenda item 9.1.9 : studies relating to spectrum needs and possible allocation of the frequency band 51.4-52.4 GHz to the fixed-satellite service (Earth-to-space) (Resolution 162 (WRC-15))
Studies required
  Compatibility between GSO FSS (E-s) in the band 51.4-52.4 GHz and EESS (passive) and ground based radiometers in the bands 50.2-50.4 GHz and 52.6-54.25 GHz .
Difficulties foreseen
  Contrary to the band 52.6-54.25 GHz, the band 50.2-50.4 GHz is not identified in the Resolution resolves 3, but studies can also be envisaged through resolves 2 depending on the interpretation of the term ‘adjacent’.
CPG responsible group
  CPG/PTB
EUMETNET position
  No opposition to the possible allocation of the frequency band 51.4-52.4 GHz to the FSS (E-s) provided that protection of EESS (passive) and ground-based radiometers is ensured.

## Slide 15: Draft Text for Report
The meeting noted the input from EUMETNET presented by Mr Tristant (Doc06.1) describing their position on WRC-19 Agenda

## Slide 16
Thank you
Merci