## Slide 1: Disaster reduction and information management - An operational view Item 2.3
Halldór Björnsson, Elín Björk Jónasdóttir, Sigrún Karlsdóttir, Sara Barsotti, Þórður Arason and & colleagues from the Icelandic Meteorological Office

## Slide 2: Structure of talk
What this talk is not about
  Disaster reduction is a big field, talk covers limited parts thereof
Short introduction to hazard monitoring as practiced at the Icelandic Meteorological Office
  Introduction to IMO
  Some notable events
Different categories of operational hazard management
  Pre –event information gathering and summarizing
  Information managment during an event
Some thoughts on information management and disaster reduction

## Slide 3: Disaster management cycle
Discussion about risk management is often structured with reference to the disaster risk management cycle.
There is a massive literature about this subject, for instance related to the UNISDR and the Sendai framework
(From the UK National Hazards Partnership, who adapted the cycle from http://eijournal.com/print/articles/disaster-management )

## Slide 4: Disaster management cycle
Discussion about risk management is often structured with reference to the disaster risk management cycle.
There is a a massive about this subject, for instance related to the UNISDR and the Sendai framework
I will only talk about information relating to risk assessment and response during an event
(From the UK National Hazards Partnership, who adapted the cycle from http://eijournal.com/print/articles/disaster-management )

## Slide 5: Icelandic Meteorological Office
The main purpose of IMO is to contribute towards increased security and efficiency in society by:
  Monitoring, analysing, interpreting, informing, giving advice and counsel, providing warnings and forecasts and where possible, predicting natural processes and natural hazards.
  Issuing public and aviation alerts about impending natural hazards, such as volcanic ash, extreme weather and flooding
Tasks
Atmosphere
Water, snow and glaciers
Earth
Ocean

## Slide 6: Infrastructure
Over 600 instruments in operation to observe natural hazards and the long term behavior of geophysical systems
Internal IT system and databases

## Slide 7: Monitoring infrastructure – a base for warnings and forecasts
water
weather
earth
other

## Slide 8: Remote sensing and forecasts
IMO is very reliant on remote sensing products and NWP models.
Forecast for Iceland and Greenland run jointly by DMI and IMO supplements a local NPW run
  Both using Harmonie
    IMO also uses ECMWF forecasts

## Slide 9
Some notable recent events (weather & water)
During winter, weather related warnings are issued on average 1 – 3 per week
From Dec 1st 2014 to March 14th 2015 there was continuously a weather related warning in place
Accumulated precipitation from Tuesday to Thursday
last week (26 – 29. Sep 2017)
Memorable storm Dec 7th 2015

## Slide 10
Eyjafjallajökull: 39 days 2 explosive phases
Widespread disruption to aviation
Grímsvötn: Intense 30 hours, duration May 21 – 30th
Little disruption outside Iceland
Bárðarbunga/Holuhraun: 6 months (Sept 2014 – Feb 2015). Effusive gas rich eruption. Gas pollution was a serious issue for local population, sulfate pollution reached continental Europe
Notable events:
Eyjafjallajökull 2010, Grímsvötn 2012 & Holuhraun in 2014/2015
(photo: Bolli Valgarðsson)
(photo: Martin Hensch, IMO)
2010
2011
2014

## Slide 11: Grímsvötn 2011
The Grimsvötn eruption was very intense but well monitored from radar and satellite.
Local ash fall south east of the volcano was very intense, making observations difficult
Some ash may have reached Greenland and SO2 went further, but otherwise this eruption only caused local problems
Two days later and the ash would have blown to Europe

## Slide 12: Grímsvötn 2011 – satellite products
10 hours into the eruption
18 hours into the eruption
32 hours into the eruption
s
Blue is ~ ash
The eruption started late on the 21 of May
Satellite images (Modis & Seviri) show the ash cloud.
AIRS sounder data shows SO2 for the next days
May 22.
May 23.
May 24.

## Slide 13: Bárðarbunga 2014
Bárðarbunga central volcano
Holuhraun eruption
16th of August 2014 – intense seismic activity
  1000 - 2000 earthquakes per day
  The generation of a dyke was followed with the seismic observations and GPS.
  First sign of subglacial eruption 23rd of August – small event that did not reach the surface
  Eruption starts Aug 31.
Notes: The stapled line shows the Bárðarbunga volcanic system. It is worth mentioning that no-one lives north of Vatnajökull or close to the eruption in the Holuhraun fissure. However this is relatively popular area to visit by tourist in summer-time.

## Slide 14: Bárðarbunga 2014
During the 3 weeks prior to the eruption we could use seismic data to monitor a dyke forming under the glacier and slowly extending north of it where a volcanic eruption started in Holuhraun
During the eruption we could monitor the caldera collapse with a GPS unit on top of the glacier
Notes: The event in Bárðarbunga started on the 16th of August. During the first two weeks the dyke going from Bárðarbunga caldera towards the northnortheast was formed. The generation of the dyke could be followed by the seismic observation and the GPS stations. On the 23rd of August there were indication that an eruption had started. This seems to have been a shortlived event and the eruption did not reach the surface. However, few days later culdron was seen with in the caldera suporting that the event of the shortlived eruption. Two to three other culdrons were located in the ice above the dyke, indicating that a similar shortlived events had occured. After the eruption started in Holuhraun the seismic activity within the dyke decreased a lot. Now the earthquakes detected in the dyke are small and relatively few. The main seismic activity, since the start of the eruption is within the Bárðarbungu caldera.

## Slide 15: Fun facts about the Holuhraun eruption !
Produced 85km2 lava field in 6 months
  Approx size of Manhattan with lava up to 5th floor
SO2 emission ~ 30-40 kt/day
  If same emission rate over one year  ~13 Mt
For comparison
Total SO2 anthropogenic emissions 2011 ~101 Mt/year
(Klimot Z. et al., 2013)
Holuhraun | ~30-40 kt/day | ~13 Mt/yr
Laki (1783-84) |  | ~120 Mt < year
Pinatubo (1991) | 17 Mt in one day | 
Etna (current) | ~ 3 kt/day | ~ 1 Mt/year

## Slide 16: Gas rich eruption

## Slide 17: Modelling the SO2 plume was a major concern
The dispersion of the SO2 plume could be predicted using VolcalPuff and ECMWF wind forecasts. Onset time verified well.
Source strength was difficult to get right – estimated using DOAS
Notes: The model is ran 2 per day, with input data from the ECMWF model. It is ran for +72 hr. At the start of each run it takes into account the gas distribution at the end of the previous run. The scale below shows the air quality based on SO2 (see next slide).

## Slide 18: Information from the public registered on a IMO website
Notes: IMO have encoraged the public to inform about gas, i.e. If they smell or experience irretation or other effects that might be related to SO2 emissions. The system is web-based and interactive so the user sees immediately the result of the information that they type in. A similar system is used for professionals in charge of handheld SO2 meaters to inform about SO2 load. This system functions well and institutes, e.g. IMO and the Environmental agency are able to extract the information out of the system for further analysis and dissimination to the public in a userfriendly format.

## Slide 19: Information for disaster risk reduction
Preparedness: Pre-event we need to collect relevant data and analyse it
Data must be standardized and long term
  Example: Sea level data. Often large tidal signal, but we need long term estimates of the residual for sea level change estimates and return periods of flood height
  For this the attention to quality must be higher than just for tidal measurements
Data has to be relevant
  Snow accumulation at a weather station may not reflect conditions in avalanche starting zones
  15 years of river data may not be valid for 1000 return period

## Slide 20: Information for disaster risk reduction
Lead up to an event: Relevant information on precursors/triggers
  Rain amount (is it going to exceed the 30 year rain?)
    Both the statistical summary and the real time data need to be accessible
    During hurricane Harvey I could look up precipitation real time and find data on return periods of rainfall events
  Is the volcano behavior consistent with an eruptive ?
    Current examples: Mt. Agung (Bali) and Ambae (Vanuatu)
Information exchange between relevant agencies/authorities becomes very important during lead up
  Important to have a program that is followed with standards in place.

## Slide 21: Information for disaster risk reduction
During an event: Bad time to build up new data streams
Our data streams are usually well prepared for the last event
    Prior to Bárðarbunga/Holuhraun we had good infra-sound arrays from the University of Florence. We also had mobile radars to monitor the ash cloud, and programs to calculate ash dispersal.
    We got an effusive eruption with gas instead of ash.
Data often contradictory and “different”
Multi-parameter combinaton approaches are promising but not tested
  An example is the VESPA system that feeds radar data into a modeling chain to estimate the volcano source strength and ash dispersal
  Such systems must have a built in redundancy or fail if data streams fail

## Slide 22: Volcanic Eruptive Source Parameter Assessment (VESPA)
Orographic blocking
View of Eyjafjallajökull from a web camera at
Hvolsvöllur, 10 May 2010 at 03:00
Detection function
µ = 220 m, σ = 370 m
For this to work, all data streams must be ok (Vespa needs only two)
An ambitious system at the University of Iceland (REFIR) will use more data streams

## Slide 23: How unusual is the wind speed?
Map of maximum
Observed wind during
one day
Is this windstrength unusual?
Similar work planned for
NWP model results

## Slide 24: Meteorological data vs other sources
Observational Meteorology is better standardized than other branches of geoscience
  Issue of data ownership is often a major hurdle in seismology and volcanology (and to an extent also in glaciology and oceanography).
  “Are you ok with someone else publishing an article based on your data?”
  Reciprocity in data sharing helps, but is difficult to enforce
  Use quiet times to establish relationships and foster existing ones
Meteorological data standardization is sometimes lacking
  Are wind gusts 3s or 1s?

## Slide 25: Publicly sourced data and the internet of things (IoT)
IMO does rely on public assistance in reporting ash fall, gas etc.
  Helpful for us as well as the public
    However data can be of varying quality
Observations building on the IoT is in vogue
  Lack of standardization, siting and data quality control etc
  Good measurement programs are serious business
Citizen science and IoT good for supplementary information but not a replacement for observation network

## Slide 26: Data formats standards
“Standards are great, that is why we have so many of them”
  New data sources invariably have new formats and may be insufficiently standardized
    New satellite instruments, ceilometers, lidars, radiosondes
  For pre-event data analysis this is not a big problem, but during an event there is no time to fix things
Lack of data standards in other branches of geoscience can lead to problems
  Little data sharing within subfields or between them.

## Slide 27: Summary and conclusions
Risk reduction depends on good data for preparedness and for an effective response during an event
Good data must be relevant, based on good measurements, preferably from a tried and tested program
During an event there will be various conflicting information
Various data sources needed
Meteorological community has a stronger data sharing ethos than geoscience at large
However, data formats and a plethora of standards may pose a problem

## Slide 28
Thank you
Merci