## Slide 1
Federal Aviation Administration
Weather Information Management
Alfred Moosakhanian
Item 5.6

## Slide 2: FAA Weather Information Management
The Federal Aviation Administration (FAA) information management utilizes System-Wide Information Management, or SWIM.
This presentation will be a high-level introduction to the following areas:
  SWIM
  The CSS-Wx Program and its use of SWIM
  Data Exchange mechanisms used by CSS-Wx
This presentation concludes with an expression of our desire to participate in the WMO TT_IM

## Slide 3: SWIM Conceptual Overview

## Slide 4: FAA NextGen Weather Systems Scope
Produces advanced aviation specific weather products
  0 to 8 hour aviation weather products
  Real-time weather radar information (e.g., ERAM)
  Convective Weather Avoidance Fields
  Wind Shear alerts
Translates weather information into weather avoidance areas for integration into decision support tools (e.g., TFMS, TBFM)
Provides Aviation Weather Display (AWD) of NextGen weather information for ATC users
Enables decommissioning of legacy weather processor systems (e.g., WARP, ITWS, CIWS)
NextGen Weather Processor (NWP)
  Provides a single source for FAA weather information and establishes enterprise level common support services using SWIM
  Focuses on weather information management, publishing to support users, and providing new interface standards and formats
  Consistent with global standards (e.g., WXXM)
  Provides geospatial data access services (WFS, WCS, WMS, WMTS)
  Enables decommissioning of legacy weather dissemination systems (e.g., WARP WINS, FBWTG, CDDS)
Common Support Services – Weather (CSS-Wx)

## Slide 5: NextGen Wx Providers/Consumers

## Slide 6: FAA NextGen Wx Systems Architecture
Common Support Services –
Weather (CSS-Wx)
NEXRAD
Lightning
Networks
Surface Obs
Networks
LLWAS/TDWR
NOAA Data
Satellite
Canadian Wx Radars
MDCRS
ASR
NAS Web Users
NextGen Weather
Processor (NWP)
Central & Terminal Processors
Stakeholders
NESG
NESG
Legacy Weather
Consumers
System Wide
Information
Management
(SWIM)
WMSCR/
ADAS
CONUS+
Domain
ARTCC & Terminal Domains
Modern Weather
Consumers
External Weather Consumers
Service
Adaptors
ARTCCs
CERAPs
ATCSCC
TRACONs
ATCTs
AWD replaces legacy displays: WARP BT, CIWS SD, ITWS SD, ITWS Web, CIWS Web
Flight Services, Providers, Airlines
Aeronautical
Information
Management
Modernization
(AIMM)
Aviation
Wx Display (AWD)

## Slide 7: Resources
https://www.faa.gov/nextgen/programs/

## Slide 8: Css-Wx Data Exchange
Section 2.3 of the “Guide on WWW Data Management” (WMO-No-788) deals with Data Exchange. It describes the limitations of the store-and-forward methodology and describes the need to support ad hoc request accommodated by request/reply mechanisms.
This next section of the presentation describes:
How CSS-Wx implements request/reply web services using Open Geospatial Consortium defined web services,
How the OGC services are extended to use publication/subscribe (pub/sub) services.

## Slide 9: CSS-Wx Data Access Web Services
Provides weather data through Web Services
  WCS, WFS, WMS, WMTS
Adheres to international standards for handling and representing geospatial data
Supports Subscription services and Request/Response message exchange patterns for routinely delivered products via the Web Services
Web Service Capabilities
  Conversions
  Filtering
  Decimation
  Quantization
  Re-projections
Web Map
Service
- Renders data as image or sets of tiled images for display
- JPEG, PNG, GIF, Tiff format
Web Feature
Service
- Filters and transforms non-gridded data sets
- WXXM 2.0 XML format
Web Coverage
Service
- Filters and transforms large gridded dataset
- NetCDF format

## Slide 10: WCS Operations
GetCapabilities
  Returns the server’s coverages (datasets offered) and acceptable request parameter values
GetCoverage
  Returns a gridded data in NetCDF format based on user specified filtering parameters that can include temporal and spatial constraints
DescribeCoverage
  Returns a full description of the requested coverages in the form of an XML document.
GetMetadata
  Returns metadata for a particular gridded product
Subscribe
Renew
Unsubscribe

## Slide 11: WFS Operations
GetCapabilities
  Returns service metadata, including supported operations, functions, and available datasets
DescribeFeatureType
  Returns an XML Schema for a specified feature type advertised as supported by the service
GetFeature
  Returns feature (point/vector) data using filtering criteria such as data type, spatial extent, and temporal extent.
GetMetadata
  Returns metadata for a particular feature
ListStoredQueries
  Returns a list of the queries stored on the server.
DescribeStoredQueries
  Returns one or more descriptions of stored queries.
Transaction
  Allows certain clients to insert feature data into the database supporting the WFS service
Subscribe
Renew
Unsubscribe

## Slide 12: WMS Operations
GetCapabilities
  Returns service metadata, including supported operations, functions, and available datasets
GetMap
  Returns a map image based on user specified parameters
GetFeatureInfo
  Returns information about a feature at a particular map location
GetLegendGraphic
  Returns a legend graphic based on the user’s specified parameters
GetMetadata
  Returns metadata for a particular named image layer
DescribeLayer
  Returns feature or coverage information about a map layer
Subscribe
Renew
Unsubscribe
Radar + OPC + Satellite

## Slide 13: WCS Static Persistent Query Subscription
JMS
A WCS consumer registers off-line with CSS-Wx to receive to receive raster data in NetCDF format.
The CSS-Wx WCS provider sends JMS messages over to NEMS whenever the dataset changes.
The WCS consumer connects to a JMS destination on NEMS to retrieve the data.
Offline Configuration
of Coverage Request

## Slide 14: WCS On-Demand Persistent Query Subscription
Web Service
JMS
A WCS Consumer issues a Subscribe Web Service request.
In the Subscribe request, the consumer includes a GetCoverage element as described in the Request/Response scenario.
The provider sends a response containing a subscription reference, the termination time, and an endpoint reference where the consumer can receive pub/sub messages.
The CSS-Wx WCS provider then sends JMS Messages with the raster data in the payload whenever the dataset changes.
The WCS consumer will continue to receive these messages until the subscription duration expires. The consumer may continue the subscription by sending a Renew request containing the subscription reference or may terminate the subscription with an Unsubscribe request.

## Slide 15: WCS Static Notification Subscription
JMS
Web Service
Offline Configuration
of Coverage Request
A WCS consumer registers off-line to receive Notification messages, that is, to receive notification that gridded (raster) data is available.
The CSS-Wx WCS provider sends a JMS Notification message informing the WCS consumer the dataset has been updated.
The Consumer may then retrieve the product using a GetCoverage operation as described in the Request/Response Exchange Scenario.

## Slide 16: WCS On-Demand Notification Subscription
JMS
Web Service
Web Service
A WCS Consumer issues a Subscribe Web Service request.
In the Subscribe request, the consumer includes a GetCoverage element as described in the Request/Response scenario.
The provider sends a response containing a subscription reference, the termination time, and an endpoint reference where the consumer can receive pub/sub messages.
The CSS-Wx WCS provider sends a JMS Notification message informing the WCS consumer the dataset has been updated.
The Consumer may then retrieve the product using a GetCoverage operation as described in the Request/Response Exchange Scenario.
The WCS consumer will continue to receive these messages until the subscription duration expires. The consumer may continue the subscription by sending a Renew request containing the subscription reference or may terminate the subscription with an Unsubscribe request.

## Slide 17: WFS and WMS Subscriptions
The same four patterns of subscription are also provided for WFS and WMS.
  WFS and WMS Static Persistent Query Subscriptions
  WFS and WMS On-Demand Persistent Query Subscriptions
  WFS and WMS Static Notification Subscriptions
  WFS and WMS On-Demand Notification Subscriptions.

## Slide 18: CONCLUSION
We have touched at a high level the information management approach of our FAA weather program, CSS-Wx. Our team has been actively involved not only in the CSS-Wx implementation program but in development of aviation standards.
  We have supported early collaboration with Eurocontrol and others on developing weather exchange models.
  We supported WMO and ICAO efforts specifically in developing the IWXXM standards.
  We currently support the ICAO Met Panel and Comm Panel for information management standards and practices development.
We would appreciate the opportunity to participate in the important work of the WMO Task Team on Information Management (TT-IM).

## Slide 19
Thank you
Merci