## Slide 1: Multi-Agency Integration of Remote Sensed GOES DCS Telemetered Hydro-Meteorological Observations
LySanias Broyles
Water Control, Rock Island District
Rock Island, IL
Chair, Satellite Telemetry Interagency Working Group (STIWG)
WMO-IOC Satcom Forum
Amsterdam, NL
08 - 11 OCT 2018
Notes: Will talk about major function of water control and how it relates to flood fight

## Slide 2: STIWG Membership
US Army Corps of Engineers
U.S. Geological Survey
U.S. Bureau of Reclamation
National Park Service
U.S. Forest Service
U.S. Bureau of Land Management
NOAA (NWS, NESDIS/NCDC and NOS)
State, Local and International groups actively participate and contribute

## Slide 3: STIWG
Formed in 1976; Coordinating with NOAA as the Satellite Data Collection System Interagency Working Group (SDCSIWG)
November 1979: Presidential Directive mandating NOAA to operate the Geostationary Operational Environmental Satellite Data Collection System (GOES DCS)
1985: Chartered as STIWG by the Interagency Advisory Committee on Water Data (IACWD) and Interdepartmental Committee for Meteorological Services and Supporting Research (ICMSSR)
  Facilitated user coordination with NOAA on use of GOES DCS
STIWG now sits under the Advisory Council on Water Information (ACWI) and the Office of Federal Coordinator for Meteorology (OFCM)
Promotes information exchange/sharing of data, research and development
Undertakes projects that benefit the GOES DCS community

## Slide 4: Working Groups
DCS Preservation
  Tasked with addressing issues pertaining to matters that impact the viability, availability and integrity of GOES DCS data from the GOES satellites.
OpenDCS Standardization
  Tasked with establishing an executable plan that will unify existing OpenDCS variants and capabilities into a single platform. The second objective is to establish a way to jointly plan and fund the new platform’s development and support by the STIWG agencies.

## Slide 5: What is GOES DCS
DCS is a data relay capability on the GOES East and West satellites
Data Collection Platforms (DCP’s) deployed in the field collect readings and perform scheduled transmissions to one of the GOES spacecrafts (dependent upon geography) for relay back to Earth ground stations
  Nearly ~8 million hydro-met observations are transmitted/day
  Direct Read-out Ground Stations (DRGS) collect data directly from the initial GOES relay
  L/HRIT DCS is GOES DCS data that is received by processing centers, repackaged and transmitted to GOES and relayed back to earth for L/HRIT ground stations with smaller dish antennas to receive
Stations allocated timeslots to transmit between 300 and 1200 baud
  Transmissions per hour dependent on assignment: e.g. hourly, half/quarter-hourly, etc.
GOES DCS is a primary system for many agencies supporting water resource management, navigation, flood control, agriculture, hydro-power, etc.

## Slide 6
GOES DCS Operation
6

## Slide 7
Figure 1 An illustration of the concentric elliptical camera and communication footprints of the GOES East and West satellites over the Americas.

## Slide 8
15,900 location subset of all GOES transmitting sites ingested by the National Weather Service (NWS) Hydrometeorological Automated Data System (HADS)

## Slide 9: GOES DCS Data Collection
Local Read-out Ground Station (LRGS) software suite
  Network-based tool - e.g. Cove Open-DCS, Sutron DCS-Toolkit
  Connects to GOES receive systems to ingest, decode, process, QA/QC, validate, transform, store and disseminate incoming messages
    Capable of interfacing with other sources
  Communicates using various protocols (including DAMS-NT) over TCP/IP
  Various routing options
    File format: SHEF, SHEF-IT, HydroJSON, Hydromet, Hydstra, etc.
    Can write directly to various database systems
      USACE Oracle Corps Water Management System (CWMS)
      USBR Oracle Hydrologic Databse (HDB)
      Postgres OpenTSDB
      And others

## Slide 15: GOES DCS Hydro-Met Integration
Inland Navigation and Water Resource Management
Operational Decision Support
Water Quality (TDG, DO, Chlorophyll, PH, turbidity, conductivity….)
Water Quantity (stage, discharge, storage, snow water equivalent….)
Flood and Drought Management/Response
Water Resource Management
Meteorological (relative humidity, solar radiance, wind vector, air temp….)
Wildfire Response (RAWS behavior and prediction, BAER post-fire precip gages)
Agriculture (soil moisture, pan evaporation, soil temperature….)
Academia
Private Industry/Economic Impacts
Alerts/Warnings and Information

## Slide 16: US Bureau of Reclamation River Levels, Reservoir Capacity and Snow Water Equivalence
USBR is the largest wholesale water supplier in the United States
  Supplies 31 million people (10 trillion gal/year)
Second largest supplier of hydro-power ($1B+/year, 3.5M homes)
Operates 600+ Water Management Projects in the Western United States
  Flood control
  Recreation (280+ recreation sites)
  Fishing
  Wildlife benefits
  Irrigation (10 million acres: 60% of US vegetables, 25% of nuts)

## Slide 20: National Ocean Service Tides and Currents PORTS Program
Physical Oceanographic Real-Time System
  Network of U.S. coastal hydro-met stations located in seaports
    Measure and disseminate real-time current data, storm forecasts/warnings, water quantity/quality, hydro-met, etc.
    Proven reliability providing data during extreme storm events
  Supports safe and efficient coastal navigation
    Provides mariners with accurate oceanographic data
      Safety: Reduces collisions and groundings by 60%
      Maximize cargo load/draft generating increased revenue (as much as $290K add’l profit/ft of draft)
      Minimize maritime passage times
      Protect coastal resources and habitat: ~$7B annual revenue from saltwater fishing
      Customizable PORTS composite plots
  Customized for local requirements
    Station instrumentation consists of as many as 50 sensors
  PUFFF – Ports Uniform Flat File Format
    Enables automated access to PORTS data via well-defined ASCII flat-file exchange specification

## Slide 24: USACE Effective Flood Control and Navigation Project Operation Benefits
  Real-time GOES data collection, acquisition, archival, decision support and dissemination
    Daily/upward reporting, studies, analysis, hydraulic forecasts, operational instructions, etc.
    Flood Inundation Mapping, Flood Impact Analysis
  Corps Water Management System (CWMS) Modeling
    Flood Impact Analysis
    Flood Inundation Mapping
    Flood Impact Assessments/Calculate Damages
  Provide daily operational forecasts/reports
  Daily Lock and dam operation for safe in-land navigation (~$250B annual benefit)
    ~200 USACE-owned Navigation Projects
  Daily Reservoir discharge operations
    ~400 USACE-owned Flood Control Projects
    Flood control, hydro-power, recreation, water supply, irrigation, etc.
  Provide data to the public, private industry, academia and other agencies

## Slide 27
USACE Modeling Mapping and Consequences Production Center creates inundation maps by incorporating real-time GOES hydro-met observations. FIM is combined with economic, land use and other information for analysis to estimate consequences/losses; fatality rates, critical infrastructure, real-estate, etc.

## Slide 29
RiverGages WaterML webservice allows users to query and retrieve data from the RiverGages database for use in their automated information systems. Based on the CUAHSI WaterML model, this information is immediately available for ingest by WaterML enabled automated systems.

## Slide 30: Lock and Dam 15 – Mississippi River
Navigation project operated by Rock Island District
Constructed in 1934
  Worlds longest roller dam at 1,203 ft
    9 gates: 100 ft long x 14.3 ft diameter
    2 gates: 100 ft long x 16.2 ft diameter
  Creates Pool 15 along Upper Mississippi River
  $3 billion in commodity transportation savings/$246 million to operate
    (1 barge = 58 semi-trailers or 15 rail cars)
Stats
  Capacity: 100,000 ac-ft
  Catchment: 88,500 sq mi
  Chamber length: Two 600 ft lock chambers at 100 ft wide
  Transit Time: 30 mins
  Average Annual Tonnage: 20 Million Tons

## Slide 33: Red Rock Dam – Des Moines River
Flood control project operated by USACE, Rock Island District
  Operated in conjunction with Saylorville Dam
Constructed 1960 - 1969
  Multi-purpose Project
    Flood control
    Water supply
    Recreation: camping, fishing, hunting, etc.
    Hydro-power (2018)
  Creates Lake Red Rock in Central Iowa
  DCP’s monitor aiding seasonal conservation pool and drought/flood mitigation operation
Stats
  Max discharge: 144,000 cfs
  Catchment: 12,320 sq mi
  Length: 5,676 ft, Height: 95 ft, Width: 13.4 ft
  Surface area: 15,250 acres
  Power generation (2018): 36.4 MW, (179,000 MWh annually for 18,000 homes)

## Slide 34
Saylorville Lake (upper left) and Red Rock Lake (lower right) are operated together during flood events.

## Slide 37: Water Quality Mission
Dissolved Oxygen
Total Dissolved Gas
Turbidity
Conductivity
Chlorophyll
Phycocyanin
Suspended Solids
Water Temperature
pH
Real-time Water Quality data provides mission critical information to operate projects within mandated constraints codified in the Water Quality Management Plan unique to each project.
Fish, wildlife, public health, safety and interest are among the chief tenets for responsible project operation.

## Slide 38: Detroit Dam - Williamette Basin - Salem, OR
Multi-purpose project
  Flood Risk Management (operated in conjunction with Big Cliff Dam)
  Hydro-power generation ( 2 generators producing 100 MW)
  Water Quality improvement (fish passage improvements)
  Songbird and waterfowl habitat
  Recreation
  Irrigation
Stats
  Length: 1,523.5 ft, Height: 463 ft
  Capacity: 3,500 ac-ft
  Shoreline: 32 mi, Lake Length: 9 mi

## Slide 40: Pittsburgh District Water Quality Monitoring Network
Funds the USGS to build, maintain and store data for a network of GOES Water Quality stations
  Provides valuable real-time data to evaluate health of lake projects
Employs buoyed stations for continuous monitoring
  Operate spring-fall each year
  Turbidity, total dissolved gas, water temperature, dissolved oxygen, pH, conductivity, etc.

## Slide 42: National Weather Service, Interagency Fire Center and Forest Service
Rapid deployed and permanent GOES transmitting stations
Provide real-time data for monitoring fire danger
  Weather Service Remote Automated Weather Stations (RAWS – behavior/predictive)
    Average 5.8MM acres burned/year from ~51K fire events/year (2008 – 2017)
  Forest Service Burned Area Emergency Response (BAER – post fire)
  National Interagency Fire Center (NIFC) – Boise, ID
  Weather information Management System – Nat’l Wildfire Coord. Grp.
    Fire and Aviation Management software for fire weather and fuel modeling
  Western Regional Climate Center – WRCC Reno, NV
Provide real-time post-fire precipitation readings
  Monitor for floods and landslides
Interagency fire coordination and response
  Forest Service, Natural Resources Conservation Service, Fish and Wildlife, Bureau of Land Management, U.S. Geological Survey and National Weather Service

## Slide 45
Post Wildfire Debris Flows, 2009 Station Fire, CA (USGS)
Fire Personnel Watch Wildfire at a Permanent RAWS Station (NIFC)

## Slide 46: Spectrum Preservation
GOES downlink operates between 1675 – 1695 MHz (DCS channelized at 1679.7 – 1680.1 MHz)
  Autonomous collection insulates from terrestrial encumbrances
  Reliable during storms and other Earth-events
  Cost effective medium for distributed hydro-met network
Desirable spectrum for terrestrial cellular network manufacturers; upper end auctioned
  GOES HRIT @ 1694.1 while 1695 – 1710 reallocated for internet mobile radio
  Commercial proposal to develop network within GOES spectrum @ 1680 MHz
    Cross-country terrestrial cell-tower LTE network infrastructure
  Tower signal strength is billions of times more powerful than downlink signal “earth” strength
    RF interference detected at various receive sites within exclusion zones
  Impacts mission of aforementioned Federal, State, Local and private agencies and organization with hydro-met interests; includes Earth and Space weather products/imagery
  Disrupted terrestrial GPS systems; proposing move to GOES allocation
  Industry proposed GOES direct receive alternative: commercial terrestrial content delivery network
Engaging users, Congress, agencies, etc. on RFI’s adverse impacts on protecting life, property, critical infrastructure, habitats and economy
  Whitepapers, briefings, symposia facilitated by STIWG, American Meteorological Society, National Hydrologic Warning Council, et. al.

## Slide 47
Figure 2 Depiction of the GOES communication spectrum. The downlink graph (top) shows the 1675 – 1695 MHz band used by satellites to relay data to Earth receive ground stations and the close proximity of the recently auctioned spectrum for wireless broadband (1695 – 1710 MHz) to the HRIT/EMWIN frequency at 1694.1 MHz.
20

## Slide 48
*GOES-R now transmits at 1679.7 – 1680.4
*GOES HRIT rebroadcast transmits at 1694.1 MHz

## Slide 49
Simulated GRB GOES-R Imager Full Disk (Mode 4, Band 1) Without Noise
Simulated GRB GOES-R Imager Full Disk (Mode 4 Band 1) with noise injected at random point. Immediate catastrophic failure of the DVB-S2 signal occurred

## Slide 50: GOES vs Terrestrial Storm Event Performance Synopsis
Performance during Natural Disasters (Credit: Nathan Holcomb NOAA/NOS/COOPS)
  NOS primarily uses Iridium and GOES to ingest data
    Also employ IP modems and phone lines
  Working to upgrade their data status reports to reflect where their data is coming from
  Large decrease in data coming from terrestrial connections immediately before, during and after hurricanes
  Large increase in GOES messages received during storm events
  GOES messages continued when IP modems and other terrestrial infrastructure dependent methods failed
    GOES message count decreased as batteries failed; no electricity and/or damaged solar panels
  Intends to use the statistics collected for further outreach to stress the need for essential data collection systems
  Important to estimate impact had there been no data during storm events

## Slide 52
By combining various wavelengths in Advanced Baseline Imager products with the lightning flash detection from the Geostationary Lightning Mapper, GOES-R can provide a “radar-like” substitute over ocean areas for aviation use.
When Hurricane Maria destroyed the radar used for weather in Puerto Rico, GOES-16’s data and OPC were used to temporarily substitute for the lack of ground radar coverage in Puerto Rico.

## Slide 53
GOES Satellites monitor Near-Earth space environment driven by solar events: GOES Electron Flux, GOES Magnetometer, GOES Proton Flux, GOES Solar X-ray Imager and GOES X-ray Flux.

## Slide 54: Spectrum Preservation Path Forward
Interagency Effort to investigate current systems’ status
  On-site RF analysis
  Determine baseline of existing receive systems
  Determine viability of spectrum sharing
  Develop and implement mitigation, monitoring and reporting measures
  Investigate viable/reasonable RFI protection
  Report findings and provide impact assessment

## Slide 55: References
•"Consequence Assessment for Dam Failure Simulations" Kurt Buchanan, CFM, USACE
•"USACE Modeling, Mapping and Consequences Production Center - Inundation Mapping Standards" Alexandra Ubben, USACE
•GOES Uses and Users and Benefits for Users and Their Constituents Dave Lubar, 2018
•http://acwi.gov/hydrology/stiwg/
•http://acwi.gov/hydrology/stiwg/Meetings/20180322/co-ops_goes_presentation_stiwg2017.pdf
•http://co-ops.nos.noaa.gov/map/index.shtml?region=Florida
•http://co-ops.nos.noaa.gov/stationhome.html?id=8720625
•http://famit.nwcg.gov/applications/RAWS
•http://lightning.umd.edu/Apps/GoesCesium/
•http://nationalwaterwaysfoundation.org/documents/INLANDNAVIGATIONINTHEUSDECEMBER2014.pdf
•http://pubs.usgs.gov/fs/fs03603/fs03603_files/fs036-03.pdf
•http://tidesandcurrents.noaa.gov/ports.html
•http://wqdatalive.com/public/15
•http://www.hec.usace.army.mil/
•http://www.hydrodb.net/
•http://www.mvr.usace.army.mil/Missions/Navigation/
•http://www.ncdc.noaa.gov/societal-impacts/wildfires/
•http://www.ndbc.noaa.gov/
•http://www.nwd-wc.usace.army.mil/nwp/wm/wq_reports.html
•http://www.nwd-wc.usace.army.mil/report/total.html
•http://www.nwp.usace.army.mil/Missions/Water-Management/Dams/
•http://www.nwp.usace.army.mil/mount-st-helens/
•http://www.nwp.usace.army.mil/Portals/24/docs/locations/bonneville/Bonneville_FS.pdf
•http://www.publications.usace.army.mil/Portals/76/Publications/EngineerRegulations/ER_1110-2-240.pdf
•http://www.redrockhydroproject.com/
•http://www.usbr.gov
•http://www.weather.gov
•https://www.fs.fed.us/naturalresources/watershed/burnedareas.shtml
•https://www.nwcg.gov/

## Slide 56
End
https://acwi.gov/hydrology/stiwg/