## Slide 1
GISC Tokyo Cloud Pilot Project
Shuichi Ikeda
ICT division, Japan Meteorological Agency
TT-eWIS 2018, 14th -16th November 2018, Beijing

## Slide 2: AMDCN of GISC Tokyo
GISC Tokyo
RTH Bangkok
NMC Manila
NMC Hanoi
2Mbps
2Mbps
NMC Nay Pyi Taw
Internet
100Mbps
MPLS Network
(NTT_COM)
NMC Vientiane
NMC Phonom Penh
Expensive,
Not high speed In comparison with internet
Non-direct connection
Non-direct connection
Inexpensive,
High speed
Expensive,
Not high speed In comparison with internet
High reliability, Secure,
Guaranteed bandwidth
High reliability, Secure,
Guaranteed bandwidth
Security measures,
Best effort
Advantage
Disadvantage

## Slide 3: Problems of Tokyo’s AMDCN
Cost
  Expensive.
Communication speed
  Not high communication speed.
Accessibility
  Some countries and Tokyo cannot establish direct links.
Scalability
  Difficult to transmit high volume data, especially satellite and NWP data.

## Slide 4: Improvements of Tokyo’s AMDCN
Cost assessments
  From dedicated lines to Internet connections
Upgrade communication speed
  High speed internet connections
Accessibility
  Internet connections
Security
  Virtual Private Network, Secure protocol
Reliability
  Backup systems and connections (when necessary)
Scalability
  Cloud service

## Slide 5: The purposes of Cloud Pilot Project
Install cloud service on the internet to exchange information, basically among GISC Tokyo’s AoR and south-east Asia countries who join the radar composite project.
Evaluate cloud service provided by private company in terms of operational (satisfy the manual on GTS?) aspects, and develop an understanding of cloud technology.
Gather opinions in Tokyo’s AoR, and analyze their needs.
Compare costs of dedicated lines and Cloud services, and check reliabilities.

## Slide 6: Cloud Pilot Project - data from NCs
NMC Bangkok
NMC Manila
NMC Hanoi
NMC Nay Pyi Taw
NMC Vientiane
NMC Phonom Penh
Internet
Communication Protocol
FTP, FTPS, SFTP, HTTP, HTTPS
GISC Tokyo
Cloud unpacks uploaded FTP files, and stores raw data on its storage.
Cloud also recompiles data into batched FTP files, and send them to JMA MSS.
Other centres
JMA Cloud
NMCs upload their batched FTP files / files to JMA Cloud

## Slide 7: Cloud Pilot Project - data to NCs
NMC Bangkok
NMC Manila
NMC Hanoi
NMC Nay Pyi Taw
NMC Vientiane
NMC Phonom Penh
Internet
Communication Protocol
FTP, FTPS, SFTP, HTTP, HTTPS
GISC Tokyo
Cloud unpacks batched FTP, and stores raw data on its storage
Other centres
JMA Cloud
RJTD0000000N.b
NMCs download data from JMA Cloud

## Slide 8: Cloud Pilot Project – Visualization tools
NMC Bangkok
NMC Manila
NMC Hanoi
NMC Nay Pyi Taw
NMC Vientiane
NMC Phonom Penh
Internet
Communication Protocol: HTTP, HTTPS
GISC Tokyo
Cloud unpacks batched FTP, and stores raw data on its storage
Other centres
JMA Cloud
RJTD0000000N.b
NMCs access to visualization tools on JMA Cloud
Cloud offers visualization tools on JMA Cloud.

## Slide 9: How to upload/download data to/from GISC Tokyo cloud - FTP -
upload
download
NMCs
GISC Tokyo’s AoR
Put batched FTP files by FTP
User directories
User directories
NMCs
GISC Tokyo’s AoR
Get batched FTP files by FTP
Finally delete them on user directories
Unpack and store
pack
From JMA MSS
Unpack and store
Pack and send it to JMA MSS

## Slide 10: How to upload/download data to/from GISC Tokyo cloud - HTTP -
upload
download
NMCs
GISC Tokyo’s AoR
Put batched FTP files by HTTP(s)
Using curl command with ID and password
Authentication web
Directories for users
NMCs
GISC Tokyo’s AoR
Get data from cloud web site
unpack
move
Check update information
From JMA MSS
Unpack and store
Pack and send it to JMA MSS

## Slide 11: Summary
Plan to Install cloud service on the internet to exchange information basically among GISC Tokyo’s AoR.
Evaluate cloud services provided by private company in term of operational aspects through this pilot project experience.
Gather opinions of Tokyo’s AoR, and analyze their needs.
Compare the cost of dedicated lines and Cloud service. consider whether current dedicated lines are completely replaced to cloud based connections, and check reliabilities.

## Slide 12
Thank you
Merci