## Slide 1: Status Report of GISC Tokyo
Yoritsugi YUGE (OHNO)
ICT division Japan Meteorological Agency (JMA)
(Doc 2.x)
ET-CTS 2019, SMN, Buenos Aires, Argentina
Date: 11-15 February 2019

## Slide 2: Communication circuit (1)
Topics:
  Establishment of a new link (Internet VPN)
    with Nay Pyi Taw in November 2016
    with Dhaka in May 2017
    with Ulaanbaatar in October 2017
  Migration from TCP socket to FTP connection
    with Exeter and Melbourne in March 2017
    with Khabarovsk in January 2018
  Establishment of a new link (IP-VPN) with Hanoi; September 2018
  Upgrading the bandwidth of MPLS access link (NTT-COM) from 2 Mbps to 6 Mbps; December 2018
Plans:
  Migration of the link with New Delhi, Bangkok, Hong Kong and Manila from the TCP socket to FTP connection in 2019-2020
  Establishment of a new link (RMDCN) with GISC Jeddah in 2019

## Slide 3: Communication circuit (2)
GISC/RTH Tokyo
GISC Washington
GISC Melbourne
GISC Beijing
GISC Offenbach
GISC Toulouse
GISC Exeter
GISC New Delhi
DCPC/RTH Khabarovsk
DCPC/RTH Bangkok
DCPC Hong Kong
GISC Seoul
NC Manila
DCPC Doha
NC Hanoi
10Mbps
64Kbps
2Mbps
2Mbps
10Mbps
6Mbps
NC Dhaka
NC Nay Pyi Taw
100Mbps
MPLS Network
(NTT Communications)
MPLS Network
Regional Meteorological Data Communication Network (RMDCN)
(GTT communications)
GISC Brasilia
64Kbps
1Mbps
128Kbps
4Mbps
16Mbps
50Mbps
100Mbps
20Mbps
6Mbps
6Mbps
NC Phnom Penh
NC Vientiane
NC Ulaanbaatar
Internet
IP-VPN
IP-VPN
Dedicated
Notes: This slide shows “Configuration of communication circuit (GTS) of GISC Tokyo”.

## Slide 4: Communication Circuit (3)
15th January 2019
Implementation status
Notes: This slide shows “Implementation status of communication circuit (GTS) connected to GISC Tokyo”.

## Slide 5: Daily Volume (1)
Text, Binary, FAX message and File
Notes: This slide shows “Daily volume on GTS circuit”. It is excluding Internet connection.

## Slide 6: Daily Volume (2)
Occupancy rate (each channel)
Notes: This slide shows occupancy rate on daily volume.
As you can see, 97-98% is binary & file (bufr & grib) data.

## Slide 7: Average Daily Download Volume on the Internet
Bandwidth 100Mbps
WIS part-B Internet Traffic
Downloading data
240 GB/Day
Notes: This slide shows average daily download volume on Internet service.
In our Internet service, we are providing Himawari-satellite data and High resolution GSM data in addition to routing data.

## Slide 8
Internet VPN connection on AMDCN of GISC Tokyo
GISC Tokyo has connected with three NC centers through Internet VPN link.
Almost NCs have two or more data connections with their neighbouring WIS centres.
Internet connection is gradually stable operation in Asia region.
Before sometimes, NC's Internet connection had traffic jam due to their Internet was sharing to get product data. And also NC’s ISP was to be in down due to electric power problem for a few days.
90 min
2 days
1 day
Before (in Apr – May 2018)
Currently (in Dec 2018 – Jan 2019)
Notes: This slide shows daily total downtime of Internet VPN connection.
GISC Tokyo has connected with three NC centers through Internet VPN link.
Almost NCs have two or more data connections with their neighbouring WIS centres.
Internet connection is gradually stable operation in Asia region.
Before sometimes, NC's Internet connection had traffic jam due to their Internet was sharing to get product data. And also NC’s ISP was to be in down due to electric power problem for a few days.
I think recently, their Internet connection is stable operation.

## Slide 9: GISC Backup (1)
GISC Beijing
GISC Backup between Beijing and Tokyo is in operational by using GTS and Internet DAR service.
GISC Melbourne
  Tokyo has two options for AoR of Melbourne; option 1: Existing GTS based backup option 2: Internet based backup Both options are already running in backup with Beijing and Offenbach.
Notes: GISC Tokyo has bilateral agreements on GISC backup with GISC Offenbach, GISC Beijing and GISC Melbourne.
GISC Backup between Beijing and Tokyo is in operational by using GTS and Internet DAR service.
GISC Melbourne and Tokyo, GISC Tokyo has two options for the Centre of AoR of Melbourne.
Option 1 is to use existing GTS based backup and option 2 is to use Internet based backup.

## Slide 10: GISC Backup (2)
GISC Offenbach
  GISC Backup between Offenbach and Tokyo is in operational by using Internet.
    To Offenbach: using FTP put
    To Tokyo : using HTTPS file upload
DCPC
NC
NC
NC
GISC Offenbach AMDCN
DCPC
NC
NC
NC
GISC Tokyo AMDCN
GISC Offenbach
GISC Tokyo
Internet
HTTPS file upload
FTP put
cache
cache
Notes: Between GISC Offenbach and Tokyo is in operational by using Internet. The centres of the Area of Responsibilities send data to Offenbach by using FTP_PUT and to Tokyo by using HTTPS file upload function. GISC Tokyo shows their received data on the Internet.

## Slide 11: WIS monitoring
https://www.wis-jma.go.jp/wcd/v1/top.html
Notes: GISC Tokyo has been operating WIS Monitoring Dashboard.
And the WIS Monitoring is a collective effort of all WIS Centres to provide comprehensive and up-to-date information that enable reports on system status including availability, stability, integrity.

## Slide 12: Disaster Recovery Site (DRS)
JMA's Disaster Recovery Site (DRS) on west side of Japan (Osaka city, 500km far from Tokyo) has been in operation since March 2015.
If the Tokyo system has a failure, JMA will switch over to Message Switching System (MSS) of Osaka DRS to continue data exchange.
The MSS of DRS has the same architecture of Tokyo's MSS and access lines of MPLS networks. Several centres finished a connectivity test and started backup operation.
500Km
Tokyo
RMDCN-NG
Osaka
AMDCN
Notes: This slide shows our Disaster Recovery Site.

## Slide 13: Recommended Text
GISC Tokyo has a high availability connection to RMDCN-NG (10Mbps+10Mbps, Platinum Service), MPLS of the NTT-Communications (6Mbps) and Internet access (100Mbps Guaranteed bandwidth).
And also GISC Tokyo has a Disaster Recovery Site (DRS) in Osaka city which is located in 500 km far west side of Tokyo.
GISC Tokyo has bilateral agreements on GISC backup with GISC Offenbach, GISC Beijing and GISC Melbourne. Its backup procedures have been in operation.
GISC Tokyo has a plan to migrate from TCP socket to FTP connection in 2019-2020.
GISC Tokyo has a plan to hold WIS Workshop in JMA HQ in 11th-12th March 2019.

## Slide 14
Thank you
Gracias
JMA HP: https://www.jma.go.jp/jma/indexe.html
GISC Tokyo Web portal: https://www.wis-jma.go.jp/

## Slide 15
1.5GB/Day
3.6GB/Day
Beijing (16Mbps) – Tokyo (10Mbps)

## Slide 16
482MB/Day
6.8GB/Day
Exeter (20Mbps) – Tokyo (10Mbps)

## Slide 17
1.3GB/Day
228MB/Day
Melbourne (4Mbps) – Tokyo (10Mbps)

## Slide 18
709MB/Day
395MB/Day
New Delhi (4Mbps) – Tokyo (10Mbps)

## Slide 19
203MB/Day
1.2GB/Day
Offenbach (50Mbps) – Tokyo (10Mbps)

## Slide 20
2.4GB/Day
147MB/Day
Seoul (4Mbps) – Tokyo (10Mbps)

## Slide 21
203MB/Day
78MB/Day
Toulouse (50Mbps) – Tokyo (10Mbps)

## Slide 22
174MB/Day
4MB/Day
Bangkok (128Kbps) – Tokyo (2Mbps)

## Slide 23
1.7GB/Day
16MB/Day
Hong Kong (1Mbps) – Tokyo (2Mbps)

## Slide 24
185MB/Day
0.3MB/Day
Manila (64Kbps) – Tokyo (2Mbps)

## Slide 25
140MB/Day
3MB/Day
Khabarovsk (dedicated 64Kbps) – Tokyo

## Slide 26
438MB/Day
0.4MB/Day
Doha (IPVPN 2Mbps)– Tokyo

## Slide 27
198MB/Day
0.1MB/Day
Hanoi (IPVPN 2Mbps)– Tokyo

## Slide 28
490MB/Day
1.4GB/Day
Washington (Internet) – Tokyo (Internet)