## Slide 1
Assigning and using
WIGOS station identifiers

## Slide 2: Structure of WIGOS Station Identifier
Local Identifier
Decided by Issuer of Identifier
Issue Number
Decided by Issuer of Identifier
Issuer of Identifier
Source of identifier (specified by WMO)
Series
0
0-20000-0-60351
0-20001-0-57816
0-20003-0-C7R
0-20004-0-XY123AB
0-999-0-EREHWON

## Slide 3: Assigning a WIGOS identifier
Have observations been exchanged from the station?
Is the station already in OSCAR/surface?
The station already has a WIGOS identifier - see OSCAR/surface
Use the identifier associated with the programme under which the observations were exchanged
Has your country a methodology for identifying national stations?
Set Issue Number to 0.
Set Local Identifier to the national identifier.
If there is more than national methodology, each methodology could be assigned an Issue Number to make sure that there are no duplicate identifiers.
Define a methodology for issuing station identifiers. The following is suggested.
Set Issue Number to 0.
Allocated Local Identifiers as a sequence number in the order the station identifiers are assigned, starting with 1.
Y
Y
Y
N
N
N

## Slide 5
Thank you
Merci