## Slide 1: Status of GISC Beijing and CMACast System
Lang Hongliang
langhl@cma.gov.cn

## Slide 2
Ulan Bator
New Delhi
Bangkok
64
Kbps
Leased line
Offenbach
Tokyo
RMDCN
MPLS VPN
4Mbps
Moscow
NESDIS
250Mbps
Hanoi
Pyongyang
3Mbps
2Mbps
512Kbps
The GTS circuits connected with GISC Beijing (RTH Beijing)
128Kbps
GISC Beijing (RTH Beijing)
EUMETSAT
2Mbps
64
Kbps
64
Kbps
64
Kbps
Seoul
4Mbps
Video+data
Hongkong
Islamabad
US
256
Kbps
Internet

## Slide 3: GISC Beijing
Started official operation as from August 15, 2011
  Exchanging metadata with BOM, DWD, INMET, JMA, Meteo France, NWS, HKO
  Available services: metadata search, data subscription, data request/reply, web data ingest, metadata ingest, …
  Available data: global exchanged data, CMA NWP products, FY satellite data, TIGGE products (from 10 product centers), …
Data dissemination
  GTS – to other WIS/GTS centers via ftp, tcp sockets
  Internet – to other centers, end-users via ftp, http, smtp
  CMACast – to other centers, end-users

## Slide 5: Integrated with the data services of CMACast
discover data, make data subscription
subscribed data
subscribed data

## Slide 6: CMA Internal DCPCs
Next step
Developing internal DCPCs, include NMC (National Meteorological Centre) DCPC, NCC (National Climate Centre) DCPC, NSMC(Nation Satellite Meteorological Centre) DCPC
Providing internal DCPC’s products via GISC Beijing portal

## Slide 7: CMACast System
C-band DVB-S2 data broadcasting system
Maximum data broadcasting capacity is about 70Mbps
Three types of user:
  CMA internal users, 31 province-level stations, 350 city-level stations, 2070 country-level station
  External users, 234 stations
  Asia-Pacific users, 20 stations
Business operation will be started in May, 2012

## Slide 8: CMACast System

## Slide 9: Statistics of CMACast system in March, 2012
Data Volume | Maximum Daily (GB) | Minimum Daily (GB) | Average Daily (GB) | Monthly Total (TB)
 | 232.92 | 177.20 | 194.82 | 6.0
File Number | Maximum Daily (K) | Minimum Daily (K) | Average Daily (K) | Monthly Total (K)
 | 1021 | 748 | 868 | 26901