## Slide 1: IP Addressing and the RMDCN Next Generation
Tony Bakker
Network and Security Section

## Slide 2: Current policy
RMDCN private network – heterogeneous network – no single admin domain
No RFC1918 IP addresses (avoid possible classes of IP addresses)
OBS provides some /26 IP address blocks for sites:
Some sites use NAT on local routers

## Slide 3: IP Addresses on RMDCN-NG
RMDCN private network – heterogeneous network – no single admin domain
Stick to current policy of no RFC1918 IP addresses
Need to migrate from OBS provided /26 IP address blocks to something else
Not critical, but it should be done if OBS is not selected as provider for the RMDCN-NG
  Recommend to do this after network migration to RMDCN-NG

## Slide 4: Who needs to change?
Group A: sites using a publicly registered IP network address
  No changes required
Group B: sites using an OBS IP address block on the RMDCN LAN segment only and then use NAT on internal router
  Small change: only devices on RMDCN LAN segment
Group C: sites using an OBS IP address block for end hosts on their LAN
  Significant change: Internal LAN devices need new IP address

## Slide 5
Have requested assistance from Tenderer for this IP address migration in ITT documents
Has to be carefully planned by sites (Group B and Group C)
Recommendation is to wait until migration to RMDCN-NG is finished
Further details to follow after Tender selection