## Slide 1: Status of implementation for WIS in Beijing
CMA WIS TEAM
National Meteorological Information Centre，China Meteorological Administration

## Slide 2: OUTLINE
GTS - RTH Beijing Status
CMA’s WIS Service - GISC Beijing
CMA’s WIS Service - DCPCs in Beijing

## Slide 3
Ulan Bator
RTH
New Delhi
RTH
Bangkok
64
Kbps
Leased line
RTH
Offenbach
RTH
Tokyo
RMDCN
MPLS VPN CLOUD
WMC
Moscow
NESDIS
250Mbps
Hanoi
Pyongyang
3Mbps
2Mbps
512Kbps
The GTS circuits connected with RTH Beijing
128Kbps
RTH Beijing
EUMETSAT
Darmstadt
2Mbps
64
Kbps
64
Kbps
64
Kbps
Seoul
4Mbps
Video+data
4Mbps
HongKong
Islamabad
256
Kbps
Internet
GTS - RMDCN upgraded to 4 Mbps ；New Internet Connection with NESDIS, Islamabad and HongKong；Establishing Video and Data Leased Line to HongKong
RTH
Khabarovsk
Alma-Ata
WMC
Melbourne
RTH
Offenbach
RTH
Tokyo
EUMETSAT
Darmstadt
Ulan Bator
Hanoi
WMC Washington

## Slide 4: GTS Software Changes in 2011
GTS protocol between Beijing and Tokyo was migrated from TCP sockets to FTP in Dec 2011
In addition to A/N, BIN and FAX channels, the A/N-urgent channel has been established.

## Slide 5: CMACast
Based on DVB-S2 standard technology
Rent a whole 36MHz C-band transponder
Up to 70Mbps date rate
More than 400GB daily data transmission
Enhanced user registration strategy
Enhanced date flow control and management
Improved interoperability with EUMETCast and GEONETCast Americas

## Slide 6: TDCF Migration Progress in RTH Beijing
Cat.1 | Cat.2 | Cat.3
SYNOP(Nov.2007) | FY-2(D/E) AMV(2005) | AMDAR (2012)
TEMP(Nov.2007) |  | 
CLIMAT(Nov.2007) |  | 

## Slide 7: BUFR Bulletin Disseminate To
RTH Offenbach
RTH Tokyo
WMC Moscow
RTH New Delhi
RTH Bangkok
NMC Seoul
NMC Pyongyang
NMC Ulan Bator
CCCC | T1T2A1
MNUB | ISM, ISI, IUS
DKPY | ISM, ISI, IUK, IUF
VHHH | ISM, IUA, IUP, INA
VMMC | ISM
Progress in RTH Beijing Responsible Area

## Slide 8
2009 - Initiated to develop WIS services in CMA
It adopts J2EE framework and layered modular design, yields simple structure and easily scalable components, and owns user-friendly web interface for accessing metadata and data services
It is fully compliant with WIS technical specifications and standards.
DAR metadata: WMO Core Profile 1.2
Metadata synchronization: OAI-PMH, FTP
Data: TAC, BUFR, CREX, GRIB, NetCDF, ….
Data collection and dissemination: TCP sockets, FTP, HTTP, SMTP/POP3, multicast, …

## Slide 9: 2011- Integrated with the data services of CMACast
Metadata Search
Metadata Bounding Box
Full-text Retrieval
Metadata List
Data dissemination
  GTS – to other WIS/GTS centers via FTP,
  Internet – to other centers, end-users via FTP, HTTP, SMTP
CMACast – to other centers, end-users

## Slide 10
GISC Beijing approved by Cg-XVI in May, 2011
In July, CMA PR sent letter to RA II member to inform them that GISC Beijing will start its operation as from 15 August 2011.
The letter was also copied to the users of CMACast in other region and WMO Secretariat.

## Slide 11
Exchanging metadata with DWD, INMET, JMA, Meteo France, HKO
Available services: metadata search, data subscription, data request/reply, web data ingest, metadata ingest, …
Welcome to access GISC Beijing services
    http://wisportal.cma.gov.cn
If you have any requirement, comment or question, please contact us
    giscadmin@cma.gov.cn

## Slide 12
Available data: global exchanged data, CMA NWP products, FY satellite data, TIGGE products (from 10 product centers), …
Data Type |  | CMACast | CMA WIS Portal
GTS data | surface observations | Yes | Yes
 | upper air observations | Yes | Yes
 | other observations | Yes | Yes
 | NWP products | Yes | Yes
TIGGE products |  | - | Yes
Satellite data | FY-2D/E data | Yes | Partly
 | FY-3A data | Partly | -
 | other satellite data | TDB | -
Others |  | TDB | -

## Slide 13
4 approaches to maintain metadata and to support WIMMS service
metadata online editor
metadata upload via web form
metadata harvesting via OAI protocol
metadata harvesting via FTP protocol
Since Feb. 2012 - Offer WIMMS

## Slide 14
19/40
3/3
4/6
2/3
0/0
0/0
Member number/ User number
User Registration Until 26th, May 2012

## Slide 15
Next step
  Develop internal DCPCs, and provide their products via GISC Beijing portal
  Ready to be assessed by ET-GDDP around June of 2012
GISC Beijing
CMA DCPC
Other GISCs
End Users
Metadata
Data

## Slide 16
No. | Product
1 | Marine weather information broadcast
2 | Tropical cyclone waring advisory
3 | Tropical cyclone FAX
4 | The Global Medium-range weather prediction T639L61
5 | Tropical cyclone ensemble prediction product
DCPC NMC (National Meteorological Centre)

## Slide 17
DCPC BCC (Beijing Climate Centre)
No. | Product
1 | Global Unusual Monthly Mean Temperatures and Precipitation
2 | Global Monthly Mean Temperatures and Anomallies
3 | Global Monthly Precipitation Totals and Percentage Anomalies
4 | Monthly Mean Sea Level Pressure and Anomalies
5 | Monthly Mean Sea Surface Temperatures and Anomalies
6 | Indices for Regional SSTA

## Slide 18
DCPC NSMC (National Satellite Meteorological Centre)
No. | Satellite | Product
1 | FY3B | MWHS/MWRI/TOU/IRAS/VIRR/MERIS/SBUS/MWRI/ERM/SIM/MERIS/MWTS Level 1 Product
2 |  | MWHS/MWRI/TOU/IRAS/VIRR/MERIS/SBUS/MWRI/ERM/SIM/MERIS/MWTS Level 2 Product
3 | FY2E | Cloud Motion Vectors Product derived from FY2E WV Image
4 |  | Normalized Geostationary Projection data from FY-2E 5 spectral channels.
5 |  | Cloud Motion Vectors Product derived from FY-2E IR Cloud Image.
6 |  | Outgoing Longwave Radiation Product.
Notes: MWHS/MWRI/TOU/IRAS/VIRR/MERIS/SBUS/MWRI/ERM/SIM/MWTS
MicroWave Humidity Sounder
MicroWave Radiation Imager
Total Ozone Unit
InfraRed Atmospheric Sounder
Visible and InfraRed Radiometer
MEdium Resolution Spectral Imager
Solar Backscatter Ultraviolet Sounder
MicroWave Radiation Imager
Earth Radiation Measurement
Solar Irradance Monitor
MicroWave Temperature Sounder

## Slide 19
Thanks for your attention!