## Slide 1: Status Report of GISC Tokyo
Yoritsugi OHNO
Japan Meteorological Agency (JMA)
ET-WISC
13-16 March 2012, Melbourne

## Slide 2: Content
Status of JMA
GISC Tokyo
Status of user registration
GISC Cache
Metadata Synchronization
Networks
Automatic Catalogue
KML
RSS
Subscription
Access Analysis

## Slide 3: Status of JMA
As designated in Sixteenth WMO Congress in June 2011, JMA has started following services of WIS Centres on 1st August 2011:
    Global Information System Centre (GISC)
    8 Data Collection or Production Centres (DCPC)
Type | Function
GISC | -
DCPC | RTH
DCPC | RSMC-Typhoon
DCPC | RSMC-Geographical
DCPC | RSMC-ATM
DCPC | Satellite Centre
DCPC | GPC-LRF ( Forecast)
DCPC | RCC (Tokyo Climate Centre)
DCPC | WDC-GG (Greenhouse Gases)
Table : List of WIS centres at JMA

## Slide 4: GISC Tokyo
Services
  Part-A
    Global Telecommunication System (GTS)
  Part-B
    Discovery, Access and Retrieval (DAR)
    Web interface to create/modify Metadata
    GISC Cache (data stored at least for 24 hours)
    Data subscription
    SATAID Service
      MTSAT Imagery and NWP products for SATAID software
    High-Resolution GSM data
  GISC Backup
http://www.wis-jma.go.jp/

## Slide 5: Status of user registration
65 registered users from 32 Members of WMO so far
GISC Tokyo
MTSAT Imagery
for NMHSs
High-resolution GSM for NMHSs
GTS message

## Slide 6: GISC Cache
GISC Tokyo stores GTS messages, DCPC's data and so on at least for 24 hours of arrival
GTS
GISC Tokyo
GSM
DCPCs
Users
http://www.wis-jma.go.jp/data/browse

## Slide 7: Metadata Synchronization
As a role of GISC, GISC Tokyo has been exchanging metadata with other operational GISCs (such as Beijing and Offenbach) by OAI-PMH (Open Archives Initiative Protocol for Metadata Harvesting) at regular intervals.
Monitoring tool at: http://toyoda-eizi.net/2011/syncmon/mon.html
GISC Tokyo
GISC Offenbach
GISC Beijing
Other GISCs

## Slide 8: Networks
Table : Current Status of RTH Tokyo |  |  |  | 
Circuit connected with | Type of circuit | Circuit speed (bps) |  | Protocol
 |  | Tokyo side | NMHS side | 
WMC Melbourne | RMDCN-MPLS (OBS) | 10M | 2M | TCP/IP (Socket, FTP)
WMC Washington |  |  | 1M | 
RTH Beijing |  |  | 4M | TCP/IP (FTP)
RTH Exeter |  |  | 2M | TCP/IP (Socket, FTP)
RTH New Delhi |  |  | 1M | TCP/IP (Socket)
RTH Khabarovsk | Dedicated (digital) | 64 k |  | 
RTH Bangkok | MPLS (NTT-COM) | 2M | 128k | 
NMC Hong Kong |  |  | 1M | TCP/IP (Socket, FTP)
NMC Manila |  |  | 64k | TCP/IP (Socket)
NMC Seoul | Dedicated (digital) | 128k |  | TCP/IP (Socket, FTP)
GISC Tokyo (RTH Tokyo)
10M x 2
2M
100M
Seoul
Khabarovsk
RMDCN MPLS
Network
(OBS)
Internet
DAR Users
NMHS users of MTSAT Imagery and High-resolution GSM
Melbourne
Washington
Beijing
Exeter
New Delhi
EUMETSAT
128K
64K
Manila
Hong Kong
Bangkok
MPLS
Network
(NTT-COM)

## Slide 9: Automatic Catalog
"Published","Updated","Region","Location","Indicator","Identifier","Access","Type","Category","Subcategory","Satellite","Discipline","Grid","Resolution","Area","Level","ReferenceTime"
"2011-11-22","2012-01-10","South-West Pacific","Australia","ABCS","WSAU21","Closed","Alphanumeric","Aviation","SIGMET","","","","","","","02 10 14 15 17 [h]"
"2012-01-31","2012-02-01","South-West Pacific","Australia","ABRF","WWPS22","Open","Alphanumeric","Warning","Warnings and weather summary","","","","","","","01 08 14 20 [h]"
"2011-12-08","2012-02-02","South-West Pacific","Australia","ADRM","ISXK48","Open","BUFR","Analysis","Cyclone","","","","","","","00 01 06 07 11 12 13 18 19 [h]"
"2011-12-23","2011-12-25","South-West Pacific","Australia","ADRM","KSXK40","Open","CREX","Surface","","","","","","","","00 06 07 12 18 19 20 23 [h]"
"2011-08-01","2012-03-01","Asia","Japan","RJTD","HECB88","Open","GRIB","","","","Global Spectral Model","Latitude/Longitude","1.25 1.25","60.0 -20.0 60.0 200.0","Surface","00 06 12 18 [h]"
Category | Detail of message
"Published", | "2011-11-22",
"Updated", | "2012-01-10",
"Region", | "South-West Pacific",
"Location", | "Australia",
"Indicator", | “ABCS",
"Identifier", | "WSAU21",
"Access", | "Closed",
"Type", | "Alphanumeric",
"Category", | "Aviation",
"Subcategory", | "SIGMET“,
"Satellite", | "",
"Discipline", | "",
"Grid", | "",
"Resolution", | "",
"Area", | "",
"Level", | "",
"ReferenceTime" | "02 10 14 15 17 [h]"
GISC Tokyo has generated data catalog like Volume C1 at daily intervals. These data have information values as data monitoring.
Data Catalog at: http://www.wis-jma.go.jp/cms/automatic_catalog_wmo_format/

## Slide 10: KML
Special at GISC Tokyo
KML is standard format for geographical data
Can be viewed with Google Earth
KML Catalogue at : http://www.wis-jma.go.jp/cms/kml/kml-catalog/
Ex. Recent surface reports mapped

## Slide 11: RSS
Warning bulletins are exceptions; their updates are provided in RSS. That is because the frequency is much lower, and all messages are plain text that is displayable by common RSS reader software. You can browse and subscribe to warnings listed at http://www.wis-jma.go.jp/cms/warning/warning-catalog/

## Slide 12: Subscription
JMA provide interactive web interface to generate sample shell script for linux (or powershell script for windows) to download data automatically.
GISC Tokyo
User
http://www.wis-jma.go.jp/data/subscribe

## Slide 13: Access Analysis
GISC Tokyo has been analyzing condition of user access by using some applications.

## Slide 14: Thank you!
http://www.jma.go.jp/jma/indexe.html